DECmate II CP/M Technical Notes















    				  DISCLAIMER

		This document file was created by scanning  the 
		original  document and then editing the scanned 
		text.  As much as possible, the  original  text 
		format  was restored.  Some format changes were 
		made to insure this  document  would  print  on 
		current laser printers using 60 lines per page.
    		The  original  spelling  and  grammar  has been 
    		preserved.


		30-Mar-1996














							       30-June-83


		       DECmate II CP/M Technical Note Index


	_________________________________________________________________

							           CP/M
	No  Title				     Revision     Release	__  _____				     ________     _______

	 1  Z80 Memory Map			     0, 16-Sep-82   1.0

	 2  RX50 Diskette Format		     3, 22-Dec-82   1.0

	 3  8BIOS Interface Codes		     7, 07-Oct-82   1.0

	 4     (withdrawn)

	 5  CP/M Support for RD51D		     1, 17-Mar-83   2.x

	 6  RX50 Diskette Format for CP/M Release 2  0, 11-Feb-83   2.x

	 7  8BIOS Interface Codes for Release 2	     4, 20-Jun-83   2.x

	 8     (withdrawn)

	 9  System Bootstrap Operation		     1, 20-Jun-83   2.x

	10  Z80 memory Map for Release 2	     0, 19-Apr-83   2.x

	11  Console Standard Modes for Release 2     0, 20-Jun-83   2.x

	12  Format of Hard Disk Backup Diskettes     0, 27-Jun-83

	13  Loading and Using Extensions to 8BIOS    0, 30-Jun-83   2.x






	R.F.Morse
	MLO3-2/E41
	DTN 223-6720


							 Rev 0, 16-Sep-82



			DECmate II CP/M Technical Note 1:

	
				  Z80 Memory Map

	_________________________________________________________________


	This note describes the allocation of the 65536. (64K) bytes of
	memory in the Z80 APU when operating under CP/M-80 version 2.2.


		 Usage		   Addresses	      Length		 _____		   _________	      ______

		 System parms	   0000..00FF	    100    256.
		 TPA		   0100..DFFF	   DF00  57088.
		 CCP		   E000..E7FF	    800   2048.
		 BDOS		   E800..F5FF	    E00   3584.
		 BIOS code	   F600..FBFF	    600   1536.
		 BIOS work area    FC00..FFFF 	    400   1024.

	When generating a CP/M image with the MOVCPM program, this is 
	described as a 63K system.		       __

	Application programs occupy the transient program area (TPA).
	Large application programs usually overlay the CCP (console
	command processor), so the limit on their size is 59136. bytes.

	This map is for the initial release of the system which supports
	RX50 and RX01/RX02 diskettes.  The release which supports the
	RD50 Winchester disk will probably require additional space for 
	the BIOS code and work areas, which will reduce the TPA size by
	1024. (1K) bytes.

	None of the storage in the 6120 side of the system is directly
	available to a CP/M application program.  (Extensive amounts of
	this storage are used by the 8BIOS program which supports ZBIOS.)



							 Rev 3, 22-Dec-82



			DECmate II CP/M Technical Note 2:


			      RX50 Diskette Format

	_________________________________________________________________

	This note describes the format and contents of the RX50 diskettes
	used by the DECmate II version of the CP/M-80 operating system.
	The description of the size, location and contents of the
	CPMIMAGE.SYS file on a system disk applies to version 1.0 for
	RX50-based systems.

	The RX50 diskette is a 5 1/4", soft-sectored, single-sided,
	double-density diskette with a track spacing of 96 tracks per
	inch.  The arrangement of address marks, sector headers, data 
	fields and gaps is that used by the 1793 LSI controller chip.  A
	diskette contains 80 tracks, numbered 0 through 79.  Each track
	contains 10 512-byte sectors, numbered 1 through 10.  This gives
	a capacity of 5,120 (5K) bytes per track and 409,600 (400K) bytes
	per diskette.

	When used for CP/M, these diskettes may be either system or data							  ______    ____
	disks.  A system disk contains the CP/M operating system and the
	necessary supporting files to allow it to be bootstrap loaded
	into an idle machine.  A data disk contains only CP/M files and
	cannot be bootstrap loaded.  The first 12 bytes of track 1,
	sector 1 are coded to mark these as CP/M disks and to distinguish
	system from data disks.  The DECmate II hardware bootstrap loader
	tests these bytes and will not attempt to load a non-system disk.


	Track usage	___________

	Tracks on a diskette are used as follows:

	     Tracks  Use	     ______  ___

	       0     On a system disk:  data for the SETUP screen,
		     keyboard map, and special user-defined display
		     character sets.  On a data disk:  sector 1 is
		     zero-filled to prevent any attempt to store SETUP
		     data on the disk and sectors 2..10 are undefined.

	       1     On a system disk:  bootstrap program to load the
		     system into an idle machine.  On a data disk:
		     sector 1 is coded to mark it as a CP/M data disk and
		     sectors 2..10 are undefined.

	     2..79   CP/M directory and data area.  These 78 tracks are
		     controlled by CP/M's file system.  They begin with a
		     128-entry CP/M directory and contain program and
		     data files.  On a system disk, the first directory
		     entry describes a protected file named CPMIMAGE.SYS

	RX50 Diskette Format					  Page 2
	_________________________________________________________________


		     which occupies tracks 75..79 and contains the CP/M
		     system image and the extended DECmate firmware.  On
		     a data disk, all 78 tracks are usable for CP/M
		     files.


	Record addressing	_________________

	The CP/M file system always transfers data to and from its
	callers in 128-byte records.  Four such records are recorded in			    _______
	each 512-byte sector on an RX50 diskette.  The blocking and
	deblocking of records is performed by the Z80 portion of the BIOS
	(called ZBIOS; its companion on the 6120 part of the machine is
	called 8BIOS).  From the CP/M point of view, a diskette contains
	78 tracks numbered 2 through 79 and each track contains 40
	records numbered 0 through 39.  These two parameters--track 
	[2..79] and record[0..39]-- are passed by BDOS to the BIOS SETTRK
	and SETSEC routines, respectively.  The ZBIOS code divides the 
	CP/M record number by four and adds one to get the (l-origin)
	physical sector number.  The remainder of this division is
	multiplied by 128 to get the offset to the start of the record
	within the sector.

	Since the BIOS and disk controller cannot access physically
	consecutive sectors without waiting for an extra revolution of
	the disk, an interleave scheme is used to map logical sectors
	into non-consecutive physical ones.  An every-other-sector (2:1)
	interleave is used, as shown in the following table:

		      Logical      Physical
		      sector	    sector		      _______	   ________
			 1	       1
			 2	       3
			 3	       5
			 4	       7
			 5	       9
			 6             2
			 7	       4
			 8	       6
			 9	       8
			10	      10

	Since there are four CP/M records in each sector, records 0..3
	are placed in physical sector 1, records 4..7 in sector 3, and so
	on.  The actual sector translation table in ZBIOS (whose address
	is in the DPH and is used by the SECTRAN routine in the BIOS)
	operates on record numbers.  It contains 40 entries to convert a 
	0-origin record number into a 0-origin interleaved record number.
	Thus its first eight entries are as follows:

	RX50 Diskette Format					  Page 3
	_________________________________________________________________



		      Logical      Interleaved
		      record	      record		      _______	   ___________
			 0		 0
			 1		 1
			 2		 2
			 3		 3
			 4		 8
			 5		 9
			 6		10
			 7	 	11
			 8		16
			 9		17
				etc.

	There is no track-to-track skew in this system; physical sector 1
	is the first logical sector on every CP/M track

	
	Space allocation	________________

	Space in the CP/M area is subdivided into allocation blocks which
	contain 2K bytes (16 records) each.  The 78 tracks of the area
	hold 390K bytes, so there are 195 allocation blocks, numbered
	0..194.  Thus every file occupies space whose size is a multiple
	of 2K.


	File directory	______________

	The CP/M file directory has 128 entry positions of 32 bytes
	each.  These occupy allocation blocks 0 and 1, which are the
	first 32 records (8 sectors) of track 2.


	System image file	_________________

	Each CP/M system disk contains a file named CPMIMAGE.SYS which
	contains the CP/M system, ZBIOS, 8BIOS, and extended DECmate II
	firmware.  This file is always represented by the first entry in
	the directory.  To protect it from accidental damage and to
	prevent if from disrupting wild-card operations such as PIP *.*,
	it has the R/O and SYS attributes and it is assigned to user 15.
	The directory entry describes the file as occupying the last 12
	allocation blocks (numbers 183..194), or 24K bytes.  Physically,
	this comprises the last 8 logical sectors of track 75 and all of
	tracks 76..79.

	RX50 Diskette Format					  Page 4
	_________________________________________________________________



	The CPMIMAGE.SYS file is divided into three parts:

	     The CP/M-80 system image.  This comprises the CCP (2048	     ________________________
	     bytes), BDOS (3584 bytes), and ZBIOS (1536 bytes).  These 7K
	     bytes correspond to the standard image described in Digital
	     Research's "CP/M 2 Alteration Guide".  This data is stored
	     in standard interleaved file format and can be read and
	     written by any CP/M program (after conquering the R/O and
	     user 15 restrictions).

		  Note:  The first record of this file is the beginning
		  of the CCP.  This contains the command input buffer,
		  which can be patched with a command to be executed
	    	  automatically after bootstrap loading.  Be sure,
		  however, to rewrite the file IN PLACE--the boot loader
		  code expects to find the system image in the exact
		  sectors described above.

	     The 8BIOS image.  This is the code executed by the 6120	     _______________
	     processor.  All calls to ZBIOS for I/O services are passed
	     to 8BIOS, which has access the the DECmate's I/O devices.
	     It occupies the last 4 logical sectors of track 76 and all
	     of track 77.

	     DECmate firmware.  This code supports the DECmate II screen	     ________________
	     and keyboard handling.  It occupies all of tracks 78 and 79
	     and is loaded into the 6120's panel memory during bootstrap
	     loading.


	Diskette initialization	_______________________

	The CP/M utility program DISKINIT is used to initialize a
	diskette as either a system or data disk.  For system disks, it
	copies tracks 0, 1, and 75..79 from another system disk and writes
	a CP/M directory on track 2 whose first entry describes
	CPMIMAGE.SYS and whose remaining entries are unused,  For data
	disks, it writes dummy information in sector 1 of tracks 0 and 1
	and writes a CP/M directory on track 2 with all its entries
	unused.

	Note that any diskette to be used with the DECmate II must be
	physically formatted by its vendor with 10 512-byte sectors on
	each of 80 tracks.  The DECmate II disk controller cannot 
	rewrite a diskette's format data.

	RX50 Diskette Format					  Page 5
	_________________________________________________________________



	Interchange with other DEC systems	__________________________________

	The CP/M parameters used for the DECmate II RX50 diskettes are
	the same as those used by the Rainbow for its CP/M-80/86 and by
	the Professional for its CP/M-80.  To summarize, these parameters
	are:

	     1)  File area in tracks 2..79;
	     2)  Physical sector interleave sequence of
			   1,3,5,7,9,2,4,6,8,10;
	     3)  Allocation block size of 2K;
	     4)  Directory containing 128 entries.

	Any DECmate II CP/M disk--system or data--can be used as a data
	disk on a Rainbow or Professional CP/M system.  A DECmate II
	system disk cannot, of course, be bootstrap loaded as a system 
	disk on either of those systems.

	RX50 Diskette Format					  Page 6
	_________________________________________________________________


		    Appendix A:  Contents of System Image File


	A CP/M system disk has a bootstrap loader and system code stored	       ______
	in tracks 1 and 75 through 80.  The contents of each sector in
	those tracks is described below.  All references are to physical
	tracks (0..79) and 512-byte sectors (1..10).


	Secondary boot	______________

	The secondary boot code occupies one sector (track 1, sector 1).
	It is written in 12-bit mode and occupies 256 (octal 400) words.
	This is the code which is brought in by the firmware loader
	during a power-on boot, and its first few bytes contain the DEC
	standard boot-block code which marks a CP/M system disk.  The
	secondary boot code source file is called BOOT2.


	Tertiary boot	_____________

	The tertiary boot code occupies two sectors (track 1, sectors 2
	and 3).  It is written in 12-bit mode and occupies 512 (octal
	100) words.  This code is loaded into field 7 by the secondary
	boot, and it reads the actual 8BIOS code into fields 0 and 1.
	The tertiary boot code source file is called BOOT3.


	8BIOS	_____

	The 8BIOS code occupies 18 sectors on parts of tracks 1, 77 and
	76.  It is written in packed mode (two words in each three bytes)
	and is 6144 (octal 14000) words long.  This code is loaded into 
	fields 0 and 1 by the tertiary boot.  The tertiary boot contains
	the following table which determines which sectors are read and
	in what order:
			   Track     Sector			   _____     ______
			      1		 4    Start field 0
			      1		 6
			      1		 8
			      1		10
			      1		 5
			      1		 7
			      1		 9
			     77		 2
			     77		 4
			     77		 6
			     77		 8
			     77		10
			     77		 3    Start of field 1
			     77		 5
			     77		 7
			     77		 9
			     77		 1
			     76		 6

	RX50 Diskette Format					  Page 7
	_________________________________________________________________


	CP/M system image	_________________

	The CPM system image occupies 14 sectors on tracks 75 and 76 and
	is written in 8-bit mode.  It is 7168 bytes long and is
	subdivided into three parts:  CCP (4 sectors, 2048 bytes), BDOS
	(7 sectors, 3584 bytes), and ZBIOS (3 sectors, 1536 bytes).  The 
	sequence of sectors for this image must correspond to the first
	14 physical sectors (56 CP/M logical records) of the CPMIMAGE.SYS
	file, since the CP/M image is installed by using ordinary BDOS
	file I/O calls.

			   Track     Sector			   _____     ______
			     75		 5    CCP, 2048 bytes
			     75		 7
			     75		 9
			     75		 2
			     75		 4    BDOS, 3584 bytes
			     75		 6
			     75		 8
			     75		10
			     76		 1
			     76		 3
			     76		 5
			     76		 7    ZBIOS, 1536 bytes
			     76		 9
			     76		 2

	DECmate firmware	________________

	The extended firmware which is loaded into 6120 panel memory
	occupies all of tracks 78 and 79.


	Uncommitted sectors	___________________

	There are three uncommitted sectors on track 76.  Sector 4 can be
	used to add 512 bytes to ZBIOS and sectors 8 and 10 can be used
	to add 682 (octal 1252) words to 8BIOS, or all three sectors can
	be used to add 1024 (octal 2000) words to 8BIOS.

			Track     Sector			_____     ______
			  76	      4
			  76	      8
			  76	     10

	In order to use these to expand 8BIOS, the sector tables in the 
	tertiary boot BOOT3 and the utility program PUT234 which writes
	the code on a system diskette, must be modified accordingly.  In 
	order to expand ZBIOS, routines RDCPM and LODCPM in 8BIOS must be
	modified.


	R.F.Morse
	DTN 223-6720
	MLO3-2/E41
	

							 Rev 7, 07-Oct-82



			DECmate II CP/M Technical Note 3:


			      8BIOS Interface Codes

	_________________________________________________________________


	This technical note describes the interface codes used for
	commands sent from the Z80 CP/M BIOS to the 6120 8BIOS.  Each
	command consists of a 4-bit command code and an 8-bit data byte.				    ____________	      _________
	In a Z80 program, a command is sent by calling the OUTBYT routine
	in the BIOS.  Most commands cause 8BIOS to generate a status or
	data byte for return to the Z80, which is received by calling the
	INBYT routine.  Two additional routines, BLKRD and BLKWR,
	transmit blocks of data (such as disk sectors) from or to 8BIOS.

	Four special call entry points have been added to the CP/M BIOS
	entry vector to permit a CP/M program to send a command to 8BIOS
	and to receive a byte from 8BIOS.  They are:

	    OUTBYT  sends a command to 8BIOS.  Entry is at offset 003Fh
		    from the BIOS vector base (whose address is in memory
		    at 0001..0002h).  Call with the command code in the
		    low 4 bits of the C register and the data byte in the
		    B register.  Returns after sending the command; the A
 		    and F registers are destroyed.

            INBYT   receives a byte from 8BIOS.  Entry is at offset 003Ch
		    from the BIOS vector base.  There are no call 
		    arguments.  Returns with the data from 8BIOS in the A
		    register with the Z and S flags set to reflect its
		    contents.  Alters no other registers.

	    BLKRD   receives a block of data from 8BIOS.  Entry is at
		    offset 0042h from the BIOS vector base.  Call with
		    the HL register addressing the first byte of the area
		    to receive the block.  On return, HL will address the
		    last byte filled, plus one.  The amount of data
		    transferred is controlled by 8BIOS (e.g. 512 bytes
		    for an RX50 disk sector or 128 bytes for an RX01
		    sector) and can be determined from the value returned
		    in HL.  Destroys registers A, B, C and F.

	    BLKWR   sends a block of data to 8BIOS.  Entry is at offset
		    0045h from the BIOS vector base.  Call with the HL
		    register addressing the first byte to be sent.  On
		    return, HL will address the last byte sent, plus one.
		    The amount of data transferred is controlled by
		    8BIOS, as described above for BLKRD.  Destroys
		    registers A, B, C and F.

	8BIOS Interface Codes					  Page 2
	_________________________________________________________________


	Commands	________

	The following table lists the command codes and their associated
	data bytes in numerical sequence.  Using an undefined code or
	code/data combination should result in no operation, but is not
	recommended!

	Code  Data  Description	____  ____  ___________

	 00    any  Signals that a Z80 "HALT" instruction has been
		    executed.  This code is generated by hardware on the 
		    Z80 board; it should not be used by software.

	 01    00   CP/M "cold boot" function.  Abandons the current
		    state of the Z80 and re-reads the CP/M system image
		    from the disk in drive A.  This replaces the stored
		    CP/M image (CCP, BIOS, and ZBIOS) for the Z80, but
		    does not reload the 8BIOS code.  A more complete			 ___
		    restart which reloads everything can be performed by
		    invoking function 02 0B to simulate a power-on reset.

	 01    01   CP/M "warm boot" function.  Must be followed by a 
	  	    call to BLKRD to read all of CCP and BIOS into Z80
		    storage.

	 01    02   Get keyboard status.  The following INBYT call will
		    return FFh if a character is available from the 
		    keyboard, or 00h if not.

	 01    03   Get printer output status.  The following INBYT call
		    will return FFh if the printer can accept an output
		    character, or 00h if not.

	 01    04   Get communication input.  The following INBYT call
		    will return the next incoming character from the 
		    communication port, waiting if necessary until one is
		    available.

	 01    05   Get keyboard input.  The following INBYT call will 
		    return the next character from the keyboard, waiting
		    if necessary until one is available.

	 01    06   Disk "home" request.  Sets the track number to 0 for
		    the next disk operation and purges any outstanding
	  	    read-ahead operation.  (Does not perform any physical
		    disk operation.)

	 01    07   Read disk sector.  Reads one sector from the
		    previously-selected drive, track and sector.  The
		    following INBYT will return 00h if the read was
		    successful, or a non-zero value if not.  If 
		    successful, a call to BLKRD must follow to transfer
		    the sector image into Z80 storage.  (BLKRD must not								    ___

	8BIOS Interface Codes					  Page 3
	_________________________________________________________________


		    be called if the read was unsuccessful!)

	 01    08   Unused.

	 01    09   Write disk sector.  Writes one sector to the
		    previously-selected drive, track and sector.  Must be
		    followed by a call to BLKWR to transfer the sector 
		    image to the 6120.  After the BLKWR call, INBYT must
		    be called.  It will return 00h if the write was
		    successful, or a non-zero value if not.

	 01    0A   Get disk type.  The following INBYT call will return
		    a code which indicates the format of the disk in the
		    previously-selected disk drive, as follows:

			00  RX01--8", single-density, 128-byte sectors,
			    26 sectors/track, 77 tracks;

			01  RX50--5", double-density, 512-byte sectors,
			    10 sectors/track, 80 tracks;

			02  VT180--5", double-density, 512-byte sectors,
			    9 sectors/track, 40 tracks;

			03  RX02--8", double-density, 256-byte sectors,
			    26 sectors/track, 77 tracks;

			04  Other--5", double-density, not RX50 or VT180
			    format (use function 02 10 to determine its
			    characteristics);

			FF  Drive not installed.

	 01    0B   Get screen output status.  Following INBYT call will
		    return FFh if ready to accept a character, or 00h if
		    not.

	 01    0C   Get printer input.  Following INBYT call will return
		    the next character from the printer input port,
		    waiting if necessary until one is available.

	 01    0D   Get printer input status.  Following INBYT call will
		    return FFh if a character is available from the 
		    printer input port, or 00h if not.

	 01    0E   Get communication output status.  Following INBYT
		    call will return FFh if the communication port can 
		    accept an output character, or 00h if not.

	 01    0F   Get communication input status.  Following INBYT call
		    will return FFh if a character is available from the 
		    communication input port, or 00h if not.

	 02    00   Enable communication XON/XOFF pacing.  XON and XOFF

	8BIOS Interface Codes					  Page 4
	_________________________________________________________________


		    characters received at the communication input port
		    will control communication output and will not be
		    available to a caller of function 01 04.  (This is
		    the default setting.)

	 02    01   Disable communication XON/XOFF pacing.  Received XON
		    and XOFF characters will not control communication 
		    output but will instead be passed to a caller of
		    function 01 04.

         02    02   Get modem status from communication port.  Following
		    INBYT call will return a byte whose low-order 4 bits
		    reflect the modem status, as follows ("one" indicates
		    a "true" value):

			bit 7--Set if any of bits 3..0 has changed since
			       the last request for modem status.
			bit 3--Ring indicator (CCITT 125)
			bit 2--Data carrier detect (CCITT 109)
			bit 1--Data set ready (CCITT 107)
			bit 0--Clear to send (CCITT 106)

	 02    03   Enable printer XON/XOFF pacing.  XON and XOFF
		    characters received at the printer input port will
		    control printer output and will not be available to a
		    caller of function 01 0C.  (This is the default
		    setting.)

	 02    04   Disable printer XON/XOFF pacing.  XON and XOFF
		    characters received at the printer input port will
		    not control printer output but will instead be passed
		    to a caller of function 01 0C.

	 02    05   Disable recognition of the SETUP key.  (The key will
		    be re-enabled at the next CP/M warm-start or by
		    function 02 0A.)

	 02    06   Send BREAK signal to communication output port.  A
		    second call to OUTBYT (with a command code of 0Ah)
		    sends a data byte whose value (0..255) specifies the
		    length of the break in units of 10 milliseconds (i.e.
		    a value of 1Ch gives a duration of 280 milliseconds).

	 02    07   Set modem control lines of communication port.  A
		    second call to OUTBYT (with a command code of 0Ah)
		    sends a data byte which is interpreted as follows:

		      bit 4--One asserts request to send (CCITT 105)			     ___
		      bit 3--One asserts data terminal ready (CCITT			     ___
			     108.2)
		      bit 2--One asserts signal rate select (CCITT 111)			     ___

	 02    08   Set communication baud rate.  A second call to OUTBYT
		    (with a command code of 0Ah) sends a data byte whose

	8BIOS Interface Codes					  Page 5
	_________________________________________________________________


		    low-order 4 bits are interpreted as follows:

			    00     50 bps	 08    1800
			    01     75		 09    2000
			    02    110		 0A    2400
			    03    134.5		 0B    3600
			    04    150		 0C    4800
			    05    300		 0D    7200
			    06    600		 0E    9600
			    07   1200		 0F   19200

		    Note:  The default value is set from the SETUP data
		    stored on the system disk.  If the rate is changed by
		    using function 02 08, that change cannot be detected
		    by SETUP, and any subsequent use of the SETUP menu
	   	    will change the baud rate back to that shown in the
		    menu.	    

	 02    09   Set printer port baud rate.  A second call to OUTBYT
		    (with a command code of 0Ah) sends a value as
		    described above for function 02 08.  The note 
		    concerning the use if SETUP also applies to the 
		    printer port.

	 02    0A   Enable SETUP key recognition.  This reverses the 
		    effect of function 02 05.

	 02    0B   Perform power-on reset.  Abandons the current state
		    of the machine and begins execution in the bootstrap
		    ROM as if power had just been turned on.

	 02    0C   Reset real-time clock.  Sets the time counter to
		    zero.

	 02    0D   Read real-time clock.  The real-time clock is a 
		    12-bit register which is incremented every 10
		    milliseconds and wraps around modulo 4096.  The value
		    is read in two INBYT calls.  The first returns the
		    high-order 4 bits of the counter in bits 3..0 (bits
		    7..4 are zero); the second returns the low-order 8 
		    bits of the counter.

	 02    0E   Get screen width.  The following INBYT call will
		    return a value of 00h if the screen width is 80
		    columns or 01h if it is 132 columns.

	 02    0F   Set communication character type.  A second call to 
		    OUTBYT (with a command code of 0Ah) sends a data byte
		    whose bits are interpreted as follows:

			bits 7..6  Number of data bits (exclusive of
				   parity bit):
					   00 -- 5 bits
					   01 -- 7 bits

	8BIOS Interface Codes					  Page 6
	_________________________________________________________________


					   10 -- 6 bits
					   11 -- 8 bits
			bits 5..4  Unused
			bits 3..2  Number of stop bits transmitted:
					   01 -- 1 stop bit
					   10 -- 1.5 stop bits
					   11 -- 2 stop bits
			bit 1      Parity sense (ignored if parity not
				   enabled):
					   0 -- ODD parity
					   1 -- EVEN parity
			Bit 0	   Parity enable:
					   0 -- disable
					   1 -- enable

		    Using this function reset the communication channel
		    and discards any pending input and output data.  The
		    mode after a system reset is 8 data bits, no parity
		    and 1 stop bit; this is not affected by the use of the
		    SETUP key.  This function does not alter the
		    communication channel's baud rate; function 02 08 does
		    that.

	 02    10   Get 5" diskette characteristics.  The next 4 INBYT
		    calls will return bytes which describe the physical
		    characteristics of the 5" disk selected by the most
		    recent call to function 06 (do not use for external
		    8" drives--no useful information can be returned).

			byte 1:  Sectors per track, a binary number in
				 the range 1..32 (01h..20h)
			byte 2:  Sector size code:
				      00h --  128 bytes
				      01h --  256 bytes
				      02h --  512 bytes
				      03h -- 1024 bytes
			byte 3:  Track density code:
				      00h -- 48 tpi
				      01h -- 96 tpi
			byte 4:  Two-sided flag:
				      00h -- single-sided
				      01h -- double-sided

	 02    11   Perform a print-screen operation.  Issuing this call
		    has the same effect as the operator's pressing the
		    "Print Screen" key.

	 02    12   Perform a setup operation.  Issuing this call has the
		    same effect as the operator's pressing the "Setup"
		    key.  This call will be ignored if SETUP recognition
		    has been disabled by function 02 05.

	 03   data  Send data character to the printer output port.

	8BIOS Interface Codes					  Page 7
	_________________________________________________________________


	 04   data  Send data character to the video screen.

	 05   data  Send data character to the communication output port.

	 06   data  Select disk drive.  "Data" is 00..03 for internal
		    RX50 drives and 04..07 for external RX01/RX02 drives.
		    A subsequent INBYT call will return 00h if the drive
		    is installed, or FFh if not.

	 07   data  Select disk track.  Two successive calls must be made
		    to send the 16-bit track number; the first call sends
		    the high-order byte.

	 08   data  Select disk sector.  Two successive calls must be
		    made to send the 16-bit sector number; the first call
		    sends the high-order byte.

	 09   data  Select disk head.  (Not presently used.)

	 0A   data  Block data output.  Used by the BLKWR routine and for
		    functions (such as 02 07) which require a data byte.


	The remaining command codes 0B..0F are not presently defined.



							 Rev 1, 17-Mar-83



			DECmate II CP/M Technical Note 5:


			CP/M Support for RD51D Hard Disk

	_________________________________________________________________


	This technical note describes modifications to the 8BIOS and
	ZBIOS modules of CP/M to accommodate the RD51D hard disk.  It 
	should be read in conjunction with the following documents:

	    1.  Programming the DECmate II for the RD51D Disk Subsystem		_______________________________________________________	

	    2.  DTN #7:  8BIOS Interface Codes for Release 2		____________________________________________

	    3.  CP/M 2 Alteration Guide (by Digital Research)		_____________________________________________


	CP/M Volumes on an RD51D	________________________

	A CP/M system may access up to four hard disk logical volumes at
	once, using disk drive letters "E" through "H".  The 8BIOS
	select-disk-drive function (command 06 xx) receives hex values
	04..07 for hard disk volumes and converts these to references to
	RD51D devices 0..3.  (devices 4 through 15 are not used by CP/M
	and should have no volumes mounted in them during CP/M 
	operation.)

	CP/M views each volume as being composed of tracks and sectors.
	Each track contains 64 logical sectors of 128 bytes, or 16
	physical sectors of 512 bytes.  Both logical and physical sectors
	are numbered beginning from 0.  The 8BIOS select-disk-sector
	function (command 08 xx) accepts physical sector numbers in the
	range 0..15; the select-disk-track function (command 07 xx)
	accepts track numbers in the range 0 through the volume size
	minus one.  (The volume size is found in the volume's directory
	entry in the two bytes beginning at offset 14.  Since this number
	represents units of 16 blocks, it is already scaled to CP/M track
	units.)  The 8BIOS select-disk-head function (command 09 xx) is
	not used.

	No sector interleave table is used by CP/M for hard disk volumes.

	The size of a CP/M volume may vary from 1 track (scarcely useful)
	to 1024 tracks (8 megabytes).  The size of the directory and the
	size of allocation blocks for the volume are computed as a 
	function of the volume size; this algorithm is described below.

	There are two types of CP/M volumes on an RD51D:  system and							  ______
	data.  These are distinguished by the byte at offset 17 in the	____

	CP/M Support for RD51D Hard Disk			  Page 2
	_________________________________________________________________


	volume's directory entry:

	     40h  Data volume.  The directory starts in block 0 and the		  ____
		  entire volume is usable for CP/M files.

	     C0h  System volume.  The first four tracks (blocks 0..63)		  ______
		  contain a bootable CP/M system, as follows:

		      Blocks  Contents		      ______  ________

			   0  System boot loader, written in 12-bit mode.
		       1..47  8BIOS code in compressed 8-bit format (this
			      area holds 16042 words, or just under four
			      fields).
		      48..51  CP/M's CCP (2048 bytes).
		      52..58  CP/M's BDOS (3584 bytes).
		      59..63  ZBIOS (up to 2560 bytes).

		  The directory begins at block 64, which is the first 
		  sector of track 4 from CP/M's point of view.

	
	Directory and allocation block sizes	____________________________________

	CP/M allocates the space on a volume to files in units called
	"allocation blocks" (ALB's).  The size of an allocation block
	varies, depending upon the size of the volume and the space
	available in the bit map area in the ZBIOS which is used by BDOS
	when the volume is logged on.  The ZBIOS contains a 1024-bit
	(128-byte) area (called the "allocation vector" or ALV) for each
	of the four devices assigned to the RD51D.  Therefore, the ALB
	size for a volume is chosen such that there will be no more than
	1024 ALB's on it.

	The CP/M directory occupies one or more consecutive ALB's
	beginning with ALB number 0.  Each entry in the directory
	describes a file (or an extent of a large file) and contains the
	numbers of the ALB's assigned to the file.  A directory entry
	occupies 32 bytes.

	The following table shows the ALB and directory sizes for the
	various ranges of volume sizes (note--these are the sizes after
	subtracting 32KB if the volume is a system volume):

	    Volume size   ALB size    Directory   ALB's for   ALB's per 
	    (kilobytes)  (kilobytes)   entries    directory     entry	    ___________  ___________  _________   _________   _________

	      16.. 256        1		  96	      3		  16
	     257.. 512	      2		 128	      2		  16
	     513..2048	      2		 256	      4		   8
	    2049..4096	      4		 384	      3		   8
	    4097..8192	      8		 512	      2		   8

	CP/M Support for RD51D Hard Disk			  Page 3
	_________________________________________________________________


	BIOS Data Tables	________________

	Two data tables in ZBIOS describe the characteristics of each
	CP/M disk device:  the "disk parameter header" (DPH) and the
	"disk parameter block" (DPB).  There is one DPH for each disk
	drive supported by the BIOS and there is one DPB for each
	different supported disk type and size.  Each DPH contains a
	pointer to the DPB which describes the disk currently mounted on
	the DPH's drive.  The contents of these are described in chapter
	10 of the CP/M 2 Alteration Guide.		  _______________________

	The DECmate II BIOS adds a 12-byte prefix to each DPH to describe
	some of the physical attribute of its device and to support
	CP/M's logical blocking/deblocking algorithm.  When a device is
	used to access an RD51D volume, the contents of these two tables
	must be adjusted to reflect the size of the mounted volume.  Data
	for the variable areas of these two blocks are set up by the
	8BIOS get-hard-disk-characteristics function (command 01 08) and
	passed to ZBIOS in two block transfers--a "D" record for the DPH
	prefix and a "P" record for the DPB.

	The D record contains 10 bytes which are moved into the prefix to	    ________
	the standard DPH.  These bytes are shown below (two-byte numeric
	values are stored low-order byte first):

	      Byte  Name    Contents	      ____  ____    ________

	      1     D_FLAG  Volume type:  81h if a CP/M volume; 00h
			    otherwise

	      2     D_TYP   Device type:  88h (constant)

	      3..4  D_BPS   Bytes per physical sector:  512 (constant)

	      5..6  D_SPT   Physical sectors per track:  16 (constant)

	      7..8  D_TPD   Number of tracks in the volume:  from the
			    volume's directory entry  (this value is
			    taken straight from the directory; it is not
			    adjusted for a "system" volume.)

	      9     D_SAB   Physical sectors per CP/M allocation block:
			    computed by the formula (ALB_SIZE * 2); this
			    value is meaningless for non CP/M volumes

	      10    D_1PS   Number of first physical sector on a track:
			    0 (constant)

	The P record contains 15 bytes which constitute a complete DPB.	    ________
	Several of these are derived from ALB_SIZE, which is the CP/M
	allocation block size expressed as a number of kilobytes.
	ALB_SIZE has one of the five values 1, 2, 4, 8 or 16.  The bytes
	in a P record are shown below (two-byte numeric values are stored
	low_order byte first):

	CP/M Support for RD51D Hard Disk			  Page 4
	_________________________________________________________________


	      Byte  Name    Contents	      ____  ____    ________

	      1..2  P_SPT   Logical sectors per track:  64 (constant)

	      3     P_BSH   Block shift factor:  the number of bits in
			    P_BLM

	      4     P_BLM   Allocation block mask:  (ALB_SIZE * 8) - 1
			    This is the number of 128-byte records in an
			    allocation block, minus 1.

	      5     P_EXM   Extent mask:  depends upon the allocation
			    block size and the number of allocation 
			    blocks in the volume, thus:
				if P_DSM < 256
				    then P_EXM - P_BLM shr 3
				    else P_EXM - P_BLM shr 4
			    where "shr" is a right-shift operation which
			    fills the vacated high-order bits with zeros.

	      6..7  P_DSM   Number of allocation blocks in the volume,
			    minus one (i.e. the highest ALB number)

 	      8..9  P_DRM   Number of directory entries, minus one.  This
			    must agree with the size implied by the
			    number of ALB's assigned to the directory in
			    P_ALD, below.  There are 32 entries per 
			    kilobyte.

	    10..11  P_ALD   Sixteen-bit map to reserve allocation blocks
			    for the directory.  Bits are set, beginning
			    with the high-order bit of byte 10 and
			    proceeding toward the low-order bit of byte
			    11, one for each ALB used for the directory.
			    For example, a volume with ALB_SIZE = 2K and
			    256 directory entries uses the first 4 ALB's
			    for the directory, so the bytes of P_ALD are
			    F0h, 00h and P_DRM is 255.

	    12..13  P_CKS   Directory checksum area size.  Not used for
			    RD51D volumes; always 0.

	    14..15  P-OFF   Offset to the track upon which the first ALB
			    starts.  0 for an RD51D data volume; 4 for a 
			    system volume.


	Non-CP/M Volume Access	______________________

	Non-CP/M volumes can be accessed by a CP/M program by using
	direct calls to ZBIOS which address physical sectors and transfer
	data in 512-byte blocks.  such a volume cannot be accessed via
	normal BDOS calls.  The 8-megabyte volume size limit does not
	apply to non-CP/M volumes.

	CP/M Support for RD51D Hard Disk			  Page 5
	_________________________________________________________________


	8BIOS Functions	_______________

	The following 8BIOS functions are used for both diskettes and
	hard disk volumes:

		 06  xx  Select disk drive
		 07  xx  Select disk track
		 08  xx  Select disk sector
		 01  06  Home (selects track 0)

		 01  07  Read disk sector
		 01  09  Write disk sector

		 01  0A  Get disk type code (code 88h has been added for
			 hard disk devices)

	Function 02 10, get diskette characteristics, may be used only
	for 5 1/4" diskettes.  Attempting to use it for 8" diskettes or a
	hard disk device will return useless bytes.

	The following new functions have been added to support the RD51D:

		 01  08  Get hard disk characteristics.  Returns DPH and			 _____________________________
			 DPB data to fill in tables in ZBIOS to reflect
			 the dimensions of the volume on the currently
			 selected device.  After sending this function 
			 code to 8BIOS, the caller must issue two BLDRD
			 calls:  the first returns a 10-byte D record and
			 the second returns a 15-byte P record.

		 02  1F  Execute RD51D command.  This is a general			 _____________________
			 function to allow a Z80 program to execute any
			 RD51D command.  After sending this function
			 code, the program must issue one OUTBYT call to
			 send the right 8 bits of the controller command
			 code (the high 4 bits are always 0).  The
			 program must then call either BLDRD or BLDWRT to
			 transfer the data required by the command.  The 
			 direction of the transfer and the number of
			 bytes transferred depend upon the command.
			 Following the block transfer, the program must 
			 issue one INBYT call to receive the error code
			 from the RD51D (0 indicates no error).

			 Note:  This call does not properly handle SET
			 block and SET PHYSICAL ADDRESS commands; these
			 require 12-bit values.  This problem is to be
			 resolved.



	R.F.Morse
	DTN 223-6720
	MLO3-2/E41

							 Rev 0, 11-Feb-83



			DECmate II CP/M Technical Note 6:


		     RX50 Diskette Format for CP/M Release 2

	_________________________________________________________________

	This note describes the format and contents of the RX50 diskettes
	used by the DECmate II version of the CP/M-80 operating system.
	The description of the size, location and contents of the
	CPMIMAGE.SYS file on a system disk applies to CP/M Release 2 for
	RX50-based systems.

	The RX50 diskette is a 5 1/4", soft-sectored, single-sided,
	double-density diskette with a track spacing of 96 tracks per
	inch.  The arrangement of address marks, sector headers, data 
	fields and gaps is that used by the 1793 LSI controller chip.  A
	diskette contains 80 tracks, numbered 0 through 79.  Each track
	contains 10 512-byte sectors, numbered 1 through 10.  This gives
	a capacity of 5,120 (5K) bytes per track and 409,600 (400K) bytes
	per diskette.

	When used for CP/M, these diskettes may be either system or data							  ______    ____
	disks.  A system disk contains the CP/M operating system and the
	necessary supporting files to allow it to be bootstrap loaded
	into an idle machine.  A data disk contains only CP/M files and
	cannot be bootstrap loaded.  The first 12 bytes of track 1,
	sector 1 are coded to mark these as CP/M disks and to distinguish
	system from data disks.  The DECmate II hardware bootstrap loader
	tests these bytes and will not attempt to load a non-system disk.


	Track usage	___________

	Tracks on a diskette are used as follows:

	     Tracks  Use	     ______  ___

	       0     On a system disk:  data for the SETUP screen,
		     keyboard map, and special user-defined display
		     character sets.  On a data disk:  sector 1 is
		     zero-filled to prevent any attempt to store SETUP
		     data on the disk and sectors 2..10 are undefined.

	       1     On a system disk:  bootstrap program to load the
		     system into an idle machine.  On a data disk:
		     sector 1 is coded to mark it as a CP/M data disk and
		     sectors 2..10 are undefined.

	     2..79   CP/M directory and data area.  These 78 tracks are
		     controlled by CP/M's file system.  They begin with a
		     128-entry CP/M directory and contain program and
		     data files.  On a system disk, the first directory
		     entry describes a protected file named CPMIMAGE.SYS

	RX50 Diskette Format for CP/M Release 2			  Page 2
	_________________________________________________________________


		     which occupies tracks 74..79 and contains the CP/M
		     system image and the extended DECmate firmware.  On
		     a data disk, all 78 tracks are usable for CP/M
		     files.


	Record addressing	_________________

	The CP/M file system always transfers data to and from its
	callers in 128-byte records.  Four such records are recorded in			    _______
	each 512-byte sector on an RX50 diskette.  The blocking and
	deblocking of records is performed by the Z80 portion of the BIOS
	(called ZBIOS; its companion on the 6120 part of the machine is
	called 8BIOS).  From the CP/M point of view, a diskette contains
	78 tracks numbered 2 through 79 and each track contains 40
	records numbered 0 through 39.  These two parameters--track 
	[2..79] and record[0..39]--are passed by BDOS to the BIOS SETTRK
	and SETSEC routines, respectively.  The ZBIOS codes divides the 
	CP/M record number by four and adds one to get the (l-origin)
	physical sector number.  The remainder of this division is
	multiplied by 128 to get the offset to the start of the record
	within a sector.

	Since the BIOS and disk controller cannot access physically
	consecutive sectors without waiting for an extra revolution of
	the disk, an interleave scheme is used to map logical sectors
	into non-consecutive physical ones.  An every-other-sector (2:1)
	interleave is used, as shown in the following table:

		      Logical      Physical
		      sector	    sector		      ______	    ______
			 1	       1
			 2	       3
			 3	       5
			 4	       7
			 5	       9
			 6             2
			 7	       4
			 8	       6
			 9	       8
			10	      10

	Since there are four CP/M records in each sector, records 0..3
	are placed in physical sector 1, records 4..7 in sector 3, and so
	on.  The actual sector translation table in ZBIOS (whose address
	is in the DPH and is used by the SECTRAN routine in the BIOS)
	operates on record numbers.  It contains 40 entries to convert a 
	0-origin record number into a 0-origin interleaved record number.
	Thus its first eight entries are as follows:

	RX50 Diskette Format for CP/M Release 2			  Page 3
	_________________________________________________________________



		      Logical      Interleaved
		      record	      record		      ______	   ___________
			 0		 0
			 1		 1
			 2		 2
			 3		 3
			 4		 8
			 5		 9
			 6		10
			 7	 	11
			 8		16
			 9		17
				etc.

	There is no track-to-track skew in this system; physical sector 1
	is the first logical sector on every CP/M track

	
	Space allocation	________________

	Space in the CP/M area is subdivided into allocation blocks which
	contain 2K bytes (16 records) each.  The 78 tracks of the area
	hold 390K bytes, so there are 195 allocation blocks, numbered
	0..194.  Thus every file occupies space whose size is a multiple
	of 2K.


	File directory	______________

	The CP/M file directory has 128 entry positions of 32 bytes each.
	These occupy allocation blocks 0 and 1, which are the first 32 
	records (8 sectors) of track 2.


	System image file	_________________

	Each CP/M system disk contains a file named CPMIMAGE.SYS which
	contains the CP/M system, ZBIOS, 8BIOS, and extended DECmate II
	firmware.  This file is always represented by the first entry in
	the directory.  To protect it from accidental damage and to
	prevent if from disrupting wild-card operations such as PIP *.*,
	it has the R/O and SYS attributes and it is assigned to user 15.
	The directory entry describes the file as occupying the last 15
	allocation blocks (numbers 180..194), or 30K bytes.  Physically,
	this comprises all of tracks 74 through 79.

	RX50 Diskette Format for CP/M Release 2			  Page 4
	_________________________________________________________________



	The CPMIMAGE.SYS file is divided into three parts:

	     The CP/M-80 system image.  This comprises the CCP (2048	     ________________________
	     bytes), BDOS (3584 bytes), and ZBIOS (2048 bytes).  These 
	     7.5K bytes correspond to the standard image described in 
	     Digital Research's "CP/M 2 Alteration Guide".  This data is 
	     stored in standard interleaved file format and can be read 
	     and written by any CP/M program (after conquering the R/O
	     and user 15 restrictions).

		  Note:  The first record of this file is the beginning
		  of the CCP.  This contains the command input buffer,
		  which can be patched with a command to be executed
	    	  automatically after bootstrap loading.  Be sure,
		  however, to rewrite the file IN PLACE--the boot loader
		  code expects to find the system image in the exact
		  sectors described above.

	     The 8BIOS image.  This is the code executed by the 6120	     _______________
	     processor.  All calls to ZBIOS for I/O services are passed
	     to 8BIOS, which has access the the DECmate's I/O devices.
	     It occupies parts of tracks 1, 75, 76 and 77 (see Appendix
	     A).

	     DECmate firmware.  This code supports the DECmate II screen	     ________________
	     and keyboard handling.  It occupies all of tracks 78 and 79
	     and is loaded in to the 6120's panel memory during bootstrap
	     loading.


	Diskette initialization	_______________________

	The CP/M utility program DISKINIT is used to initialize a
	diskette as either a system or data disk.  For system disks, it
	copies tracks 0, 1 and 74..79 from another system disk and writes
	a CP/M directory on track 2 whose first entry describes
	CPMIMAGE.SYS and whose remaining entries are unused,  For data
	disks, it writes dummy information in sector 1 of tracks 0 and 1
	and writes a CP/M directory on track 2 with all its entries
	unused.

	Note that any diskette to be used with the DECmate II must be
	physically formatted by its vendor with 10 512-byte sectors on
	each of 80 tracks.  The DECmate II disk controller cannot rewrite
	a diskette's format data.

	RX50 Diskette Format for CP/M Release 2			  Page 5
	_________________________________________________________________



	Interchange with other DEC systems	__________________________________

	The CP/M parameters used for the DECmate II RX50 diskettes are
	the same as those used by the Rainbow for its CP/M-80/86 and by
	the Professional for its CP/M-80.  To summarize, these parameters
	are:

	     1)  File area in tracks 2..79;
	     2)  Physical sector interleave sequence of
			   1,3,5,7,9,2,4,6,8,10;
	     3)  Allocation block size of 2K;
	     4)  Directory containing 128 entries.

	Any DECmate II CP/M disk--system or data--can be used as a data
	disk on a Rainbow or Professional CP/M system.  A DECmate II
	system disk cannot, of course, be bootstrap loaded as a system 
	disk on either of those systems.

	RX50 Diskette Format for CP/M Release 2			  Page 6
	_________________________________________________________________


		    Appendix A:  Contents of System Image File


	A CP/M system disk has a bootstrap loader and system code stored	       ______
	in tracks 1 and 74 through 80.  The contents of each sector in
	those tracks is described below.  All references are to physical
	tracks (0..79) and 512-byte sectors (1..10).


	Secondary boot	______________

	The secondary boot code occupies one sector (track 1, sector 1).
	It is written in 12-bit mode and occupies 256 (octal 400) words.
	This is the code which is brought in by the firmware loader
	during a power-on boot, and its first few bytes contain the DEC
	standard boot-block code which marks a CP/M system disk.  The
	secondary boot code source file is called BOOT2.


	Tertiary boot	_____________

	The tertiary boot code occupies two sectors (track 1, sectors 2
	and 3).  It is written in 12-bit mode and occupies 512 (octal
	1000) words.  This code is loaded into field 7 by the secondary
	boot, and it reads the actual 8BIOS code into fields 0, 1 and 2.
	The tertiary boot code source file is called BOOT3.


	8BIOS	_____

	The 8BIOS code occupies 30 sectors on parts of tracks 1, 77, 76 
	and 75.  It is written in packed mode (two words in each three 
	bytes) and is 10240 (octal 24000) words long.  This code is 
	loaded into fields 0, 1 and 2 by the tertiary boot.  The tertiary 
	boot contains the following table which determines which sectors 
	are read and in what order:

	RX50 Diskette Format for CP/M Release 2			  Page 7
	_________________________________________________________________


			   Track     Sector			   _____     ______
			      1		 4    Start field 0
			      1		 6
			      1		 8
			      1		10
			      1		 5
			      1		 7
			      1		 9
			     77		 2
			     77		 4
			     77		 6
			     77		 8
			     77		10

			     77		 3    Start of field 1
			     77		 5
			     77		 7
			     77		 9
			     77		 1
			     76		 4
			     76		 6
			     76		 8
			     76		10
			     76		 2
			     76		 5
			     76		 7

			     76		 9    Start of field 2
			     76		 1
			     76		 3
			     75		 6
			     75		 8
			     75		10

		       Table A-1.  8BIOS Image Sector Map


	CP/M system image	_________________

	The CPM system image occupies 15 sectors on tracks 74 and 75 and
	is written in 8-bit mode.  It is 7680 bytes long and is
	subdivided into three parts:  CCP (4 sectors, 2048 bytes), BDOS
	(7 sectors, 3584 bytes), and ZBIOS (4 sectors, 2048 bytes).  The 
	sequence of sectors for this image must correspond to the first
	15 physical sectors (60 CP/M logical records) of the CPMIMAGE.SYS
	file, since the CP/M image is installed by using ordinary BDOS
	file I/O calls.

	RX50 Diskette Format for CP/M Release 2			  Page 8
	_________________________________________________________________


			   Track     Sector			   _____     ______

			     74		 1    CCP, 2048 bytes
			     74		 3
			     74		 5
			     74		 7

			     74		 9    BDOS, 3584 bytes
			     74		 2
			     74		 4
			     74		 6
			     74		 8
			     74		10
			     75		 1

			     75		 3    ZBIOS, 2048 bytes
			     75		 5
			     75		 7
			     75		 9

		       Table A-2.  ZBIOS Image Sector Map


	DECmate firmware	________________

	The extended firmware which is loaded into 6120 panel memory
	occupies all of tracks 78 and 79.


	Uncommitted sectors	___________________

	There are two uncommitted sectors on track 75.  Sectors 2 and 4 
	can be used to add 682 (octal 1252) words to 8BIOS, or 1024 bytes 
	to ZBIOS or can be split between them.

			Track     Sector			_____     ______
			  75	      2
			  75	      4

	In order to use these to expand 8BIOS, the sector tables in the 
	tertiary boot BOOT3 and the utility program PUT234 which writes
	the code on a system diskette, must be modified accordingly.  In 
	order to expand ZBIOS, routines RDCPM and LODCPM in 8BIOS must be
	modified.


	R.F.Morse
	DTN 223-6720
	MLO3-2/E41
	

							 Rev 7, 20-Jun-83



			DECmate II CP/M Technical Note 7:


		       8BIOS Interface Codes for Release 2

	_________________________________________________________________





	This Tech Note has not been found -- yet.

							 Rev 1, 20-Jun-83


			DECmate II CP/M Technical Note 9:


			   System Bootstrap Operation

	_________________________________________________________________


	This note describes the operation of the DECmate II system
	bootstrap under three conditions:

	    -- At power-on,
	    -- when Remove and Do are pressed while the SETUP screen is
	       displayed,
	    -- When the panel request instruction PR3, 6 is issued.

	This description applies to systems which have panel code ROM
	chips at level 19 or greater.  These support the optional RD51D
	hard disk system as well as the standard RX50 diskette drive.


	Power-on	________

	When system power is turned on, the ROM code first does basic
	system checks (these result in the screen patterns full of "U"
	and "a"), and then searches for a bootable system disk in either
	RX50 drive 0 or (if installed) on the RD51 hard disk.  This 
	power-on boot search operates as follows:	____________________

	     REPEAT

		  IF RX50 drive 0 is ready
			    AND track 1 sector 1 has bootable-disk code
			    AND track 0 sector 1 has valid firmware
		       THEN attempt to load the system firmware and the
				      operating system from diskette
		       ELSE display the flashing diskette picture.

		  IF RD51 is installed and ready
			    AND block 0 indicates valid firmware
			    AND there is a volume marked with the
				      "startup" flag which is bootable
		       THEN load the system firmware, mount the startup
				      volume on device 0, and attempt to
				      load the operating system from it.

	     UNTIL a system is successfully loaded.

	For a system which does not have an RD51, this simply attempts to
	boot from RX50 drive 0 until a valid bootable disk is inserted.
	For a system with both RX50 and RD51 drives, it will boot from

	System Bootstrap Operation				  Page 2
	_________________________________________________________________


	whichever becomes ready first.  Thus, if the RD51 has a valid
	startup volume and no diskette is in drive 0, the RD51 will be
	booted.  If there is a bootable diskette in drive 0, it will be
	used in preference to the RD51.  The normal spinup delay of 15 to
	20 seconds for the RD51 gives ample time to insert a diskette and
	close its door to preempt a hard-disk boot.

	
	REMOVE option of SETUP	______________________

	When the standard system SETUP screen is displayed, pressing the
	Remove and Do keys initiates a power-on boot search operation				       ____________________
	exactly as described above for power-on.  Thus if a user has been
	running from the RD51 and wishes to change to a diskette-resident
	system (e.g. WPS), he can do this by entering SETUP, inserting
	the WPS system disk in diskette drive 0, and pressing Remove and
	Do.  Conversely, if he wishes to go from a diskette-resident
	system to the RD51, he need only be sure that diskette drive 0 is
	not ready (door open) before pressing Remove and Do.


	Panel Request 3	_______________

	Function 6 of panel request 3 is invoked by the following 6120
	instruction sequence:

			    PR3
			    0006
			    -1

	The action performed depends upon the contents of the
	accumulator, as follow:

		  AC   Action		  __   ______
		   0   Display the SETUP screen
		  -1   Display the 6120 HALT screen
		  -2   Attempt to boot from RX50 drive 0
		  -3   Attempt to boot from the RD51 volume presently
		       mounted on logical device 0.

	If either boot attempt fails, the system then goes to the 
	power-on boot search process described above.

	Warning:  This PRQ should not be used to change between	_______			  ___
	diskette-loaded and hard-disk-loaded systems.  This is because
	the panel code firmware is not reloaded when this PRQ is issued.
	When the firmware was loaded, it noted which device--diskette or
	hard disk--it was loaded from, and thereafter always refers to

	System Bootstrap Operation				  Page 3
	_________________________________________________________________


	that device when the SETUP function is invoked.  Therefore, using
	PR3, 6 to change from, say, a diskette-based operating system to
	one loaded from the hard disk will not alter the firmware, which
	will still attempt to use the diskette for a SETUP operation.


	R.F.Morse
	DTN 233-6720
	MLO3-2/E41

							 Rev 0, 19-Apr-83



			DECmate II CP/M Technical Note 10:


			  Z80 Memory Map for Release 2

	_________________________________________________________________


	This note describes the allocation of the 65536. (64K) bytes of
	memory in the Z80 APU when operating under CP/M 2.2 release 2.
	There are two maps:  one for diskette-only systems and one for
	systems which support an RD51 hard Disk.

	Diskette-only system (nominal size of 63K):	____________________

		 Usage		   Addresses	      Length		 _____		   _________	      ______

		 System parms	   0000..00FF	    100    256.
		 TPA		   0100..DFFF	   DF00  57088.
		 CCP		   E000..E7FF	    800   2048.
		 BDOS		   E800..F5FF	    E00   3548.
		 BIOS code	   F600..FBFF	    600   1536.	    
		 BIOS work area    FC00..FFFF	    400   1024.


	Diskette and hard disk system (nominal size of 62K):	_____________________________

		 Usage		   Addresses	      Length		 _____		   _________	      ______

		 System parms	   0000..00FF	    100    256.
		 TPA		   0100..DBFF	   DB00  56064.
		 CCP		   DC00..E3FF	    800   2048.
		 BDOS		   E400..F1FF	    E00   3548.
		 BIOS code	   F200..F9FF	    800   2048.	    
		 BIOS work area    FA00..FFFF	    600   1536.

	Application programs occupy the transient program area (TPA).
	Large application programs usually overlay the CCP (console
	command processor), so the limit on their size is the sum of the
	sizes of the TPA and the CCP from the tables.
	
	The area described as "BIOS code" is loaded from the CP/M system
	image during a cold start.  It may actually have some work area
	at its end if the assembled code is smaller than the maximum.
	The top of the BIOS code cannot exceed address FD00 in any
	system, since the monitor program which transfers data from the 
	6102 to the Z80 during a cold start begins there.


	R.F.Morse
	DTN 223-6720
	MLO3-2/E41

							 Rev 0, 20-Jun-83



			DECmate II CP/M Technical Note 11:


		       Console Standard Modes for Release 2

	_________________________________________________________________

	This note describes what CP/M does upon cold starts and warm
	starts to set the console and keyboard to a standard state.  The
	large number of programmable operating modes, display character
	sets, and keyboard interpretations means that an application
	program can leave the system in such a state that it is difficult
	or impossible to enter a command to CP/M or to execute subsequent
	applications.  Therefore, the CP/M BIOS takes the steps described
	below whenever it receives control after initial loading (a "cold
	start") and after every application program ends (a "warm
	start").

	CP/M establishes the following conditions for the display:

	    -- USASCII character set
	    -- ANSI level 2 control sequences
	    -- 7-bit mode (insensitive to the high-order bit of any
		    character sent to the screen.
	    -- full-screen scrolling region
	    -- character-replace mode
	    -- no auto-wrap at the end of a line
	    -- line-feed mode (not new-line)
	    -- normal character rendition
	    -- cursor visible

	For the keyboard:

	    -- keyboard unlocked
	    -- top row function keys active
	    -- the three keys above the "+" key generate ESC, BS and LF
	    -- function keys emit the two-character CSI prefix "ESC ["
	    -- 7-bit mode
	    -- auto-repeat enabled
	    -- keypad in numeric mode
	    -- arrow keys generate cursor-positioning codes

	The following things are not changed:

  	    -- screen width
	    -- cursor style
	    -- keyclick
	    -- black or white screen background
	    -- scrolling speed
	    -- "caps lock" vs. "shift lock"
	    -- COMPOSE key activation

	Console Standard Modes for Release 2			  Page 2
	_________________________________________________________________


	    -- current case of the keyboard

	Note that the preceding means that two of the items on the SETUP
	screen are overridden by CP/M:  the cursor is made visible and the
	terminal mode is made ANSI (shown as "VT100" on the setup menu).

	Application programs may issue the appropriate control sequences
	to alter the display and keyboard features to suit themselves.
	In particular, a communication program may choose to change to
	full level 2 mode with 8-bit characters in order to emulate a
	VT2xx terminal, and a text processing program may use the full
	DEC multinational character set and 8-bit character codes.


	Warm start actions	__________________

	The following actions take place (in the order shown) whenever
	CP/M is initially loaded and whenever it reloads its console
	command processor (CCP) following the execution of an application
	program:

	    -- Enter ANSI mode (in case terminal is in VT52 mode)
			   ESC <

	    -- Terminate control string
			   ESC \

	    -- Select level 2 mode with 2-character CSI
			   ESC [ 6 2 ; 1 " p

 	    -- Enable keyboard auto-repeat
			   ESC [ ? 8 h

	    -- Make cursor visible
			   ESC [ ? 2 5 h

	    -- Activate the ESC, BS, and LF keys
			   PR3, 0010, -1  with AC=0000

	    -- Select 7-bit host mode
			   PR3, 0014, -1  with AC=0000


	(This sequence can be sent to the console at any time by calling
	the BIOS OUTBYT routine to send command 02 23, as described in
	DTN#7, 8BIOS Interface Codes.)	       _____________________


	Invoking 8-bit mode	___________________

	Application programs which wish to use the full 8-bit 
	capabilities of the terminal firmware must use an extended BIOS
	command (see DTN#7) to execute a panel request in the 6120.  To
	invoke 8-bit mode, send command 02 21 followed by the two
	hexadecimal data bytes 0C and 01 (this executes the instruction

	Console Standard Modes for Release 2			  Page 3
	_________________________________________________________________


	sequence PR3, 0014, -1  with 0001 in the AC).

	The ANSI sequence  ESC [ 6 2 ; 1 " p  which invokes level 2
	operation also sets all the top row function keys to generate
	multicharacter control sequences.  If the one-character ESC, BS,
	and LF codes are needed from the keys so labelled, the panel
	request listed above under warm start actions must be issued
	after sending the ANSI sequence.  This can be accomplished by	_____
	sending extended BIOS command 01 21 followed by data bytes 08 and
	00.

	
	Compatibility with CP/M release 1	_________________________________

	The standard console modes described above are generally the same 
	as those established by a warm start in CP/M release 1 for the
	DECmate II.  Release 2 is more thorough:  it also sets the
	character set to USASCII, turns off autowrap, and sets the
	scrolling region to full screen and absolute origin mode.  Unlike
	release 1, the case shift of the keyboard is not altered during a
	cold start.  This means that it will be lower-case if the system
	firmware was loaded as part of the cold start (as in loading from
	a diskette), but may be either case if CP/M was invoked from some
	other system (e.g. the master menu) in a Winchester environment.


	R.F.Morse
	DTN 223-6720
	MLO3-2/E41

							 Rev 0, 27-Jun-83



			DECmate II CP/M Technical Note 12:


		       Format of Hard Disk Backup Diskettes


	_________________________________________________________________


	This note describes the manner in which the contents of an RD51
	hard disk volume are transcribed to one or more RX50 diskettes to
	create a literal backup copy.  These backup diskettes are written
	by the "HD" utility program (both the Master Menu and CP/M
	versions) and are intended only for use by that program--they are
	not compatible with any operating system's file format.

	Each backup diskette contains up to 790 blocks from a hard disk
	volume.  As many diskettes as required by the volume's size are
	used, and all save the last diskette contain 790 blocks from the
	volume.  The diskettes are numbered in sequence, starting from 1.
	This sequence number and the number of diskettes used to hold the
	volume are recorded in a label record, whose contents are
	described below.


	Volume data arrangement	_______________________

	A volume is copied to diskettes by reading its blocks in
	ascending order from block 0 through block n-1, where n is the
	number of blocks in the volume.  Each group of 10 blocks is
	written onto one track of a diskette.  To enhance performance,
	the diskette sectors are written in an interleaved pattern which
	enables writing (or reading) a track in two revolutions.  The
	sequence of sector numbers is 1, 3, 5, 7, 9, 2, 4, 6, 8, 10.
	Thus, for example, hard disk block 0 is written into diskette
	sector 1, block 1 into sector 3, block 9 into sector 10, and
	block 10 into sector 1 of the next diskette track.

	Seventy-nine tracks of each diskette (except possibly the last)
	are used in descending track number sequence from track 79 down
	through track 2, and then track 0 (track 1 is reserved for the
	label).  This apparently perverse ordering is intended to reduce
	the chances that an operating system will recognize the first
	diskette of a backup copy as an OS-format diskette.

	The contents of the tracks of the last diskette of a backup set
	which are not required to hold volume data are unspecified.
	Likewise, the contents of the unused sectors in the last track of 
	the last diskette are also unspecified.

	Format of Hard Disk Backup Diskettes			  Page 2
	_________________________________________________________________


	Diskette labels	_______________

	A label record is written into sector 1 of track 1 of each backup
	diskette.  (Sectors 2 through 10 of track 1 are not used; their
	contents are unspecified.)  This label identifies the volume from
	which the backup was made and contains the date and time of the
	backup.  The label record is identical for every diskette of a
	backup set, except for the sequence number.  When a backup copy
	is read to restore it to a hard disk, the HD utility checks that
	all the diskette labels are identical in order to prevent mixing
	diskettes from backup copies made at different times.

	The contents of the label are described below.  Byte positions
	are given as decimal offsets from the beginning of the sector.
	All unused bytes (0..255 and 366..511) are binary zero.

	      Bytes      Contents	    _________  _____________

	     256..263  Signature pattern:  the 7 ASCII characters
				   "RDBackup" followed by a NULL

	     264..287  24-byte volume directory entry, exactly as read
				   from the hard disk's directory, except
				   as noted:
	     264..271      volume name
	     272..275      passwords
	     276..277      starting block--set to 0
	     278..279      volume size in units of 8K (low-order byte
				   first)
	          280      volume flags--set to hex 10 ("valid volume"
				   value)
		  281      OS-type flags
	     282..287      Miscellaneous data

	          288  Diskette sequence number:  8-bit unsigned binary,
				   beginning with 1
		  289  Number of diskettes in backup set:  8-bit unsigned
				   binary
	     290..298  Date of backup:  8 ASCII characters "mm/dd/yy"
				   followed by a NULL
	     299..304  Time of backup:  5 ASCII characters "hh:mm"
				   followed by a NULL
	     305..365  User's remark:  0 to 60 ASCII characters, the last
				   followed by a NULL



	R.F.Morse
	DTN 223-6720
	MLO3-2/E41


							Rev 0, 7/1/83 Fri



			DECmate II CP/M Technical Note 13:


		      Loading and Using Extensions to 8BIOS

	_________________________________________________________________

	This note describes the use of the 8BIOS reverse mini-monitor
	(RMM) by CP/M-80 application programs.  The RMM features are a
	part of release 2 of DECmate II CP/M 2.2.  The RMM is used to 
	load data to and from the 6120 program memory.  These data may be
	stored in either 8 or 12 bit modes; the data content is
	irrelevant to the RMM.

	Uses for such data may be

	    o   Program overlay storage for the Z80

	    o   Data storage for the Z80
	    
	    o   Additional BIOS functionality required by a CP/M
		application and not presently implemented by Digital

	For purposes of explanation, the reader is assumed to
	be familiar with DTN #7 - 8BIOS Interface Codes for Release 2 of
	DECmate II CP/M-80.  With reference to DTN #7 - there are nine
	8BIOS functions available for implementation of the RMM.  These
	are:

	02 17	 Set block transfer address
	02 18	 Set block transfer count

	02 19	 Block transfer to 6120 in 12-bit mode
	02 1A	 Block transfer to 6120 in 8-bit mode
	02 1B	 Block transfer from 6120 in 12-bit mode
	02 1C	 Block transfer from 6120 in 8-bit mode

	02 1D	 Start 6120 execution at transfer address
	02 1E	 Restore interrupt vector

	0A xx	 Reserved for user functions

	A thorough knowledge of PDP-8 architecture and programming is
	assumed by the user of the RMM if it is desired to add 8BIOS
	functionality by means of the RMM.  Guidelines for memory and
	interrupt usage are set forth in this note.

	Loading and Using Extensions to 8BIOS			  Page 2
	_________________________________________________________________


	Use of the RMM for data storage	_______________________________

	Regardless of the user's choice of data length (8-bit or 12-bit)
	the order of function calls remains the same.  To exchange a
	block of data between the Z80 and 6120 main memory, use the
	following procedure:

	    Set the 6120 transfer address - this is a 15-bit address
	    transferred in two bytes.

	    CAUTION -- the user is not protected from overwriting any				   ___
	    6120 memory area!  Consult the section in this note entitled
	    '6120 Memory Map'.

	    Set the 6120 transfer count - this is a positive 12-bit
	    number of bytes (or 12-bit words) to be transferred in this
	    block.  The minimum number of byte/words transferred per
	    block transfer allowed is one (1); maximum is 4096 decimal.
	    The transfer count function requires two data bytes to
	    describe the 12-bit count.  Note that a transfer count of
	    zero will result in a full field (4096) transfer.  Field
	    boundaries can not be crossed during a single block transfer
	    operation.  Attempts to do so will result in a wrap-around
	    within the field boundary described by the transfer address.

	    Request the block transfer function (either 8-bit or 12-bit
	    mode).  The next Z80 program function should be to perform a
	    BLKWRT (to move data from the Z80 to the 6120) or a BLKRD (to
	    move data from the 6120 to the Z80).  The 6120 counts the
	    number of transfers and terminates the block transfer.  Note
	    - the user program is responsible for initializing the Z80
	    for performing the BLKWRT or BLKRD (see DTN #7).

	Loading and Using Extensions to 8BIOS			  Page 3
	_________________________________________________________________


	6120 Memory Map	_______________

	Field    Octal Location(s)    Contents - Description	_________________________________________________________________

	  0	 0000-0200	      RESERVED - 8BIOS data storage
		 0201		      Address of communications interrupt
				      service routine (ISR)
		 0202		      Address of printer input ISR
		 0203		      Address of keyboard ISR
		 0204		      Address of printer output ISR
		 0205		      Address of modem ISR
		 0206		      Address of 100 Hz clock ISR
		 0207		      Address of function Axx CALL
		 0210		      Field of function Axx CALL
		 0211		      Interrupt Vector Terminator
		 0212-0221	      AVAILABLE for use by RMM for one				      _________			   ___
				      cross-field interrupt call
		 0222-7777	      RESERVED - 8BIOS program code and
				      stacks

	  1	 0000-7777	      RESERVED - 8BIOS program code

	  2	 0000-7777	      RESERVED - 8BIOS program code and
				      data storage

	  3	 0000-7777	      AVAILABLE for use by RMM				      _________

	  4	 0000-7777	      RESERVED - 8BIOS data storage

	  5	 0000-7777	      RESERVED - 8BIOS data storage

	  6	 0000-7777	      AVAILABLE for use by RMM				      _________

	  7	 0000-7777	      AVAILABLE for use by RMM				      _________



	Use of the 8BIOS Interrupt Vector	_________________________________

	There are eight fixed locations at the beginning of 8BIOS which
	contain the interrupt vector locations.  For users desiring to
	replace interrupt service code or to add additional BIOS
	functions, the following discussion is of interest.

	The interrupt vector resides in 6120 main memory field 0,
	beginning at location 201.  As described in the '6120 Memory
	Map', each location from 201 to 205 contains an address pointer
	into the beginning of reserved interrupt service routines.  The
	beginnings of each ISR must reside in field 0 of the 6120 memory.			       ____
	Once execution of an ISR begins in field 0, the user is free to
	transfer control into an AVAILABLE field for his/her own use as
	an alternative ISR.

	Loading and Using Extensions to 8BIOS			  Page 4
	_________________________________________________________________


	Room has been reserved from 0212-0221 for cross-field calls to a
	user supplied ISR.  Since it is expected that user-supplied ISRs
	will principally be used to augment communications support, only
	one reserved area has been made available in field 0 which does
	not require the user to overwrite a reserved portion of 8BIOS.
	If a second type of ISR must be supplied by the user, then it is
	at the user's discretion to overwrite a portion of 8BIOS code.
	That code is non-recoverable except by re-booting CP/M.

	Location 207 (octal) in the Interrupt Service Vector contains the
	address that the user wishes to transfer control to for
	extensions to 8BIOS through the use of Function Axx.  Location
	210 is used to hold the field (3, 6 or 7) that the Axx parser
	resides in.  The format for the field is 'X0' where 'X' is the
	field number, ie: 30 in location 210 means that the ISR resides
	in field 3.

	With reference to DTN #7, note that Function 1xx is broken into a
	main function (100 hex), and sixteen sub-functions (00 - 0F hex).
	When the Z80 program requests any function from 100h to 10Fh,
	8BIOS parses the two low order digits in the function call to
	determine the sub-function; then executes that function.  If
	additional data are required to be passed to or from the 6120 by
	the function (ie: Function 10A - Get Disk Type Code), then those
	data are sent and received as a part of the function, with
	control returning to the 8BIOS IDLE routine.

	Therefore, it is  up to the user to perform similar parsing for
	Function Axx.  If only one additional BIOS function is desired by
	the user, then the two low order digits passed (Axx) may be also							 __
	used to pass a byte of data to the user function.

	All Axx function parsing and processing; stack house-keeping and
	non Digital-supplied interrupt service is the responsibility of
	the user.

	When the user wishes to return to basic 8BIOS functionality, and
	the BIOS control path has not been disturbed (through use of
	Function 21D - Execute 6120 code), Function 21E (Restore
	Interrupt Vector) may be issued.  Function 21E replaces the
	present contents of the Interrupt Service Vector with the 
	original contents for locations 0201-0210.  All control and ISR
	structure is then returned to the Digital-supplied 8BIOS.

	WARNING - no flags, variables or locations are guaranteed to be
	preserved in any future releases of the DECmate II CP/M product
	unless specified within this document.


	Program Structure in 8BIOS	__________________________

	The BIOS code supplied by Digital makes use of the two data
	stacks available in the 6120.  Stack one is the CALL/RETURN

	Loading and Using Extensions to 8BIOS			  Page 5
	_________________________________________________________________

	
	stack; stack two is a DATA stack.  An important distinction is
	made between local routines and cross-field callable routines.		     ______________	_____________________________
	
	Local routines are those which reside in a given field, and can
	only be called from, and return control to that field.

	Cross-field callable routines are identified in BIOS listings as
	'ROUTINE NAME X0', where x0 is a field value (00, 10, 20).  These
	routines can be called from any field, and automatically return
	control to the proper PC in the calling field.

	For both types of routines, stack one is used to preserve the
	return address, and field if necessary.  In the following 
	examples, ROUNAM stands for a routine name; field 7 is used only
	for example purposes.

	Example of code to call a routine starting at location 0200, as a 
	local routine:	_____________	

	    PPC1	   /form return address and save on stack 1
	    JMP I ROUNAM   /jump indirect to ROUNAM


	Example of code to return to caller as a portion of a local							      _____
	routine:	_______

	    RTN1	   /return to PC from stack 1

	Example of code to call a cross-field routine, starting in field				  ___________________
	7:

	    CLA	           /start with cleared AC
	    RIF		   /place present instruction field in AC
	    PAC1	   /place present instruction field on stack 1
	    CIF 70	   /change to called routine instruction field
	    PPC1	   /form return address and save on stack 1
	    JMP I ROUNAM   /jump indirect to ROUNAM

	Example of code to return to caller as a portion of a cross-field							      ___________
	routine:	_______

	    POP1	   /get return address from stack 1
	    DCA GOTO	   /save as the return address
	    POP1	   /get return instruction field from stack 1
	    TAD (CIF 00    /add a CIF 00 instruction to form full CIF
			   /needed
	    DCA .+1	   /and place the built CIF instruction in line
	    0		   /position holder for the CIF
	    JMP I GOTO	   /jmp indirect back to caller

	It is important to understand the implications of Function Axx in
	terms of CALL and RETURN.  The Axx function is defined to be a
	cross-field callable routine.  As such, the Interrupt Vector has

	Loading and Using Extensions to 8BIOS			  Page 6
	_________________________________________________________________


	a dummy routine address when BIOS is startup up.  This feature
	protects the user from an inadvertent call to Function Axx before
	the RMM has been used to place a new Axx vector in place.  The
	dummy routine merely returns control to the BIOS IDLE routine.
	Once the user describes, via the Interrupt Vector, the field and
	address of the user's installed Function Axx, a call to that
	function will be a cross-field call.  Therefore, stack 1 will
	contain (at the top) the return address, and then one level down,
	the return instruction field.  A return  from this routine is then
	responsible to use the data on the stack to do a 'proper' return.

	Furthermore, the active data field is not changed by calling
	Function Axx, it is the responsibility of ALL cross-field called
	routines to: 1) establish the present data field to be what the
	routine requires; and 2) preserve the data field found at entry
	into the routine so that when control is returned to the calling
	code, the data field will be properly set for that code.


	C.P.Gerstle
	MLO3-2/E41
	DTN 223-2703