DECmate Slushware Implementation Notes	______________________________________



				  20 July 1984

		     DECmate SLUSHWARE Implementation Notes


	 Written by:	.......................	Kenny House
						ML03-2/E41
						DMATE:: HOUSE
						DTN 223-6652

	 Reviewed by:	....................... Don Rice - MLO3-2/E41




	COPYRIGHT (C) 1982, 1983, 1984 - DIGITAL EQUIPMENT CORPORATION







































				      page 1

	DECmate Slushware Implementation Notes	______________________________________


				PREFACE

	This is a Component Software Product  Specification.  It  is  the
	definitive  description  of the goals, capabilities, and external
	characteristics of the DECmate SLUSHWARE.

	Associated Documents:

		DECmate II SPECIFICATION, REV 4, John Kirk, 8-AUG-82

		DECMATE III SPECIFICATION, Larry Narhi.

		LK200 FUNCTIONAL SPECIFICATIONS, JAN-82

		LK201 KEYBOARD DESIGN SPECIFICATION, 8-0CT-81

		CRT 9007 VIDEO PROCESSOR AND CONTROLLER (VPAC)
		  PRELIMINARY PRODUCT DESCRIPTION,SMC,SEPTEMBER-81

		6120 CMOS 12-BIT PARALLEL MICROPROCESSOR, PURCHASE
		  SPECIFICATION, 31-MAY-78

		DEC STANDARD #169, STANDARD CODED GRAPHIC CHARACTER
		  SETS FOR HARDWARE AND SOFTWARE, L. FRAMPTON, 29-MAY-82

		DEC STANDARD #138, DRAFT, REGISTRY OF CONTROL FUNCTIONS
		  FOR CHARACTER IMAGING DEVICES, J. T. HSU, ll-MAY-82

		DEC STANDARD #70, TIA VIDEO STANDARD REFERENCE MANUAL,
		  R. SUDAMA, 15-MAY-83


























				      page 2

	DECmate Slushware Implementation Notes	______________________________________


				 Change History:

	DATE		ISSUE #	 	DESCRIPTION/SUMMARY OF CHANGES
	----		-------		------------------------------

	09-FEB-82	  1		Version 1.0 (draft).
	18-FEB-82 	  2 		Added detail as per input from
					reviewers.
	02-MAR-82 	  3 		More detail as per input.
	05-MAR-82 	  4 		clarification per review meeting.
	l9-JUL-82  	  5 		clarification and expansion.
	29-JUL-82 	  6 		clarification and expansion.
	26-NOV-82 	  7 		clarification and expansion
	20-JUN-83 	  8 		clarification and expansion
	l9-JUL-84 	  9 		clarification and expansion,
					added appendices A, B, C, D, F, G.








































				      page 3

	DECmate Slushware Implementation Notes	______________________________________


    1.0  PRODUCT SUMMARY

	The DECmate  SLUSHWARE  is  a  program  which  contains  loaders,
	keyboard   and  display  interfaces,  and  basic  keyboard/screen
	terminal emulation capability.

	With addition of application software, the  DECmate  can  perform
	as  a  special-purpose  computer  (e.g.,  a  word  processor or a
	terminal emulator) or as a general-purpose computer.

	The product is designed to be extensible, just as  the  SLUSHWARE
	itself evolved from that of the DECmate I.  Optional capabilities
	for the DECmate include both  hardware  and  software  additions.
	The  cross-loader feature of the SLUSHWARE allows this additional
	software (drivers and diagnostics) to be effectively brought into
	the SLUSHWARE: thus product functionality may be enhanced without
	any change to the basic SLUSHWARE.

	The expected lifetime of the SLUSHWARE is that of the  6120-based
	DECmate product line.

	The SLUSHWARE is written for, and is constrained to, the hardware
	of  the  DECmate  II  and  III base systems.  Any changes to this
	hardware may necessitate a change to the SLUSHWARE.
































				      page 4

	DECmate Slushware Implementation Notes	______________________________________


    2.0  ENVIRONMENT

    2.1  USER ENVIRONMENT

	The SLUSHWARE is transparent to the user.

    2.2  HARDWARE ENVIRONMENT

	The basic DECmate  hardware  as  described  in  the  "DECmate  II
	SPECIFICATION"  and  "DECmate  III SPECIFICATION" is the complete
	hardware  environment  for  the  SLUSHWARE.  Optional   hardware,
	whether  or  not mentioned in the specification, has no impact on
	the SLUSHWARE, since applications software provides  drivers  and
	diagnostics for all options.

    2.2 1  HARDWARE SUPPORTED

	As  a   reference,   the   SLUSHWARE   supports   this   hardware
	configuration.

		6120 CPU
		32 Kwords of main memory
		32 Kwords of control panel memory
		SMC VPAC 9007 CRT controller
		LK201 keyboard
		1 (or 2) RX50 floppy disks
		Printer port interface (FDX serial asynch line)
		Real time clock (100Hz)

	The SLUSHWARE is loaded to control panel RAM during the  power-up
	sequence  by  ROM  firmware.   SLUSHWARE  executes from panel RAM
	thereafter.

    2.2.2  HARDWARE EXCLUDED

	Options are excluded from this specification, including, but  not
	limited  to,  auxiliary  processor options, mass storage options,
	and graphics options.


    2.3  SOFTWARE ENVIRONMENT

	SLUSHWARE resides in panel RAM fields zero through  three.  Field
	seven is used by ROM firmware.  Executable code is in fields zero
	and one.  Tables (dynamic and static) are in fields zero  through
	three and field seven.  Screen RAM is in fields two and three.

	Fields four through six in panel RAM are  available  for  use  by
	application  software.   It  is not recommended to use this space
	for  executable  code,  since  interrupts  are   disabled   while
	executing  panel  code.  Field seven in panel RAM may be used for
	temporary buffers;  The user must be aware that this area may  be




				      page 5

	DECmate Slushware Implementation Notes	______________________________________

	obliterated by firmware (for Set-Up,  Halt,  crossboot  requests)
	and that the high addresses in this field are expected to be used
	for compose tables.

	Application  software  interfaces  with  the  terminal   emulator
	function  of  the  SLUSHWARE  for  standard character display and
	keyboard handling (see section 3.7).  Panel request  instructions
	allow  non-standard  control  of  the  slushware environment (see
	section 3.11).

	The SLUSHWARE is upward-compatible from the  DECmate  I  firmware
	except  as  noted.   Most  standard applications software for the
	DECmate I will run unmodified on the DECmate II and  the  DECmate
	III.

	The PR2 instruction is not supported; it is correctly ignored.

	The PR3 instruction (panel request for execution of control panel
	subroutine)  is  not  compatible  with the DECmate I (see section
	3.11); previously documented PR3s are correctly ignored.

	The LEDs on the keyboard are not  accessible  to  user  programs;
	they  are  treated  differently from the DECmate I since all LEDs
	are pre-assigned.

	Clock IOTs are different from the DECmate I.

	Any software which  relied  on  specific  knowledge  of  internal
	firmware  (such  as  buffer or subroutine addressing) is excluded
	from the above compatibility statement.

	Features  are  provided  to  support  a  TIA-compatible  terminal
	emulation  program  at  the  user  level.  TIA levels l and 2 are
	supported.

    
2.4  SERVICE ENVIRONMENT

	SLUSHWARE: Not applicable.

	SELF-TEST: None.
















				      page 6

	DECmate Slushware Implementation Notes	______________________________________


    3.0  SOFTWARE CAPABILITIES

	The   SLUSHWARE   provides  interfaces,   functionalities,    and
	diagnostics as described in this section.

    3.1  KEYBOARD INTERFACE

	The SLUSHWARE interfaces to a  LK201  keyboard  via  a  Universal
	Asynchronous Receiver-Transmitter (UART) contained in the DECmate
	hardware configuration.   The UART  is  hardware  programmed  for
	4800 BAUD, one stop bit, eight data bits, and no parity.  See the
	LK201 Functional Specification for more detail.

	These instructions are available to the  SLUSHWARE  for  keyboard
	interface.

		KBRSF (6111) -  skip if KB receiver flag set, then clear
				KB receiver flag

		KBIE (6115) -	set/clear KB interrupt enable
				AC<ll> : 0 = clear
					 1 = set

		KBRD (6116) - 	Read from keyboard
				AC<4:11> <-- KB buffer
				AC<0:3> unchanged

		KBLS (6056) - 	Write to keyboard
				KB buffer <--AC<4:11>

		KBTSF (6051) - 	Skip if KB transmitter set, clear KB
				transmitter flag.

	Note that SLUSHWARE must be the  only  program  that  clears  the			    ____
	keyboard  receiver or transmitter flags by executing the KBRSF or
	KBTSF or the CAF instructions.  If an application program  clears
	either  or both of these flags, the SLUSHWARE will not be able to
	control the LK201 keyboard correctly.  A panel request  has  been
	provided  to  issue the CAF instruction without losing control of
	these flags;  use of this panel request may cause a keystroke  to
	be lost.

	Note that there are only four LEDs on  the  LK201  Keyboard,  and
	they  are  pre-assigned  to 'Hold Screen', 'Lock', 'Compose', and
	'Wait'.  The DECmate I had five user-programmable LEDs which  are
	no longer available.

    3 1.1  KEYBOARD INPUT INTERFACE

	Keycodes are read from the UART as they are  sent  by  the  LK201
	keyboard.  (See appendix D for a list of LK201 keycodes.)

	Keycodes are interpreted as error sequence,  identification  (ID)



				      page 7

	DECmate Slushware Implementation Notes	______________________________________

	sequence, and normal characters.  SHIFT, CONTROL,  CAPSLOCK,  and
	ALLUP  codes  are  used  to set translation states for subsequent
	keycodes.  METRONOME  is  used  for  auto-repeat  of  the  latest
	character.  KBDLOCKED  is  used  to  acknowledge  a HOLD command.

	Incoming  keycodes  are  translated  via  table-driven  code   in
	SLUSHWARE  for  ease  of  switching character sets.  The table is
	loaded from track 00 of  the  system  disk  at  power-on  by  ROM
	firmware.  The  keyboard translation table for the main key array
	may be cross-loaded by  application  software  to  handle  non-US
	keyboard layouts.

	These modes affect the keyboard input handling.

		Auto-repeat mode
		Keyboard action mode
		Keypad numeric/application mode
		Cursor key mode
		ANSI/VT52 mode
		Level l/Level 2 terminal emulation mode
		Keyclick enable/disable mode
		Host Port Environment
		C1 Transmission mode
		Caps_Lock/Shift_Lock mode

		Compatibility mode
		Compose enable/disable mode
		IDIN mode	
		Local function key mode
		Single-character function key mode

	Translated keycodes are passed to applications software in the AC
	when  the  keyboard  is  read  by  the  user  with the KCC or KRB
	instructions (see Section 3.7.2).

	No keyboard error detection or  error  handling  is  provided  in
	SLUSHWARE.

	Refer to the keyboard section  of  the  DEC  Terminals  Interface
	Architecture  Video SRM (DEC STD 70) for codes generated from the
	keyboard and applicable modes.


    3.1.1.1  Compatibility mode

	At power-on, and when the compatibility mode has been reset,  the
	top-row  function keys and the editing keys act incompatibly with
	the TIA SRM.  The ESC, BS and LF keys  send  the  appropriate  C0
	character.  Other  non-local  function keys and editing keys send
	a control sequence ESC [ Pn ~, where  the  numeric  parameter  is
	that of the TIA SRM Level 2.

	If the compatibility mode has been selected, these  keys  act  in
	accordance with the TIA SRM.



				      page 8

	DECmate Slushware Implementation Notes	______________________________________

	The compatibility mode may be set or  reset  using  PR3/0010/7777
	(see section 3.11).

    3.1.1.2  Compose Enable/Disable Mode

	At power-on, and when  the  compose  mode  has  been  reset,  the
	'compose  character'  key  is disabled.  No code is generated for
	this key, no keyclick is sounded, and the compose  LED  is  never
	turned on.

	If the compose mode has been set,  the  'compose  character'  key
	acts  in  accordance  with  the  TIA  SRM.  Note that the compose
	tables must be cross-loaded by the user (see appendix ??).

	The compose mode may be set or  reset  using  PR3/0016/7777  (see
	section 3.11).

    3.1.1.3 IDIN mode

	At power-on, and when the IDIN mode has been reset, the  keyboard
	acts normally (consistent with other keyboard modes).

	If the IDIN mode has been set, no translation is performed on any
	received keycode.  Each keycode is sent to the user directly.  No
	output (keyclick, bell, LEDs) will be made to the keyboard.  This
	mode  is  intended  for  use  with a device other than a standard
	LK201 keyboard (such as the IDIN).  Note that  if  this  mode  is
	selected  when  an  LK201  keyboard  is  in  the system, the user
	assumes responsibility for handling all keyboard functions.

	The IDIN mode may  be  set  or  reset  using  PR3/0020/7777  (see
	section 3.11).

    3.1.1.4  Local Function Key Mode

	At power-on, and when the local function key mode is  reset,  the
	local  function  keys 'Print_screen', 'Set_Up', 'F4', and 'Break'
	are transmitted to the user via control  sequences  as  described
	in the TIA SRM.  The 'Hold' key is handled by slushware.

	If the local function key mode is set, the local function keys do
	not transmit any codes to the user.  The history of these keys is
	available to the user via a panel request (see section 3.11).

	The  local  function  key  mode  may  be  set  or   reset   using
	PR3/0012/7777 (see section 3.11).

    3.1.1.5  Single-character Function Key Mode

	At power-on, and when the single-character function key  mode  is
	reset,  the top row function keys, editing keys, cursor keys, and
	the application keypad keys act as described under  Compatibility





				      page 9

	DECmate Slushware Implementation Notes	______________________________________

	mode (see section 3.1.1.1).

	If the single-character function key mode is  set,  each  of  the
	above  keys is sent to the user as a single twelve-bit word.  The
	main key array is unaffected.  The format of the word follows.

	bits <04-11>	LK201 keycode
	bit <03>	1 = single-character function key,
			0 = normal key
	bit <02>	1 = shifted, 0 = unshifted
	bit <01>	1 = controlled, 0 = uncontrolled
	bit <00>	1 = locked, 0 = unlocked

	The 'Compose Character' key is affected by this mode only if  the
	compose  mode is disabled;  when the compose mode is enabled, the
	'Compose Character' key is used to initiate a compose sequence.

	The single-character function key mode may be set or reset  using
	PR3/0027/7777  (see  section 3.11).  See appendix D for a list of
	the LK201 keycodes that may be transmitted when this mode is set.

    3.1.2  KEYBOARD OUTPUT INTERFACE

	Commands are sent to the LK201 keyboard via the UART as the  need
	arises  (i.e.,  not  restricted  to end-of-frame or end-of-line).
	Valid commands to the keyboard are these.

		Set auto-repeat rates and timeouts for buffer
		Select mode for functional group
		Select auto-repeat buffer for functional group
		Resume keyboard transmission
		Inhibit keyboard transmission
		Light LEDs
		Turn off LEDs
		Disable keyclick
		Enable keyclick, set keyclick volume
		Disable CNTL keyclick
		Enable CNTL keyclick
		Sound keyclick
		Disable bell
		Enable bell, set bell volume
		Sound bell
		Temporary auto-repeat inhibit
		Request keyboard ID
		Reinitiate keyboard
		Jump to test mode

	User escape sequences are defined to select keyboard  auto-repeat
	and  to  select  keyboard transmission enable (see Section 3.10).
	A panel request allows direct transmission to the  keyboard  (see
	section  3.11).   Panel  requests  allow  application  control of
	keyboard case (upper/lower), bell volume, keyclick  volume,  Lock
	mode  (Caps/shift),  Compose  mode  (enable/disable),  IDIN  mode




				      page 10

	DECmate Slushware Implementation Notes	______________________________________

	(enable/disable), and single-character function key mode (enable/
	disable) (see section 3.11).

	A control code is defined to sound the bell (see section 3.7.1).

	During normal operation of SLUSHWARE, these command sequences may
	be issued to the LK201 keyboard.

		LED on - used to turn on each of the LEDs on the
		  keyboard as appropriate.

		LED off - used to turn off each of the LEDs on the
		  keyboard as appropriate.

		enable keyclick, sound keyclick, disable keyclick - used
		  to sound a click to signify to the user that a key has
		  been pressed and that the key is not muted.  This
		  sequence is not issued when the keyclick is disabled.

		enable bell, sound bell - used to sound a beep when the
		  C0 control code for BEL has been received from
		  application software.

	 	enable bell, temporary autorepeat inhibit, sound bell -
		  used to sound a bell to signify to the operator that
		  an illegal compose sequence has been entered.  This
		  beep is about half the volume of the normal beep.

		temporary autorepeat inhibit - used to prevent keys from
		  autorepeating.  This sequence is issued whenever a key
		  is pressed as part of a compose sequence, whenever a
		  muted key is pressed, whenever the 'Return' key is
		  pressed, and whenever a METRONOME keycode is received
		  from the LK201 without a valid precedent.

    3.1.3  KEYBOARD POWER-UP

	The keyboard interface is tested and set as part of  the  DECmate
	ROM firmware power-up sequence (see section 3.8).

	When control is passed to SLUSHWARE, the following  commands  are
	sent to the keyboard.

		Disable keyclick
		Return and Tab keys - autorepeat buffer 1
		Application Function keys - autorepeat buffer 0
		Editing keys - autorepeat buffer 0
		Enable autorepeat

	This default is selectable via the ROM firmware setup menu.

		auto-repeat enabled/disabled





				      page 11

	DECmate Slushware Implementation Notes	______________________________________

	The keyboard  LEDs  are  also  set  or  reset  according  to  the
	corresponding state of the software flags; they will all be off.

	At the completion of the power-up, the keyboard is  unlocked  and
	is in lower-case mode.


     3.2  VIDEO DISPLAY INTERFACE

	The SLUSHWARE interfaces to a  SMC  VPAC  9007  video  controller
	(Cathode  Ray  Tube  Controller,  CRTC),  and  to special-purpose
	hardware of the DECmate.

	These instructions are available to the SLUSHWARE for controlling
	the CRTC.

		ESSF 	6121 	Skip on End-of-Frame interrupt,
				clear End-of-Frame.

		LSCREG 	6122 	Load CRTC register number from AC<6:11>,
				load cursor visibility enable from AC<01>,
				load cursor visibility disable from AC<00>.

		??	6123 	If Data Field is odd: load user character
				RAM character number from AC<1:7>, raster
				line number from AC<8:11>;
				If Data Field is even: load user character
				RAM data from AC<4:11>.
				(Only available on DECmate II.)

		LDCTRC 	6124	Write selected CRTC register from AC<4:11>.

		DPAR 	6126 	Load control register from AC:
				00 - erase bit 0
				01 - erase bit 1
				04 - 80/132 column mode (0 -> 80)
				05 - video enable (0 -> disable)
				08 - extended character set mode (0 -> 
				     clear)
				09 - user character set mode (0 -> clear)
				10 - cursor mode (0 -> block, 1 ->
				     underscore)
				11 - screen mode (0 -> white on black).

		RDCRTC 6127	Read selected CRTC register to AC<4:11>.


    3.2.1  VIDEO DISPLAY INPUT INTERFACE

	The SLUSHWARE is interrupted at the end of each video frame.  The
	state  of  the End-Of-Frame (EOF) flag may be tested by software.
	There is no way to determine the state of  the  CRTC  other  than
	waiting for an EOF.




				      page 12

	DECmate Slushware Implementation Notes	______________________________________

	N. B.: the light pen interrupt is not supported in SLUSHWARE.

	Note that SLUSHWARE must be the  only  program  that  clears  the			    ____
	end-of-frame  flag by executing the ESSF or CAF instruction.  The
	CRTC hardware vertical interrupt line must be reset by  SLUSHWARE
	before  the  CRTC  will cause another end-of-frame interrupt;  if
	an  application  program  clears  the  end-of-frame   flag,   the
	SLUSHWARE  will  not  be  able to  control  the   video   display
	correctly.   A  panel  request has been provided to issue the CAF
	instruction without losing control of the end-of-frame flag.


    3.2.2  VIDEO DISPLAY OUTPUT INTERFACE

	The CRTC operates in a single row buffer, contiguous row  address
	table  mode.  The  SLUSHWARE maintains the contiguous row address
	table and the row data in control panel RAM.

	At each display line, the CRTC  performs  a  Direct-Memory-Access
	(DMA)  of  the  data for the next display line.  The DMA lasts 64
	micro-seconds and occurs each  640  micro-seconds  (see  hardware
	specifications);   both  SLUSHWARE  and  application programs are
	locked out during DMA.

	Refresh for dynamic memory is ensured by appropriate handling  of
	the  row address table (see hardware specifications).  Two extra,
	invisible  rows  are  included  for  memory  refresh  during  the
	vertical retrace interval.

	Row attributes are encoded as the  two  high  bytes  of  the  row
	address.

		00 - single height, single width
		01 - single height, double width
		10 - double height, double width, top half
		11 - double height, double width, bottom half

	Character attributes are encoded as the four  high  bits  of  the
	character data.

		lxxx - blink
		xlxx - underscore
		xxlx - bold
		xxxl - reverse video

	The most significant bit of the character data is  used  for  the
	blink  attribute  (as  above)  or  as  a  flag  for  the extended
	character set, depending on the state of the  extended  character
	set mode flag.

	Characters to be displayed and cursor  control  escape  sequences
	are passed to SLUSHWARE from applications software in the AC with
	the TLS instruction or in the argument  string  of  a  PR1  panel
	request.



				      page 13

	DECmate Slushware Implementation Notes	______________________________________

	Both 7-bit and 8-bit environments are supported.  A panel request
	has been defined to select the host port environment (see section
	3.11).

	Graphic character sets G0, G1, G2 and G3  are  supported.  Escape
	sequences  have  been  defined for designating the character sets
	for these (see section 3.10).

	Graphic character sets GL and GR are  supported.   These  may  be
	invoked   to  the G0, G1, G2 and G3 sets via escape sequences and
	control codes (see sections 3.10 and 3.11).

	Control codes from both the C0 and the C1 control character  sets
	are supported (see section 3.7.1).

	Applications software may directly read to and write from display
	memory  using  the  PR0  and  PR1 panel request instructions (see
	section 3.11).  The block move panel request may also be used  to
	move data from user memory to display memory.

	Screen  and line  erase  functions  are  performed  by  the  CRTC
	according  to the erase bits in the CRT control word (accessed by
	the DPAR instruction) and the current cursor position.

		ERASE BIT 0	ERASE BIT 1 	FUNCTION
		-----------	-----------	--------
		1		0		Erase line from current
						cursor to end.
		1		1		Erase screen from current
						cursor to end.
		0		0		Erase off.

	Note that the erase-in-line feature of the hardware is  not  used
	by   SLUSHWARE   versions   220  and  later.   All  erase-in-line
	operations are performed entirely by software.

	N. B.: horizontal scroll is not supported by firmware.

	N. B.: multi-paging is not supported by firmware.


    3.3  DISK INTERFACE

	The disk  interface  supports  RX50-compatible  floppy  disk  and
	RD51-compatible Winchester disk controllers.

	The ROM firmware resets the disk interface  at  power-up  of  the
	DECmate.

	The disk bootstrap routine is loaded from control  panel  ROM  to
	main memory and executed upon power-up of the DECmate.

	Note that the power-up sequence differs from that of the  DECmate
	I in that the bootstrap is automatic in the current DECmate.



				      page 14

	DECmate Slushware Implementation Notes	______________________________________

	The DECmate I used a SETUP sequence to request the bootstrap.

	The SLUSHWARE resides on tracks 78 and 79  of  the  system  disk.
	Early  versions  were  formatted as 12-bit words;  later versions
	are formatted as 8-bit words.  The first sector is always written
	in  12-bit  mode.   The  SLUSHWARE performs a selfload if old ROM
	code loads it in 12-bit mode.

	The keyboard language map (to support foreign keyboards)  resides
	on track 00 of the system disk.

	The text messages used for the SETUP menu reside on track  00  of
	the system disk.

	The text messages for the HALT display  reside  on  track  00  of
	the system disk.

	Note that slushware does not access track 00 for any  data;  this
	is done only by ROM firmware.


    3.4  LOADERS

    3.4.1  CONTROL PANEL MEMORY TO MAIN MEMORY CROSS-LOADER

	Data in the control panel memory may be moved to main memory  RAM
	via the PR3/50XY instruction (see section 3.11).

    3.4.2  MAIN MEMORY TO CONTROL PANEL MEMORY CROSS-LOADER

	Data in the main memory may be moved to control panel RAM via the
	PR3/40XY instruction (see section 3.11) .

    3.4.3  FLOPPY DISK TO MAIN MEMORY BOOTSTRAP LOADER

	Data in the 'boot block' of the floppy is moved  to  main  memory
	RAM during SLUSHWARE initialization.

    3.4.4  FLOPPY DISK TO CONTROL PANEL MEMORY SLUSHWARE LOADER

	At power-up, SLUSHWARE is loaded from the system disk to  control
	panel  memory  by ROM firmware.  The first block is always in 12-
	bit mode.  Subsequent blocks are either in 12-bit mode or  in  8-
	bit  mode  (older  versions  are  in 12-bit).  Early ROM firmware
	loads all blocks in 12-bit mode,  then  transfers  control  to  a
	routine  in  the first block.  This routine reloads the remaining
	blocks in 8-bit mode if necessary.

    3.4.5  COMMUNICATION LINK TO MAIN MEMORY DOWNLOADER

	Main memory RAM may be loaded with data from another computer via
	a  serial  communications  link  with  the DECmate.  This must be
	controlled by an applications program, not by SLUSHWARE.




				      page 15

	DECmate Slushware Implementation Notes	______________________________________

    3.5  PRINTER PORT INTERFACE

	The ROM firmware resets the printer port interface at power-up of
	the DECmate.  The printer port baud rate is a SETUP parameter.

	The PR3/0000/7777 function to print a character is  provided  for
	backward  compatibility  with  the  DECmate I (see section 3.11).
	Use of this function is not recommended.

	Media Copy, Printer-Extent  Mode,  Printer-Controller  Mode,  DEC
	Hard Copy, and Print-Form-Feed Mode (the printer extension to TIA
	SRM) are not supported in SLUSHWARE.

	The response to the ANSI control  sequence  request  for  printer
	status is always 'not there' (see section 3.10).


    3.6  REAL TIME CLOCK INTERFACE

	The real time clock is tested at power-up by  ROM  firmware.  Its
	interrupt is disabled following the test.

	SLUSHWARE does not handle the real time clock.

	Note that the clock IOTs differ from those of the DECmate I.


    3.7  TERMINAL EMULATION

	The  SLUSHWARE  emulates   a  DEC  Level  2  terminal   for   the
	applications  software  running in main memory (see the Video SRM
	for a complete description of Level 2 emulation mode).

	An application program, which  is  not  provided  as  a  part  of
	SLUSHWARE,  is required to emulate a terminal for a host computer
	attached to the communications port.  This  program  must  handle
	communications with the host and printer;  any ANSI controls that
	would affect these operations must be trapped and handled by  the
	emulation program.

    3.7.1  TERMINAL OUTPUT (DISPLAY) EMULATION

	These instructions are emulated by the SLUSHWARE.

		TCF  6042 - clear AC

		TLS  6046 - 'display' character in AC, AC unchanged

	SLUSHWARE  receives  data  and  commands  from  the  applications
	software in the AC with the TLS instruction.

	TLS data  are  either  graphic  characters,  control  characters,
	escape  sequences,  control  sequences,  or control strings.  The




				      page 16

	DECmate Slushware Implementation Notes	______________________________________

	data are treated as seven or eight bit  characters  depending  on
	the   state  of  the  Host  Port  Environment  and  the  terminal
	emulation level.

	Displayable characters are stored  in  display  memory.   Current
	character  attributes  are  merged  and  stored  with the display
	characters.  The cursor position is modified as  appropriate  for
	the  line  characteristics  and the condition of the new-line and
	autowrap characteristics. Both the left and  right  hand  control
	and  character sets (C0, GL, C1 and GR) may be used in the eight-
	bit environment; the right hand sets map to the left hand set  in
	the seven-bit environment (see DEC Standard 169).

	These modes and states affect the received character handling.

		ANSI/VT52 mode
		Level_l/Level_2 terminal emulation mode
		7-bit/8-bit Host Port Environment
		80/132 Column mode
		Line Rendition
		Character Rendition
		New_Line/Line_Feed mode
		Autowrap mode
		Tab stops
		Single_Shift
		Locking shifts
		Designated character sets
		Control string in progress
		Scroll mode
		Scroll region
		Origin mode
		Insertion/replacement mode

	Escape sequences are processed as appropriate for  the  ANSI/VT52
	and  terminal  emulation  level modes selected.  Power-up mode is
	determined by the SETUP parameters stored on the disk.

	Specific escape sequences are listed  in  section  3.10  of  this
	specification.

	Control characters that are handled by the SLUSHWARE  are  listed
	below.

	C0 control characters:

		NUL  000  Null character
		SEL  007  Sound bell on keyboard
		BS   010  Backspace
		HT   011  Horizontal tab
		LF   012  Line feed
		VT   013  Vertical tab (treated as line feed)
		FF   014  Form feed (treated as line feed)
		CR   015  Carriage return
		SO   016  Shift out, maps GL to G1 character set



				      page 17

	DECmate Slushware Implementation Notes	______________________________________

		SI   017  Shift in, maps GL to G0 character set
		CAN  030  Cancel
		SUB  032  Substitute, displays an error character
		ESC  033  Escape
		DEL  177  Delete (ignored)

	C1 control characters (only available in Level_2, 8-bit host port
	environment),  note that these are identical to the two character
	expansion escape sequences identified below:

		IND  204  Index (esc D)
		NEL  205  New line (esc E)
		HTS  210  Horizontal tab set (esc H)
		RI   215  Reverse index (esc M)
		SS2  216  Single shift 2, maps next GL character to
			  G2 set (esc N)
		SS3  217  Single shift 3, maps next GL character to
			  G3 set (esc O)
		DCS  220  Device control string introducer (esc P)
	 	CSI  233  Control string introducer (esc [)
		ST   234  String terminator (esc backslash)
		OSC  235  Operating system command introducer (esc ])
		PM   236  Privacy message introducer (esc uparrow)
		APC  237  Application program command introducer (esc
			  underscore)


    3.7.2  TERMINAL INPUT (KEYBOARD) EMULATION

	These instructions are emulated by SLUSHWARE.

		KCC  6032 - get next character ready, clear AC

		KRS  6034 - logical or AC with ready character

		KRB  6036 - AC <- ready character, get next ready
			    character

	SLUSHWARE sends data to the applications software in the AC  when
	the KRB or KRS instructions are emulated.
	
	Data are either ASCII codes and escape sequences translated  from
	the  LK201  keycode  inputs,  or  escape  sequence  responses  to
	applications software requests.

	Incoming keycodes from the LK201  are  translated  to  characters
	according  to  the  keyboard translation map (see section 3.1.1).
	It is possible  to  type  an  escape  sequence  directly  on  the
	keyboard:   this  will  be  transmitted to applications software,
	which can test character timing to determine the  source  (manual
	or automatic) of the escape sequence.

	The SLUSHWARE responds  to  requests  for  status  (e.g.,  cursor
	position,  device attributes, identification, printer status, UDK



				      page 18

	DECmate Slushware Implementation Notes	______________________________________

	lock status) with escape sequences (see  section  3.10).   
	
	Escape sequences  generated  by  the  SLUSHWARE may be introduced 
	by two seven-bit characters or by a single eight-bit C1 character
	depending  on  the  environment and the C1 Transmission mode (see
	DEC STD 169).


    3.8  POWER-ON INITIALIZATION

	At power-on of the DECmate, the firmware ROM contents  are  moved
	to  RAM,  the  RAM DATA flag is set and all further firmware code
	executes from RAM.  The ROM firmware performs a rudimentary self-
	test.  Upon  successful  completion  of  the  self-test,  the ROM
	firmware loads the SLUSHWARE (functional firmware) from disk into
	panel  RAM.  The  SLUSHWARE  initializes  the base hardware, sets
	modes based on setup  parameters,  and  then  executes  the  disk
	bootstrap.

	The default programming of the  hardware  is  discussed  in  each
	section.

	These modes are set during slushware initialization.

		Top/bottom margins to 1;24
		Origin mode reset (absolute)
		Cursor position home (1;1)
		Screen cleared
		Character rendition normal
		Line rendition single width (all lines)
		Insert/replace mode reset (replace)
		G0, G1, G2, G3 designated according to TIA spec
		GL invoked to G0
		GR invoked to G2
		Newline off
		Autowrap disabled
		Tab stops set every eight columns (9, 17, 25....)
		Screen blank enabled

		Keyboard action mode reset (keyboard enabled)
		Cursor key mode reset
		Keypad mode reset (numeric)
		Caps_lock/Shift_lock mode reset (Caps_lock)
		Compose mode disabled
		Keyboard lock mode reset (lower case)
		IDIN mode disabled
		Local function key mode reset
		Single-character function key mode reset
		Compatibility mode reset (incompatible)


    3.9  SETUP FUNCTIONS

	These parameters may be changed by SETUP.



				      page 19

	DECmate Slushware Implementation Notes	______________________________________

		Column mode (80 or 132 columns)
		Cursor style (block or underline)
		Cursor visibility (enabled or disabled)
		Scroll mode (jump or smooth)
		Screen mode (white-on-black or black-on-white)
		Keyclick mode (enabled or disabled)
		ANSI mode (ANSI or VT52)
		Terminal emulation mode (level 1 or level 2)
		Host Port Environment (7-bit or 8-bit)
		Autorepeat mode (enabled or disabled)
		bell Enable and Volume
		Keyclick Enable and Volume
		Printer port baud rate
		Communications port baud rate

	Several addresses have been  assigned  in  control  panel  memory
	field zero for setup parameters.

	      0024   -  bit mask for these parameters
		<11> 	Column mode (0=80 1=132)
		<10> 	Cursor style (0=block, 1=underscore)
		<09> 	Cursor visibility (0=on 1=off)
		<08> 	Scroll mode (0=jump, 1=slow)
		<07> 	screen mode (0=light on dark, 1=reverse)
		<06>	Keyclick mode (0=on, 1=off)
		<05> 	Terminal emulation mode (0=ANSI, 1=vt52)
		<04> 	Terminal emulation mode (0=level 1, 1=level 2)
		<03> 	C1 transmission mode (0=7-bit, 1=8-bit)
		<02> 	Host port environment (0=7-bit, 1=8-bit)
		<01> 	Bell enable mode (0=enabled, 1=disabled)
		<00> 	Autorepeat mode (0=enabled, 1=disabled)

	      0025  - 	Printer port baud rate
		00  -	50 baud
		01  -	75 baud
		02  - 	110 baud
		03  -	134.5 baud
		04  - 	150 baud
		05  -	300 baud *
		06  -	600 baud *
		07  - 	1200 baud *
		10  - 	1800 baud
		11  - 	2000 baud
		12  - 	2400 baud *
		13  - 	3600 baud
		14  - 	4800 baud */**
		15  -	7200 baud
		16  - 	9600 baud *
		17  - 	19200 baud
		(* implies available in DECmate II ROM firmware SETUP,
		 ** implies available in DECmate III ROM firmware
	 	 SETUP.)





				      page 20

	DECmate Slushware Implementation Notes	______________________________________

	      0026  -	Communication port baud rate
		00  -	50 baud
		01  - 	75 baud		
		02  -	110 baud
		03  - 	134.5 baud
		04  - 	150 baud
		05  - 	300 baud */**
		06  - 	600 baud *
		07  - 	1200 baud */**
		10  - 	1800 baud
		11  - 	2000 baud
		12  - 	2400 baud */**
		13  - 	3600 baud
		14  - 	4800 baud */**
		15  - 	7200 baud
		16  - 	9600 baud */**
		17  - 	19200 baud
		(* implies available in DECmate II ROM firmware SETUP,
		 ** implies available in DECmate III ROM firmware
		 SETUP. )

	      0027 - bit mask for these parameters
		<09-11> Keyclick volume (7=minimum, ...0=maximum)
		<06-08> Bell volume (7=minimum, ...0=maximum)
		<05> 	reserved for graphics cursor visibility
		<03-04> reserved for graphics monitor configuration
		<01-02> reserved
		<00> 	must be 0 for keyclick volume to work

	The setup parameters are changed in panel  memory  to  match  the
	current  state of the corresponding mode.  This is performed when
	the RIS escape sequence is received and when the PR3  request  to
	move  data  from  panel  memory  to  user memory is issued.  This
	feature is intended to allow  system  programs  running  in  user
	memory to obtain the state of these modes.

	These selected  SETUP  parameters  are  used  at  power-on,  upon
 	receipt  of  a  reset-to-initial-state  escape sequence, and upon
	return from  the  setup  menu.   Note  that  all  parameters  are
	set/reset  according  to  their condition at exit from SETUP, not
	just those parameters most recently  changed.  The  ROM  firmware
	SETUP  menu can be invoked by a panel request (see section 3.11).
	Native language text for  the  menu  resides  on  the  disk.   An
	application  program  could  be  written to emulate a SETUP menu;
	SLUSHWARE supports escape sequences and panel requests to  select
	each of the modes in the setup (see sections 3.10 and 3.11).

	Users of the DECmate should  be  aware  that  saving  the  Set-Up
	parameters on the system disk will save all the above parameters.
	The DECmate II ROM firmware Set-Up screen does  not  display  all
	these  parameters,  so  parameters  that have been changed by the
	application program may get saved without the operator's explicit
	knowledge.




				      page 21

	DECmate Slushware Implementation Notes	______________________________________

    3.10  ESCAPE SEQUENCES

	These escape and control sequences are interpreted by the DECmate
	SLUSHWARE.

	ANSI mode:
	----------

	ESC D	 - IND, INDEX

	ESC E	 - NEL, NEXT LINE

	ESC H	 - HTS, HORIZONTAL TAB SET

	ESC M	 - RI, REVERSE INDEX

	ESC N	 - SS2, SINGLE SHIFT 2

	ESC O	 - SS3, SINGLE SHIFT 3

	ESC P	 - DCS, DEVICE CONTROL STRING INTRODUCER

	ESC Z	 - DECID, REQUEST TERMINAL ID

	ESC [	 - CSI, CONTROL STRING INTRODUCER

	ESC \	 - ST, STRING TERMINATOR

	ESC _	 - APC, APPLICATION PROGRAM CONTROL INTRODUCER

	ESC ]	 - OSC, OPERATING SYSTEM CONTROL INTRODUCER

	ESC ^	 - PM, PRIVACY MODE INTRODUCER

	ESC SP F  - S7ClT, SEND C1 CONTROL CHARACTER AS TWO SEVEN-BIT
		   CHARACTERS

	ESC SP G  - S8C1T, SEND C1 CONTROL CHARACTER AS SINGLE SEVEN-BIT
		   CHARACTER

	ESC # 3  - DECDHLT, SELECT DOUBLE-HEIGHT LINE, TOP
	
	ESC # 4  - DECDHLB, SELECT DOUBLE HEIGHT LINE, BOTTOM

	ESC # 5  - DECSWL, SELECT SINGLE-WIDTH LINE

	ESC # 6  - DECDWL, SELECT DOUBLE-WIDTH LINE

	ESC # 8  - DECALN, SCREEN ALIGNMENT PATTERN

	ESC ( F  - SCS, DESIGNATE G0 SET (SEE BELOW FOR VALUES OF F)

	ESC ) F  - SCS, DESIGNATE G1 SET (SEE BELOW)




				      page 22

	DECmate Slushware Implementation Notes	______________________________________

	ESC * F  - SCS, DESIGNATE G2 SET (SEE BELOW) **

	ESC + F  - SCS, DESIGNATE G3 SET (SEE BELOW) **

		AVAILABLE CHARACTER SETS ARE
		A  - UK ASCII *
		B  - US ASCII
		I  - JIS KATAKANA */***
		J  - JIS ROMAN GRAPHIC SET *
		K  - GERMAN *
		R  - FRENCH *
		Y  - ITALIAN *
		Z  - SPANISH *
		0  - SPECIAL GRAPHICS (LINE DRAWING SET)
		1  - ALTERNATE CHARACTER ROM *
		2  - ALTERNATE ROM SPECIAL GRAPHICS *
		3  - FRENCH-CANADIAN *
		4  - DUTCH *
		5  - FINNISH *
		6  - NORWEGIAN-DANISH *
		7  - SWEDISH *
		<  - DEC EIGHT-BIT MULTINATIONAL SUPPLEMENTAL CHARACTER
		     SET **
		>  - DEC TECHNICAL CHARACTER SET *
		SP @  - USER-DEFINED BASE CHARACTER SET */***
		SP A  - USER-DEFINED SPECIAL CHARACTER SET */***
	
		(* Implies character attribute blink lost at  designation
		of this character set.)

		(*** Implies not available on the DECmate III. These sets
		are  available on the DECmate II, but are not recommended
		due to cross-product compatibility.)

	ESC 7  - SC, SAVE CURSOR

	ESC 8  - RC, RESTORE CURSOR

	ESC =  - DECKPAM, KEYPAD APPLICATION MODE

	ESC >  - DECKPNM, KEYPAD NUMERIC MODE

	ESC c  - RIS, RESET TO INITIAL STATE

	ESC n  - LS2, MAP GL TO THE G2 CHARACTER SET **

	ESC o  - LS3, MAP GL TO THE G3 CHARACTER SET **

	ESC ~  - LS1R, MAP GR TO THE G1 CHARACTER SET **

	ESC }  - LS2R, MAP GR TO THE G2 CHARACTER SET **

	ESC |  - LS3R, MAP GR TO THE G3 CHARACTER SET **




				      page 23

	DECmate Slushware Implementation Notes	______________________________________

	CSI Pn @  - ICH, INSERT Pn CHARACTERS **

	CSI Pn A  - CUP, CURSOR UP Pn LINES

	CSI Pn B  - CUD, CURSOR DOWN Pn LINES

	CSI Pn C  - CUD, CURSOR FORWARD Pn COLUMNS

	CSI Pn D  - CUB, CURSOR BACKWARD Pn COLUMNS
	
	CSI Pn ; Pm H  - DCA, DIRECT CURSOR POSITIONING

	CSI Ps J  - ED, ERASE IN DISPLAY
		(Ps: 0-TO END,
		     1-FROM START,
		     2-ENTIRE)

	CSI Ps X  - EL, ERASE IN LINE
		(Ps: 0-TO END,
		     1-FROM START,
		     2-ENTIRE)

	CSI Pn L  - IL, INSERT Pn LINES

	CSI Pn M  - DL, DELETE Pn LINES

	CSI Pn P  - DCH, DELETE Pn CHARACTERS

	CSI Pn X  - ECH, ERASE Pn CHARACTERS

	CSI Pn c  - DA1, PRIMARY DEVICE ATTRIBUTES
		  (Pn: 0-REQUEST ATTRIBUTES, RESPONSE CSI 6 1; 1 c)

	CSI > Pn c  - DA2, SECONDARY DEVICE ATTRIBUTES REQUEST
		  (Pn: 0-REQUEST ATTRIBUTES,
			RESPONSE CSI > 3; SLUSHrev; ROMrev c)

	CSI Pn; Pm f  - HVP, HORIZONTAL AND VERTICAL POSITION

	CSI Ps g  - TBC, TABULATION CLEAR
		(Ps: 0-CLEAR THIS,
		     3-CLEAR ALL)

	CSI Ps h  - SM, SET MODE (SEE BELOW FOR PARAMETERS)

	CSI Ps l  - RM, RESET MODE
		(Ps: 2 - KAM, KEYBOARD ACTION MODE
		     4 - IRM, INSERTION-REPLACEMENT MODE
		     20 - LNM, LINE FEED/NEW LINE MODE)

	CSI Ps m  - SGR, SELECT GRAPHIC RENDITION
		(Ps: 0 - DEFAULT, ALL ATTRIBUTES OFF
		     1 - BOLD
		     4 - UNDERLINED



				      page 24

	DECmate Slushware Implementation Notes	______________________________________

	  	     5 - BLINKING
		     7 - REVERSE VIDEO
		     22 - UN-BOLD
		     24 - UN-UNDERLINE
		     25 - UN-BLINK
		     27 - UN-REVERSE)

	CSI Ps n  - DSR, DEVICE STATUS REPORT
		(Ps: 5-REQUEST STATUS,
		       RESPONSE CSI 0 n,
		     6-REQUEST POSITION REPORT,
		       RESPONSE CSI Pr ; Pc R)

	CSI ? Ps n  - DECDSR, DEVICE STATUS REPORT
		(Ps: 15-REQUEST PRINTER STATUS,
		        RESPONSE CSI ? 1 3 n,
		     25-REQUEST UDK LOCK STATUS,
			RESPONSE CS: ? 2 3 n)

	CSI ! p  - DECSTR, SOFT TERMINAL RESET

	CSI Pn ; Pm " p  - DECSCL, SELECT COMPATIBILITY LEVEL
		(Pn: 61-SELECT LEVEL 1,
		     62-SELECT LEVEL 2, Pm: 1-SELECT 7-BIT C1,
					    0 OR 2-SELECT 8-BIT C1)

	CSI Pn; Pm r  - STBM, SET TOP AND BOTTOM MARGINS

	CSI ? Pn h  - DECSM, SET MODE (SEE BELOW FOR PARAMETERS)

	CSI ? Pn l  - DECRM, RESET MODE (SEE BELOW)
		(Pn: 1 - DECCKM, CURSOR KEY MODE
		     2 - DECSNM, ANSI MODE (IGNORED BY SET MODE)
		     3 - DECCOL, COLUMN MODE
		     4 - DECSCLM, SCROLLING MODE
		     5 - DECSCNM, SCREEN MODE
		     6 - DECOM, ORIGIN MODE
		     7 - DECAWM, AUTO-WRAP MODE
		     8 - DECARM, AUTO-REPEAT MODE
		     25 - DECCEM, CURSOR VISIBILITY MODE)

	(** implies only available in Level 2 terminal emulation mode.)


	VT52 mode:
	----------

	ESC A  - CURSOR UP

	ESC B  - CURSOR DOWN

	ESC C  - CURSOR FORWARD

	ESC D  - CURSOR BACKWARD



				      page 25

	DECmate Slushware Implementation Notes	______________________________________


	ESC F  - SELECT GRAPHICS CHARACTER SET

	ESC G  - SELECT USASCII CHARACTER SET

	ESC H  - CURSOR HOME

	ESC I  - REVERSE LINE FEED

	ESC J  - ERASE TO END OF DISPLAY

	ESC K  - ERASE TO END OF LINE

	ESC Y G1 Gc  - DIRECT CURSOR ADDRESS

	ESC Z  - TERMINAL IDENTIFY TYPE

	ESC <  - ENTER ANSI COMPATIBILITY MODE

	ESC "  - KEYPAD APPLICATION MODE

	ESC >  - KEYPAD NUMERIC MODE



	There are some functions and controls that are not to be used  by
	new  software.   Conforming  software will be ensured wider cross
	product compatibility by avoiding these features.

	VT52 emulation mode - This will not be implemented by future
	     terminals.

	NEL - CR LF has the same effect and should be used for wider
	     compatibility.

	DECID - This sequence may be redefined.  Use DA1 instead.

	DECALN - This has been provided for use by manufacturing and
	     diagnostics.  Different terminals will implement this
	     function differently.

	SCS - These character sets are not recommended because the
	     characters in these sets can be displayed from the DEC
	     Multinational character sets (US ASCII and DEC
	     Supplemental Graphics) and the character attribute blink
	     is lost when these sets are selected:
		UK ASCII
		German
		French
		French-Canadian
		Italian
		Spanish
		Dutch
		JIS Roman
		Finnish


				      page 26

	DECmate Slushware Implementation Notes	______________________________________

		Swedish
		Norwegian-Danish

	     These character sets are not recommended because the
	     character attribute 'blink' is lost when they are
	     designated.
		Katakana
		Alternate ROM
		Alternate ROM special graphics

	     These character sets are not recommended because of
	     non-standard designation sequence and because the
	     character attribute 'blink' is lost when they are
	     designated.
		User-defined base character set
		User-defined special character set

	RIS - This function is implemented differently on different
	     terminals, the communications link may be broken.  Use
	     DECSTR instead.

	LS2, LS3, LS1R - Conforming software will only invoke GL to G0
	     or G1, and will only invoke GR to G2 or G3.

	HVP - This function may be redefined in the future.  Use DCA
	     instead for the same functionality.

	DECAWM - The autowrap function is implemented differently on
	     different terminals.  Conforming software will handle line
	     formatting by itself.

	These user-preference features should not be modified.
	     DECCOL - column mode
	     DECSCLM - scrolling mode
	     DECSCNM - screen mode
	     DECARM - auto-repeat mode

    3.11  PANEL TRAPS AND INTERRUPTS

	These traps are handled in the SLUSHWARE.

	Power-on
	Bootstrap
	  End-of-frame	
	  user IOT emulation
	  Keyboard
	Panel request
	Halt
	Real time clock (only at power-up)

	Note that the PR2 (execute setup) and the  PR3  (execute  control
	panel subroutine) instructions are different from the DECMATE I.

	These  panel  requests  executed  in  application  software   are



				      page 27

	DECmate Slushware Implementation Notes	______________________________________

	interpreted by SLUSHWARE.

	PR0 - Read display data, location to be accessed is specified  in
	the  two  locations  following  the  instruction.  Home  is  0,0.
	Return is made to CALL+3 with the display character  in  the  AC.
	Note  that  the  returned  value is an address into the character
	generator ROM and thus may not be a recognizable character  code.
	The layout of the character generator ROM is TBS.

	CALL, 	PR0 	/panel request
		ROW 	/physical row number
		COL 	/physical column number

	PR1 - write display data,  each  location  and  the  data  to  be
	written   are   specified  in  three-word  blocks  following  the
	instruction.  Home is 0,0.  The request is terminated by a  7777.
	Return is made to the location following the 7777 terminator.

	CALL, 	PRl	/panel request
		ROW	/physical row number
		COL	/physical column number
		DATA	/character to display (map address)
		.
		.
		.
		7777	/terminator

	PR2 - not implemented.   This  is,  however,  correctly  ignored:
	Return is made to CALL+2 for DECmate I compatibility.

	PR3 -  Request  panel  memory   functions,   the   function   and
	function-specific   arguments  are  specified  in  the  locations
	following the instruction.  Return is  made  following  the  7777
	terminator.

	CALL, 	PR3	/panel request
		FUNCT	/function
		ARG1	/first argument (optional)
		ARG2	/second argument (optional)
		.
		.
		.
		7777	/terminator (mandatory)
	
	function 0000 - print character in the accumulator.
			No arguments.
			This is implemented solely for backward
			compatibility with the DECmate I, and is not
			recommended for use.  If the printer sends an
			XOFF to the SLUSHWARE, the system will hang in
			panel memory until an XON is received.

	function 0001 - select video enable/disable from AC<11>,
			0 = enable, 1 = disable.



				      page 28

	DECmate Slushware Implementation Notes	______________________________________

			No arguments.
			This allows user control over screen
			visibility.  Disabling the screen will not
			cause display memory contents to be erased.

	function 0002 - select extended character enable/disable from
			AC<11>.
			0 = disable, 1 = enable.
			No arguments.
			This allows use of the high two quadrants of
			the character generator ROM (and the user-
			defined character RAM on the DECmate II).  When
			enabled, the character attribute bit 'blink' is
			preempted for use as a ninth address bit.

	function 0003 - select user character enable/disable from
			AC<11>.
			0 = disable, 1 = enable.
			No arguments.
			This allows use of the user-defined character
			generator RAM.  When this flag and the extended
			character flag are set, the 'blink' bit is used
			as a ninth address bit.

	function 0004 - select cursor style from AC<11>.
			0 = block, 1 = underline.
			No arguments.

	function 0005 - execute power-on clear.
			No arguments, no return is made due to forced
			restart.
			This function causes execution of the ROM
			firmware power-on routine.

	function 0006 - execute ROM firmware functions.
			AC at entry selects the ROM function to
			perform,
			0000 - Execute SETUP menu,
			7777 - Execute HALT screen,
			7776 - Execute floppy bootstrap,
			7775 - Execute Winchester bootstrap.
			No arguments, return, if any, follows the 7777
			terminator.

	function 0007 - request display status.
			No arguments, on return AC = 0 implies the
			display is stable, AC = 7777 implies the
			display is busy.
			This allows the user program to synchronize
			panel requests with the character-oriented
			control stream, especially when the display
			screen is involved.





				      page 29

	DECmate Slushware Implementation Notes	______________________________________

	function 0010 - select compatibility mode from AC<11>.
			0 = send ESC/BS/LF for those keys, send escape
			sequences from all other function keys.
			1 = handle function keys according to DEC STD
			70.
			No arguments.
			This function allows local application
			functions to access all function keys in level
			1 and relieves the application of having to
			translate an escape sequence to identify the
			ESC, BS and LF keys.  When compatibility mode
			is set, a terminal emulation program can easily
			mimic a standard DEC terminal.

	function 0011 - select keyboard case from AC<11>.
			0 = lower-case, 1 = upper-case
			No arguments.
			This function allows an operating system to
			select the keyboard 'lock' function when it
			first boots up.  Systems that do not handle
			lower-case keyboard entry should force the
			keyboard to upper-case.

	function 0012 - select local function key mode from AC<11>.
			0 = send escape sequences for the local
			function keys.
			1 = maintain a history of the local function
			keys (for access by PR3/13).
			No arguments.
			This function provides the application program
			with a mechanism of identifying the local
			function keys without the application's having
			to parse escape sequences.

	function 0013 - read local function key history into AC.
			Bits <09-11> = Print/Shift/Ctrl,
			bits <06-08> = Set-Up/Shift/Ctrl,
			bits <03-05> = F4/Shift/Ctrl,
			bits <00-02> = Break/Shift/Ctrl.
			No arguments.
			The local function key history is cleared
			immediately following execution of this
			function.  The AC equals zero if this function
			is executed when the local function key mode is
			reset.

	function 0014 - select Host Part Environment from AC<11>.
			0 = 7-bit, 1 = 8-bit
			No arguments.
			This function allows selection of the data path
			width between the user and the SLUSHWARE.  When
			set to 7-bits, the SLUSHWARE will strip the
			eighth bit of data received from the user and
			slushware will not send any data to the user



				      page 30

	DECmate Slushware Implementation Notes	______________________________________

			with the eighth bit set;  C1 control characters
			will be sent as the corresponding expansion
			escape sequence.

	function 0015 - select CAPS/SHIFT_LOCK mode from AC<11>.
			0 = CAPS_LOCK, 1 = SHIFT_LOCK.
			No arguments.
			This function allows the slushware to interpret
			the keyboard map according to local customs of
			the country (notably, France and Italy use a
			Shift-lock keyboard mode).  When this mode is
			set for Shift_lock, the lock state is reset
			whenever the 'shift' key is pressed.  When in
			Caps_lock, the lock state is toggled by
			pressing the 'lock' key and is unaffected by
			the 'shift' key.

	function 0016 - select COMPOSE mode enable/disable from AC<11>.
			0 = disable compose mode,
			1 = enable compose mode.
			No arguments.
			The compose character function requires the
			user to have cross-loaded a set of compose
			tables into panel memory (see appendix ??).

	function 0017 - select screen blank enable from AC<11>.
			0 = enable auto-blanking of the screen after
			half an hour,
			1 = disable auto-blank feature.
			No arguments.
			When this function is executed, the screen is
			enabled and the screen blank counters are
			reset.

	function 0020 - select IDIN mode from AC<11>.
			0 = disable IDIN mode,
			1 = enable IDIN mode.
			No arguments.
			This function allows an application program to
			communicate directly with a device connected to
			the keyboard port.  When this mode is enabled,
			the SLUSHWARE does not translate any data nor
			does SLUSHWARE automatically transmit any
			commands to the keyboard port.

	function 0021 - select keyclick volume or disable from AC.
			7777 implies disable keyclick,
			0007 turns on keyclick at lowest volume,
			volume increases from 0007 through 0000,
			0000 turns on keyclick at maximum volume.
			No arguments.

	function 0022 - select bell volume or disable from AC.
			7777 implies disable bell,



				      page 31

	DECmate Slushware Implementation Notes	______________________________________

			0007 turns on bell at lowest volume,
			volume increases from 0007 through 0000,
			0000 turns on bell at maximum volume.
			No arguments.

	function 0023 - select 132 column enable/disable from AC<11>.
			0 = 132 column mode allowed,
			1 = 132 column mode disabled (request for 132
			column mode will be treated as a request for 80
			column mode).
			No arguments.

	function 0024 - select soft_terminal_reset enable from AC<11>.
			0 = enable soft_terminal_reset,
			1 = disable soft_terminal_reset (to prevent
			side effects of selecting conformance level).
			No arguments.

	function 0025 - select cursor disable from AC<11>.
			0 = enable cursor,
			1 = disable cursor.
			This function allows temporary disabling of the
			cursor without affecting the user selection of
			cursor visibility.
			No arguments.

	function 0026 - select screen display width without clearing
			screen from AC<11>.
			0 = select 80 columns,
			1 = select 132 columns.
			Execution of this function does not affect the
			row address table.
			No arguments.

	function 0027 - select single character function key mode from
			AC<11>.
			0 = reset single_character_function_key mode,
			1 = set single_character_function_key mode.
			No arguments.

	function 0030 - execute a CAF instruction.
			This function executes a CAF (clear all flags)
			instruction without killing SLUSHWARE flags.
			Use of the CAF instruction by the user can
			cause SLUSHWARE to hang forever, and is not
			recommended.  It is possible to lose a
			keystroke upon execution of this function.
			No arguments .

	function 40NM - load data from user memory field M to control
			panel memory field N.  Arguments are
			1) user memory start address,
			2) panel memory start address,
			3) two's complement of number of words to



				      page 32

	DECmate Slushware Implementation Notes	______________________________________

			transfer,
			4) 7777 as terminator.
			The size of the buffer to be moved must be
			limited if the application software is to
			handle interrupts.  Note that interrupts are
			suppressed during panel execution.

	function 50NM - load data from control panel memory field M to
			user memory field N.  Arguments are
			1) panel memory start address,
			2) user memory start address,
			3) two's complement of number of words to
			transfer,
			4) 7777 as terminator.
			The size of the buffer to be moved must be
			limited if the application software is
			to handle interrupts.  Note that interrupts
			are suppressed during panel execution.

	function 60N0 - transfer control to panel memory field N,
			arguments are
			1) address to which the transfer is made,
			2) 7777 as terminator.
			If return is made, it should follow the 7777
			terminator.

	function 7000 - send data directly to keyboard, each 8-bit
			datum following the function number is passed
			to the keyboard (high nibble must be 0000),
			terminates with a 7777.  No attempt is made
			to check for reasonableness of data sent.

	function 71N0 - pass screen control data to user buffer in
			field N.  Arguments are
			1) user buffer start address, and
			2) 7777 as terminator.
			The return buffer is 29 decimal words long
			its format is
			1 - column mode (0=80, -1=132),
			2 - origin mode (0=absolute, -1=relative)
			3 - top row of scroll region
			4 - bottom row of scroll region
			5 - crt controller (DPAR) word
			6-29 - high words of row address table.
			This function allows an application program to
			get the information required for printing a
			copy of the video display.

	function 72N0 - display character string from buffer in field N
			(block TLS).  Arguments are
			1) address of character string, and
			2) 7777 as terminator.
			This function is equivalent to issuing a number
			of TLSs.  The contents of the string must be



				      page 33

	DECmate Slushware Implementation Notes	______________________________________

			graphic characters from GL and GR;  the string
			is terminated by the first C0 or C1 control
			character (including NUL).  This function must
			not be used if the screen display is actively
			scrolling or if autowrap or character insertion
			modes are enabled.

	function 7300 - position cursor to the specified row and
			column.  Arguments are
			1) row number (1 - 24), and
			2) column number (1 - 131).
			This function is equivalent to a direct cursor
			address escape sequence (CUP) and the row and
			column addressing is subject to the same
			interpretation.  This function must not be used
			if the screen display is actively scrolling or
			if autowrap or character insertion modes are
			enabled


    3.12  COMMUNICATION INTERFACE

	The ROM firmware resets the communication interface  at  power-up
	of  the  DECmate.  The  initial state will be set to asynchronous
	operation with one stop bit, eight data bits and no  parity.  The
	SLUSHWARE  sets the communication port baud rate according to the
	latest setup parameters (see section 3.9).

	When the power-up sequence is complete, and thereafter, SLUSHWARE
	does not handle the communication interface.



























				      page 34

	DECmate Slushware Implementation Notes	______________________________________

    4.0  PUBLICATIONS

	TBS.

    5.0	 PACKAGING

	SLUSHWARE is delivered  on  tracks  78  and  79  of  each  system
	diskette.

    6.0  INSTALLABILITY

	Installation of the SLUSHWARE is  transparent  to  the  user.   A
	patch utility allows easy update of SLUSHWARE on the disk.

    7.0  EASE OF USE

	DECMATE  SLUSHWARE  is  upward  compatible  from  the  DECMATE  I
	firmware,  and it is transparent to current applications software
	with specified exceptions.

	The additional features available with the DECMATE are  designed
	as  extensions  to the DECMATE I.  Use of these features will be
	familiar to current users.

    8.0  PERFORMANCE

	SLUSHWARE is constrained to return to user  memory  within  three
	milliseconds   for   normal   functions,   since  interrupts  are
	suppressed during panel code execution.  User memory must  handle
	all  pending  interrupts whenever they occur and further must run
	down any UART activity.

	Host port baud rates of 9600 maximum  can  be  handled  (if  line
	pacing   is   controlled   properly   by   XON/XOFF  protocol  in 	
	application software).

	Some panel requests can cause SLUSHWARE  execution  to  take  too
	long (see section 3.11).

    9.0	 RELIABILITY

	The tests by which the SLUSHWARE reliability is measured are TBS.

    10.0  MAINTAINABILITY

	All new SLUSHWARE is written in 6120 assembly language.  Comments
	in  the  code  provide  a  functional description of the code and
	point out specific interface  details  with  the  hardware.   The
	SLUSHWARE   is   loaded   from  disk  at  power-on.   Performance
	enhancement can be done with a release of a diskette (no hardware
	changes required).






				      page 35

	DECmate Slushware Implementation Notes	______________________________________

	Versions  of  SLUSHWARE  are  identified  with  a   monotonically
	increasing  identification  number.   This number is in the first
	location of the first sector of  SLUSHWARE  on  the  system  disk.
	This  value  is  also stored in address (1)0020 of panel RAM (for
	versions 232 and later).  This value is also available  in  octal
	ASCII  as the second parameter of the response to the DA2 request
	(for versions 243 and later).

	It is a goal of the SLUSHWARE  developers  to  maintain  backward
	compatibility so that applications that run with earlier versions
	of SLUSHWARE will work unmodified with later versions.

    11.0  MAINTENANCE SERVICE

	TBS.

    12.0  COMPATIBILITY

    12.1  PRODUCT COMPATIBILITY

	The DECmate SLUSHWARE is backward compatible with the  DECmate  I
	firmware except as noted.

	There are no user-programmable LEDs.
	
	There is no short/long buffer (not required).

	The PR2 and PR3 instruction have been changed.

	The clock IOTs have been changed.

	All video and cursor control features  are  compatible  with  the
	Video SRM (DEC STD 70).

	The DEC 8-bit DEC multinational  supplemental  character  set  is
	supported.   Note  that the DECmate II character generator ROM is
	missing the copyright sign,  the  capital  OE  ligature  and  the
	lower-case oe ligature; these will image as a space.

    12.2  STANDARDS CONFORMANCE

	TBS.

    12.3  INTERNATIONALIZATION

	The SLUSHWARE supports USASCII keyboard as a  standard.  Optional
	applications  software  allow expansion to french, german, dutch,
	french-canadian, and other keyboards as required.

	The SLUSHWARE supports character display for these languages.

	USASCII





				      page 36

	DECmate Slushware Implementation Notes	______________________________________

	UKASCII
	French
	German
	Dutch
	French-Canadian
	Spanish
	Italian
	Norwegian/Danish
	Swedish
	Finnish
	JIS Katakana *
	JIS Roman
	DEC multinational supplemental set

	(* implies not available on the DECmate III.)

	A compose function to create display characters  is  provided  in
	SLUSHWARE.  The compose tables must be crossloaded by application
	software.

	It is recommended that all applications run  in  Level  2,  8-bit
	mode  using  the  DEC  Supplemental  character  set  for  maximum
	transportability.  It is the intent of DEC to migrate  away  from
	national    replacement   character   sets   toward   the   8-bit
	multinational character set.

	ROM  firmware  uses  diskette  track  00   for   country-specific
	information  (halt  screen  text, setup screen text, and keyboard
	translation map).

    13.0  EVOLVABILITY

	Foreign language support is table driven.

	Escape sequence parsing is table driven.

	Keycode  translation  is  table  driven;   the  tables   may   be
	crossloaded by application software.

	Compose  sequences  are  table  driven;   the  tables   must   be
	crossloaded by application software.

    14.0  COSTS

	TBS

    15.0  TIMELINESS

	A working version of at least a subset of the firmware is  to  be
	available  by  7-JUN-82  for product introduction at the National
	Computer Conference (NCC).  Done.

	The product will be  announced  10-MAY-82.   Some  parts  of  the
	firmware  will  be  demonstrable at that time.  Done, DECmate was



				      page 37

	DECmate Slushware Implementation Notes	______________________________________

	able to demonstrate WPS-8 at that time.

    16.0  CONSTRAINTS AND TRADE-OFF

	SLUSHWARE may not use panel RAM fields four through  six.   These
	fields are reserved for use by application software.

	SLUSHWARE loadable image (code and  tables)  is  limited  to  two
	tracks on the diskette.

    17.0  GLOSSARY

    17.1  GLOSSARY - ACRONYMS

	CPU	Central Processing Unit
	DMA	Direct Memory Access
	ROM	Read Only Memory
	RAM	Random Access Memory (read/write)
	CRT	Cathode Ray Tube (video display)
	CRTC	CRT controller
	RTC	Real Time Clock
	UART	Universal Asynchronous Receiver-Transmitter
	TBS	To Be Specified
	LED	Light Emitting Diode (display light)
	ASCII	American Standard Code for Information Interchange
	USASCII United States ASCII
	UKASCII United Kingdom ASCII
	JMS 	Jump to subroutine
	PDL 	Program Design Language
	TIA 	Terminals Interface Architecture
	SRM 	Systems Reference Manual


    17.2  GLOSSARY - NUMBERS

	6120 	Harris' PDP-8 microcomputer
	6121	Programmable I/O controller




















				      page 38

	DECmate Slushware Implementation Notes	______________________________________

	APPENDIX A - KEYBOARD MAP LAYOUT


	This appendix defines the translation table format to be used for
	the  main  key  array  of  the  LK201 keyboard.  This area of the
	keyboard contains alphabetic, punctuation and control characters.
	Function  keys,  cursor  keys,  editing  keys and keypad keys are
	separate areas of the keyboard are handled differently.

	The following keys are excluded from the main  key  array  table,
	even though they are physically contiguous.

		Ctrl
		Lock
		Shift (right and left)
		Compose Character

	The table is in increasing order of keycodes, with  each  keycode
	entry  containing  four  values.   Each  value  is  the resulting
	character code to be sent to the user depending  on  the  current
	state  of  'Shift',  'Lock', 'Ctrl', and the Caps_lock/Shift_lock
	mode.  The first of the four entries is transmitted when the  key
	is  pressed  and  the  'shift',  'lock' and 'ctrl' states are all
	reset.  The second entry is sent if the 'shift' state is set  and
	the  'ctrl' state is reset.  The second value is sent also in the
	condition of 'lock' mode and shift_lock mode set and 'shift'  and
	'ctrl'  reset.   The  third entry is sent if the 'lock' and Caps_
	lock modes are set and the 'ctrl' and 'shift'  modes  are  reset.
	The  fourth  entry  is  sent  if  the  'ctrl'  mode  is set.  The
	following chart summarizes the above discussion.

		shift	lock	ctrl	caps/shift	column
		-----	----	----	----------	------

		off	off	off 	caps 		normal
		on 	off 	off 	caps 		shift
		off 	on 	off 	caps 		caps
		on 	on 	off 	caps 		shift
		off 	off 	on 	caps 		ctrl
		on 	off 	on 	caps 		ctrl
		off 	on 	on 	caps 		ctrl
		on 	on 	on 	caps 		ctrl
		off 	off 	off 	shift 		normal
		on 	off 	off 	shift 		shift
		off 	on 	off 	shift 		shift
		on 	on 	off 	shift 		shift
		off 	off 	on 	shift 		ctrl
		on 	off 	on 	shift 		ctrl
		off 	on 	on 	shift 		ctrl
		on 	on 	on 	shift 		ctrl

	The keyboard map table below matches that of the standard DECmate
	american  keyboard.  This differs from the TIA specification only
	in that the DECmate keyboard generates a 030 octal character from
	the key combination Ctrl-Delete;  DEC  STD  70  states  that  the


				      page 39

	DECmate Slushware Implementation Notes	______________________________________

	Delete key is unmodified by the Ctrl key.

	The character values are given in octal.  Note that a zero  value
	does not transmit a character code to the user;  the zero is used
	to signify a muted key.   Note  that  a  4000  octal  value  does
	transmit a NUL character to the user (this value is stored on the
	diskette as a 377 octal).  The key codes are in decimal.	

		normal  shift   caps	ctrl	key	key	legend
						pstn	code
		------  -----   ----	----	----	----	------

		177	177	177	030	E13	188	Delete
		015	015	015	015	C13	189	Return
		011	011	0ll	011	D00	190	Tab
		140	176	140	036	E00	191	' ~
		061	041	061	000	E01	192	1 !
		161	121	121	021	D01	193	Q
		141	101	l0l	001	C01	194	A
		172	132	132	032	B01	195	Z
		000	000	000	000	-	196	unused
		062	100	062	4000	E02	197	2 @
		167	127	127	027	D02	198	W
		163	123	123	023	C02	199	S
		170	130	130	030	B02	200	X
		074	076	074	000	B00	20l	< >
		000	000	000	000	-	202	unused
		063	043	063	033	E03	203	3 #
		145	105	105 	005	D03	204	E
		144	104	104	004	C03	205	D
		143	103	103	003	B03	206	C
		000	000	000	000	-	207	unused
		064	044	064	034	E04	208	4 $
		162	122	122	022	D04	209	R
		146	106	106	006	C04	210	F
		166	126	126	026	B04	211	V
		040	040	040	4000	A01 to	212	<space>
		040	040	040	4000	A09	213	<space>
		065	045	065	035	E05	214	5 %
		164	124	124	024	D05	215	T
		147	107	107	007	C05	216	G
		142	102	102	002	B05	217	B
		000	000	000	000	-	218	unused
		066	136	066	036	E06	219	6 ^
		171	131	131	031	D06	220	Y
		150	110	110	010	C06	221	H
		156	116	116	016	B06	222	N
		000	000	000	000	-	223	unused
		067	046	067	037	E07	224	7 &
		165	125	125	025	D07	225	U
		152	112	112	012	C07	226	J
		155	115	115	015	B07	227	M
		000	000	000	000	-	228	unused




				      page 40

	DECmate Slushware Implementation Notes	______________________________________

		normal  shift   caps	ctrl	key	key	legend
						pstn	code
		------  -----   ----	----	----	----	------
		070	052	070	177	E08	229	8 *
		151	111	111	0ll	D08	230	I
		153	113	113	013	D08	231	K
		054	054	054	000	B08	232	, ,
		000	000	000	000	-	233	unused
		071	050	071	000	E09	234	9 (
		157	117	117	017	D09	235	O
		154	114	114	014	C09	236	L
		056	956	956	999	B09	237	. .
		000	000	000	000	-	238	unused
		060	051	060	000	E10	239	0 )
		160	120	120	020	D10	240	P
		000	000	000	000	-	241	unused
		073	072	073	000	C10	242	; :
		057	077	057	037	B10	243	/ ?
		000	000	000	000	-	244	unused
		075	053	075	000	E12	245	= +
		135	175	135	035	D12	246	] }
		134	174	134	034	C12	247	\ |
		000	000	000	000	-	248	unused
		055	137	055	000	Ell	249	- _
		133	173	133	033	Dll	250	[ {
		047	042	047	000	Cll	251	' "
		000	000	000	000	-	252	unused
		000	000	000	000	-	253	unused
		000	000	000	000	-	254	unused
		000	000	000	000	-	255	unused



























				      page 41

	DECmate Slushware Implementation Notes	______________________________________


	APPENDIX B - ODT TABLE LAYOUT

	The ODT table provides a mechanism for user programs to determine
	absolute locations in panel RAM without constraining SLUSHWARE to
	fix these addresses for all time.  The initial entries in the ODT
	table are used by the CPODT debugger.

	The ODT table itself is allowed to change location  in  different
	versions  of  SLUSHWARE,  since  a  table pointer exists in fixed
	locations of panel RAM.  The table  field  (times  eight)  is  in
	location (0)0005;  the table address is in location (0)0004.

	Each entry in the ODT table consists of  two  words.   The  first
	word  is  an  address;  the second word is a field (times eight).
	Offsets are in octal.

		offset  value
 		------  -----

		0	saved status at panel entry
		2	saved AC at panel entry
		4	saved MQ at panel entry
		6	saved panel status at panel entry
		10	saved PC at panel entry
		12	saved character rendition at panel entry
			bit <00> is blink,
			bit <01> is underline,
			bit <02> is bold,
			bit <03> is reverse video
		14	saved GL character set at panel entry (this is an
			address to a code map in field one)
		16	saved GR character set at panel entry (this is an
			address to a code map in field one)
		20	saved keyboard lock state at panel entry
			0000=Off, 7777=on
		22	saved keyboard hold state at panel entry
			0000=off, 7777=on
		24	power-on routine entry point
		26	SLUSHWARE exit routine entry point
		30	keyboard receive routine entry point
		32	keyboard transmit routine entry point
		34	video end-of-frame processor routine entry point
		36	character receive routine entry point
		40	character transmit routine entry point
		42	halt processor routine entry point
		44	enqueue character to user routine entry point
		46	end of SLUSHWARE exit routine
		50	patch area in field zero (for CPODT)
		52	patch area in field one (for CPODT)
		54	CRTC row address table
		56	keyboard main array translation map
		60	enqueue string to user routine entry point
		62	country-specific patch area
		64	compose tables
		66	date and time block, the first two words form a

				      page 42

	DECmate Slushware Implementation Notes	______________________________________

			24-bit binary counter (low address is lsw) which
			is incremented by SLUSHWARE at each end-of-frame,
			the next two words are reserved for a date stamp
			(format ??)





















































				      page 43

	DECmate Slushware Implementation Notes	______________________________________

	APPENDIX C - COMPOSE CHARACTER TABLES

	The SLUSHWARE supports the 'Compose Character' key to introduce a
	compose sequence.  Non-spacing diacriticals, found on many non-US
	keyboards, are also supported.  Because of space limitations, the
	compose  tables  are not included as part of the SLUSHWARE on the
	system diskette;  these tables must  be  crossloaded  into  panel
	memory by an operating system or application.

	Each operating system should set up its  environment  at  initial
	boot time:  this initialization includes crossloading the compose
	tables and enabling the compose function.   An  operating  system
	could  choose  to  disable  compose;  it may not be sufficient to
	assume that the power-on state of SLUSHWARE will be  the  current
	state  since utilities like MASTER MENU allow booting of a system
	at times other than power-on.

	The following 6120  source  code  contains  executable  code  and
	tables  for crossloading the American compose tables.  The coding
	set used is DEC multinational, which includes US  ASCII  and  DEC
	multinational supplemental.  Operating systems that will only run
	in 7-bit mode may choose to crossload only the 7-bit  portion  of
	these  tables.   Operating  systems  that  use a different coding
	scheme (e.g., national replacement sets) must modify these tables
	for that code set.

	/ THIS 6120 CODE LOADS A COMPOSE TABLE AND SELECTS COMPOSE MODE.
	/
	AC0001= CLA CLL IAC
  	AC4000= CLA CLL CML RAR
	PR3=	6236
	/
	/
		FIELD 0
		*200
	/
	START,	CLA CLL
	/
	LBL0,	PR3		/READ ODT TABLE FROM PANEL RAM
	LBL1,	5000
		0004		/FROM PANEL (0)0004 AND (0)0005
		ODTPTR		/INTO LOCAL STORAGE
		-2
		7777
	/
		CLA CLL		/BUILD PRQ TO READ ODT TABLE
		TAD	ODTPTR
		DCA	LBL3
		TAD	ODTPTR+1
		CLL RTR
		CLL RAR
		TAD	LBL1
		DCA	LBL2
	/
		PR3		/READ ODT TABLE


				      page 44

	DECmate Slushware Implementation Notes	______________________________________

	LBL2,	0		/(MODIFIED IN CODE)
	LBL3,	0		/(MODIFIED IN CODE)
		ODTTAB		
		-70
		7777
	/
		TAD I 	XODT64	/BUILD PRQ TO READ COMPOSE TABLE LOCATION
		SNA
		JMP	LBL8	/NO ROOM IN PANEL RAM, SKIP CROSS LOAD
		DCA 	LBL7
		AC4000
		TAD I 	XODT65
		DCA	LBL6
	/
		PR3		/PANEL REQUEST TO CROSSLOAD COMPOSE TABLES
	LBL6,	0		/(MODIFIED IN CODE)
		CMPTAB		/FROM USER ADDRESS 'CMPTAB'
	LBL7, 	0		/(MODIFIED IN CODE)
		CMPTAB-CMPTEN	/MOVE ENTIRE TABLE
		7777		/TERMINATOR
	LBL8,	AC0001		/SELECT COMPOSE MODE ON
		PR3		/WITH PR3
		0016
		7777
	/
		CLA CLL		/THAT'S ALL, RETURN TO OS8
		JMP I 	K7600
	/
	/
	K7600,	7600		/OS8 ENTRY POINT
	/
	ODTPTR, ZBLOCK 2	/POINTER TO ODT TABLE IN PANEL RAM
	/
	XODT56, ODTTAB+56
	XODT57, ODTTAB+57
	XODT64, ODTTAB+64
	XODT65,	ODTTAB+65
	/
	/
	/ COMPOSE TABLES
	/
	/ THE FIRST TABLE LISTS POSSIBLE DEAD DIACRITICALS (FROM NAPLPS
	/ NON-SPACING DIACRITICAL COLUMN) AND THEIR CORRESPONDING IMAGING
	/ CHARACTERS.  THIS ALLOWS FOR SMALLER SECONDARY TABLES (SINCE,
	/ FOR EXAMPLE, A SINGLE ENTRY SUFFICES FOR ACUTE AND APOSTROPHE).
	/ THIS TABLE IS ALWAYS 0020 OCTAL WORDS LONG.
	/
	/ 	IMAGE		DEAD	NAME
	/ 	CODE		CODE
	/
	CMPTAB, 200		/200	VECTOR
		140		/201	GRAVE --> GRAVE
		047		/202	ACUTE --> APOSTROPHE
		136		/203	CIRCUMFLEX --> CIRCUMFLEX	



				      page 45

	DECmate Slushware Implementation Notes	______________________________________

		176		/204	TILDE --> TILDE
		205		/205	MACRON
		206		/206	BREVE
		207		/207	DOT
		042		/210	UMLAUT --> DOUBLE QUOTE
		057		/211	SLANT --> SLASH
		212		/212	RING
		054		/213	CEDILLA --> COMMA
		137		/214	UNDERLINE --> UNDERLINE
		215		/215	DOUBLE ACUTE
		216		/216	OGONEK
		217		/217	CARON
	/
	/ THE NEXT TABLE LISTS EACH IMAGING CHARACTER (040-176) AND EACH
	/ DEAD DIACRITICAL (200-217), POINTING EACH 'FIRST KEY' TO A
	/ TABLE OF POSSIBLE 'SECOND KEYS'.  TABLE ADDRESSES ARE RELATIVE
	/ TO THE START OF COMPOSE TABLE AREA 'CMPTAB'.  INVALID 'FIRST
	/ KEYS' POINT TO A DUMMY SECONDARY TABLE.  DELETE IS INCLUDED
	/ FOR EASE OF PROGRAMMING, BUT MUST POINT TO DUMMY.
	/
	/	ROUTINE		CHAR	CHAR
	/	ADDRESS		CODE	IMAGE
	/
		SPACE-CMPTAB	/040	' '
		BANG-CMPTAB	/041	'!'
		DBLQT-CMPTAB	/042	'"'
		DUMMY-CMPTAB	/043	'#'
		DUMMY-CMPTAB	/044	'$'
		DUMMY-CMPTAB	/045	'%'
		DUMMY-CMPTAB 	/046	'&'
		ACUTE-CMPTAB	/047	'''
		LPAREN-CMPTAB 	/050 	'('
		RPAREN-CMPTAB 	/051 	')'
		STAR-CMPTAB 	/052 	'*'
		PLUS-CMPTAB 	/053 	'+'
		COMMA-CMPTAB 	/054 	','
		MINUS-CMPTAB 	/055 	'-'
		PERIOD-CMPTAB 	/056 	'.'
		SLASH-CMPTAB	/057	'/'
		ZERO-CMPTAB	/060	'0'
		ONE-CMPTAB	/061	'1'
		TWO-CMPTAB	/062	'2'
		THREE-CMPTAB	/063	'3'
		DUMMY-CMPTAB	/064	'4'
		DUMMY-CMPTAB	/065	'5'
		DUMMY-CMPTAB	/066	'6'
		DUMMY-CMPTAB	/067	'7'
		DUMMY-CMPTAB	/070	'8'
		DUMMY-CMPTAB	/071	'9'
		DUMMY-CMPTAB	/072	':'
		DUMMY-CMPTAB	/073	';'
		LANGLE-CMPTAB 	/074 	'<'
		EQUAL-CMPTAB 	/075 	'='
		RANGLE-CMPTAB 	/076 	'>'



				      page 46

	DECmate Slushware Implementation Notes	______________________________________

		QUERY-CMPTAB	/077	'?'
		DUMMY-CMPTAB 	/100	'@'
		UPPERA-CMPTAB 	/101	'A' - START OF UPPER CASE
		DUMMY-CMPTAB 	/102	'B'   ALPHABETICS
		UPPERC-CMPTAB 	/103	'C'
		DUMMY-CMPTAB 	/104	'D'
		UPPERE-CMPTAB 	/105	'E'
		DUMMY-CMPTAB 	/106	'F'
		DUMMY-CMPTAB 	/107	'G'
		DUMMY-CMPTAB 	/110	'H'
		UPPERI-CMPTAB 	/111	'I'
		DUMMY-CMPTAB 	/112	'J'
		DUMMY-CMPTAB 	/113	'K'
		UPPERL-CMPTAB 	/114	'L'
		DUMMY-CMPTAB 	/115	'M'
		UPPERN-CMPTAB 	/116	'N'
		UPPERO-CMPTAB 	/117	'O'
		UPPERP-CMPTAB 	/120	'P'
		DUMMY-CMPTAB 	/121	'Q'
		DUMMY-CMPTAB 	/122	'R'
		UPPERS-CMPTAB 	/123	'S'
		DUMMY-CMPTAB 	/124	'T'
		UPPERU-CMPTAB 	/125	'U'
		DUMMY-CMPTAB 	/126	'V'
		DUMMY-CMPTAB 	/127	'W'
		UPPERX-CMPTAB 	/130	'X'
		UPPERY-CMPTAB 	/131	'Y'		
		DUMMY-CMPTAB 	/132	'Z'
		DUMMY-CMPTAB 	/133	'['
		DUMMY-CMPTAB 	/134	'\'
		DUMMY-CMPTAB 	/135	']'
		CIRCUM-CMPTAB 	/136	'^'
		ULINE-CMPTAB 	/137	'_'
		GRAVE-CMPTAB 	/140	'GRAVE'
		LOWERA-CMPTAB 	/141 	'A' - LOWER CASE ALPHABETICS
		DUMMY-CMPTAB 	/142	'B'
		LOWERC-CMPTAB 	/143	'C'
		DUMMY-CMPTAB 	/144	'D'
		LOWERE-CMPTAB	/145	'E'
		DUMMY-CMPTAB 	/146	'F'
		DUMMY-CMPTAB 	/147	'G'
		DUMMY-CMPTAB 	/150	'H'
		LOWERI-CMPTAB 	/151	'I'
		DUMMY-CMPTAB 	/152	'J'
		DUMMY-CMPTAB 	/153	'K'
		LOWERL-CMPTAB 	/154	'L'
		DUMMY-CMPTAB 	/155	'M'
		LOWERN-CMPTAB 	/156	'N'
		LOWERO-CMPTAB 	/157	'O'
		LOWERP-CMPTAB 	/160	'P'
		DUMMY-CMPTAB 	/161	'Q'
		DUMMY-CMPTAB 	/162 	'R'
		LOWERS-CMPTAB 	/163	'S'
		DUMMY-CMPTAB 	/164	'T'



				      page 47

	DECmate Slushware Implementation Notes	______________________________________

		LOWERU-CMPTAB 	/165	'U'
		DUMMY-CMPTAB 	/166 	'V'
		DUMMY-CMPTAB 	/167 	'W'
		LOWERX-CMPTAB 	/170 	'X'
		LOWERY-CMPTAB 	/171 	'Y'
		DUMMY-CMPTAB 	/172 	'Z'
		DUMMY-CMPTAB 	/173 	'{'
		VRTBAR-CMPTAB 	/174 	'|'
		DUMMY-CMPTAB 	/175 	'}'
		TILDE-CMPTAB 	/176 	'~'
		DUMMY-CMPTAB 	/177 	DELETE  (DELETE ALWAYS INVALID)
	/
		DUMMY-CMPTAB 	/200 	VECTOR - DEAD DIACRITICALS
		GRAVE-CMPTAB 	/201 	GRAVE
		ACUTE-CMPTAB 	/202 	ACUTE
		CIRCUM-CMPTAB 	/203 	CIRCUMFLEX
		TILDE-CMPTAB 	/204 	TILDE
		DUMMY-CMPTAB 	/205 	MACRON
		DUMMY-CMPTAB 	/206 	BREVE
		DUMMY-CMPTAB 	/207 	DOT
		DBLQT-CMPTAB 	/210 	UMLAUT
		DUMMY-CMPTAB 	/211 	SLANT
		STAR-CMPTAB	/212	RING
		COMMA-CMPTAB	/213	CEDILLA
		DUMMY-CMPTAB	/214	UNDERLINE
		DUMMY-CMPTAB	/215	DOUBLE ACUTE
		DUMMY-CMPTAB	/216	OGONEK
		DUMMY-CMPTAB	/217	CARON
	/
	/ THE SECONDARY TABLES ARE EACH TERMINATED WITH A 0000.  EACH
	/ ENTRY IS TWO WORDS:  THE FIRST IS THE 2'S COMPLEMENT OF A
	/ CHARACTER THAT FORMS A VALID COMPOSE SEQUENCE WITH THE FIRST
	/ CHARACTER (THAT POINTED TO THIS TABLE), THE SECOND WORD IS THE
	/ RESULTING COMPOSED CHARACTER.
	/
	DUMMY, 	0000 		/DUMMY TABLE, JUST A TERMINATOR
	/
	SPACE, 	-042; 	042 	/DOUBLE QUOTE
		-047; 	047 	/APOSTROPHE
		-136; 	136 	/CIRCUMFLEX
		-140; 	140 	/GRAVE
		-176; 	176 	/TILDE
		-052; 	260 	/DEGREE <-- <SPACE> *
		0000
	/
	DBLQT,	-040; 	042 	/DOUBLE QUOTE
		-141; 	344 	/LITTLE A-UMLAUT
		-145; 	353 	/LITTLE E-UMLAUT
		-151; 	357 	/LITTLE I-UMLAUT
		-157; 	366 	/LITTLE 0-UMLAUT
		-165; 	374 	/LITTLE U-UMLAUT
		-171; 	375 	/LITTLE Y-UMLAUT
		-101; 	304 	/BIG A-UMLAUT
		-105; 	313 	/BIG E-UMLAUT



				      page 48

	DECmate Slushware Implementation Notes	______________________________________

		-111; 	317	/BIG I-UMLAVT
		-117; 	326	/BIG 0-UMLAUT	
		-125; 	334	/BIG U-UMLAUT
		-131; 	335	/BIG Y-UMLAUT
		0000
	/
	ACUTE,	-040; 	047	/APOSTROPHE <-- ACUTE+SPACE
		-101; 	301	/CAPITAL 'A' WITH ACUTE
		-105; 	311	/CAPITAL 'E' WITH ACUTE
		-111; 	315	/CAPITAL 'I' WITH ACUTE
		-117; 	323	/CAPITAL 'O' WITH ACUTE
		-125; 	332	/CAPITAL 'U' WITH ACUTE
		-141; 	341	/LOWERCASE 'A' WITH ACUTE
		-145; 	351	/LOWERCASE 'E' WITH ACUTE
		-151; 	355	/LOWERCASE 'I' WITH ACUTE
		-157; 	363	/LOWERCASE 'O' WITH ACUTE
		-165; 	372	/LOWERCASE 'U' WITH ACUTE
		0000
	/
	CIRCUM, -040; 	136 	/CIRCUMFLEX <--CIRCUMFLEX+SPACE
		-101; 	302 	/CAPITAL 'A' WITH CIRCUMFLEX
		-105; 	312 	/CAPITAL 'E' WITH CIRCUMFLEX
		-111; 	316 	/CAPITAL 'I' WITH CIRCUMFLEX
		-117; 	324 	/CAPITAL 'O' WITH CIRCUMFLEX
		-125; 	333 	/CAPITAL 'U' WITH CIRCUMFLEX
		-141; 	342 	/LOWERCASE 'A' WITH CIRCUMFLEX
		-145; 	352 	/LOWERCASE 'E' WITH CIRCUMFLEX
		-151; 	356 	/LOWERCASE 'I' WITH CIRCUMFLEX
		-157; 	364 	/LOWERCASE 'O' WITH CIRCUMFLEX
		-165; 	373 	/LOWERCASE 'U' WITH CIRCUMFLEX
		-060; 	260 	/DEGREE <-- ZERO+CIRCUMFLEX
		-062; 	262 	/SUPERSCRIPT TWO <-- TWO+CIRCUMFLEX
		-063; 	263 	/SUPERSCRIPT THREE <-- THREE+CIRCUMFLEX
		-056; 	267 	/MIDDLE DOT <-- PERIOD+CIRCUMFLEX
		-061; 	271 	/SUPERSCRIPT ONE <-- ONE+CIRCUMFLEX
		-057; 	174 	/VERTICAL BAR <-- SLASH+CIRCUMFLEX
		0000
	/
	GRAVE,	-040; 	140 	/GRAVE <--GRAVE+SPACE
		-101; 	300 	/CAPITAL 'A' WITH GRAVE
		-105; 	310 	/CAPITAL 'E' WITH GRAVE
		-111; 	314 	/CAPITAL 'I' WITH GRAVE
		-117; 	322 	/CAPITAL 'O' WITH GRAVE
		-125; 	331 	/CAPITAL 'U' WITH GRAVE
		-141; 	340 	/LOWERCASE 'A' WITH GRAVE
		-145; 	350 	/LOWERCASE 'E' WITH GRAVE
		-151; 	354 	/LOWERCASE 'I' WITH GRAVE
		-157; 	362 	/LOWERCASE 'O' WITH GRAVE
		-165;	371	/LOWERCASE 'U' WITH GRAVE
		0000
	/
	TILDE, 	-040; 	176 	/TILDE <-- TILDE+SPACE
		-101; 	303 	/CAPITAL 'A' WITH TILDE
		-116;	321 	/CAPITAL 'N' WITH TILDE



				      page 49

	DECmate Slushware Implementation Notes	______________________________________

		-117; 	325	/CAPITAL 'O' WITH TILDE
		-141; 	343	/LOWERCASE 'A' WITH TILDE
		-156; 	361	/LOWERCASE 'N' WITH TILDE
		-157; 	365	/LOWERCASE 'O' WITH TILDE
		0000
	/
	BANG,	-041; 	241	/INVERTED BANG <-- BANG+BANG
		-120; 	266	/PARAGRAPH <-- BANG+P(UPPERCASE)
		-160; 	266	/PARAGRAPH <-- BANG+P(LOWERCASE)
		-123; 	247	/SECTION <-- BANG+S(UPPERCASE)
		-163; 	247	/SECTION <-- BANG+S(LOWERCASE)
		0000
	/
	LPAREN, -055; 	173	/LEFT BRACE <-- LEFT PAREN+MINUS
		-050; 	133	/LEFT BRACKET <-- LEFT PAREN+LEFT PAREN
		0000
	/
	RPAREN, -055; 	175	/RIGHT BRACE <-- RIGHT PAREN+MINUS
		-051; 	135	/RIGHT BRACKET <-- RIGHT PAREN+RIGHT PAREN
		0000
	/
	STAR, 	-040; 	260	/DEGREE <-- ASTERISK+SPACE
		-101; 	305	/CAPITAL 'A' WITH RING <-- 'A'+ASTERISK
		-141; 	345	/LITTLE 'A' WITH RING <-- 'A'+ASTERISK
		0000
	/
	PLUS,	-053; 	043	/NUMBER SIGN <-- PLUS+PLUS
		-055; 	261	/PLUS/MINUS <-- PLUS+MINUS
		0000

	/
	COMMA, 	-040; 	054	/COMMA <-- COMMA+SPACE
		-103; 	307	/CAPITAL 'C' WITH CEDILLA <-- 'C'+COMMA
		-143; 	347	/LITTLE 'C' WITH CEDILLA <-- 'C'+COMMA
		0000
	/
	MINUS, 	-050; 	173	/LEFT BRACE <-- LEFT PAREN+MINUS
		-051; 	175	/RIGHT BRACE <-- RIGHT PAREN+MINUS
		-114; 	243	/POUND STERLING <-- MINUS+'L'(UPPERCASE)
		-154;	243	/POUND STERLING <-- MINUS+'L'(LOWERCASE)
		-131; 	245	/YEN <-- MINUS+'Y'(UPPERCASE)
		-171; 	245	/YEN <-- MINUS+'Y'(LOWERCASE)
		-053; 	261	/PLUS/MINUS <-- MINUS+PLUS
		0000
	/
	PERIOD, -136; 	267	/MIDDLE DOT <-- PERIOD+CIRCUMFLEX
		0000
	/
	SLASH, 	-057; 	134	/BACKSLASH <-- SLASH+SLASH
		-074; 	134	/BACKSLASH <-- SLASH+LEFTANGLE
		-136; 	174	/VERTICAL BAR <-- SLASH+CIRCUMFLEX
		-103; 	242	/CENT <-- SLASH+'C'(UPPERCASE)
		-143; 	242	/CENT <-- SLASH+'C'(LOWERCASE)
		-125; 	265	/MICRON <-- SLASH+'U'(UPPERCASE)
		-165; 	265	/MICRON <-- SLASH+'U'(LOWERCASE)


				      page 50

	DECmate Slushware Implementation Notes	______________________________________

		-117; 	330	/UPPEROSLASH <-- SLASH+UPPERO
		-157; 	370	/LOWEROSLASH <-- SLASH+LOWERO
		0000
	/
	ZERO,	-123; 	247	/SECTION <-- ZERO+'S'(UPPERCASE)
		-163; 	247	/SECTION <-- ZERO+'S'(LOWERCASE)
		-130; 	250	/CURRENCY <-- ZERO+'X'(UPPERCASE)
		-170; 	250	/CURRENCY <-- ZERO+'X'(LOWERCASE)
		-103; 	251	/COPYRIGHT <-- ZERO+'C'(UPPERCASE)
		-143; 	251	/COPYRIGHT <-- ZERO+'C'(LOWERCASE)
		-136; 	260	/DEGREE <-- ZERO+CIRCUMFLEX
		0000
	/
	ONE, 	-136;	271	/SUPERSCRIPT '1' <-- '1'+CIRCUMFLEX
		-062;	275	/ONE-HALF <- '1 '+'2' (IN ORDER)
		-064;	274	/ONE-QUARTER <-- '1'+'4' (IN ORDER)
		0000
	/
	TWO, 	-136;	262	/SUPERSCRIPT '2' <-- '2'+CIRCUMFLEX
		0000
	/
	THREE,	-136;	263	/SUPERSCRIPT '3' <-- '3'+CIRCUMFLEX
		0000
	/
	LANGLE, -074; 	253	/LEFT ANGLE QUOTE <-- LEFT ANGLE+LEFT ANGLE
		-057; 	134	/BACKSLASH <-- LANGLE+SLASH
		0000
	/
	EQUAL, 	-114; 	243	/POUND STERLING <-- EQUAL+'L'(UPPERCASE)
		-154; 	243	/POUND STERLING <-' EQUAL+'L'(LOWERCASE)
		-131; 	245	/YEN <- EQUAL+'Y'(UPPERCASE)
		-171; 	245	/YEN <-- EQUAL+'Y'(LOWERCASE)
		0000
	/
	RANGLE, -076; 	273	 /RIGHT ANGLE QUOTE <-- RIGHT ANGLE+RIGHT ANGLE
		0000
	/
	QUERY, 	-077; 	277	/INVERTED QUERY <-- QUERY+QUERY
		0000
	/
	UPPERA, -101; 	100	/COMMERCIAL AT (@) <-- 'A'+'A'(UPPERCASE)
		-141; 	100	/COMMERCIAL AT (@) <-- A+A (MIXED CASE)
		-137; 	252	/FEMININE ORDINAL <-- UNDERSCORE+'A'(UPPERCASE)
		-140; 	300	/'A' WITH GRAVE <-- 'A'+GRAVE
		-047; 	301	/'A' WITH ACUTE <-- 'A'+APOSTROPHE
		-136; 	302	/'A' WITH CIRCUMFLEX <-- 'A'+CIRCUMFLEX
		-176; 	303	/'A' WITH TILDE <-- 'A'+TILDE
		-042; 	304	/'A' WITH UMLAUT <-- 'A'+DOUBLEQUOTE
		-052; 	305	/'A' WITH RING <-- 'A'+ASTERISK
		-105; 	306	/AE DIPHTHONG <-- 'A'+'E'(UPPERCASE)
		 0000
	/
	LOWERA, -141; 	100	/COMMERCIAL AT (@) <-- 'A'+'A'(LOWERCASE)
		-101; 	100	/COMMERCIAL AT (@) <-- A+A (MIXED CASE)



				      page 51

	DECmate Slushware Implementation Notes	______________________________________

		-137; 	252	/FEMININE ORDINAL <-- UNDERSCORE+'A'(LOWERCASE)
		-140; 	340	/'A' WITH GRAVE <-- 'A'+GRAVE
		-047; 	341	/'A' WITH ACUTE <-- 'A'+APOSTROPHE
		-136; 	342	/'A' WITH CIRCUMFLEX <-- 'A'+CIRCUMFLEX
		-176; 	343	/'A' WITH TILDE <-- 'A'+TILDE
		-042; 	344	/'A' WITH UMLAUT <-- 'A'+DOUBLEQUOTE
		-052; 	345	/'A' WITH RING <-- 'A'+ASTERISK
		-145; 	346	/AE DIPHTHONG <-- 'A'+'E'(LOWERCASE)
		0000
	/
	UPPERE, -140; 	310	/'E' WITH GRAVE <-- 'E'+GRAVE
		-047; 	311	/'E' WITH ACUTE <-- 'E'+APOSTROPHE
		-136; 	312	/'E' WITH CIRCUMFLEX <-- 'E'+CIRCUMFLEX
		-042; 	313	/'E' WITH UMLAUT <-- 'E'+DOUBLEQUOTE
		0000
	/
	LOWERE, -140; 	350	/'E' WITH GRAVE <-- 'E'+GRAVE
		-047; 	351	/'E' WITH ACUTE <-- 'E'+APOSTROPHE
		-136; 	352	/'E' WITH CIRCUMFLEX <-- 'E'+CIRCUMFLEX
		-042; 	353	/'E' WITH UMLAUT <-- 'E'+DOUBLEQUOTE
		0000
	/
	UPPERI, -140; 	314	/'I' WITH GRAVE <-- 'I'+GRAVE
		-047; 	315	/'I' WITH ACUTE <-- 'I'+APOSTROPHE
		-136; 	316	/'I' WITH CIRCUMFLEX <-- 'I'+CIRCUMFLEX
		-042; 	317	/'I' WITH UMLAUT <-- 'I'+DOUBLEQUOTE
		0000
	/
	LOWERI, -140; 	354	/'I' WITH GRAVE <-- 'I'+GRAVE
		-047; 	355	/'I' WITH ACUTE <-- 'I'+APOSTROPHE
		-136; 	356	/'I' WITH CIRCUMFLEX <-- 'I'+CIRCUMFLEX
		-042; 	357	/'I' WITH UMLAUT <-- 'I'+DOUBLEQUOTE
		0000
	/
	UPPERC, -054; 	307	/'C' WITH CEDILLA <-- COMMA+'C'(UPPERCASE)
		-057; 	242	/CENT <-- SLASH+'C'(UPPERCASE)
		-174, 	242	/CENT <-- VERTICAL BAR+'C'(UPPERCASE)
		-060; 	251	/COPYRIGHT <-- ZERO+'C'(UPPERCASE)
		-117; 	251	/COPYRIGHT <-- 'O'+'C'(UPPERCASE)
		-157; 	251	/COPYRIGHT <-- O+C (MIXED CASE)
		0000
	/
	LOWERC, -054; 	347	/'C' WITH CEDILLA <-- COMMA+'C'(LOWERCASE)
		-057; 	242	/CENT <-- SLASH+'C'(LOWERCASE)
		-174; 	242	/CENT <-- VERTICAL BAR+'S'(LOWERCASE)
		-060; 	251	/COPYRIGHT <-- ZERO+'C'(LOWERCASE)
		-157; 	251	/COPYRIGHT <-- 'O'+'C'(LOWERCASE)
		-117; 	251	/COPYRIGHT <-- O+C (MIXED CASE)
		0000
	/
	UPPERO, -140; 	322	/'O' WITH GRAVE <-- 'O'+GRAVE
		-047; 	323	/'O' WITH ACUTE <-- 'O'+APOSTROPHE
		-136; 	324	/'O' WITH CIRCUMFLEX <-- 'O'+CIRCUMFLEX
		-176; 	325	/'O' WITH TILDE <-- 'O'+TILDE



				      page 52

	DECmate Slushware Implementation Notes	______________________________________

		-042; 	326	/'O' WITH UMLAUT <-- 'O'+DOUBLEQUOTE
		-105; 	327	/OE DIPHTHONG <-- 'O'+'E'(UPPERCASE)
		-057; 	330	/'O' WITH SLASH <-- SLASH+'O' (UPPERCASE)
		-123; 	247	/SECTION <-- 'O'+'S' (UPPERCASE)
		-163; 	247	/SECTION <-- O+S (MIXED CASE)
		-130; 	250	/CURRENCY <-- 'O'+'X' (UPPERCASE)
		-170; 	250	/CURRENCY <-- O+X (MIXED CASE)
		-103; 	251	/COPYRIGHT <-- 'O'+'C' (UPPERCASE)
		-143; 	251	/COPYRIGHT <-- O+C (MIXED CASE)
		-137; 	272	/MASCULINE ORDINAL <--
				/  UNDERSCORE+'O'(UPPERCASE)
		0000
	/
	LOWERO, -140; 	362	/'O' WITH GRAVE <-- 'O'+GRAVE
		-047; 	363	/'O' WITH ACUTE <-- 'O'+APOSTROPHE
		-136; 	364	/'O' WITH CIRCUMFLEX <-- 'O'+CIRCUMFLEX
		-176; 	365	/'O' WITH TILDE <-- 'O'+TILDE
		-042; 	366	/'O' WITH UMLAUT <-- 'O'+DOUBLEQUOTE
		-145; 	367	/OE DIPHTHONG <-- 'O'+'E'(LOWERCASE)
		-057; 	370	/'O' WITH SLASH <-- SLASH+'O'(LOWERCASE)
		-163; 	247	/SECTION <-- 'O'+'S' (LOWERCASE)
		-123; 	247	/SECTION <+- O+S (MIXED CASE)
		-170; 	250	/CURRENCY <-- 'O'+'X' (LOWERCASE)
		-130; 	250	/CURRENCY <-- O+X (MIXED CASE)
		-143; 	251	/COPYRIGHT <-- 'O'+'C' (LOWERCASE)
		-103; 	251	/COPYRIGHT <-- O+C (MIXED CASE)
		-137; 	272	/MASCULINE ORDINAL <--
				/  UNDERSCORE+'O'(LOWERCASE)
		0000
	/	
	UPPERU, -140; 	331	/'U' WITH GRAVE <-- 'U'+GRAVE
		-047; 	332	/'U' WITH ACUTE <-- 'U'+APOSTROPHE
		-136; 	333	/'U' WITH CIRCUMFLEX <-- 'U'+CIRCUMFLEX
		-042; 	334	/'U' WITH UMLAUT <-- 'U'+DOUBLEQUOTE
		0000
	/
	LOWERU, -140; 	371	/'U' WITH GRAVE <-- 'U'+GRAVE
		-047; 	372	/'U' WITH ACUTE <-- 'U'+APOSTROPHE
		-136;	373	/'U' WITH CIRCUMFLEX <-- 'U'+CIRCUMFLEX
		-042; 	374	/'U' WITH UMLAUT <-- 'U'+DOUBLEQUOTE
		0000
	/
	UPPERL, -055; 	243	/POUND STERLING <-- MINUS+'L'(UPPERCASE)
		-075; 	243	/POUND STERLING <-- EQUAL+'L'(UPPERCASE)
		0000
	/
	LOWERL, -055; 	243	/POUND STERLING <-- MINUS+'L'(LOWERCASE)
		-075; 	243	/POUND STERLING <-- EQUAL+'L'(LOWERCASE)
		0000
	/
	UPPERN, -176; 	321	/'N' WITH TILDE <-- TILDE+'N' (UPPERCASE)
		0000
	/
	LOWERN, -176; 	361	/'N' WITH TILDE <-- TILDE+'N' (LOWERCASE)



				      page 53

	DECmate Slushware Implementation Notes	______________________________________

		0000
	/
	UPPERP, -041; 	266	/PARAGRAPH <-- BANG+'P' (UPPERCASE)
		0000
	/
	LOWERP, -041; 	266	/PARAGRAPH <-- BANG+'P' (LOWERCASE)
		0000
	/
	UPPERS, -060; 	247	/SECTION <-- ZERO+'S' (UPPERCASE)
		-117; 	247	/SECTION <-- 'O'+'S' (UPPERCASE)
		-157; 	247	/SECTION <-- S+LOWERO
		-041; 	247	/SECTION <-- S+!
		0000
	/
	LOWERS, -060; 	247	/SECTION <-- ZERO+'S' (LOWERCASE)
		-157; 	247	/SECTION <-- 'O'+'S' (LOWERCASE)
		-117; 	247	/SECTION <-- S+O (MIXED CASE)
		-041; 	247	/SECTION <-- S+!
		-163; 	337	/SHARP S <-- 'S'+'S' (LOWERCASE)
		0000
	/
	UPPERX, -060; 	250	/CURRENCY <-- ZERO+'X' (UPPERCASE)
		-117; 	250	/CURRENCY <-- 'O'+'X' (UPPERCASE)
		-157; 	250	/CURRENCY <-- X+O (MIXED CASE)
		0000
	/
	LOWERX, -060; 	250	/CURRENCY <-- ZERO+'X' (LOWERCASE)
		-157; 	250	/CURRENCY <-- 'O'+'X' (LOWERCASE)
		-117; 	250	/CURRENCY <-- X+O (MIXED CASE)
		0000
	/
	UPPERY, -055; 	245	/YEN <-- MINUS+'Y' (UPPERCASE)
		-075; 	245	/YEN <-- EQUAL+'Y' (UPPERCASE)
		-042; 	335	/'Y' WITH UMLAUT <--
				/ DOUBLEQUOTE+'Y' (UPPERCASE)
		0000
	/
	LOWERY, -055; 	245	/YEN <-- MINUS+'Y' (LOWERCASE)
		-075; 	245	/YEN <-- EQUAL+'Y' (LOWERCASE)
		-042; 	375	/'Y' WITH UMLAUT <--
				/ DOUBLEQUOTE+'Y' (LOWERCASE)
		0000
	/
	ULINE,	-101; 	252	/FEMININE ORDINAL <--
				/ UNDERSCORE+'A' (UPPERCASE)
		-141; 	252	/FEMININE ORDINAL <--
				/ UNDERSCORE+'A' (LOWERCASE)
		-117; 	272	/MASCULINE ORDINAL <-- UNDERSCORE+'O' (UPPER)
		-157; 	272	/MASCULINE ORDINAL <-- UNDERSCORE+'O' (LOWER)
		0000
	/
	VRTBAR, -103; 	242	/CENT <-- VERTICAL BAR+'C' (UPPERCASE)
		-143; 	242	/CENT <-- VERTICAL BAR+'C' (LOWERCASE)
		0000



				      page 54

	DECmate Slushware Implementation Notes	______________________________________

	/
	DEGREE, -040;	260	/DEGREE <-- DEGREE+SPACE
		-101;	305	/'A' WITH RING <-- DEGREE+'A' ( UPPERCASE )
		-141,	345	/'A' WITH RING <-- DEGREE+'A' (LOWERCASE)
		0000
	/
	CMPTEN=	.			/END OF COMPOSE TABLES
	/
	/
	$S$$$$$S















































				      page 55

	DECmate Slushware Implementation Notes	______________________________________

	APPENDIX D - LK201 KEYCODE TABLE

	The 8-bit keycodes transmitted  by  the  LK201  keyboard  to  the
	keyboard  input  port  of  the  DECmate  are  associated with key
	location according to the following table.  Keycodes are in octal.

		key 	    key     	description
		position    code
		--------    ----    	-----------

					local function keys

		G99	    126		Hold_Screen
		G00	    127		Print_Screen
		G01	    130		Set-Up
		G02	    131		F4  Local_Function
		G03	    132		Break

					Top-row function keys

		G05	    144		F6    Interrupt
		G06	    145		F7    Resume
		G07	    146		F8    Cancel
		G08	    147		F9    Main Screen
		G09	    150		F10   Exit	

		Gll	    161		Fll   (ESC)
		G12	    162 	F12   (BS)
		G13	    163 	F13   (LF)
		G14	    164 	F14   Additional_Options

		G15	    174 	F15   Help
		G16	    175 	F16   Do

		G20	    200 	F17
		G21	    201 	F18
		G22	    202 	Fl9
		G23	    203		F20    Hyph_Push/Hyph_Pull

					Editing keys

		E16	    212		Find
		E17	    213		Insert_Here
		E18  	    214		Remove
		D16	    215		Select
		D17	    216		Prev_Screen
		D18	    217		Next_Screen

					Application keys

		A20	    222		0   Advance
		A22	    224		.   Sel
		A23	    225		Enter  <>  Swap




				      page 56

	DECmate Slushware Implementation Notes	______________________________________

		B20	    226		1   Back_Up
		B21	    227		2   Line		
		B22	    230		3   Upper_Case
		C20	    231		4   Word
		C21	    232		5   Para
		C22	    233		6   Bold
		C23	    234		,   Paste
		D20	    235		7   Sent
		D21	    236		8   Tab_Pos
		D22	    237		9   Under_Line
		D23	    240		-   Cut
		E20	    241		PF1   <gold>
		E21	    242		PF2   Page
		E22	    243		PF3   Del_Word
		E23	    244		PF4   Del_Char

					Cursor keys

		B16	    247		<left_arrow>
		B18	    250		<right_arrow>
		B17	    251		<down_arrow)
		A17	    252		<up_arrow>

					Special control keys

		B99,B11     256		Shift (left and right)
		C99	    257		Ctrl
		C00	    260		Lock
		A99	    261		Compose_Character
		E13	    274		<x|  Word/Char (delete)
		C13	    275		Return
		D00	    276		Tab

					Main array of qraphic keys
					(legends shown are for the
					American keyboard)

		E00	    277		' ~
		E01	    300		1 !
		D01	    301		Q
		C01	    302		A
		B01	    303		Z
		E02	    305		2 @
		D02	    306		W
		C02	    307		S
		B02	    310		X
		B00	    311		< >
		E03	    313		3 #
		D03	    314		E
		C03	    315		D
		B03	    316		C
		E04	    320		4 $
		D04	    321		R
		C04	    322		F
		B04	    323		V


				      page 57

	DECmate Slushware Implementation Notes	______________________________________

		A01-	    324		<space>
		 -A09	    325		<space>
		E05	    326		5 %
		D05	    327		T
		C05	    330		G
		B05 	    331		B
		E06	    333		6 ^
		D06	    334		Y
		C06	    335		H
		B06	    336		N
		E07  	    340		7 &
		D07	    341		U
		C07	    342		J
		B07	    343		M
		E08	    345		8 *
		D08	    346		I
		C08	    347		K
		B08	    350		, ,
		E09	    352		9 (
		D09	    353		O
		C09	    354		L
		B09	    355		. .
		E10	    357		0 )
		D10	    360		P
		C10	    362		; :
		B10	    363		/ ?
		E12	    365		= +
		D12	    366		] }
		C12	    367		\ |
		Ell	    371		- _
		Dll	    372		[ {
		Cll	    373		' "

					Special keycodes

		-	    000		keyboard hardware ID
		-	    001		keyboard firmware ID
		-	    075		key down on power up error code
		-	    076		power up self-test error code
		-	    177		reserved for LK201 internal use
		-	    263		all ups
		-	    264		metronome
		-	    265		output error
		-	    266		input error
		- 	    267		KBD LOCKED acknowledge
		-	    270		TEST MODE acknowledge
		-	    271		PREFIX to keys down
		-	    272		MODE CHANGE acknowledge









				      page 58

	DECmate Slushware Implementation Notes	______________________________________

	APPENDIX E - CHARACTER GENERATOR ROM LAYOUT

	Most display characters on the DECmate II, and all characters  on
	the  DECmate  III,  are generated by the video display controller
	from the character generator ROM.  The  mapping  of  display  RAM
	contents  to  a  visible  character  is given in the table below.
	Addresses are in octal.

		address 	character
		-------		---------

		Note that the following character addresses (range 000
		- 037) map directly to the DEC line drawing set
		character codes 137 - 176 (by adding 137 to the ROM
		address)

		000		blank
		001		filled diamond
		002		half-tone, blotch
		003		HT
		004		FF
		005		CR
		006		LF
		007		degree
		010		plus-minus
		011		NL
		012		VT
		013		lower-right corner
		014		upper-right corner
		015		upper-left corner
		016		lower-left corner
		017		cross
		020		horizontal line at top of cell
		021		horizontal line at mid-top of cell
		022		horizontal line at middle of cell
		023		horizontal line at mid-bottom of cell
		024		horizontal line at bottom of cell
		025		vertical line with horizontal line to right
		026 		vertical line with horizontal line to left
		027		horizontal line with vertical line up
		030		horizontal line with vertical line down
		031		vertical line
		032		less than or equal
		033		greater than or equal
		034		lower-case pi
		035		not equal
		036		pound sterling
		037		middle dot

		Note that the following character addresses (in the
		range 040 to 176) map directly to the US ASCII coding.

		040		space
		041		! exclamation point, bang



				      page 59

	DECmate Slushware Implementation Notes	______________________________________

		042		" double quote
		043		# number sign, cross hatch, octothorpe
		044		$ dollar sign
		045		% percent
		046		& ampersand
		047		' apostrophe, acute
		050		( left parenthesis
		051		) right parenthesis
		052		* asterisk
		053		+ plus
		054		, comma
		055		- minus, hyphen
		056		. period
		057		/ slash
		060		0 zero
		061		1 one
		062		2 two
		063		3 three
		064		4 four
		065		5 five
		066		6 six
		067		7 seven
		070		8 eight
		071		9 nine
		072		: colon
		073		; semicolon
		074		< left angle, left caret
		075		= equal
		076		> right angle, right caret
		077		? question mark, query
		100		@ commercial at
		101		A
		102		B
		103		C
		104		D
		105		E
		106 		F
		107		G
		110		H
		111		I
		112		J
		113		K
		114		L
		115		M
		116		N
		117		O
		120		P
		121		Q
		122		R
		123		S
		124		T
		125		U
		126		V
		127		W



				      page 60

	DECmate Slushware Implementation Notes	______________________________________

		130		X
		131		Y
		132		Z
		133		[ left bracket
		134		\ back slash
		135		] right bracket
		136		^ caret, circumflex, up arrow
		137		_ underscore
		140		grave
		141		a
		142		b
		143		c
		144		d
		145		e
		146		f
		147		g
		150		h
		151		i
		152		j
		153		k	
		154		l
		155		m
		156		n
		157		o
		160		p
		161		q
		162		r
		163		s
		164		t
		165		u
		166		v
		167		w
		170		x
		171		y
		172		z
		173		{ left brace, left curly bracket
		174		| vertical bar (broken on DECmate II,
				  solid on DECmate III)
		175		} right brace, right curly bracket
		176		~ tilde

		177		error character, backwards query

		200		Y-acute (DECmate III only)
		201		y-acute (DECmate III only)
		202		florin (DECmate III only)
		203		dutch ij (DECmate III only)
		204		3/4 (DECmate III only)
		205		blank
		.
		.
		.
		240		blank




				      page 61

	DECmate Slushware Implementation Notes	______________________________________

		Note that the following character addresses (range 241
		through 376) map directly to the DEC multinational
		supplemental character set, where those characters are
		defined.  Additional characters have been added to the
		DECmate III character generator ROM for support of the
		emerging ANSI multinational character set.

		241		upside down exclamation point
		242		cent
		243		pound sterling
		244		umlaut, diaresis (DECmate III only,
				not DEC supplemental)
		245		yen
		246		broken vertical bar (DECmate III only,
				not DEC supplemental)
		247		section
		250		universal currency
		251		copyright (DECmate III only)
		252		feminine ordinal
		253		left angle quotation mark	
		254		logical not (DECmate III only,
				not DEC supplemental)
		255		blank
		256		registered sign (DECmate III only, not DEC
				supplemental)
		257		overline (DECmate III only, not DEC
    				supplemental)
		260		degree
		261		plus/minus
		262		superscript 2
		263		superscript 3
		264		blank
		265		micro, mu
		266		paragraph, pilcrow
		267		middle dot
		270		blank
		271		superscript 1
		272		masculine ordinal
		273		right angle quotation mark
		274		1/4
		275		1/2
		276		blank
		277		inverted question mark
		300		A-grave
		301		A-acute
		302		A-circumflex
		303		A-tilde
		304		A-umlaut
		305		A-ring
		306		AE dipthong
		307		C cedilla
		310		E-grave
		311		E-acute
		312		E-circumflex
		313		E-umlaut
		314		I-grave

				      page 62

	DECmate Slushware Implementation Notes	______________________________________

		315		I-acute
		316		I-circumflex
		317		I-umlaut
		320		capital icelandic eth (DECmate III only,
				not DEC supplemental)
		321		N-tilde
		322		O-grave
		323		O-acute
		324		O-circumflex
		325		O-tilde
		326		O-umlaut
		327		OE ligature (DECmate III only)
		330		O-slash
		331		U-grave
		332		U-acute
		333		U-circumflex
		334		U-umlaut
		335		Y-umlaut
		336		capital icelandic thorn (DECmate III only,
				not DEC supplemental)
		337		german small sharp s
		340		a-grave
		341		a-acute
		342		a-circumflex
		343		a-tilde
		344		a-umlaut
		345		a-ring
		346		ae dipthong
		347		c cedilla
		350		e-grave
		351		e-acute
		352		e-circumflex
		353		e-umlaut
		354		i-grave
		355		i-acute
		356		i-circumflex
		357		i-umlaut
		360		small icelandic eth (DECmate III only,
				not DEC supplemental)
		361		n-tilde
		362		o-grave
		363		o-acute
		364		o-circumflex
		365		o-tilde
		366		o-umlaut
		367		oe ligature (DECmate III only)
		370		o-slash
		371		u-grave
		372		u-acute
		373		u-circumflex
		374		u-umlaut
		375		y-umlaut
		376		small icelandic thorn (DECmate III only,
				not DEC supplemental)



				      page 63

	DECmate Slushware Implementation Notes	______________________________________

		377		blank

		Note that the following character addresses (in the
		range 400 - 437) map directly to the DECmate I
		alternate ROM special graphic characters 137 - 176 by
		subtracting 241 octal from the ROM address.

		400		upper left quarter block
		401		upper right quarter block
		402		lower right quarter block
		403		lower left quarter block
		404		left half block
		405		right half block
		406		upper half black
		407		lower half block
		410		lower right 3/4 block
		411		lower left 3/4 block
		412		upper right 3/4 block
		413		upper left 3/4 block
		414		upper left plus lower right quarter blocks
		415		upper right plus lower left quarter blocks
		416		middle dot
		417		right middle dot
		420		grave
		421		tilde
		422		circumflex
		423		OE ligature
		424		oe ligature
		425		lower dot
		426		lower middle dot
		427		middle dot
		430		upper middle dot
		431		upper dot
		432		bottom 1/5 block
		433		bottom 2/5 block
		434		bottom 3/5 block
		435 		bottom 4/5 block
		436		solid block
		437		upper right dot plus lower left dot

		440		blank

		Note that the following addresses (in the range	441 - 476)
		map directly to the DECmate I alternate character set
		codes 041 - 176 by subtracting 400 octal.

	 	441		cent
		442		yen
		443		pound sterling
		444		dollar
		445		pesetas
		446		florin
		447		section
		450		paragraph, pilcrow



				      page 64

	DECmate Slushware Implementation Notes	______________________________________

		451		left angle quotation mark
		452		right angle quotation mark
		453		inverted exclamation mark
		454		inverted question mark
		455		plus/minus
		456		equal
		457		registered mark
		460		1/4
		461		1/2
		462		3/4
		463		superscript 2
		464		superscript 3
		465		universal currency symbol
		466		upper middle dot plus lower right dot
		467		7 with slash
		470		logical or, solid vertical bar
		471		small dutch ij
		472		upper middle dot plus lower middle dot
		473		acute
		474		degree
		475		umlaut
		476		micro, mu
		477		german small sharp s
		500		A-acute
		501		A-grave
		502		A-circumflex
		503		A-umlaut
		504 		A-ring
		505 		A-tilde
		506 		AE ligature
		507 		C-cedilla
		510 		capital icelandic eth
		511 		E-acute
		512 		E-grave
		513 		E-circumflex
		514 		E-umlaut
		515 		I-acute
		516 		I-grave
		517 		I-circumflex
		520 		I-umlaut
		521 		N-tilde
		522 		O-acute
		523 		O-grave
		524 		O-circumflex
		525 		O-umlaut
		526 		O-tilde
		527 		O-slash
		530 		U-acute
		531 		U-grave
		532 		U-circumflex
		533 		U-umlaut
		534 		Y-acute
		535 		capital icelandic thorn
		536 		masculine ordinal



				      page 65

	DECmate Slushware Implementation Notes	______________________________________

		537		Y-umlaut
		540		a-acute
		541		a-grave
		542		a-circumflex
		543		a-umlaut
		544		a-ring
		545		a-tilde
		546		ae ligature
		547		c-cedilla
		550		small icelandic eth
		551		e-acute
		552		e-grave
		553		e-circumflex
		554		e-umlaut
		555		i-acute
		556		i-grave
		557		i-circumflex
		560		i-umlaut
		561		n-tilde
		562		o-acute
		563		o-grave
		564		o-circumflex
		565		o-umlaut
		566		o-tilde
		567		o-slash
		570		u-acute
		571		u-grave
		572		u-circumflex
		573		u-umlaut
		574		y-acute
		575		small icelandic thorn
		576		feminine ordinal

		577		blank
		.
		.
		.
		640		blank

		Note that the following ROM addresses (in the range 641
		- 776) map directly to the DEC technical character set
		codes 041 - 176 by subtracting 600 octal.  This is true
		only for the DECmate III ROM;  the DECmate II ROM has
		katakana in this area.

		641		left radical
		642		top left radical
		643		horizontal connector
		644		top integral
		645		bottom integral
		646		vertical connector
		647		top left square bracket
		650		bottom left square bracket
		651		top right square bracket



				      page 66

	DECmate Slushware Implementation Notes	______________________________________

		652		bottom right square bracket
		653		top left parenthesis
		654		bottom left parenthesis		
		655		top right parenthesis	
		656		bottom right parenthesis
		657		left middle curly brace
		660		right middle curly brace
		661		top left summation
		662		bottom left summation
		663		top vertical summation connector
		664		bottom vertical summation connector
		665		top right summation
		666		bottom right summation
		667		right middle summation
		670		blank
		671		blank
		672		blank
		673		blank
		674		less than or equal
		675		not equal
		676		greater than or equal
		677		integral
		700		therefore
		701		proportional to
		702		infinity
		703		divided by
		704		delta
		705		del, nabla
		706		capital phi
		707		capital gamma
		710		approximate to
		711		similar or equal to
		712		capital theta
		713		times, cross product
		714		capital lambda
		715		if and only if, iff
		716		implies
		717		identical to
		720		capital pi
		721		capital psi
		722		blank
		723		capital sigma, summation
		724		blank
		725		blank
		726		radical
		727		capital omega
		730		capital xi
		731		capital upsilon
		732		included in
		733		includes
		734		intersection
		735		union
		736		logical and
		737		logical or (boolean)



				      page 67

	DECmate Slushware Implementation Notes	______________________________________

		740		logical not
		741		small alpha
		742		small beta
		743		small chi
		744		small delta
		745		small epsilon
		746		small phi
		747		small gamma
		750		small eta
		751		small iota
		752		small theta
		753		small kappa
		754		small lambda
		755		blank
		756		small nu
		757		partial derivitive
		760		small pi
		761		small psi
		762		small rho
		763		small sigma
		764		small tau
		765		blank
		766		function
		767		small omega
		770		small xi
		771		small upsilon
		772		small zeta
		773		left arrow
		774		upward arrow
		775		right arrow
		776		downward arrow

		777		blank
























				      page 68

	DECmate Slushware Implementation Notes	______________________________________

	APPENDIX F - FIXED ADDRESSES IN PANEL RAM

	The following addresses have been fixed by the SLUSHWARE
	developers.  Consideration has been given to application programs,
	ROM firmware, debugging utilities (CPODT), and operating systems.

	Addresses are in octal, preceded by the field in parentheses.

	Address	  Description

	(0)0000   program counter (PC) at panel entry, initially loaded
		  with the SLUSHWARE ID with the high bit used to
		  indicate the disk format.

	(0)0001   6201, ROM firmware checks this value to verify that
		  there is slushware on the disk.

	(0)0002   0033, ROM firmware checks this value to verify that
		  there is slushware on the disk.

	(0)0003   0077, ROM firmware checks this value to verify that
		  there is slushware on the disk.

	(0)0004   ODT table address pointer.

	(0)0005   ODT table field pointer.

	(0)0020   accumulator (AC) at panel entry.

	(0)0021   status at panel entry.

	(0)0022   panel status at panel entry.

	(0)0023   multiplier quotient (MQ) at panel entry.

	(0)0024-(0)0027   Set-Up words, see section 3.9.

	(0)7777   entry point to panel code.

	(1)0000-(1)0007   handshake area between SLUSHWARE and ROM
		  firmware, TBD ??

	(1)0020   SLUSHWARE identification.

	(1)0021   ROM firmware identification, from location (7)0100 at
		  power-on.

	(1)3660-(1)3737   row address table used by ROM firmware for
		  Set-Up and Halt screens.

	(1)5125-(1)5177   operating system information area. Registered
		   users of this area are:
		  (1)5125-(1)5126  WPS




				      page 69

	DECmate Slushware Implementation Notes	______________________________________

		  (1)5127-(1)5130  CP/M-80	
		  (1)5131-(1)5132  COS-310
		  (1)5133-(1)5132  OS278
		  (1)5135-(1)5136  Master Menu
		  Operating systems developers must register with the
		  SLUSHWARE developers before using this area.

	(1)5360-(1)5777 keyboard map, see appendix D.

















































				      page 70

	DECmate Slushware Implementation Notes	______________________________________

	APPENDIX G - REVIEW OF MODIFICATIONS PER VERSION OF SLUSHWARE

	The SLUSHWARE program has been modified over the course  of  many
	months  to  provide  additional features, to improve performance,
	and of course to fix bugs.  The following  list  documents  these
	modifications.

	VERSION    	DESCRIPTION

	411	29 JUN 84 - K. A. House
	     1) fix graphics initialization to use a more reliable test for
		presence of a 'new' graphics board (see if 6150 instruction
		skips, old board or no board will not skip);
	     2) default setup to graphics cursor enable and text to color
		monitor.

	410	27 JUN 84 - K. A. House
	     1) fix 'CAF' PRQ (PR3/30/7777) to clear AC, LINK, GT and IEFF;
	     2) add graphics board initialization to  force  text  to  both
		monochrome and color monitors.

	407	25 JUN 84 - K. A. House
	     1) clear    queue     to     user     when     set/resetting
		single-character-function mode to avoid mixed data;
  	     2) don't reset local-function-key mode when doing RIS;
	     3) ensure character addressing set up properly when  erasing
		entire line with ED1 and had been in double width (hadn't
		been able to get past column 40);
	     4) change norwegian/danish display set:
		100 is @ (was A-umlaut),
		136 is ^ (was U-umlaut),
		140 is grave (was a-umlaut),
		176 is umlaut (was u-umlaut);
	     note: handling of restore cursor when scroll region limited
		and  origin  mode  set and saved cursor is out of bounds
		still not correct.

	406	31 MAY 84 - K. A. House
	     1) modify 'soft-terminal-reset' to leave newline mode alone,
		and to initialize cursor save buffer to defaults;
	     2) respond to request for UDK lock status with esc [ ? 2 3 n
		(no UDK support);
	     3) determine compose table location from ROM data at power-on,
		mark invalid space as 0000 in the ODT table (allows an
		application to enter its own compose table location);
	     4) don't allow compose mode to be set if there isn't a valid
		table location;
	     5) parameterize compose table handling to allow user-defined
		table (address and field);
	     6) adjust top and bottom when restoring cursor to handle case
		of  cursor outside scroll region when origin mode restored
		'set'.

	405	21 MAY 84 - K. A. House
	     1) send a NUL to user as 0000 (not 4000).


				      page 71

	DECmate Slushware Implementation Notes	______________________________________

	404	18 MAY 84 - K. A. House
	     1) wait at least two EOFs in 'crtini' to ensure screen erased;
	     2) don't clear DPAR erase bits when screen is to be erased as
		a side-effect;
	     3) turn off wait LED when KAMMOD reset in DECSTR;
	     4) enable screen video whenever   PR3/17/7777   is   issued,
		regardless of state requested;
	     5) don't ignore C1 controls received when scrolling.

	403	10 MAY 84 - K. A. House
	     1) fix local function keys in compatibility mode  (had  been
		mute in level 1);
	     2) save code in power-on  routine by initializing parameters
		in load rather than in code;
	     3) fix  initialization  of  DEC  multinational  supplemental
		character  set  (hadn't  mapped unused codes to the error
		character);
	     4) add PR3/0030/7777 to issue the CAF IOT and  handle  LK201
		and  EOF  flags  (may  drop  a keystroke, may be in panel
		memory for up to 20 milliseconds), a CAF  issued  by  the
		user can kill SLUSHWARE by eating its flags;
	     5) attempt to minimize screen jitter during IL, DL, and STBM
		by adjusting RAT before moving line data;
	     6) attempt to alleviate slow scroll granularity by  handling
		EOF  during  panel  execution  except  when  certain long
		duration events take place.

	402 	07 MAY 84 - K. A. House
	     1) add PR3/0026/7777 to select column mode without  clearing
		screen;
	     2) add PR3/0027/7777 to select single-char function key mode;
	     3) remove mask to eight bits for characters sent to user (via
		KRB, etc).

	401 	04 MAY 84 - K. A. House
	     1) ensure hardware erase  bits  are  cleared  at  the  first
		available EOF (had caused ED0 to act as ED2 sometimes).

	400 	01 MAY 84 - K. A. House
	     1) bump revision to indicate that we run on DECmate III  and
		IV as well as DECmate II.

	311	01 MAY 84 - K. A. House
	     1) fix cursor style Set-Up bug.

	310	01 MAY 84 - K. A. House
	     1) ensure cursor style maintained in Set-Up bits;
	     2) make C1-xmit-introducer mode independent of level 2  mode
		and host-port-environment (must test all three when ready
		to xmit a C1 control character);
	     3) lock the keyboard when queue to user is within 16 decimal
		characters of full (was 8, didn't allow for DA2 response).





				      page 72

	DECmate Slushware Implementation Notes	______________________________________

	307	24 APR 84 - K. A. House
	     1) return to user during processing of DECALN cause  we  had
		been dropping comm characters;
	     2) expand EOFCTR data block, adding two words at the end for
		operating systems to store a date, initialized to zeroes;
	     3) add PR3/0024/7777 to enable/disable DECSTR, to avoid side
		affects of selecting terminal mode during setup;
	     4) add PR3/0025/7777 to  enable/disable  cursor  visibility,
		allows  Set-Up to supress cursor without affecting user's
		cursor selection.

	306	19 APR 84 - K. A. House
	     1) add   a  two-word  counter  of  end-of-frame  interrupts,
		pointed to by the ODT table;
	     2) change   operation   of   'wpsmod'  (PR3/10/7777)  to  be
		'compatibility' mode, reset always passes esc-bs-lf as C0
		controls and other function keys as sequences, set  obeys
		TIA spec;
	     3) change autorepeat rate of non-local keys to match rest of
		keyboard (30 hz).

	 305	10 APR 84 - K. A. House
	     1) fix  handling  of  temporary   variables   when   sending
		characters to user, had hung up keyboard if function keys
		not KRBed by user fast enough;
	     2) disable  katakana  and  user-defined  character  sets  if
		DECmate III or IV;
	     3) add routine for accessing DEC technical character set for
		DECmate  III  or  IV,  won't  be  in user-RAM, will be in
		quadrant 4 of ROM.

	304	03 APR 84 - K. A. House
	     1) fix autorepeat (i hope);
	     2) fix compose (i hope);
	     3) fix keyboard error bell.

	303	02 APR 84 - K. A. House
	     1) add autorepeat to Set-Up parameters;
	     2) allocate  fixed  addresses  (1)0020   and   (1)0021   for
		SLUSHWARE and ROM IDs;
	     3) allocate space in  field  7  for  compose  tables  to  be
		cross-loaded by user;
	     4) ensure VT and FF handled as LF for pending character stuff;
	     5) add some compose code (not complete).

	302	02 MAR 84 - K. A. House
	     1) add ROM ID as third parameter of DA2 response;
	     2) load Set-Up parameter word  with  current  states  before
		starting setup or PRQing panel data to user;
	     3) avoid redundent keyboard LED code at power-on;
	     4) add PR3/0023/7777  to  disable  132  column  mode  escape
		sequence requests;
	     5) change CRTC programming if ROM ID says we are  a  DECmate
		IIe OR III.



				      page 73

	DECmate Slushware Implementation Notes	______________________________________

	301	21 DEC 83 - K. A. House
	     1) fix cursor save/restore to clean up variable  usage  (had
		gotten corrupted by unsynchronized prqs).

	300	19 DEC 83 - K. A. House
	     1) take out extra EOFs  from  erase-in-display  (wasn't  the
		right fix);
	     2) fix erase-in-display from right column by  faking  cursor
		to  left of next row and by clearing current character in
		software.

	277	16 DEC 83 - K. A. House
	     1) fix set single width line in 132-column mode (had cleared
		a field of display memory);
	     2) add pointer to keyboard map in the  ODT  table  to  allow
		applications  to cross-load maps for non-US or scientific
		keyboards;
	     3) wait two more EOFs when erasing display (had   failed  to
		erase-to-end if on top row).

	276	07 NOV 83 - K. A. House
	     1) bug fix: turn off 'Wait' LED when keyboard reenabled;
	     2) bug fix: fix PRQ block moves;
	     3) bug fix: fix bell ringing code;
	     4) expand setup parameters to include keyclick volume,  bell
		disable,  bell  volume,  VT200 mode, introducer mode, and
		host port environment;
	     5) clear queue to user  upon  selection  or  deselection  of
		'idin' mode (to avoid mixed data types);
	     6) don't  send  automatic  commands   (bell,   click,   LED,
		autorepeat inhibit) to keyboard when in 'idin' mode;
	     7) allow '>'  as  a  designating  final  character  for  the
		user-defined  character  set  (since we load the user RAM
		with the technical character set).

	275 	04 NOV 83 - K. A. House
	     1) bug fix: turn off  'Wait'  LED  when  keyboard  reenabled
		after queue to user emptied;
	     2) bug fix: hold off keyboard if not enough room in queue to
		user (had gotten partial escape sequences);
	     3) bug fix: ensure autorepeating key ignored after  keyboard
		reenabled (hadn't kept track of last valid keystroke);
	     4) tighten PRQ loops  used  for  transferring  data  to/from
		panel RAM;
	     5) add pointer to row address table in the ODTTAB (to  clean
		up use of fast block moves to display memory);
	     6) add PR3/0020/7777 to select an 'idin' mode, in which  all
		keycodes  are  passed  directly to the user (for handling
		idin hardware);
	     7) add PR3/0021/7777 to select  keyclick  volume  (had  lost
		capability  of  disabling  keyclick  when we started soft
		keyboard disable);
	     8) add PR3/0022/7777 to select bell volume.




				      page 74

	DECmate Slushware Implementation Notes	______________________________________

	274	13 OCT 83 - K. A. House
	     1) change spanish display set from section to acute  accent,
		and from tilde to umlaut accent;
	     2) add finnish (5), norwegian/danish (6),  and  swedish  (7)
		national  display  sets  with the given final designating
		character;
	     3) add PR3/0017/7777 to allow selection of screen auto-blank
		enable/disable (AC<11> = 0 implies ok to blank, = 1
		implies never blank) .

	273	07 OCT 83 - K. A. House
	     1) remove top and bottom margins from save cursor buffer;
	     2) allow 'Tab' key to auto-repeat.

	272	08 AUG 83 - K. A. House
	     1) allow 'Hold Screen' to work even if keyboard disabled;
	     2) allow local function keys when keyboard disabled if local
		function key mode is set, sound keyclick;
	     3) change 'kbybrd' routine to put the keycode  into  the  MQ
		before  testing  for  keyboard locked; 4) handle 'shift',
		'control', 'caps'  and  'allups'  when  the  keyboard  is
		disabled.

	271	05 AUG 83 - K. A. House
	     1) all non-US national character display sets lose blink  to
		get extended address;
	     2) change  italian  display  to  lower-case   i-grave,   was
		upper-case;
	     3) change french display to umlaut, was tilde;
	     4) change dutch display to 3/4 (was  @),  to  lower-case  ij
		(was  left  bracket),  to umlaut (was left brace), and to
		florin (was vertical bar);
	     5) move  initialization  of  C1  xmit  mode  and  WPS   mode
		(esc-bs-lf)  to  reset-to-initial-state  (was  in  return
		from Set-Up, causing programmed esc-bs-lf  keys  to  turn
		into escape sequences after setup);
	     6) handle multiple selective parameters for tab clear;
	     7) change response to DA1 to 'level 2', was 'level 1';
	     8) change panel request handling to use a lookup table  (was
		hard-coded);
	     9) added  Master  Menu  to   list   of   operating   systems
    		registered;
	    10) added PRQs 12 and 13 for handling local function keys.

	270	01 JUL 83 - K. A. House
	     1) fix 'ED' and 'EL' (bug from previous version);
	     2) fix shift-lock mode (bug from previous version).

	267	01 JUL 83 - R. A. House ;
	     1) added  note  for  reserved  space  in   field   one   for
		operating system dependent information;
	     2) received 240(8) character displays as the error character,
		was ignored;
	     3) handle multiple selective parameters in 'ED' and 'EL';
	     4) perform soft reset if VT52 mode  selected  from  level  2
		(not level 1 though);

				      page 75

	DECmate Slushware Implementation Notes	______________________________________

	     5) VT52 mode only returns to level 1 (never level 2);
	     6) 'decsc' and 'decrc' save the scrolling  regions  in  both 
		levels, was just level 2;
	     7) 'sgr' can selectively  disable  character  attributes  in 
		both levels, was just level 2;
	     8) 'ich' allowed only in level 2, was in both levels;
	     9) 'decstr'  turns  on  cursor,  regardless  of  the  Set-Up 
		selection;
	    10) in shift-lock mode, typing the 'Shift' key will turn  off 
		the lock state if set, was just like caps-lock mode;
	    11) reset 'shift' and 'control' flags when invoking ROM  code 
		for Set-Up, etc.

	266	15 JUN 83 - K. A. House
	     1) remove Set-Up bits that are not supported by  ROM  Set-Up 
		code   (conformance   level,   host   port   environment,  
		caps/shift lock mode, compose enable mode).

	265	13 JUN 83 - K. A. House
	     1) swap entry points for C1 xmission  mode  selection  (were 
		backwards).

	264	10 JUN 83 - K. A. House
	     1) change range check in PR3 dispatcher to allow new commands;
	     2) change number of Set-Up bits  used  to  allow  for  newly
		assigned bits.


	263	10 JUN 83 - K. A. House
	     1) add caps/shift lock mode to Set-Up bits and make a PRQ to 
		select it;
	     2) add compose enable to Set-Up  bits  and  make  a  PRQ  to
		enable/disable it;
	     3) remove extra copies of printer and comm baud rates;
	     4) move 'exit' to follow 'mod10' (saves code, easier to read);
	     5) remove extraneous CLAs from 'mod10'  and  'exit'  (speeds
		processing);
	     6) speed up 'sluin5' by adding returns from  the  middle  of 
		the routine;
	     7) add soft terminal reset escape sequence (esc [ ! p);
	     8) allow selection of VT52 mode from level 1;
	     9) don't change C1 xmit mode when selecting VT52 mode (never 
		used);
	    10) reset character mask when exiting VT52 mode;
	    11) ensure no autowrap pending  when  restoring  cursor  with
		resulting cursor not at the end of the line;
	    12) ensure tab clear  default  is  to  clear  tab  stop  (had 
		ignored it);
	    13) move clear single shift and autowrap pending from  sftrst 
		to risrt;
	    14) ensure keyboard activity keeps screen from blanking, even 
		if keyboard disabled;
	    15) handle caps/shift lock in keyboard code;




				      page 76

	DECmate Slushware Implementation Notes	______________________________________

	    16) remove keyboard reset code (shft-cntl-cr);
	    17) modify local function key sequences  for  shift  (?)  and
		control (>); 
	    18) translate dead  diacriticals  to  USASCII  equivalent  if
		compose disabled (may conflict with some national display 
		sets);
	    19) fix bug in spanish display set (capital N tilde was wrong);
	    20) move VT52 character set selection to front of lookup table  
		to  speed  processing  (hope to minimize need for xoffs in 
		'monsta' and 'hpsalc'.

	262	26 MAY 83 - K. A. House
	     1) move 'rqdsps' from 7600 page, had been  losing  the  tail 
		end of 'prqdsp'.

	261	26 MAY 83 - K. A. House 
	     1) ensure reset_to_initial_state calls the soft_terminal_reset  
		routine (common code had been moved in previous version);
	     2) ensure entire save_cursor_buffer saved  at  power_on,  so 
		that  level  2  restore  cursor  has something to use for 
		scroll margins;
	     3) add  keyboard  power_on_reset  via  the  key  combination
		'shift-control-return';
	     4) don't allow the select_environment PRQ to select an 8-bit  
		mask  in  level 1 (still sets 8-bit environment for later 
		use in level 2);
	     5) mask characters to 7 or  8  bits  from  user  PRQ  before
		calling 'displa', take mask out of 'dochar';
	     6) only allow selective disablings of  character  renditions 
		in level 2.

	260	25 MAY 83 - K. A. House
	     1) ensure modified instructions in self-load are initialized 
		dynamically;
	     2) expand cursor save buffer for scroll margins;
	     3) set G2 and G3 to DEC_supplemental if in level 2 (at  soft 
		terminal reset);
	     4) don't change host_port_environment except via PRQ or Set-Up;
	     5) only allow 8-bits in level 2;
	     6) fix setting wps_mode at return from Set-Up;
	     7) make a soft_terminal_reset subroutine;
	     8) only allow S7C1T and S8C1T in level 2.

	257	24 MAY 83 - K. A. House
	     1) fix self-load so initial constants are not modified  (had   
		wiped out system disks when saving setup parameters using 
		old ROMS);
	     2) change save/restore cursor so level 2 buffer contains  GR 
		and the scroll margins;
	     3) add  parameters to select graphic rendition to selectively 
		disable character display attributes;
	     4) change crossfield dispatchers so only data field  set  up  
		only  at entry (had set up data and instruction fields at 
		entry and exit).



				      page 77

	DECmate Slushware Implementation Notes	______________________________________

	256	12 MAY 83 - K. A. House 
	     1) wait an extra EOF in 'crtini' before  erasing  screen  to 
		sync with the CRTC;
	     2) add a 'prqact' flag (PRQ active)  so  that  the  'wtfram'
		routine won't return to the user during PRQ processing.

	255	12 MAY 83 - K. A. House
	     1) ensure data field  reset  in  'blnkln'  (had  overwritten 
		display field during erase-from-start-of-display);
	     2) move wait for EOFs from 'dosetu' to 'dsetup' to fix error  
		in erasing top line when using Set-Up menu to switch from 
		132 to 80 column mode;
	     3) move 'tdata' and increase its size (may have  overwritten
		start of 'eofpro' so no escape sequence was ever parsed.

	254	09 MAY 83 - K. A. House
	     1) move 'rat', 'tdata', and 'partb' out  of  page  1  (can't
	 	overwrite  locations  200-377 cause old ROMs rewrite this 
		area when saving Set-Up parameters);
	     2) wait a couple of EOFs upon return from  ROM  Set-Up  menu
		(should  allow  subsequent  erases  to sync properly, had 
		been improperly erasing the screen);
	     3) ensure keyboard LEDs properly set/reset at RIS (in kbxqin);
	     4) disable keyclick twice at kbxqin (RIS) in case the  first 
		is  interpreted by the keyboard as the final parameter of 
		an interrupted  keyboard  command  string (ensures it  is 
		seen as a command).

	253	05 MAY 83 - K. A. House
	     1) clear the 'CRTC' word at entry to  the  reset-to-initial-
		state  routine  so  that subsequent setting of individual 
		bits doesn't get out of synch (had seen  a  problem  with 
		reverse video).

	252	05 MAY 83 - K. A. House
	     1) allow 'ich' in level 1 (TIA spec changed);
	     2) when resetting to Set-Up parameters, set  up  the  screen 
		type  (normal  or  reverse video) before initializing the 
		CRTC (hope to fix bug seen when booting CP/M  in  gerstle 
		mode);
	     3) at start of reset-to-initial-state code, wait two end-of-
		frames  to  allow  the  keyboard transmitter queue to run 
		down (hope to fix bug of  'Hold Screen'  LED  turning  on 
		when booting CP/M);
	     4) ensure in 8-bit  environment  before  allowing  8-bit  C1 
		introducers when selecting conformance level;
	     5) don't ring the keyboard error bell  when  an  inoperative 
		key  is  typed (compose or invalid control key) (TIA spec 
		changed);
	     6) terminate processing of an unimplemented  control  string 
		upon  receipt  of  esc,  can,  sub,  or  any  C1  control 
		character (TIA spec changed, may  terminate  on  most  C0 
		control characters eventually??).




				      page 78

	DECmate Slushware Implementation Notes	______________________________________

	251	04 APR 83 - K. A. House
	     1) try forcing data and instruction fields at entry and exit 
		of  cross-field  dispatch  routines (shouldn't need this, 
		but may help catch a bug).

	250	04 APR 83 - K. A. House
	     1) handle 'Wait' LED on  return  from  calling  pushsl  from 
		field 0 (ensures correct state of the LED);
	     2) remove  'Hold Screen'  key  escape  sequence  from  table 
		(never used).

	247	01 APR 83 - K. A. House
	     1) handle 'Wait' LED on return from  calling  'pushsl'  from
		field  one,  rather  than  calling  back from field zero. 
		(had been  corrupting  the  crossfield  dispatch  routine 
		return addresses).

	246	01 APR 83 - K. A. House
	     1) change pointers to strings for keyboard control to  point 
		to one address prior to the string;
	     2) enable autorepeat when initializing keyboard;
	     3) fix bug in keyclick (had sense of flag inverted);
	     4) fix bug in handling  editing  keys  (had  crashed  if  an
		editing key was typed); 
	     5) cleanup user queue routines (silset, popsil, pushsl);
	     6) make a separate routine to handle the 'Hold Screen' LED.

	245	31 MAR 83 - K. A. House
	     1) do double skips for keyboard transmit and  receive  flags 
		to avoid hardware bug;
	     2) ensure 'sndkbq' returns with AC = 0000;
	     3) send a string to keyboard  for  received  BEL  character,
		rings bell at maximum volume;
	     4) use half-volume bell for keyboard errors;
	     5) don't allow auto-repeat of keyboard errors.

	244	30 MAR 83 - K. A. House
	     1) terminate escape sequence on  receipt  of  a  C1  control
		character;
	     2) put error characters in the DEC multinational supplemental
		set in place of any undefined characters;
	     3) ensure cursor homed for screen alignment display;
	     4) handle esc-bs-lf keys appropriately for conformance at ris;
	     5) do soft keyboard disable, handle  keyclick  in  firmware,
		ring bell for keyboard errors;
	     6) add 'sndkbq' routine to send commands strings to keyboard;
 	     7) initialize keyboard to autorepeat non-local function keys
		and editing keys;
	     8) add a routine to handle the keyboard 'Wait' LED, call  it
		whenever 'kammod' or 'locked' flags are changed.

	243	29 MAR 83 - K. A. House
	     1) move 'crtc' to page zero;
	     2) ensure CRTC syncs properly after call to ROM  for  Set-Up 
		or  Halt  screens  (fake history of column width to 80 to 
		mimic those screens;

				      page 79

	DECmate Slushware Implementation Notes	______________________________________

	     3) ensure VT52 mode only accessible from level 1;
	     4) don't  handle  end_of_frame  stuff  at  panel  exit  (see 
		version 242), just clear the EOF flag;
	     5) add erase character function (ech);
	     6) add  slushware  version  number   to   secondary   device
		attributes response.

	242	29 MAR 83 - K. A. House
	     1) fix bug in field zero to field  one  crossfield  dispatch
		receiver routine;
	     2) handle end_of_frame interrupt if  ESSF  flag  is  set  at  
		panel  exit (this makes slow scroll look smooth but could 
		cause  problems  with  the  display  if  lots  of   stuff 
		happening around the vertical blanking interval, try this 
		for a while);
	     3) wait one-half second before  reenabling  the  CRTC  video
		whenever  the  CRTC  has  been stopped for a column width
		change, this should allow the  CRTC  to  resync  and  not
		bounce so much.

	241	28 MAR 83 - K. A. House
	     1) fix  bugs  from  previous  edit  related  to   crossfield
		references and changed labels;
	     2) reenable PRQ code that was disabled  in  version  234  to
		make room for self-load and other junk.

	240	25 MAR 83 - K. A. House
	     1) add crossfield dispatch routines;
	     2) move keyboard processing code to field one to  make  more 
		room in field zero;
	     3) change subroutine calls to standard format 'JMS I XYYYYY';
	     4) initialize screen blank counters at power-on;
	     5) move sgrtab to field zero to save some CDF commands.

	237	23 MAR 83 - K. A. House
	     1) move row address table to field 0, address 0200;
	     2) move csi parameter storage to field 0, address 0314;
	     3) don't attempt to clean up the RAT for RAM refresh  if  in
		132-column mode (don't need);
	     4) speed up line swap for RAT cleanup by doing twice as much
		per loop;
	     5) change character_code_to_generator_ROM_address routine to
		use 140(8) word tables, had used 200(8) word tables;
	     6) move field one dynamic tables to high part  of  field  to 
		make  room  for  code  loaded in as SLUSHWARE (loads from 
		(0)0000 to (1)5123).

	236	22 MAR 83 - K. A. House
	     1) fix self-load bug, had tried to read an extra sector from
		track 79.;
	     2) clear control_string_in_progress flag (dcsflg) when doing 
		a RIS;
	     3) increment blank screen counter whenever the  end_of_frame
		flag is cleared (try to handle blank screen function even
		when doing lots of other stuff).


				      page 80

	DECmate Slushware Implementation Notes	______________________________________

	235	21 MAR 83 - K. A. House
	     1) ensure cannot tab past the right margin (fixes an old bug
		that hadn't surfaced);
	     2) ensure dangling labels from commented-out PR3 code return
		properly;
	     3) change rest  of  auto-incrementing  registers  references 
		from '1x' to 'REG1X';
	     4) change self-load code to use  the  RX50  convention  that
		first sector is 01, not 00;
	     5) fix self-load error reporting so it does JMS to ROM code,
		not JMP;
	     6) add a CLA before accessing (1)0000  for  test  of  system
		device (floppy or winnie);
	     7) ensure keyboard queue initialized before first attempt to
		enqueue in 'risrt'.

	234	18 MAR 83 - K. A. House
	     1) comment out a page of PRQ  code  to  make  room  for  the
		self-load code;
	     2) add code to power-on startup to perform  SLUSHWARE  self-
		load if old ROMs (pre-winnie) and new SLUSHWARE (8-bit);
	     3) change auto-incrementing register references from 'lx' to
		'REGlx' for ease of tracking usage;
	     4) add a subroutine, 'adtbhc', that  homes  the  cursor  and
		adjusts the top and bottom margins;
	     5) don't clear control-string-in-progress flag  for  CAN  or
		SUB, only supposed to clear for ST or ESC \;
	     6) ensure  no  pending  single  shift  (SS2  or  SS3)   when
		selecting VT52 emulation mode;
	     7) ensure autowrap-pending flag  is  cleared  when  entering
		autowrap mode;
	     8) move tab stops to field three, (3)7000;
	     9) absorb 'crsre' routine into 'crsres', never called alone;
	    10) change 'sgr' to save space;
	    11) ensure no 8-bit C1 introducers sent in 7-bit environment;
	    12) wait a few more frames when  switching  column  modes  to
		alleviate screen bounce;
	    13) remove 'EL0' code, never used;
	    14) ensure CRTC  initialized  earlier  in  the  RIS  code  to
		alleviate screen bounce;
	    15) ensure undefined characters in the DEC  supplemental  set 
		are displayed as errors.

	233	17 MAR 83 - K. A. House
	     1) ensure startup code executed before boot from winchester;
	     2) fix bug in 'proman', had caused 'Delete' key to look like 
		a 'Return' key.

	232	15 MAR 83 - K. A. House
	     1) ensure screen erased when column mode set or reset;
	     2) ensure column width restored on return from Set-Up menu;
	     3) boot  winchester  system  on  startup  if   loaded   from 
		winchester;




				      page 81

	DECmate Slushware Implementation Notes	______________________________________

	     4) handle select_conformance_level_2 second parameter  as  a 
		select_C1_transmission_mode,
	     5) limit  insert/delete  line  count  to  scroll  only   the 
		available lines;
	     6) change PR3/0006 to execute ROM code with a select word in 
		the   AC  (0=Set-Up,  -l=Halt,  -2=boot  floppy,  -3=boot 
		winchester), was just execute Set-Up menu;
	     7) save  SLUSHWARE  version  number  in  field  one  address 
		'frmver' so we can access it later if necessary.

	 231	14 MAR 83 - K. A. House
	     1) add spanish and italian character sets;
	     2) avoid stopping CRTC when setting column mode if no change
		implied (prevents screen bounce);
	     3) ensure control-m doesn't expand to cr-lf in newline mode;
	     4) re-enable ich code (now required);
	     5) add level l/level 2 selection to the Set-Up bit pattern;
	     6) add 7/8 bit environment selection to the Set-Up bit pattern;
	     7) reserve first  eight  decimal  words  in  field  one  for
		firmware/SLUSHWARE handshaking;
	     8) change selection of 7/8 bit  environment  from  set/reset
		escape sequence to a panel request;
	     9)	ensure firmware row address table (used for Set-Up, Halt,
		and  startup)  is not wiped out when loading SLUSHWARE in
		8-bit (3:2) mode.

	230	15 FEB 83 - K. A. House
	     1) fix bug in insert/delete line that put errors in  RAT  if 
		limited scrolling region and origin mode set;
	     2) change crtst routine to not  use  MQ  (had  caused  first 
		keycode after screen blank to get corrupted);
	     3) re-enable select_conformance_level_2 for ease of debugging;
	     4) make 'sluin5'  a  subroutine  to  ensure  modularity  and 
		remove pathological connection;
	     5) change level 2 default to 7-bit C1 introducers;
	     6) change end-of-frame handling to  save  code  (in  wtfram, 
		scrlup, scrldn, EL0, ED1, ERSWT);
	     7) delay reverting to single width on erased lines until the 
		lines are erased;
	     8) eliminate  'ich'  escape  sequence  and  code  cause  the 
		function has been eliminated from the TIA spec;
	     9) eliminate send-receive mode cause the function  has  been 
		removed from the TIA spec.

	227	28 JAN 83 - K. A. House
	     1) change PR3 14 to  PR3  7300  (can't  use  arguments  with 
		direct dispatch PR3).

	226	28 JAN 83 - K. A. House
	     1) allow control characters to autorepeat;
	     2) blank screen if no keyboard activity for about 30 minutes,
		reenable on any keystroke;
	     3) add PR3 14 to do cursor positioning;
	     4) add PR3 72X0 to write character strings.



				      page 82

	DECmate Slushware Implementation Notes	______________________________________

	225	10 JAN 83 - K. A. House
	     1) ensure delete doesn't abort escape sequence (in sluin),
	     2) change  printer  status  request  from   esc [ 1 5 n   to 
		esc [ ? 1 5 n,
	     3) change  printer  status  report   from   esc [ 1 3 n   to 
		esc [ ? 1 3 n;
	     4) remove unreferenced labels and constants.

	224	13 DEC 82 - K. A. House 
	     1) change insert character code to shuffle  four  characters 
		per loop (in chins),
	     2) change delete character code to erase two characters  per
		loop (in dch),
	     3) break up reset-to-initial-state code in attempt  to  make 
		9600 baud (in risrt),
	     note that hardware will support 8  mhz  panel  code  because 
		John Kirk is a genius.

	223	09 DEC 82 - K. A. House
	     attempt to speed up processing (to support 9600  baud)  with 
	     	these changes:
	     1) optimize table lookup internal loop (xlook);
	     2) optimize loop in designate special graphics set (spcsgr;
	     3) only use 136 positions  (was  256)  in  tab  stops  table 
		(tabint, tabclr);
	     4) optimize clear_all_tabs inner loop (tabacl);
	     5) optimize save/restore cursor inner loop and use an  extra
		frame (mapmov, crssr);
	     6) move display enable to very end of CRT initialization, add
		a few more frames to further reduce screen bounce (crtini);
	     7) optimize inner loop of character set designation  (usasc,
		bldmap);
	     8) clear only up to column 132 (was 256) when changing  line
		attributes (dhlb, dhlt, dwl, swl);
	     9) move save and restore cursor to top of their lookup table
		(fltab)

	222	08 DEC 82 - K. A. House
	     1) wait for EOF flag on return from halt processor,
	     2) don't allow selection of C1  announcer  modes  except  in 
		level ii ,
	     3) don't allow designation of  supplemental  set  except  in 
		level ii ,
	     4) initialize G2 set to USASCII (was supplemental set),
	     5) don't allow selection  of  8-bit  environment  except  in 
		level ii,
	     6) don't allow selection of level ii compatibility mode,
	     7) remove 'doset' code (was entry to setup via esc [ 1 3 tilde
		- unused),
	     8) change DA2 response  to  csi > 3 little-c  (released  for
		DECmate II internal interface by TIA),
	     9) don't load  prelude  to  the  RAT  (no  longer  used  for
		erase-from-start-of-display),




				      page 83

	DECmate Slushware Implementation Notes	______________________________________

	    10) wait several more  frames  following  CRT  initialization 
		(try to avoid screen bounce).

 	221	02 DEC 82 - K. A. House
	     1) fix bugs (typos) from version 220,
	     2) move call to clear EOF flag to end of EOF routine,
	     3) fix return from sluin for pending characters,
	     4) do  erase-from-start-of-screen  in  software  instead  of
		hardware,
	     5) optimize erase function dispatch processing,
	     6) combine cursor visibility control with EOF flag clear  in
		clreof.

	220	02 DEC 82 - K. A. House
	     1) do erase-in-line in software instead of hardware (problem
		with 4 Mhz clock).

	217	24 NOV 82 - K. A. House
	     1) make  cursor  application  mode  independent  of   keypad
		application mode (in 'procur'),
	     2) move power-on-clear code to high page in field 0 so the jump
		to rom works correctly (bug didn't allow 16d roms to work),
	     3) reset autowrap-pending flag (lstcol) in ich and dch,
	     4) change device attributes report and  select  conformation
		level to use 61/62 instead of 51/52 (in sclvl and da),
	     5) don't allow ich unless in level ii (vt200 mode),
	     6) change cursor line attribute  to  single  width  if  line 
		fully erased with erase-in-display (ed),
	     7) change decaln to use cross  from  the  line  drawing  set 
		instead of 'e',
	     8) don't treat gr's 240(8) as a space - ignore it instead,
	     9) move row address table up by two addresses in field 1 for
		erase-from-start-of-display.

	 216	05 NOV 82 - K. A. House
	     1) ensure auto-repeat doesn't conflict with CPODT patch area 
		at kbybrd+1,
	     2) ensure correct  return  from  sluin  after  dealing  with 
		pending character from EOF,
	     3) fix cursor visibility code at EOF.

	215	03 OCT 82 - K. A. House
	     1) fix scroll region cursor addressing bungle,
	     2) stop and start CRT controller at  CRTC  init  and  column 
		mode change.

	214	08 OCT 82 - K. A. House
	     1) fix 'getpar' so it doesn't loop forever on zero parameters
		(if they're to be ignored).

	213	08 OCT 82 - K. A. House
	     1) ensure keyboard  LED  matches  logical  caps  lock  state
		(currently  off)  in  the  power-on sequence (reboot from 
		setup goes through that code).



				      page 84

	DECmate Slushware Implementation Notes	______________________________________

	212	08 OCT 82 - K. A. House
	     1) fix panel request 0011 to  properly  return  the  display
		status (logical or of crtbsy and scrbsy).

	211	08 OCT 82 - K. A. House
	     1) add panel requests for select-keyboard-case  (AC<11>=0 ->
		lower,  =1 -> upper)  and request-display-status (returns 
		AC=0000 -> stable, =7777 -> unstable).

	210	07 OCT 82 - K. A. House
	     1) disallow use of esc [ 1 3 tilde to invoke the setup  menu 
		by  patching  the  tilde  out  of the csi final character 
		lookup table (can still do setup menu using PR3;6;-1).

	207	07 OCT 82 - K. A. House
	     1) change local function key order (was: hold, print, break, 
		setup,  fn4;  is:  hold,  print, setup, fn4 (reserved for 
		data/talk), break),
	     2) change   setup   invocation   to   esc [ 1 3 tilde   (was 
		esc [ 1 4 tilde).

	206	07 OCT 82 - K. A. House
	     1) fix RAT cleanup so line attributes  don't  cause  display 
		jumbling.

	205	06 OCT 82 - K. A. House
	     1) fix RAT cleanup for RAM refresh so that  line  attributes 
		stay at the proper lines.

	204	06 OCT 82 - K. A. House
	     1) change error character to reverse query (will be  in  the 
		character generator ROM at position 177),
	     2) ensure autowrap looks like cursor movement for the cursor 
		visibility control,
	     3) fix so screen doesn't erase after 'setup'.

	203	06 OCT 82 - K. A. House
	     1) use cursor history over two frames  to  determine  cursor 
		visibility  (turn off cursor if only graphics now but had 
		cursor movement previously).

	202	06 OCT 82 - K. A. House
	     1) go to  8-bit  mode  and  generate  function  key  control
		sequences when selecting VT200 mode,
	     2) do all CRTC cursor positioning at  end-of-frame  to  make
		the cursor do-the-right-thing,
	     3) change CRTC vertical synch width (from 13 to 3).

	201 	01 OCT 82 - K. A. House
	     1) ensure a NUL from the keyboard gets enqueued to the user.

	200	01 OCT 82 - K. A. House
	     1) ensure a received  space  character  appears  in  display
		memory as a 040 so PR0 requests can differentiate between 
		erased  and  over-written  screen  data  (for  DECmate  I
		compatibility).

				      page 85

	DECmate Slushware Implementation Notes	______________________________________

	177	29 SEP 82 - K. A. House
	     1) change panel entry to  process  each  bit  in  the  panel 
		status  word  (was  doing one-per-entry causing incorrect 
		emulation of certain instructions),
	     2) change mod30/mod40/mod50 to subroutines,
	     3) remove mod60 (unknown panel trap) cause we just exit anyway.

	176	28 SEP 82 - K. A. House
	     1) ignore csi sequences with colons in them,
	     2) fix  final  character  dispatching  for  non-private  csi
		sequences,
	     3) fix csi intermediate parsing.

	175	27 SEP 82 - K. A. House
	     1) add secondary device attributes request (esc [ > little-c)
		and response,
	     2) change ansi parser to accept additional private parameters 
		(?>=<),
	     3) add  select  compatibility  mode   (esc [ ps " little-p),
	     change sndstr to get strings from field 1,
	     4) don't do these unless in VT200 (level 2) mode:
		LS2/LS3/LS1R/LS2R/LS3R,
	     5) change selection of  7/8-bit  environment  to  an  escape
		sequence (was a PRQ),
	     6) add code to setup return to deselect VT200 mode and select
		7-bit mask/environment/introducers and send esc/bs/lf from
		function keys.

	174 	25 SEP 82 - K. A. House
	     1) fix PR3 move functions so they never wrap around in a field.

	173 	24 SEP 82 - K. A. House
	     1) change initial RAT to avoid erase-from-start-of-display's
		clearing the tab stops table,
	     2) change tab initialization routine to do 256 columns.

	172 	24 SEP 82 - K. A. House
	     1) remove fix from PR3 moves.

	171 	23 SEP 82 - K. A. House
	     1) fix PR3 move data instructions (were moving too much data).

	170 	23 SEP 82 - K. A. House
	     1) fix   momentary   visibility   of   26th   line    during
		erase-in-display for reverse video.

	167 	23 SEP 82 - K. A. House
	     1) clear EOF flag at panel  exit  in  attempt  to  alleviate 
		smooth 	scroll synch problems.

	166 	22 SEP 82 - K. A. House
	     1) attempt to alleviate smooth  scroll  granularity  for  lf
		(scrlup),
	     2) attempt to fix smooth scroll synch problem (sspost).



				      page 86

	DECmate Slushware Implementation Notes	______________________________________

	165	22 SEP 82 - K. A. House
	     1) fix  cursor  addressing  following  set  top  and  bottom 
		margins function,
	     2) attempt to fix smooth scroll synch problem (sspost),
	     3) pick up device attributes response from a text string,
	     4) respond as a level one display terminal  with  132-column
		extension.

	164	22 SEP 82 - K. A. House
	     1) synchronize RAT cleaning with EOF  to  support  comm  for
		IL/DL/STBM,
	     2) don't enable keyboard if user wants it disabled.

	163	21 SEP 82 - K. A. House
	     1) limit PR3 moves to one field (no wrap),
	     2) turn off cursor during active scroll,
	     3) fix equates for KRB2 and KSF2.

	162	20 SEP 82 - K. A. House
	     1) invoke code to rearrange RAT for IL, D1 and STBM.

	161	20 SEP 82 - K. A. House
	     1) change 'mode' to colmod ',
	     2) invoke ROM-based code for halt processing,
	     3) expand CPODT patch areas to seven words,
	     4) change ODTTAB (delete 'kbybrd+l',  change  'pushsl+l'  to
		'pushsl'),
	     5) add code to rearrange RAT for RAM refresh (not yet called).

	160	16 SEP 82 - K. A. House
	     1) attempt to fix smooth scroll EOF synchronization,
	     2) add PR3 71X0 for passing 'print screen' data to user,
	     3) ensure RAT set up at power-on.

	157	15 SEP 82 - K. A. House
	     1) move CRTC tables to field one,
	     2) build RAT initialization table in field one,
	     3) don't clear display on return from 'setup' unless  column
		mode has changed.

	156	15 SEP 82 - K. A. House
	     1) change default communications baud rate to 1200,
	     2) don't do GR shifts (LS1R, LS2R, LS3R) in 7-bit environment,
	     3) don't reset lstcol for DCH or ICH,
	     4) set cursor to left margin for IL and DL.

	155	13 SEP 82 - K. A. House
	     1) move floppy bootstrap and keyboard maps to field 1,
	     2) add PR3 7000 to send user data to keyboard,
	     3) ignore SS2 and SS3 in VT52 mode,
	     4) expand C0 dispatch table to avoid individual tests,
	     5) change C1 lookup table to a dispatch table for speed.





				      page 87

	DECmate Slushware Implementation Notes	______________________________________

	154	10 SEP 82 - K. A. House
	     1) add PR3 0010 for selecting special  function  key  output
		(e .g ., esc or esc 1 2 3 tilda),
	     2) add distinct character sets for VT52 mode,
	     3) ensure GR characters masked to 7 bits for use  in  escape
		sequences,
	     4) force 7-bit  environment  when  selecting  VT52  or  ANSI 
		(VT100) modes (also use 7-bit introducers),
	     5) ensure introducer mode reset when selecting 7-bit mode,
	     6) expand 'risrt' to reset  more  modes  to  their  defaults 
		(kam, curkey, srm, arm, irm, altkpd),
	     7) turn cursor on for direct cursor positioning,
	     8) ignore SI, SO, LS2, and LS3 in VT52 mode.

	153	08 SEP 82 - K. A. House
	     1) fix 'decid' entry to avoid parameter check.

	152	08 SEP 82 - K. A. House
	     1) change 'EOF' to correctly disable cursor,
	     2) use hardware erase at column mode change.

	151	07 SEP 82 - K. A. House
	     1) fix autowrap,
	     2) move dispatch and lookup tables to field 1,
	     3) change 'wtfram' so it doesn't hang in panel memory,
	     4) move foreign character tables to field 1,
	     5) move 'ODTTAB' to field 1,
	     6) break cursor save/restore code up to allow return to user
		memory,
	     7) don't fill first 32. characters of maps,
	     8) ensure character 040 is always a space.

	150	01 SEP 82 - K. A. House
	     1) fix VT52 cursor positioning to bottom line,
	     2) this version was frozen  as  version  3147  and  released 
		30-aug-82.

	147	30 AUG 82 - K. A. House
	     1)	change sense of  the  set/reset  ANSI  mode  ANSI  escape
		sequence.

	146	30 AUG 82 - K. A. House
	     1) fix character set designation,
	     2) ensure location 177 of every map is the error character.

	145	30 AUG 82 - K. A. House
	     1) add 2nd user-defined character set,
	     2) fix designating sequences for user-defined chars,
	     3) fix CPODT tables.

	144	28 AUG 82 - K. A. House
	     1) fix ICH/DCH,





				      page 88

	DECmate Slushware Implementation Notes	______________________________________

	     2) ensure multi-line scroll downs aren't jumpy in smooth mode,
	     3) add CPODT table,
	     4) reset autowrap pending flag for SCOLM/HT/IL/DL,
	     5) don't reset character attributes for DECALN,
	     6) complete RIS for TIA compatibility.

	143	28 AUG 82 - K. A. House
	     1) fix autowrap,
	     2) ensure multi-line smooth scroll ups aren't jumpy.

	142	27 AUG 82 - K. A. House
	     1) make autowrap compatible with TIA spec,
	     2) don't hold off CR during scroll,
	     3) ensure  26th  line  doesn't  become  visible   after   an 
		erase-in-display,
	     4) fix vertical jitter during smooth scroll,
	     5) remove  attempted  fix  of  horizontal   jitter   problem 
		(hardware bug).

	141	27 AUG 82 - K. A. House
	     1) move field one parameters around,
	     2) parameterize constants,
	     3) add last column flag for autowrap,
	     4) make RIS/SC/RC compatible with TIA specs,
	     5) try to fix CLREOF screen jitter,
	     6) send character to user if compose key struck.

	140	25 AUG 82 - K. A. House
	     1) use keyboard map loaded by ROM firmware  (can  no  longer 
		use NCC 2-rom set),
	     2) attempt to fix VT52 cursor positioning,
	     3) abort control sequences on receipt of CAN or SUB,
	     4) ensure RIS clears the CRTC ext char addr and user flags.

	137	24 AUG 82 - K. A. House
	     1) default baud rates to 4800,
	     2) modify layout for CPODT,
	     3) constrain ICH/DCH to visible data,
	     4) get rid of visible 26th line in reverse  video  (make  it
		reverse spaces).

	136	23 AUG 82 - K. A. House
	     1) recover from lost source file!!
	     2) fix upper half of jis katakana character set,
	     3) fix alternate ROM special graphics character set,
	     4) allow set/reset to handle several parameters.

	135	18 AUG 82 - K. A. House
	     1) fix erase from start of display.

	134	18 AUG 82 - K. A. House
	     1) fix erase in display.

	133	18 AUG 82 - K. A. House
	     1) fix erase in display functions.


				      page 89

	DECmate Slushware Implementation Notes	______________________________________


	132	18 AUG 82  K. A. House
	     1) set- erased lines to single width,
	     2) add field 3 statement to ensure correct loading.

	131	17 AUG 82 - K. A. House
	     1) invert sense of send-receive mode,
	     2) delete references to left column,
	     3) fix display address routine to handle data  above  scroll
		region in relative origin mode.

	130	16 AUG 82 - K. A. House
	     1) fix to hold off user input during scroll after escape,
	     2) turn cursor on for graphic characters,
	     3) don't send 8-bit characters to user when in 7-bit mode,
	     4) fix ED2 to erase from physical top of screen,
	     5) ensure error character available in each quadrant of  the
		character generator ROM .

	127	12 AUG 82 - K. A. House
	     1) fix problems with smooth scroll,
	     2) add PR3 function 50XY to move data from panel memory  to 
		user memory.

	126	11 AUG 82 - K. A. House
	     1) process EOF after user flag at panel entry,
	     2) clear EOF flag at entry to EOF processor,
	     3) absorb common code into movutw,
	     4) change scrldn to match fixes in scrlup,
	     5) move selection of 26 line  RAT  to  end  of  post  smooth 
		scroll stuff.

	125 	10 AUG 82 - K. A. House
	     1) changes to help firmware beat the  CRTC  to  the  RAT  at 
		start of frame,
	     2) use some common code for cursor movements,
	     3) fix partial screen smooth scroll.

	124	09 AUG 82 - K. A. House
	     1) change shuffle for scrldn  and  ssprep to  get  to  first 
		RAT line be fore CRTC does,
	     2) change some of the keyboard control codes.

	123	05 AUG 82 - K. A. House
	     1) attempt to fix smooth scroll jumpiness,
	     2) wait a couple of extra frames on column mode change  (any 
		CRT initialization).

	122	04 AUG 82 - K. A. House
	     1) fix range check for set/reset,
	     2) fix alt ROM special graphics.






				      page 90

	DECmate Slushware Implementation Notes	______________________________________

	121 	04 AUG 82 - K. A. House
	     1) fix smooth scroll by making 26th line visible  (but  full 
		of blanks),
	     2) add parameter 25 for set/reset cursor visibility.

	120	03 AUG 82 - K. A. House
	     1) add PR3 for power-on clear,
	     2) restore PR3 for executing setup menu,
	     3) ensure extra display line is single width,
	     4) select 25-line RAT during smooth scroll.

	117	28 JUL 82 - K. A. House
	     1) add constants at addresses 1-3,
	     2) use common dispatch code,
	     3) clean up power-up code a little,
	     4) fix french character set,
	     5) abort escape sequence with C1 character,
	     6) change user set designation,
	     7) remove PR3 functions for cursor enable and execute  setup
		menu.

	116	22 JUL 82 - K. A. House
	     1) limit CUU and CUD to scrolling region,
	     2) home cursor on STBM.

	115	22 JUL 82 - K. A. House
	     1) add DCS, API, OSC, PM, and ST handling.

	114	21 JUL 82 - K. A. House
	     1) fix baud rate setup.

	113	20 JUL 82 - K. A. House
	     1) blank cursor for displayed characters,
	     2) fix output from function keys,
	     3) fix ANSI sequences for locking shifts,
	     4) set baud rates in setup function.
 
	112	16 JUL 82 - K. A. House
	     1) fix CR to CRLF conversion.

	111	16 JUL 82 - K. A. House
	     1) expand keyboard CR to CR-LF if in newline mode,
	     2) add jis roman graphic character set,
	     3) change selection of 7 or 8 bit environment to a PR3.

	110	15 JUL 82 - K. A. House
	     1) fix extra half line in smooth scroll.

	107	15 JUL 82 - K. A. House
	     1) fix function key code generation,
	     2) fix control code range check.

	106	15 JUL 82 - K. A. House
	     1) add high range check for control characters.



				      page 91

	DECmate Slushware Implementation Notes	______________________________________

	105	15 JUL 82 - K. A. House
	     1) add escape sequence entry to setup menu,
	     2) disable  blink  attribute  when  in  extended   character
		addressing mode.

	104	13-JUL-82 - DTR
	     1) fixed PRQ3 to properly check for a -1 terminator,
	     2) fixed move from ROM to RAM in dsetup

	103	13 JUL 82 - K. A. House
	     1) fix keyboard transmission,
	     2) add PR3/6/7777 for setup function.

	102	12 JUL 82 - K. A. House
	     1) attempt to fix scroll up.

	l0l	12 JUL 82 - K. A. House
	     1) change order of setup parameters.

	100	09 JUL 82 - K. A. House
	     1) add screen mode to setup parameters,
	     2) fix smooth scroll (i hope).

	77	09 JUL 82 - K. A. House
	     1) set CRTC to 25 lines at first inkling of smooth scroll,
	     2) add keyclick to RIS.

 	76	09 JUL 82 - K. A. House
	     1) attempt to set up for smooth scroll soon enough to handle 
		the first line,
	     2) add reset from 'setup' block code,
	     3) attempt to fix cursor disable at EOF.

	75	08 JUL 82 - K. A. House
	     1) establish 'setup' block,
	     2) change column mode parameter to 0000 and 7777,
	     3) fix blinking bottom line in smooth scroll.

	74	07 JUL 82 - K. A. House
	     1) start user characters from 041 (was 040),
	     2) attempt to fix smooth scroll.

	73	07 JUL 82 - K. A. House
	     1) fix sspost,
	     2) use 'blotch' for error character,
	     3) fix smooth scroll,
	     4) build complete character map.

	72	06 JUL 82 - K. A. House
	     1) attempt to fix HT and BS and RI.

	71	06 JUL 82 - K. A. House
	     1) fix smooth scroll,
	     2) change HT and BS to affect only horizontal cursor.



				      page 92

	DECmate Slushware Implementation Notes	______________________________________

	70 	06 JUL 82 - K. A. House
	     1) attempt to fix 26-line RAT/24-line display.	

	67	06 JUL 82 - K. A. House
	     1) clean up page zero,
	     2) fix 26-line RAT handling.

	66	01 JUL 82 - K. A. House
	     1) use 26-line RAT for RAM refresh.

	65	24 JUN 82 - K. A. House
	     1) fix PR3 handling,
	     2) add foreign character sets.

	64	23 JUN 82 - K. A. House
	     1) fix  alt  ROM  and  alt  ROM  special  sets  (they   were
		interchanged).

	63	23 JUN 82 - K. A. House
	     1) use 4000 bit for extended characters.

	62	23 JUN 82 - K. A. House
	     1) fix 61's bugs (some of them),
	     2) add auto-select of extended character and user modes  for 
		those character sets,
	     3) re-enable 132. col.

	61	22 JUN 82 - K. A. House
	     1) add cursor off mode,
	     2) add 7 or 8 bit introducer mode,
	     3) add more locking shifts,
	     4) add more character sets,
	     5) add PRQs for cursor style,  cursor  visibility,  extended 
		character mode, user character mode.

	60	17 JUN 82 - K. A. House
	     1) now fixing the run-time errors.

	57	17 JUN 82 - K. A. House
	     1) fix 38 errors from version 56.

	56	16 JUN 82 - K. A. House
	     1) change  character  translation  to  meet  new   standards 
		(G0 - G3, GL & GR),
	     2) add eight bit translation,
	     3) add eight bit control characters,
	     4) allow choice of 'esc [' or 'csi' on output,
	     5) add LS2R & LS3R.

	55	14 JUN 82 - K. A. House
	     1) fix decaln again,
	     2) fix line attribute selection again.

	54	14 JUN 82 - K. A. House



				      page 93

	DECmate Slushware Implementation Notes	______________________________________

	     1) fix decaln cursor bungle, 
	     2) fix single width line erase bungle.

	53	14 JUN 82 - K. A. House
	     1) fix double width stuff,
	     2) clear line attributes when scrolled off screen,
	     3) reinitialize CRTC for decaln.

	52	14 JUN 82  K. A. House
	     1) fix 'ind',
	     2) add double width selection code.

	51	10 JUN 82 - K. A. House
	     1) fix IL and DL with origin mode and partial scroll region;
	     2) add DA and DECID.

	50	10 JUN 82 - K. A. House
	     1) move CRTC  data  row  initialization  to  precede  smooth 
		scroll activity (for IL, DL),
	     2) change scroll to match VT100 performance (on LF, FF,  VT,
		IND, RI, NEL, autowrap) with limited scroll regions.

	47	09 JUN 82 - K. A. House
	      1) fix smooth scroll down,
	      2) fix scroll up for limited scrolling regions.
	
	46	08 JUN 82 - K. A. House
	      1) fix scroll,
	      2) fix screen alignment,
	      3) add IL and DL to the parsing tables.

	45	07 JUN 82 - K. A. House
	      1) clean up page zero,	
	      2) fix EOF processor,
	      3) compress keyboard IOT processing,
	      4) add local mode,
	      5) add insert/delete line(s),
	      6) add screen alignment display,
	      7) fix cursor position report,
	      8) add PR3 print character and select video enable.

	44	03 JUN 82 - K. A. House
	      1) don't reset/start CRT chip,
	      2) swap order of test for user request and EOF.

	43	28 MAY 82 - K. A. House
	      1) fix KRS handling,
 	      2) disable clock interrupts at power-on.

	42	28 MAY 82 - K. A. House
	      1) fix control character decoding,
	      2) fix scroll,
	      3) speed up character display, etc.




				      page 94

	DECmate Slushware Implementation Notes	______________________________________

	41	27 MAY 82 - K. A. House
	     1) add look-ahead character buffering during scroll operations.

	40	27 MAY 82 - K. A. House
	     1) fix smooth scroll down,
	     2) set smooth scroll rate to two rasters per frame,
	     3) fix reset to initial state.

	37	26 MAY 82 - K. A. House
	     1) fix smooth scroll,
	     2) add smooth scroll down.

	36	25 MAY 82 - K. A. House
	     1) fix smooth scroll.

	35	25 MAY 82 - K. A. House
	     1) fix smooth scroll.

	34	25 MAY 82 - K. A. House
	     1) fix smooth scroll,
	     2) add smooth scroll down.

	33	24 MAY 82 - K. A. House
	     1) add some more smooth scroll stuff.

	32	24 MAY 82 - K. A. House
	     1) add some smooth scroll stuff for checkout.

	31	21 MAY 82 - K. A. House
	     1) fix erase from start of display (i hope).

	30	20 MAY 82 - K. A. House
	     1) add delete character (dch),
	     2) supress leading zeroes for cursor position report (cpr).

	27	20 MAY 82 - K. A. House
	     1) fix erase from start of display (?).

	26	19 MAY 82 - K. A. House
	     1) fix erase from start of display again.

	25	19 MAY 82 - K. A. House
	     1) fix erase from start of display (ED1).

	24	19 MAY 82 - K. A. House
	     1) add erase from start to cursor (EL1, ED1)

	23	19 MAY 82 - K. A. House
	     1) speed up and fix character insertion.

	22	18 MAY 82 - K. A. House
	     1) add insert character (ICH),
	     2) change dspad to build a CDF instruction in 'xdispl'.




				      page 95

	DECmate Slushware Implementation Notes	______________________________________

	21	18 MAY 82 - K. A. House
	     1) add single shifts,
	     2) reset to initial.

	20	13 MAY 82 - K. A. House
	     1) add PR3 handling,
	     2) fix character set selection,
	     3) fix PRQ 'getdat' routine.

	17	13 MAY 82 - K. A. House
	     1) add panel request handling.

	16	12 MAY 82 - K. A. House
	     1) send capital R with cursor position report.

	15	12 MAY 82 - K. A. House
	     1) wait for first end-of-frame at power-on.

	14	12 MAY 82 - K. A. House
	     1) fix scroll bug,
	     2) add origin mode to save cursor code .

	13	12 MAY 82 - K. A. House
	     1) fix set/reset returns.

	12	12 MAY 82 - K. A. House
	     1) reset halt flag,
	     2) fix ttitto dispatching,
	     3) reduce code size of set/reset.

	11	12 MAY 82 - K. A. House
	     1) add keyboard lock/unlock per silo status.

	10	12 MAY 82 - K. A. House
	     1) change ttitto dispatching to go faster,
	     2) delete check for power-on flag.

	7	12 MAY 82 - K. A. House
	     1) change character conversion to go faster.

	XX	11 MAY 82 - K. A. House
	     1) avoid multiple KCFs.

	XX	11 MAY 82 - K. A. House
	     1) fix set/reset auto-repeat (keyboard commands wrong).

	XX	08 MAY 82 - K. A. House
	     1) add set/reset auto-repeat.

	XX	08 MAY 82 - K. A. House
	     1) don't check erase done bit.

	XX	08 MAY 82 - K. A. House
	     1) fix keyboard xmit enqueueing,
	     2) fix KRS handling.


				      page 96

	DECmate Slushware Implementation Notes	______________________________________

	XX	07 MAY 82 - K. A. House
	     1) fix hold LED polarity,
	     2) dummy out the 132 character mode select table entry.

	XX	06 MAY 82 - K. A. House
	     1) fix scroll once more,
	     2) ensure  characters  generated   by   SLUSHWARE   announce 
		themselves to the user.

	XX	06 MAY 82 - K. A. House
	     1) fix scroll,
	     2) VT52 cursor handling,
	     3) hold screen return,
	     4) backslash caps value.

	XX	06 MAY 82 - R. A. House
	     1) fix keyboard function key determination

	XX	05 MAY 82 - R. A. House
	     1) add ANSI set/reset primitives,
	     2) add VT52 escape sequence parsing and keycode translation.

	XX	04 MAY 82 - K. A. House
	     1) add LEDs,
	     2) general clean-up.

	XX	04 MAY 82 - K. A. House
	     1) add hold screen,
	     2) fix scroll,
	     3) etc.

	XX	03 MAY 82 - K. A. House
	     1) add device status report.

	XX	03 MAY 82 - K. A. House
	     1) fix scroll within screen.

	XX	02 MAY 82 - K. A. House
	     1) fix keyboard transmit routines,
	     2) fix set top and bottom margins,
	     3) add home cursor to origin mode changes,
	     4) add ANSI set and reset modes to parse tables.

	XX	01 MAY 82 - K. A. House
	     1) fix erase functions,
	     2) speed up display.

	XX	01 MAY 82 - K. A. House
	     1) add erase functions,
	     2) break out write cursor as a separate routine.

	XX	30 APR 82 - K. A. House
	     1) removed disk loader.




				      page 97

	DECmate Slushware Implementation Notes	______________________________________

	XX	29 APR 82 - K. A. House
	     1) added keyboard transmit routines,
	     2) cursor save-restore,
	     3) newline mode,
	     4) fixed initial tab positions,
	     5) etc.

	XX	29 APR 82 - D. Rice
	     1) added handling of ESC, BS and LF keys

	XX	28 APR 82 - K. A. House
	     1) fix cursor update,
	     2) other fixes.

	XX	27 APR 82 - K. A. House
	     1) add synchronization to EOF.

	XX	27 APR 82 - K. A. House
	     1) corrected problems to get characters to the screen properly

	XX	27 APR 82 - K. A. House
	     1) more bug fixing (RAT setup, ESC flag).

	XX	26 APR 82 - K. A. House
	     1) fix bugs from ROM testing,
	     2) add tabs.

	XX	26 APR 82 - K. A. House
	     1) add rudimentary main memory code.

	XX	25 APR 82 - K. A. House
	     1) fix bugs

	XX	24 APR 82 - K. A. House
	     1) clean up top level,
	     2) comments,
	     3) etc.

	XX	23 APR 82 - K. A. House
	     1) add D. Rice's top level code

	XX	22 APR 82 - K. A. House
	     1) add J. Kirk's boot code,
	     2) clean up

	XX	21 APR 82 - K. A. House
	     1) cleaned up links,
	     2) added initialization

	XX	20 APR 82 - K. A. House
	     1) added primitives, constants, definitions






				      page 98

	DECmate Slushware Implementation Notes	______________________________________

	APPENDIX H - MODIFICATIONS SINCE ISSUE 9 OF THIS DOCUMENT

	The SLUSHWARE program has been modified over the course  of  many
	months  to  provide  additional features, to improve performance,
	and of course to fix bugs.  The following  list  documents  the
	modifications made since issue 9 of this document.

	VERSION    	DESCRIPTION

	422	23 DEC 85 - K. A. House
	     1) fix handling of autorepeat at RIS (had failed to  get  it 
		from setup params, always turned it on).

	421	22 NOV 85 - K. A. House
	     1) reset eofok flag on every  panel  exit  (had  stayed  set 
		until  we  got  an eof while in panel RAM), this seems to 
		make slow scroll look smoother;
	     2) move label tabcl8 to correct place (had been in the wrong 
		routine!);
	     3) additional test for cursor visibility: if cursor movement 
		and  have  been  in  panel RAM for a long time, then make 
		cursor invisible for just this frame (crt timing  changes 
		in  420 caused a phantom cursor to appear on the top line 
		sometimes);
	     4) in clreof routine, change  skp  to  jmp  to  next  useful 
		instruction to save time;
	     5) at  restore  cursor,  force  cursor  visibility  off   by 
		pretending  to  have  graphic chars after cursor movement 
		(looked bad when cursor was forced on);
	     6) in mapmov routine, avoid calling adjtbd (unnecessary here, 
		had forced cursor on when doing save/restore cursor).

	420	23 SEP 85 - K. A. House
	     1) use 25 (decimal) lines for CRTC programming  for both the 
		DECmate  II  and  III.  this  saves room in slushware and 
		gives us more time at the end-of-frame.  RAM  refresh  is 
		handled by an extra (26th) line given to us gratis by the 
		CRTC controller chip.

	417	14 AUG 85 - K. A. House
	     1) try to fix DECmate III problem with double-wide lines set 
		immediately  after  a  change  in  column  width.  by  a) 
		waiting  a  couple  of  frames  to   synchronize   before 
		programming  CRTC and external logic, and b) changing the 
		number of vertical lines in the CRTC programming from  26 
		(decimal) to 25 (decimal) only for the DECmate III.

	416	03 JUL 85 - K. A. House 
	     1) add swiss nrc, designated by '=';
	     2) fix unimplemented intermediates, had  caused  early  exit 
		from  parser  and printed what should have been the final 
		character;
	     3) save blink character rendition in  these  nrcs:  germany, 
		italy,  swedish,  jis  roman,  swiss, and finland - still 
		lose blink for france, spain, dutch, and norway/denmark;


				      page 99

	DECmate Slushware Implementation Notes	______________________________________

	     4) fix compose error bell volume, had sometimes been  louder 
		than normal, should be softer.
 
	415	29 MAR 85 - K. A. House 
	     1) fix graphics option initialization  on  DECmate  II,  had 
		failed to force text to display on the color monitor (was 
		a bad equate for one of the graphics IOTs).

	414	08 MAR 85 - K. A. House 
	     1) fix graphics option initialization  on  DECmate  II,  had 
		failed  to clear the screen when 19H ROMS were installed, 
		worked fine with 19N ROMs; DECmate III has been ok;
	     2) fix smooth scroll bug that caused bottom line  to  revert 
		to single width;
	     3) add another setup word in page zero;
	     4) reserve two bits in setup word for storing terminal id;
	     5) fix the following addresses so applications can determine 
		terminal  state:  (0)0044 altkpd, (0)0045 nlmmod, (0)0112 
		top, (0)113 bottom, (3)7000 tabs;
	     6) add the following entries to  ODT  table:  irmmod,  wrap, 
		curkey, kammod.

	413	12 SEP 84 - K. A. House 
	     1) append shift/lock/control bits  to  main  array  keys  in 
		single-character-function_key  mode  (these high bits had 
		been  cleared),  this  change  is  necessary  for  MS-DOS 
		extended calls used by Lotus 1-2-3.

	412	06 AUG 84 - K. A. House 
	     1) fix graphics  initialization  to  ensure  display  memory 
		cleared  by  waiting  until  screen memory cleared before 
		synching videos and writing all four registers  two  with 
		7777 (DECmate II failed at times to fully clear screen);
	     2) fix graphics initialization to ensure text forced to both 
		monitors for a new board (DECmate III had failed to reset 
		register one at a software reboot).





















				      page 100