OS/8 SOFTWARE SUPPORT MANUAL


				  (Version 3)




















				  DISCLAIMER

		This document file was created by scanning  the
		original  document and then editing the scanned
		text.  As much as possible, the	 original  text
		format	was restored.  Some format changes were
		made to insure this  document  would  print  on
		current laser printers using 60 lines per page.
		The  original  spelling	 and  grammar  has been
		preserved.


		1-Sep-1996











			 OS/8 SOFTWARE SUPPORT MANUAL



				  (Version 3)





			       DEC-S8-OSSMB-A-D






























	    -------------------------------------------------------
	    | Order additional copies as directed on the Software |
	    | Information page at the back of this document.      |
	    -------------------------------------------------------


	    digital equipment corporation * maynard, massachusetts


					       First Printing, January 1973
							 Revised, June 1974





     The information in this document is subject to change without notice
     and should not be construed as a commitment by Digital Equipment
     Corporation.  Digital Equipment Corporation assumes no responsibility
     for any errors that may appear in this manual.

     The software described in this document is furnished to the purchaser
     under a license for use on a single computer system and can be copied
     (with inclusion of DIGITAL's copyright notice) only for use in such
     system, except as may otherwise be provided in writing by DIGITAL.

     Digital Equipment Corporation assumes no responsibility for the use
     or reliability of its software on equipment that is not supplied by
     DIGITAL.







	 Copyright (C) 1973, 1974 by Digital Equipment Corporation





     The HOW TO OBTAIN SOFTWARE INFORMATION page, located at the back of
     this document, explains the various services available to DIGITAL
     software users.

     The postage prepaid READER'S COMMENTS form on the last page of this
     document requests the user's critical evaluation to assist us in
     preparing future documentation.






     The following are trademarks of Digital Equipment Corporation:

       CDP              DIGITAL          INDAC            PS/8
       COMPUTER LAB     DNC              KA10             QUICKPOINT
       COMSYST          EDGRIN           LAB-8            RAD-8
       COMTEX           EDUSYSTEM        LAB-8/e          RSTS
       DDT              FLIP CHIP        LAB-K            RSX
       DEC              FOCAL            OMNIBUS          RTM
       DECCOMM          GLC-8            05/8             RT-ll
       DECTAPE          IDAC             PDP              SABR
       DIBOL            IDACS            PHA              TYPESET 8
							  UNIBUS









				    PREFACE



     The 8K Operating  System  (OS/8)  is  an  extremely  powerful  program
     development  system.   OS/8 greatly expands the capabilities of any 8K
     PDP-8, 8/I, 8/L, 8/E, or PDP-12 computer having the necessary disk	 or
     DECtape  storage.	 Use  of  OS/8,	 is described in detail in the OS/8
     HANDBOOK (DEC-S8-OSHBA-A-D).

     This manual covers a wide range of advanced topics	 pertinent  to	the
     experienced  user.	 In Chapter 1 the various basic system concepts are
     described and terms are defined.  Chapter 2 explains  the	process	 by
     which  user  programs  call  upon	the  system  for the performance of
     important operations including loading device  handlers,  opening	and
     closing  files,  and chaining to other programs.  Chapter 3 covers the
     functions of the Command Decoder and  the	means  by  which  the  user
     program  can  employ  its	services.   Chapter  4 explains the use and
     operation of the device handlers in  detail.   Chapter  5	covers	the
     details  of  "custom  tailoring"  a  system,  including how to write a
     device handler for a non-standard device.

     Technical information, intended to enhance the information in the OS/8
     HANDBOOK,	as  well  as  this  manual, can be found in the Appendices.
     Appendix A details the OS/8 directory  structure  and  gives  standard
     file  format.  Appendix B describes the system data base and gives the
     layouts of the system areas.  Appendix C  gives  a	 complete  list	 of
     system  error  messages.	Appendix D illustrates some useful advanced
     techniques and programming "tricks" for  use  with	 the  OS/8  system.
     Appendix  E  is  a complete list of the standard ASCII character codes
     meaningful to OS/8. Finally, Appendix F describes a set of generalized
     I/O routines for use under the OS/8 system.






















				      iii



				   CONTENTS


								       Page

     CHAPTER 1	       OS/8 CONCEPTS AND TERMINOLOGY		       1-1

	     1.1       SOFTWARE COMPONENTS OF OS/8		       1-1

	     1.2       FILES					       1-2
	     1.2.1     File Names and Extensions		       1-2
	     1.2.2     File Structured Devices			       1-2
	     1.2.3     File Types				       1-3
	     1.2.4     File Directories and Additional
		       Information Words			       1-3

	     1.3       CORE CONTROL BLOCK			       1-4
	     1.3.1     Program Starting Address			       1-5
	     1.3.2     Job Status Word				       1-5
	     1.3.3     Software Core Size			       1-6

	     1.4       DEVICE NAMES AND DEVICE NUMBERS		       1-6

	     1.5       THE DEVICE AND FILENAME PSEUDO-OPS	       1-7

     CHAPTER 2	       USER SERVICE ROUTINE			       2-1

	     2.1       CALLING THE USR				       2-1
	     2.1.1     Standard USR Call			       2-1
	     2.1.2     Direct and Indirect Calling Sequence	       2-2

	     2.2       SUMMARY OF USR FUNCTIONS			       2-3
	     2.2.1     FETCH Device Handler			       2-4
	     2.2.2     LOOKUP Permanent File			       2-6
	     2.2.3     ENTER Output (Tentative) File		       2-7
	     2.2.4     The CLOSE Function			       2-8
	     2.2.5     Call Command Decoder (DECODE)		       2-10
	     2.2.6     CHAIN Function				       2-10
	     2.2.7     Signal User Error			       2-12
	     2.2.8     Lock USR in Core (USRIN)			       2-13
	     2.2.9     Dismiss USR from Core (USROUT)		       2-13
	     2.2.10    Ascertain Device Information (INQUIRE)	       2-14
	     2.2.11    RESET System Tables			       2-15

     CHAPTER 3	       THE COMMAND DECODER			       3-1

	     3.1       COMMAND DECODER CONVENTION		       3-1

	     3.2       COMMAND DECODER ERROR MESSAGES		       3-3

	     3.3       CALLING THE COMMAND DECODER		       3-3

	     3.4       COMMAND DECODER TABLES			       3-4
	     3.4.1     Output Files				       3-5
	     3.4.2     Input Files				       3-5
	     3.4.3     Command Decoder Option Table		       3-6
	     3.4.4     Example					       3-7

				      iv




								      Page

	     3.5       SPECIAL MODE OF THE COMMAND DECODER	       3-10
	     3.5.1     Calling the Command Decoder Special Mode	       3-10
	     3.5.2     Operation of the Command Decoder in Special
		       Mode					       3-10

	     3.6       CCL AND THE COMMAND DECODER		       3-11

	     3.7       USEFUL LOCATIONS IN BATCH		       3-11

	     3.8       CCL TABLES				       3-12

     CHAPTER 4	       USING DEVICE HANDLERS			       4-1

	     4.1       CALLING DEVICE HANDLERS			       4-1

	     4.2       DEVICE DEPENDENT OPERATIONS		       4-4
	     4.2.1     Teletype (TTY)				       4-4
	     4.2.2     High-Speed Paper Tape Reader (PTR)	       4-4
	     4.2.3     High-Speed Paper Tape Punch (PTP)	       4-5
	     4.2.4     Line Printer (LPT)			       4-5
	     4.2.5     Cassettes				       4-7
	     4.2.6     Card Reader (CDR)			       4-8
	     4.2.7     TM8E Handler				       4-8
	     4.2.8     File Structured Devices			       4-12
	     4.2.9     TD8E DECtape				       4-12
	     4.2.10    KL8E Teletype Handler			       4-13

     CHAPTER 5	       RECONFIGURING THE OS/8 SYSTEM		       5-1

	     5.1       WRITING DEVICE HANDLERS			       5-1

	     5.2       INSERTING DEVICE HANDLERS INTO OS/8	       5-5

     APPENDIX A	       OS/8 FILE STRUCTURES			       A-1

	     A.1       FILE DIRECTORIES				       A-1
	     A.1.1     Directory Entries			       A-2
	     A.1.2     Number and Size of 05/8 Files		       A-3
	     A.1.3     Sample Directory				       A-3

	     A.2       FILE FORMATS				       A-4
	     A.2.1     ASCII and Binary Files			       A-4
	     A.2.2     Core Image (.SV format) Files		       A-5
	     A.2.3     Relocatable FORTRAN Library File		       A-8

     APPENDIX B	       DETAILED LAYOUT OF THE SYSTEM		       B-1

	     B.1       LAYOUT OF THE SYSTEM DEVICE		       B-1

	     B.2       LAYOUT OF THE OS/8 RESIDENT PROGRAM	       B-3

	     B.3       SYSTEM DEVICE TABLES			       B-5
	     B.3.1     Permanent Device Name Table		       B-5


				       v




								      Page

	     B.3.2     User Device Name Table			       B-6
	     B.3.3     Device Handler Residency Table		       B-6
	     B.3.4     Device Handler Information Table		       B-6
	     B.3.5     Device Control Word Table		       B-7
	     B.3.6     Device Length Table			       B-8

     APPENDIX C	       SYSTEM ERROR CONDITIONS AND MESSAGES	       C-1

	     C.1       SYSTEM HALTS				       C-1

	     C.2       USR ERRORS				       C-2

	     C.3       KEYBOARD MONITOR ERRORS			       C-3

	     C.4       CCL ERROR MESSAGES			       C-4

	     C.5       COMMAND DECODER ERRORS			       C-7

     APPENDIX D	       PROGRAMMING NOTES			       D-1

	     D.1       THE DEFAULT FILE STORAGE DEVICE, DSK	       D-1

	     D.2       MODIFICATION TO CARD READER HANDLER	       D-2

	     D.3       SUPPRESSION OF CARRIAGE RETURN/LINE FEED
		       IN FORTRAN				       D-4

	     D.4       ACCESSING THE SYSTEM DATE IN A FORTRAN
		       PROGRAM					       D-4

	     D.5       DETERMINING CORE SIZE ON PDP-8 FAMILY
		       COMPUTERS				       D-5

	     D.6       USING PRTC12-F TO CONVERT OS/8 DECTAPES
		       TO OS/12 LINCTAPES			       D-6

	     D.7       NOTES ON LOADING DEVICE HANDLERS		       D-7
	     D.7.1     Problem with Multiple Input Files	       D-7
	     D.7.2     Dynamically Loading Device Handlers	       D-8

	     D.8       AVAILABLE LOCATIONS IN THE USR AREA	       D-9

	     D.9       ACCESSING ADDITIONAL INFORMATION WORDS
		       IN OS/8					       D-9
	     D.9.1     After a LOOKUP or ENTER			       D-9
	     D.9.2     After a CLOSE				       D-10
	     D.9.3     Rewriting the Current Directory Segment	       D-10

	     D.10      SABR PROGRAMMING NOTES			       D-11
	     D.10.1    Optimizing SABR Code			       D-11
	     D.10.2    Calling the USR and Device Handlers from
		       SABR Code				       D-13



				      vi




								      Page

     APPENDIX E	       CHARACTER CODES AND CONVENTIONS		       E-1

     APPENDIX F	       OS/8 INPUT/OUTPUT ROUTINES		       F-1

	     F.1       GENERAL DESCRIPTION			       F-1

	     F.2       SUBROUTINE FUNCTIONS			       F-1

	     F.3       SUBROUTINE PARAMETERS			       F-3
	     F.3.1     Example					       F-4
	     F.3.2     Subroutine Listing			       F-5

     INDEX							       I-1









































				      vii







				   CHAPTER 1

			OS/8 CONCEPTS AND TERMINOLOGY



     Before examining the details of the OS/8  system,	the  reader  should
     first  be	familiar  with the simpler techniques and terms used within
     the framework of the OS/8 system.	The material in this chapter, along
     with that contained in the OS/8 HANDBOOK, provides the tools needed to
     pursue the later chapters.



     1.1  SOFTWARE COMPONENTS OF OS/8

     There are four main components of the OS/8 system:

	  1.  The Keyboard Monitor performs commands specified by the  user
	      at  the keyboard console.	 The nine Keyboard Monitor commands
	      (ASSIGN, DEASSIGN, GET, SAVE, ODT, RUN, R, START,	 and  DATE)
	      are explained in Chapter 1 of the OS/8 HANDBOOK.

	      User programs can exit to the Keyboard Monitor by executing a
	      JMP  to  location	 7600  in field 0. All JMPs to 7600 must be
	      made with the  DATA  FIELD  set  to  zero.   This	 saves	the
	      contents	of  locations 0000 to 1777 in field 0 and loads the
	      Keyboard Monitor which could be called by a JMP  to  location
	      7605 in field 0. In this latter case the contents of core are
	      not saved, which conserves some time.

	      Existing system programs, device handlers,  and  the  Command
	      Decoder  test  for the CTRL/C character in the terminal input
	      buffer and, on finding  this  character,	abort  the  current
	      operation	 and perform a JMP to 7600 in field 0. Thus, typing
	      CTRL/C is the conventional method	 of  calling  the  Keyboard
	      Monitor from the console.

	  2.  Device handlers, which are  subroutines  for  performing	all
	      device-oriented  input/output  operations, can be utilized by
	      any  program.   These  subroutines  have	 standard   calling
	      sequences	 and  "mask"  from  the	 user  program	the special
	      characteristics of the  I/O  device.   In	 this  way,  device
	      independent  I/O	is  achieved.	A  detailed  description of
	      device handlers is found in Chapter 4.

	  3.  The User Service Routine (USR)  is  to  a	 program  what	the
	      Keyboard	Monitor	 is to the user.  For example, programs can
	      request the  USR	to  fetch  device  handlers,  perform  file
	      operations  on  any device, chain to another program, or call
	      the Command Decoder.  A full description of the USR functions
	      is found in Chapter 2.


				      1-1

			OS/8 CONCEPTS AND TERMINOLOGY


	  4.  The Command Decoder interprets a command line  typed  by	the
	      user  to indicate input and output files and various options.
	      The command line format is described in detail in	 Chapter  1
	      of the OS/8 HANDBOOK.  The Command Decoder removes the burden
	      of this repetitive operation from the user's program.  A full
	      description  of  the  Command  Decoder's function is found in
	      Chapter 3.

	  5.  Two other components, ABSLDR and ODT, are not logically  part
	      of  the  OS/8  system.  However, in the sources and listings,
	      ABSLDR is combined with the Keyboard Monitor and USR.  ODT is
	      combined with the command decoder.



     1.2 FILES

     Files are basic units of the OS/8 system, and a thorough understanding
     of	 file  structure is required for its use.  A file is any collection
     of data to be  treated  as	 a  unit.   The	 format	 of  this  data	 is
     unimportant;   for	 example,  OS/8	 can  manipulate  several  standard
     formats, including ASCII files, binary files, and	core  image  files.
     The  important  consideration  is	that  the  data forms a single unit
     within the system.



     1.2.1 File Names and Extensions

     An individual file is identified by its file name and extension.	The
     file  name	 consists  of up to six alphanumeric characters, optionally
     followed by a two character extension.  The extension is often used to
     clarify the format of the data within the file.  For example, an ASCII
     file used as input to PAL8 might be given a PA extension, while a core
     image file has a SV extension.



     1.2.2 File Structured Devices

     Devices that can be logically divided into a number of 256-word blocks
     and  have	the  ability  to  read and write from any desired block are
     called  file  structured  devices.	  Disks	 and  DECtapes	 are   file
     structured devices while a paper tape reader or terminal is not.

     Cassettes and magnetic tapes form an intermediate case.  They  may	 be
     treated  directly as non-file structured devices, or the program MCPIP
     may appear to be file structured.

     The system device (SYS) in any OS/8 system is always file	structured,
     as is the default storage device, DSK.

     All OS/8 file structured devices must be logically divided into  these
     256-word  blocks.	 Hence,	 256  words is considered the standard OS/8


				      1-2

			OS/8 CONCEPTS AND TERMINOLOGY


     block size.  Some	devices,  like	RK8,  DECtape,	and  LINCtape,	are
     physically	 divided  into blocks.	These physical blocks should not be
     confused with the logical 256-word blocks.	 For example, DECtapes must
     be	 formatted  with standard 129-word physical blocks.  A logical OS/8
     block consists of the first 128  words  of	 two  consecutive  physical
     DECtape  blocks.  The 129th word of every DECtape block is not used by
     OS/8. Similarly, LINCtapes are formatted with 129 (or 128)	 words	per
     block but never 256, as this format is unacceptable to OS/8.

     A given OS/8 file consists of one or more	sequential  blocks  of	256
     words  each  (consecutively numbered). A minimum of one block per file
     is required, although a single file could occupy all of the blocks	 on
     a device.



     1.2.3  File Types

     Three different types of files exist in the OS/8 system:

	  1.  An "empty file" is a contiguous area of unused blocks.  Empty
	      files are created when permanent files are deleted.

	  2.  A "tentative file" is a file that is open	 to  accept  output
	      and  has not yet been closed.  Only one tentative file can be
	      open on any single device at one time.

	  3.  A "permanent file" is a file that has been given a fixed size
	      and  is  no  longer  expandable.	 A  tentative  file becomes
	      permanent when it is closed.

     To further understand file types, consider what occurs when a file	 is
     created.	Normally, the User Service Routine, in creating a tentative
     file, first locates the largest empty file	 available  and	 creates  a
     tentative file in that space.  This establishes the maximum space into
     which the file can expand.	 The user program then writes data into the
     tentative	file.  At the end of the data, the program calls the USR to
     close the tentative file, making it a permanent file.  The USR does so
     and  allocates whatever space remains on the end of the tentative file
     to a new, smaller, empty file.



     1.2.4  File Directories and Additional Information Words

     To maintain records of the files on a device, OS/8 allocates blocks  1
     through  6	 of  each  file	 structured  device  as the file directory.
     Entries in this directory inform the system of  the  name,	 size,	and
     location  of  each	 file,	including all empty files and the tentative
     file, if one exists.  For a detailed description of the entries in the
     file directory, see Appendix A.

     Each entry in a directory can, optionally, have  extra  storage  words
     called   Additional  Information  Words.	The  number  of	 Additional


				      1-3

			OS/8 CONCEPTS AND TERMINOLOGY


     Information Words is determined at the time the directory is initially
     created  (normally by using the /S or /Z features of PIP;	see Chapter
     1 of the OS/8 HANDBOOK.

     Whenever Additional Information Words are used, the first one for each
     file  entry  is used to store the value of the System Date Word at the
     time the file was created.	 OS/8 automatically uses one extra word per
     entry  for	 the  date.   This value is set by executing a DATE command
     (see Chapter 1 of the OS/8 HANDBOOK) which codes the current date into
     memory location 07666 in the following format:



			0	3 4	   8 9	     11
		       +---------+----------+----------+
		       |	 |	    |	       |
		       +---------+----------+----------+
			  MONTH	     DAY      YEAR-1970
			(1-14(8))  (1-37(8))	(0-7)



     A date word of 0 implies that no DATE command has been executed  since
     the system initialization.

     The values of  Additional	Information  Words  beyond  the	 first	are
     user-defined.   See  Appendix  D for further information on Additional
     Information Words.



     1.3  CORE CONTROL BLOCK

     Associated with each core image file (SV file)  is	 a  block  of  data
     called  the  Core Control Block.  The Core Control Block is a table of
     information containing the program's starting address, areas  of  core
     into  which  the program is loaded, and the program's Job Status Word.
     The Core Control Block is created at the time the program is loaded by
     ABSLDR  or	 other	means  and  is written onto the SV file by the SAVE
     operation.	 More information on the Core Control Block can be found in
     the  description  of  core	 image	files  in  section A.2.2. Note that
     specifying arguments to the SAVE command as described in Chapter 1	 of
     the OS/8 HANDBOOK, can alter the contents of the target program's Core
     Control Block.

     When a program is loaded, the starting address and Job Status Word are
     read  from the Core Control Block and saved in core.  The Core Control
     Block itself is saved in the last 200 (octal) words of block 37 on the
     system  device  unless  the program was loaded with the R (rather than
     GET or RUN) command.






				      1-4

			OS/8 CONCEPTS AND TERMINOLOGY


     1.3.1  Program Starting Address

     The current starting address (used by the START command) is stored	 in
     two words at locations 07744 and 07745. The format of these words is:

		 LOCATION	 CONTENTS	 NOTES		 ________	 ________	 _____

		   07744	   62n3	      n is the field in
					      which to start.

		   07745	   nnnn	      Starting address of
					      the program.



     1.3.2  Job Status Word

     The  Job  Status  Word  contains  certain	flags  that   affect   OS/8
     operations,  such	as  whether  to	 save  core when loading the USR or
     Command Decoder.  The Job Status Word for	the  program  currently	 in
     core   is	 saved	 at  location  07746  and  contains  the  following
     information:

	       Bit Condition	   Meaning	       _____________	   _______

	       Bit 0 = 1	   File does not load into locations 00000
				   to 01777.

	       Bit 1 = 1	   File does not load into locations 00000
				   to 01777.

	       Bit 2 = 1	   Program must be reloaded before it can
				   be restarted.

	       Bit 3 = 1	   Program does not destroy the contents of
				   the highest existing memory field, an
				   optimization for the Batch system.

	       Bits 4 thru 9	   Reserved for future use.

	       Bit 10 = 1	   Locations 00000 to 01777 need not be
				   saved when calling the Command Decoder.

	       Bit 11 = 1	   Locations 10000 to 11777 need not be
				   saved when calling the USR.

     When bit 2 of the Job Status Word is 1, any attempt to perform a START
     (without an explicit address) results in a

	       NO!!

     error message being printed.  As this bit is always zero in  the  Core
     Control Block, the user program is expected to internally set this bit
     (in location 7746) if a program is not  restartable.   This  could	 be


				      1-5

			OS/8 CONCEPTS AND TERMINOLOGY


     done as follows:

		    CDF 0
		    TAD I (7746	    /LOAD JOB STATUS WORD
		    AND (6777
		    TAD (1000
		    DCA I (7746	    /JOB IS NOT RESTARTABLE

     The Job Status Word can be updated from the user's program or with the
     ABSLDR /P	option,	 thus providing optimization of tape (disk) motion.
     More information on the  Core  Control  Block  can	 be  found  in	the
     description of Core Image (SV) files found in Appendix A.

     Bit 3 of the JSW (Job Status Word) is used as an optimization for	the
     Batch  operating  system.	 If  a	program can never cause the highest
     existing memory field to be altered, this	bit  should  be	 set.	For
     example,  EDIT,  PIP,  FORT,  and	SABR can never use memory above 8K.
     Thus, they should set bit 3 of the	 JSW.	Programs  such	as  ABSLDR,
     LOADER,  PAL8 and CREF can alter all of core.  They should perhaps not
     have bit 3 on.  Note that the more core that exists, the more unlikely
     it	 is  that a program will destroy upper core.  Thus, on 28K systems,
     only the largest FORTRAN programs can alter field 6 and,  in  general,
     bit 3 should be set.



     1.3.3  Software Core Size

     Location 07777 contains the software  core	 size  in  bits	 6-8.  This
     represents the highest memory field available for use by OS/8. If bits
     6-8 contain 0, all of the available memory is used.  Most	OS/8  cusps
     interrogate  this word to determine how much memory is available.	The
     other bits of this location are reserved for use by BATCH	and  should
     not be touched by user programs.



     1.4  DEVICE NAMES AND DEVICE NUMBERS

     The OS/8 system can accommodate up to 15 separate devices.	 In Chapter
     1	of  the	 OS/8  HANDBOOK	 the reader is introduced to the concept of
     device names.  Briefly, each device on the	 system	 is  recognized	 by
     either  a permanent device name (such as PTR or DTAl) which is created
     when the system is built, or a user-defined device name determined	 by
     an	 ASSIGN	 command.   The system insures that the user-defined device
     name takes precedence.  For example,

	       .ASSIGN DSK DTA4

     causes all future references to DTA4 to address the device DSK.

     In calling the User Service Routine, a  device  can  be  alternatively
     recognized by a device number.  Each device on the system has a unique
     predefined number in the range 1 to 17 (octal) assigned  at  the  time


				      1-6

			OS/8 CONCEPTS AND TERMINOLOGY


     the  system  is  generated.   Thus,  user	programs have the choice of
     referring to a device by either name or number.  Referencing a  device
     by	 name  is  preferable,	as it maintains device independence for the
     program.

     Accessing devices by number should be done only when  the	appropriate
     number  has been obtained from a USR INQUIRE CALL.	 Except for SYS and
     DSK, the 05/8 peripherals do not have fixed numbers;  instead,  device
     numbers  vary  whenever BUILD is used to modify a system.	Thus, it is
     suggested that reference by name be used whenever possible.

     To determine whether a  device  name  is  recognized  in  the  system,
     attempt  to  ASSIGN  that	device.	  For example, to determine whether
     LINCtape handlers are called LTA or DTA, perform:

	       .DEASSIGN
	       .AS LTA0

     If the system responds with a dot (.), LTA0 does indeed exist.  If the
     system responds with:

	       LTA0 NOT AVAILABLE


     no device named LTA0 is present.



     1.5  THE DEVICE AND FILENAME PSEUDO-OPS

     Several of the USR functions  take	 device	 names	or  file  names	 as
     arguments.	  To  simplify	the task of generating these arguments, the
     DEVICE and FILENAME pseudo-ops have been added to the PAL8 Assembler.

     A	device	name  consists	of  a  two  word  block,  containing   four
     alphanumeric  characters  in  six-bit  ASCII  format.  A block in this
     format can be created by the DEVICE pseudo-op as follows:

	       DEVICE DTA1

     generates the following two words:

	       0424
	       0161

     similarly, the FILENAME pseudo-op creates a four word block, the first
     three  words  of  which  contain  the file name and the fourth word of
     which contains the file extension.	 For example:

	       FILENAME PIP.SV

     generates the following four words:




				      1-7

			OS/8 CONCEPTS AND TERMINOLOGY


	       2011
	       2000
	       0000
	       2326

     Note that positions for characters 4 through 6 are filled with zeros.

     The DEVICE and  FILENAME  pseudo-ops  are	used  in  examples  in	the
     following chapters.















































				      1-8







				   CHAPTER 2

			     USER SERVICE ROUTINE



     The User Service Routine, or USR, is a collection of subroutines which
     perform  the  operations  of opening and closing files, loading device
     handlers, program chaining, and calling the Command Decoder.  The	USR
     provides  these  functions not only for the system itself, but for all
     programs running under the OS/8 system.



     2.1  CALLING THE USR

     Performing any USR function is as simple as giving a JMS  followed	 by
     the  proper  arguments.   Calls to the USR take a standardized calling
     sequence.	This standard call should be studied before progressing	 to
     the operation of the various USR functions.



     2.1.1  Standard USR Call

     In the remainder of this chapter, the following  calling  sequence	 is
     referenced:

	       TAD VAL		   The contents of the AC is applicable	 in
				   some cases only.

	       CDF N		   Where N is  the  value  of  the  current
				   program field multiplied by 10 (octal).

	       CIF 10
	       JMS I (USR	   Where USR is either 7700 or	0200,  (see
				   section 2.1.2).

	       FUNCTION		   This word contains an integer from 1	 to
				   13	 (octal)   indicating	which	USR
				   operation is to be performed.

	       ARG(l)		   The number and meaning of these argument
				   words  varies  with	the  particular USR
				   function to be performed.

	       error return	   When	 applicable,  this  is	the  return
				   address for all errors.

	       normal return	   The operation was successful.  The AC is
				   cleared  and	 the  data  field is set to
				   current field.


				      2-1

			     USER SERVICE ROUTINE


     This calling sequence can	change	from  function	to  function.	For
     example,  some functions take no value in the AC and others have fewer
     or	 greater  numbers  of  arguments.   Nonetheless,  this	format	 is
     generally followed.

     The value	of  the	 data  field  preceding	 the  JMS  to  the  USR	 is
     exceedingly  important.   The  data  field	 MUST be set to the current
     field, and the instruction field MUST be set to 1. Note that a CDF	 is
     not  explicitly required if the data field is already correct.  When a
     doubt exists as to the data field setting, an explicit CDF	 should	 be
     executed.

     There are three other restrictions which apply to all  USR	 calls,	 as
     follows:

	  1.  The USR can never be called from any  address  between  10000
	      and 11777. Attempting to do so results in the:

		   MONITOR ERROR 4 AT xxxxx  (ILLEGAL USR CALL)

	      message and termination of program execution.  The  value	 of
	      xxxxx  is	 the  address  of the calling sequence (in all such
	      MONITOR ERROR messages).

	  2.  Several USR calls take address pointers as arguments.   These
	      pointers always refer to data in the same memory field as the
	      call.

	  3.  When calling the USR from field  1,  these  address  pointers
	      must  never  refer  to  data  that  lies in the area 10000 to
	      11777.



     2.1.2  Direct and Indirect Calling Sequence

     A user program can call the USR in two ways.  First, by  performing  a
     JMS to location 17700 In this case, locations 10000 to 11777 are saved
     on a special area on the system device, and the  USR  is  then  loaded
     into  10000  to  11777. When the USR operation is completed, locations
     10000 to 11777 are restored to their previous values.

				      NOTE

		    By setting bit 11 of the Job Status Word
		    to	a  1, the user can avoid this saving
		    and restoring of  core  when  preserving
		    core is unnecessary.

     Alternatively, a program can opt to keep the USR permanently  resident
     in	 core  at locations 10000 to 11777 by using the USRIN function (see
     section 2.2.8). Once the USR has been brought into core,  a  USR  call
     can  be  made  by performing a JMS to location 10200. This is the most
     efficient way of calling the  USR.	  When	USR  operations	 have  been


				      2-2

			     USER SERVICE ROUTINE


     completed,	 the  program  restores	 locations  10000 to 11777 to their
     initial state by executing the  USROUT  function,	if  necessary  (see
     section 2.2.9).



     2.2  Summary of USR Functions

	  Function
	    Code	 Name			Operation	  ________	 ____			_________

	    1		 FETCH	   Loads  a  device  handler   into   core.
				   Returns   the   entry   address  of	the
				   handler.

	    2		 LOOKUP	   Searches  the  file	directory  on	any
				   device  to  locate a specified permanent
				   file.

	    3		 ENTER	   Creates and opens for output a tentative
				   file on a specified device.

	    4		 CLOSE	   Closes the currently open tentative file
				   on  the  specified  device and becomes a
				   permanent  file.   Also,  any   previous
				   permanent  file  with the same file name
				   and extension is deleted.

	    5		 DECODE	   Calls the Command Decoder.  The function
				   of  the  Command Decoder is described in
				   Chapter 3.

	    6		 CHAIN	   Loads a specified core image	 file  from
				   the system device and starts it.

	    7		 ERROR	   Prints an error message of the form USER
				   ERROR n AT LOCATION xxxxx.

	   10		 USRIN	   Loads the  USR  into	 core.	 Subsequent
				   calls to the USR are by an effective JMS
				   to location 10200.

	   11		 USROUT	   Dismisses the USR from core and restores
				   the previous contents of locations 10000
				   to 11777.

	   12		 INQUIRE   Ascertains whether a given device exists
				   and,	 if  so,  whether its handler is in
				   core.

	   13		 RESET	   Resets system tables	 to  their  initial
				   cleared state.

	   14-17		   Not	currently   used,   these   request
				   numbers are reserved for future use.

				      2-3

			     USER SERVICE ROUTINE


     An attempt to call the USR with a code greater than  13  (octal)  will
     currently	cause  a  Monitor  Error  4  message  to be printed and the
     program to be aborted.



     2.2.1  FETCH Device Handler	  Function Code = 1

     Device handlers must be loaded into core so as to be available to	the
     USR  and  user  program  for  I/O	operations  on that device.  Before
     performing a LOOKUP, ENTER, or  CLOSE  function  on  any  device,	the
     handler for that device must be loaded by FETCH.

     The FETCH function takes two distinct forms:

	  1.  Load a device handler corresponding to a given device name.

	  2.  Load a device handler corresponding to a given device number.

     First, the following is an example of loading a handler by	 name  from
     memory field 0:

	       CLA	      /AC MUST BE CLEAR
	       CDF 0	      /DF = CURRENT FIELD
	       CIF 10	      /IF = 1
	       JMS I (USR
	       1	      /FUNCTION CODE = 1
	       DEVICE DTA3    /GENERATES TWO WORDS: ARG(1)
			      /AND ARG(2)
	       6001	      /ARG(3)
	       JMP ERR	      /ERROR RETURN
	       .	      /NORMAL RETURN
	       .
	       .

     ARG(1) and ARG(2) contain the device name in standard format.  If	the
     normal  return  is	 taken,	 ARG(2)	 is  changed  to  the device number
     corresponding to the device loaded.   ARG(3)  contains  the  following
     information:

	      Bits 0 to 4 contain the page number into which the handler is
	      loaded.

	      Bit 11 is 0 if the user program  can  only  accept  a  1-page
	      handler.

	      Bit 11 is 1 if there is room for a 2-page handler.

     Notice that in the example above, the handler for DTA3 is to be loaded
     into locations 6000 to 6177. If necessary, a two page handler could be
     loaded;  the second page would be placed in locations  6200  to  6377.
     After a normal return, ARG(3) is changed to contain the entry point of
     the handler.



				      2-4

			     USER SERVICE ROUTINE


     A different set of arguments is used to  fetch  a	device	handler	 by
     number.  The following is an example of this form:

	       TAD VAL	      /AC IS NOT ZERO
	       CDF 0	      /DF = CURRENT FIELD
	       CIF 10	      /IF = 1
	       JMS I (USR
	       1	      /FUNCTION CODE = 1
	       6001	      /ARG(1)
	       JMP ERR	      /ERROR RETURN
	       .	      /NORMAL RETURN
	       .
	       .

     On entry to the USR, the AC contains the device number in bits 8 to 11
     (bit  0  to  7 are ignored). The format for ARG(1) is the same as that
     for ARG(3) in the previous example.  Following a normal return  ARG(1)
     is replaced with the entry point of the handler.

     The conditions that can cause an error return to occur in	both  cases
     are as follows:

	  1.  There is no device corresponding to the given device name	 or
	      device number, or

	  2.  An attempt was made to load a two page handler into one page.
	      If  this	is  an	attempt	 to  load  the handler by name, the
	      contents of ARG(2) have been changed already to the  internal
	      device number.

     In addition, one of the  following	 Monitor  errors  can  be  printed,
     followed by a return to the Keyboard Monitor:

	       Error Message			  Meaning	       _____________			  _______

	  MONITOR ERROR 4 AT xxxxx	Results if bits 8 to 11 of the AC
	  (ILLEGAL USR CALL)		are zero  (and	bits  0	 to  7	are
					non-zero).

	  MONITOR ERROR 5 AT xxxxx	Results if a read error occurs
	  (I/O ERROR ON SYS)		while loading the device handler.

     The FETCH function checks to see if the handler is in core, and if	 it
     is	 not,  then  the  handler  and all co-resident handlers are loaded.
     While the FETCH operation is essentially a simple one, the user should
     be aware of the following points:

	  1.  Device handlers are always loaded into memory field 0.

	  2.  The entry point that is returned	may  not  be  on  the  page
	      desired.	 This  would  happen  if  the  handler were already
	      resident.

	  3.  Never attempt to load a handler into the 7600  page  or  into
	      page 0. Never load a two page handler into the 7400 page.

				      2-5

			     USER SERVICE ROUTINE


     For more information on using device handlers, see Chapter 4.

				      NOTE

		    Two	 or   more   device   handlers	 are
		    "co-resident"   when   they	  are	both
		    included in the same  one  or  two	core
		    pages.   For  example,  the	 paper	tape
		    reader   and    punch    routines	 are
		    co-resident,  as  are  the eight DECtape
		    handler routines.



     2.2.2  LOOKUP Permanent file	   Function Code = 2

     This request locates a permanent file entry on a given device, if	one
     exists.  An example of a typical LOOKUP would be:

	       TAD VAL	   /LOAD DEVICE NUMBER
	       CDF 0	   /DF=CURRENT FIELD
	       CIF 10	   /IF = 1
	       JMS I (USR
	       2	   /FUNCTION CODE = 2
	       NAME	   /ARG(1), POINTS TO FILE NAME
	       O	   /ARG(2)
	       JMP ERR	   /ERROR RETURN
	       .	   /NORMAL RETURN
     NAME,     FILENAME PROG.PA

     This request looks up a permanent file entry with	the  name  PROG.PA.
     The  device number on which the lookup is to be performed is in AC bit
     8 to 11. ARG(1) contains a pointer to the file name.   Note  that	the
     file name block must be in the same memory field as the call, and that
     it cannot be in locations 10000 to 11777. The device handler must have
     been  previously  loaded  into  core.   If the normal return is taken,
     ARG(l) is changed to  the	starting  block	 of  the  file	and  ARG(2)
     contains  the  file  length  in  blocks  as a negative number.  If the
     device specified  is  a  readable,	 non-file  structured  device  (for
     example,  the  papertape  reader),	 then ARG(1) and ARG(2) contain the
     file length in blocks as a negative number.  If the  device  specified
     is a readable, non-file structured device (for example, the paper tape
     reader), then ARG(1) and ARG(2) are both set to zero.

     If the error return is taken, ARG(1) and ARG(2)  are  unchanged.	The
     following conditions cause an error return:

	  1.  The device specified is a write-only device.

	  2.  The file specified was not found.

     In addition,  specifying  illegal	arguments  can	cause  one  of	the
     following	monitor	 errors,  followed  by	a  return  to  the Keyboard
     Monitor:


				      2-6

			     USER SERVICE ROUTINE


	       Error Message			  Meaning	       _____________			  _______

	  MONITOR ERROR 2 AT xxxxx	Results if an I/O error occurred
	  (DIRECTORY I/O ERROR)		while reading the device directory.

	  MONITOR ERROR 3 AT xxxxx	Results if the device  handler	for
	  (DEVICE HANDLER NOT IN CORE)	the  specified	device	is  not	 in
					core.

	  MONITOR ERROR 4 AT xxxxx	Results if bits 8 to 11 of  the	 AC
	  (ILLEGAL USR CALL)		are zero.

     The LOOKUP function is the standard method of opening a permanent file
     for input.



     2.2.3  ENTER Output (Tentative) File	   Function Code = 3

     The ENTER function is used to create a tentative file entry to be used
     for output.  An example of a typical ENTER function is as follows:

	       TAD VAL		   /AC IS NOT ZERO
	       CDF 0		   /DF = CURRENT FIELD
	       CIF 10		   /IF = 1
	       JMS I (USR
	       3		   /FUNCTION CODE = 3
	       NAME		   /ARG(1) POINTS TO FILE NAME
	       0		   /ARG(2)
	       JMP ERROR	   /ERROR RETURN
	       .		   /NORMAL RETURN
	       .
	       .
     NAME,     FILENAME PROG.LS

     Bits 8 to 11 of the AC contain  the  device  number  of  the  selected
     device;   the  device handler for this device must be loaded into core
     before performing an ENTER function.  If bits 0 to 7  of  the  AC	are
     non-zero,	this value is considered to be a declaration of the maximum
     length of the file.  The ENTER function searches  the  file  directory
     for the smallest empty file that contains at least the declared number
     of blocks.	 If bits 0 to 7 of the AC  are	zero,  the  ENTER  function
     locates the largest available empty file.

     On a normal return, the contents  of  ARG(1)  are	replaced  with	the
     starting  block  of the file.  The 2's complement of the actual length
     of the created tentative file in blocks (which  can  be  equal  to	 or
     greater  than  the	 requested  length)  replaces  ARG(2).	If the file
     directory contains any Additional Information Words, the  system  DATE
     (location	17666)	is written as the first Additional Information Word
     of the newly created tentative file at this time.





				      2-7

			     USER SERVICE ROUTINE


				      NOTE

		    If	the  selected  device  is  not	file
		    structured but permits output operations
		    (e.g., the high speed punch), the  ENTER
		    operation	always	succeeds.   In	this
		    case, ARG(l) and ARG(2) are both  zeroed
		    on return.

     If the error return is taken, ARG(1) and ARG(2)  are  unchanged.	The
     following conditions cause an error return:

	  1.  The device specified by bits 8 to 11 of the AC is a read only
	      device.

	  2.  No empty file exists which  satisfies  the  requested  length
	      requirement.

	  3.  Another tentative file is already active on this device (only
	      one output file can be active at any given time).

	  4.  The first word of the file name was 0 (an illegal file name).

     In addition, one of the following monitor errors can  occur,  followed
     by a return to the Keyboard Monitor:

	       Error Message			   Meaning	       _____________			   _______

	  MONITOR ERROR 2 AT xxxxx	 Result if an I/O error occurred
	  (DIRECTORY I/O ERROR)		 while reading or writing the device
					 directory.

	  MONITOR ERROR 3 AT xxxxx	 Results if the device handler for
	  (DEVICE HANDLER NOT IN CORE)	 the  specified	 device	 is  not  in
					 core.

	  MONITOR ERROR 4 AT xxxxx	 Results if AC bits 8 to 11 are
	  (ILLEGAL USR CALL)		 zero.

	  MONITOR ERROR 5 AT xxxxx	 Read error on the system device
	  (I/O ERROR ON SYS)		 while bringing in the overlay	code
					 for the ENTER function.

	  MONITOR ERROR 6 AT xxxxx	 Results if a directory overflow
	  (DIRECTORY OVERFLOW)		 occurred  (no	room  for  tentative
					 file entry in directory).



     2.2.4 The CLOSE Function		Function Code = 4

     The CLOSE function has a dual purpose:  first, it is used to close the
     current  active  tentative	 file, making it a permanent file.  Second,
     when a tentative file becomes permanent it is necessary to remove	any


				      2-8

			     USER SERVICE ROUTINE


     permanent file having the same name;  this operation is also performed
     by the CLOSE function.  An example of CLOSE usage follows:

	       TAD VAL		   /GET DEVICE NUMBER
	       CDF 0		   /DF=CURRENT FIELD
	       CIF 10		   /IF=1
	       JMS I (USR
	       4		   /FUNCTION CODE = 4
	       NAME		   /ARG(1)
	       15		   /ARG(2)
	       JMP ERR		   /ERROR RETURN
	       .		   /NORMAL RETURN
	       .
     NAME,     FILENAME PROG.LS

     The device number is contained in AC bits 8 to  11	 when  calling	the
     USR.   ARG(1)  is	a pointer to the name of the file to be deleted and
     ARG(2) contains the number of blocks to be used for the new  permanent
     file.

     The normal sequence of operations on an output file is:

	  1.  FETCH the device handler for the output device.

	  2.  ENTER the tentative file on the output  device,  getting	the
	      starting block and the maximum number of blocks available for
	      the file.

	  3.  Perform the actual output using the device  handler,  keeping
	      track  of how many blocks are written, and checking to insure
	      that the file does not exceed the available space.

	  4.  CLOSE the tentative file, making	it  permanent.	 The  CLOSE
	      operation	 would	always	use the same file name as the ENTER
	      performed in step 2. The closing file length would have  been
	      computed in step 3.

     After a normal  return  from  CLOSE,  the	active	tentative  file	 is
     permanent	and  any  permanent  file  having  the	specified file name
     already stored on the device is deleted.  If the specified device is a
     non-file  structured device that permits output (the paper tape punch,
     for example) the CLOSE function will always succeed.

				      NOTE

		    The user must be careful to specify	 the
		    same  file	names  to  the ENTER and the
		    CLOSE functions.  Failure to do  so	 can
		    cause   several   permanent	 files	with
		    identical  names  to   appear   in	 the
		    directory.	If CLOSE is intended only to
		    be used to delete  some  existing  file,
		    then the number of blocks, ARG(2) should
		    be zero.


				      2-9

			     USER SERVICE ROUTINE



     The following conditions cause the error return to be taken:

	  1.  The device specified by bits 8 to 11 of the AC is a read only
	      device.

	  2.  There is neither an active tentative file to be made  into  a
	      permanent	 file, nor a permanent file with the specified name
	      to be deleted.

     In addition, one of the following Monitor errors can occur:

	       Error Message			  Meaning	       _____________			  _______

	  MONITOR ERROR 1 AT xxxxx	Results if the length specified by
	  (CLOSE,ERROR)			ARG(2) exceeded the allotted space.

	  MONITOR ERROR 2 AT xxxxx	Results	 if  an	 I/O error occurred
	  (DIRECTORY I/O ERROR)		while reading or writing the device
					directory.

	  MONITOR ERROR 3 AT xxxxx	Results if the device handler for
	  (DEVICE HANDLER NOT IN CORE)	the  specified	 device	 is  not  in
					core.

	  MONITOR ERROR 4 AT xxxxx	Results if AC bits 8 to 11 are
	  (ILLEGAL USR CALL)		zero.



     2.2.5  Call Command Decoder (DECODE)	Function Code = 5

     The DECODE function causes the USR to load	 and  execute  the  Command
     Decoder.	The  Command  Decoder accepts (from the Teletype) a list of
     input and output devices and files, along with various  options.	The
     Command  Decoder  performs	 a LOOKUP  on  all  input  files,  sets up
     necessary tables in the top page of field 1, and returns to  the  user
     program.  These operations are described in detail in Chapter 3, which
     should be read before attempting to use the DECODE function.

     A typical call to the Command Decoder looks as follows:

	       CDF 0		   /DF=CURRENT FIELD
	       CIF 10		   /IF=1
	       JMS I (USR
	       5		   /FUNCTION CODE = 5
	       2001		   /ARG(1), ASSUMED INPUT EXTENSION
	       0		   /ARG(2), ZERO TO PRESERVE ALL
				   /TENTATIVE FILES
	       .		   /NORMAL RETURN
	       .
	       .

     ARG(1) is the assumed input extension, in the preceding example it	 is


				     2-10

			     USER SERVICE ROUTINE


     ".PA".  On	 return	 from the Command Decoder, information is stored in
     tables located in the top page of memory field 1. The DECODE  function
     also  resets  all	system	tables	as in the RESET function (see RESET
     function,	section	 2.2.11)  if  ARG(2)  is  0  all  currently  active
     tentative	files  remain  open;   if  ARG(2) is non-zero all tentative
     files are deleted and the	normal	return	is  to	ARG(2)	instead	 of
     ARG(2)+1.

     The DECODE	 function  has	no  error  return  (Command  Decoder  error
     messages are given in Chapter 3). However, the following Monitor error
     can occur:

	       Error Message			  Meaning	       _____________			  _______

	  MONITOR ERROR 5 AT xxxxx	I/O error occurred while reading or
	  (I/O ERROR ON SYS)		writing on the system device.



     2.2.6  CHAIN Function	  Function Code = 6

     The CHAIN function permits a program to load and start another program
     with  the restriction that the program chained to must be a core image
     (.SV) file located on the system device.  A typical implementation	 of
     the CHAIN function looks as follows:

	       CDF 0		   /DF=CURRENT FIELD
	       CIF 10		   /IF=1
	       JMS I (USR
	       6		   /FUNCTION CODE = 6
	       BLOCK		   /ARG(1), STARTING BLOCK NUMBER

     There is no normal or error return from CHAIN.  However, the following
     monitor error can occur:

	       Error Message			  Meaning	       _____________			  _______

	  MONITOR ERROR 5 AT xxxxx	I/O error occurred while reading or
	  (I/O ERROR ON SYS)		writing on the system device.

	  CHAIN ERR			If an attempt is made to CHAIN to a
					file  which  is	 not  a	 core image
					(.SV) file.  Control returns to the
					keyboard monitor.

     The CHAIN function loads a core  image  file  located  on	the  system
     device  beginning	at  the	 block number specified as ARG(1) (which is
     normally determined by performing a LOOKUP on the desired file  name).
     Once loaded, the program is started at an address one greater than the
     starting address specified by the program's Core Control Block.

     CHAIN automatically performs a USROUT function (see section 2.2.9)	 to
     dismiss the USR from core, and a RESET to clear all system tables see
     section 2.2.11), but CHAIN does not delete tentative files.


				     2-11

			     USER SERVICE ROUTINE


     The areas of core altered by the CHAIN function are determined by	the
     contents  of  the	Core Control Block of the core image file loaded by
     CHAIN.  The Core Control Block for the file is set up by other  ABSLDR
     or	 LOADER	 programs.  It can be modified by performing a SAVE command
     with specific arguments.  Every page of core in  which  at	 least	one
     location  was  saved  is  loaded.	 If  the  page	is  one of the "odd
     numbered" pages (pages 1, 3, etc.; locations 0200	to  0377,  0600	 to
     0777,  etc.),  the previous page is always loaded. In  addition, CHAIN
     always alters the contents of locations 07200 to 07577.


				     NOTE

		    CHAIN destroys a necessary part  of the
		    ODT resident  breakpoint routine.  Thus
		    an	ODT  breakpoint should	 never	 be
		    maintained across a CHAIN.

     With the above exceptions, programs can pass data back  and  forth	 in
     core while chaining.  For example, FORTRAN programs normally leave the
     COMMON area in memory field 1 unchanged.  This COMMON area can then be
     accessed by the program activated by the CHAIN.



     2.2.7  Signal User ERROR	      Function Code = 7

     The USR can be called to print a user error  message  for	a  program.
     The following is a possible ERROR call:

	       CDF 0		   /DF = CURRENT FIELD
	       CIF 10		   /IF = 1
	       JMS I (USR
	       7		   /FUNCTION CODE = 7
	       2		   /ARG(1), ERROR NUMBER

     The ERROR function causes a message of the form:

	       USER ERROR n AT xxxxx

     to be printed.  Here n is the error number given as ARG(1); n must	 be
     between  0	 and  11  (octal),  and	 xxxxx is the address of ARG(1). If
     ARG(1) in the sample call above were at location 500 in field  0,	the
     message:

	       USER ERROR 2 AT 00500

     would be printed.	Following the message, the USR returns	control	 to
     the Keyboard Monitor, preserving the user program intact.

     The error number is arbitrary.  Two numbers  have	currently  assigned
     meanings:




				     2-12

			     USER SERVICE ROUTINE


	       Error Message			  Meaning	       _____________			  _______

	  USER ERROR 0 AT xxxxx		During a RUN, GET,  or	R  command,
					this  error  message indicates that
					an error occurred while loading the
					core image.

	  USER ERROR 1 AT xxxxx		While executing a FORTRAN or  SABR
					program, this error indicates that
					a call was  made to  a	subroutine
					that was not loaded.



     2.2.8  Lock USR in Core (USRIN)	   Function Code = 10

     When making a number of calls to the USR  it  is  advantageous  for  a
     program  to avoid reloading the USR each time a USR call is made.	The
     USR can be brought into core and kept there for subsequent use by	the
     USRIN  function.  The calling sequence for the USRIN function looks as
     follows:


	       CDF 0		   /DF = CURRENT FIELD
	       CIF 10		   /IF = 1
	       JMS I (7700
	       10		   /FUNCTION CODE = 10
	       .		   /NORMAL RETURN
	       .
	       .

     THE USRIN function saves the contents of locations 10000 to  11777	 on
     the  system  scratch  blocks,  provided the calling program loads into
     this area as indicated by the current JSW, and  loads  the	 USR,  then
     returns control to the user program.

				      NOTE

		    If bit 11 of the current Job Status Word
		    is	a  one,	 the USRIN function will not
		    save the  contents	of  locations  10000
		    thru 11777.



     2.2.9  Dismiss USR from Core (USROUT)	 Function Code = 11

     When a program has loaded the USR into core with  the  USRIN  function
     and  no  longer wants or needs the USR in core, the USROUT function is
     used to restore the original contents of locations 10000 to 11777. The
     calling sequence for the USROUT function is as follows:





				     2-13

			     USER SERVICE ROUTINE


	       CDF 0		   /DF = CURRENT FIELD
	       CIF 10		   /IF = 1
	       JMS I (200	   /DO NOT JMS TO 17700!!
	       11		   /FUNCTION CODE = 11
	       .		   /NORMAL RETURN
	       .
	       .

     The  USROUT  function  and	 the  USRIN  function	are   complementary
     operations.   Subsequent calls to the USR must be made by performing a
     JMS to location 7700 in field 1.

				       NOTE

		    If bit 11 of the current Job Status Word
		    is	a  1,  the  contents of core are not
		    changed by the USROUT function.  In this
		    case  USROUT  is  a	 redundant operation
		    since core	was  not  preserved  by	 the
		    USRIN function.



     2.2.10  Ascertain Device Information (INQUIRE) Function Code = 12

     On some occasions a user may wish to determine  what  internal  device
     number  corresponds  to  a	 given	device	name  or whether the device
     handler for a specified device is in core, without actually performing
     a	FETCH  operation.   INQUIRE performs these operations for the user.
     The function call for INQUIRE  closely  resembles	the  FETCH  handler
     call.

     INQUIRE, like FETCH, has two distinct forms:

	  1.  Obtain the device number corresponding to a given device name
	      and  determine  if  the  handler	for  that device is in core
	      (example shown below).

	  2.  Determine if the handler	corresponding  to  a  given  device
	      number is in core.

     An example of the INQUIRE call is shown below:

	       CLA		   /AC MUST BE CLEAR
	       CDF 0		   /DF = CURRENT FIELD
	       CIF 10		   /IF = 1
	       JMS I (USR
	       12		   /FUNCTION CODE = 12
	       DEVICE DTA3	   /GENERATES TWO WORDS:
				   /ARG(1) AND ARG(2)
	       0		   /ARG(3)
	       JMP ERR		   /ERROR RETURN
	       .		   /NORMAL RETURN
	       .
	       .

				     2-14

			     USER SERVICE ROUTINE


     ARG(1) and ARG(2) contain the device name in  standard  format.   When
     the  normal  return  is  taken  ARG(2) is changed to the device number
     corresponding to the given name, and ARG(3) contains either the  entry
     point  of	the device handler if it is already in core, or zero if the
     corresponding device handler has not yet been loaded.

     A slightly different set of arguments  is	used  to  inquire  about  a
     device by its device number:

	       TAD VAL		   /AC IS NON-ZERO
	       CDF 0		   /DF = CURRENT FIELD
	       CIF 10		   /IF = 1
	       JMS I (USR
	       12		   /FUNCTION CODE = 12
	       0		   /ARG(1)
	       JMP ERR		   /ERROR RETURN
	       .		   /NORMAL RETURN
	       .
	       .

     On entry to INQUIRE, AC bits 8 to 11 contain the device number.

				      NOTE

		    If AC bits O to 7 are non-zero, and bits
		    8  to  11  are  zero  (an illegal device
		    number) a:

			      MONITOR ERROR 4 AT xxxxx

		    message is printed and program execution
		    is terminated.

     On normal return ARG(1) is set  to	 the  entry  point  of	the  device
     handler  if it is already in core, or zero if the corresponding device
     handler has not yet been loaded.  The error return in  both  cases	 is
     taken  only  if there is no device corresponding to the device name or
     number specified.



     2.2.11  RESET System Tables	 Function Code = 13

     There are certain occasions when it is desired  to	 reset	the  system
     tables,  effectively removing from core all device handlers except the
     system handler.  An example of the RESET function is shown below:

	       CDF 0		   /DF = CURRENT FIELD
	       CIF 10		   /IF = 1
	       JMS I (USR
	       13		   /FUNCTION CODE = 13
	       0		   /0 PRESERVES TENTATIVE FILES
	       .		   /NORMAL RETURN
	       .
	       .

				     2-15

			     USER SERVICE ROUTINE


     RESET zeros all entries except the one for the system  device  in	the
     Device  Handler  Residency	 Table	(see  section  B.3.3,  removing all
     device handlers, other than that for the  system  device,	from  core.
     This  should be done anytime a user program modifies any page in which
     a device handler was loaded.

     RESET has the additional function of  deleting  all  currently  active
     tentative files (files that have been entered but not closed). This is
     accomplished by zeroing bits 9 through 11 of every entry in the Device
     Control Word Table (see section B.3.5).

     If RESET is to be used in this last  fashion,  to	delete	all  active
     tentative files, then ARG(1) must be non-zero and the normal return is
     to ARG(1) rather than to ARG(1)+1. For  example,  the  following  call
     would serve this purpose

	       CDF 0		   /DF:CURRENT FIELD
	       CIF 10		   /IF = 1
	       JMS I (USR
	       13		   /FUNCTION CODE = 13
	       CLA CMA		   /NON-ZERO:

     The normal return would execute the CLA CMA and all  active  tentative
     files on all devices would be deleted.  The Keyboard Monitor currently
     does not reset the Monitor tables.	 If user programs which do not call
     the  Command  Decoder  are	 used,	it  is wise to do a RESET operation
     before loading device handlers.  The RESET will ensure that the proper
     handler will be loaded into core.




























				     2-16







				   CHAPTER 3

			      THE COMMAND DECODER



     OS/8 provides a powerful subroutine called the Command Decoder for use
     by all system programs.  The Command Decoder is normally called when a
     program starts running.  When called, the Command Decoder prints an  *
     and  then	accepts	 a  command  line  from	 the  console Teletype that
     includes a list  of  I/O  devices,	 file  names,  and  various  option
     specifications.   The  Command  Decoder validates the command line for
     accuracy, performs a LOOKUP on all input files, and  sets	up  various
     tables for the calling program.

     The operations performed by the Command Decoder greatly  simplify	the
     initialization  routines  of  all	OS/8 programs.	Also, since command
     lines all have a standard basic structure, the Command  Decoder  makes
     learning to use OS/8 much easier.



     3.1  COMMAND DECODER CONVENTIONS

     Chapter 1 of the OS/8 HANDBOOK describes the syntax  for  the  command
     line  in  detail.	 A brief synopsis is given here only to clarify the
     later discussion in this chapter.

     The command line has the following general form:

	       *output files < input files/ (options)

     There can be 0 to 3 output files and 0 to 9 input files specified.

	  Output File Format			       Meaning	  __________________			       _______

	  EXPLE.EX			Output to a file named EXPLE.EX	 on
					device	 DSK   (the   default  file
					storage device).

	  LPT:				Output to  the	LPT.   This  format
					generally   specifies	a  non-file
					structured device.

	  DTA2:EXPLE.EX			Output to a file named EXPLE.EX	 on
					device DTA2.

	  DTA2:EXPLE.EX[99]		Output to a file named EXPLE.EX	 on
					device	DTA2. A maximum output file
					size of 99 blocks is specified.

	  null				No output specified.


				      3-1

			      THE COMMAND DECODER


     An input file specification has one of the following forms:

	  Input File Format			     Meaning	  _________________			     _______

	  DTA2:INPUT			Input from a file named INPUT.df on
					device	DTA2.  "df"  is the assumed
					input file extension  specified	 in
					the Command Decoder.

	  DTA2:INPUT.EX			Input from a file named INPUT.EX on
					device	DTA2.	In  this  case	.EX
					overrides the  assumed	input  file
					extension.

	  INPUT.EX			Input from a file named INPUT.EX.
					If there is no previously specified
					input device, input is from  device
					DSK,   the   default  file  storage
					device;	   otherwise,	the   input
					device	is  the	 same  as  the last
					specified input device.

	  PTR:				Input from  device  PTR;   no  file
					name   is   needed   for   non-file
					structured devices.

	  DTA2:				Input from device DTA2 treated as a
					non-file structured device, as, for
					example, in the PIP command line:

					     *TTY:/L<DTA2:

					In both of the last two formats, no
					LOOKUP operation is performed since
					the  device  is	  assumed   to	 be
					non-file structured.

	  null				Repeats	 input	from  the  previous
					device specified (must not be first
					in input list, and must refer to  a
					non-file  structured  device).	For
					example:

					     * <PTR:,,

					(two  null  files)  indicates  that
					three paper tapes are to be loaded.

				      NOTE

		    Whenever a file extension is left off an
		    input  file	 specification,	 the Command
		    Decoder first performs a LOOKUP for	 the
		    given name appending a specified assumed
		    extension.	 If  the  LOOKUP  fails,   a

				      3-2

			      THE COMMAND DECODER


		    second  LOOKUP  is	made  for  the	file
		    appending a null (zero) extension.

     The Command Decoder verifies that the  specified  device  names,  file
     names, and extensions consist only of the characters A through Z and 0
     through 9. If not, a syntax error is generated and the command line is
     considered to be valid.

     There are	two  kinds  of	options	 that  can  be	specified:   first,
     alphanumeric  option  switches  are  denoted  by a single alphanumeric
     character preceded by a slash (/) or a string of  characters  enclosed
     in	 parentheses;	secondly,  a  numeric option can be specified as an
     octal number from 1 to 37777777 preceded by an equal sign	(=).  These
     options are passed to the user program and are interpreted differently
     by each program.

     Finally, the Command Decoder permits the command line to be terminated
     by either the RETURN or ALT MODE key.  This information is also passed
     to the user program.



     3.2  COMMAND DECODER ERROR MESSAGES

     If an error in the command line is detected by  the  Command  Decoder,
     one  of  the  following  error  messages  is printed.  After the error
     message, the Command Decoder starts a new line, prints an *, and waits
     for another command line.	The erroneous command is ignored.

	       Error Message			 Meaning	       _____________			 _______

	  ILLEGAL SYNTAX		The  command  line   is	  formatted
					incorrectly.

	  TOO MANY FILES		More than  three  output  files	 or
					nine  input  files  were specified.
					(Or in special mode,  more  than  1
					output	file  or  more than 5 input
					files.)

	  device DOES NOT EXIST		The specified device name does	not
					correspond  to any permanent device
					name or any  user  assigned  device
					name.

	  name NOT FOUND		The specified input file  name	was
					not found on the selected device.



     3.3 CALLING THE COMMAND DECODER

     The Command Decoder is initiated by the DECODE function  of  the  USR.
     DECODE  causes  the  contents  of locations 0 to 1777 of field 0 to be


				      3-3

			      THE COMMAND DECODER


     saved on the system scratch blocks, and Command Decoder to be  brought
     into  that	 area  of core and started.  When the command line has been
     entered and properly interpreted, the Command  Decoder  exits  to	the
     USR,  which restores the original contents of 0 to 1777 and returns to
     the calling program.

				      NOTE

		    By setting bit 10 of the Job Status Word
		    to	a  1  the user can avoid this saving
		    and restoring of core for programs	that
		    do not occupy locations 0 to 1777.

     The DECODE call can reside in the area between 0000 to 1777 and  still
     function correctly.  A typical call would appear as follows:

			 CDF 0	   /SET DATA FIELD TO CURRENT FIELD
			 CIF 10	   /INSTRUCTION FIELD MUST BE 1
			 JMS I (USR /USR=7700 IF USR IS NOT IN CORE
				   /OR USR=0200 IF USRIN WAS PERFORMED
			 5	   /DECODE FUNCTION = 5
			 2001	   /ARG(1),ASSUMED INPUT EXTENSION
			 0	   /ARG(2),ZERO TO PRESERVE
				   /ALL TENTATIVE FILES
			 .	   /NORMAL RETURN
			 .
			 .

     ARG(1) is the assumed input extension.  If an input file name is given
     with  no  specified  extension,  the  Command Decoder first performs a
     LOOKUP for a file having the given name with  the	assumed	 extension.
     If	 the LOOKUP fails, the Command Decoder performs a second LOOKUP for
     a file having the given name and a null  (zero)  extension.   In  this
     example, the assumed input extension is ".PA".

     DECODE performs an automatic RESET operation (see section	2.2.11)	 to
     remove  from  core	 all device handlers except those equivalent to the
     system device.  As in the	RESET  function,  if  ARG(2)  is  zero	all
     currently	 active	 tentative  files  are	preserved.   If	 ARG(2)	 is
     non-zero, all tentative files are deleted and DECODE returns to ARG(2)
     instead of ARG(2)+1.

     As the Command Decoder normally handles all of its own  errors,  there
     is no error return from the DECODE operation.



     3.4  COMMAND DECODER TABLES

     The Command decoder sets up various tables in the top page of field  1
     that describe the command line typed to the user program.





				      3-4

			      THE COMMAND DECODER


     3.4.1  Output Files

     There is room for three entries in the output file table  that  begins
     at location 17600. Each entry is five words long and has the following
     format:

		  0  1	2  3  4	 5  6  7  8  9	10 11
		+-------------------------------------+
	WORD 1	| USER SPECIFIED	|4 BIT-DEVICE |
		| FILE LENGTH		|    NUMBER   |
		+-----------------+-----+-------------+
	WORD 2	| FILE NAME	  |   FILE NAME	      |\
		| CHARACTER 1	  |   CHARACTER 2     | |
		+-----------------+-------------------+ |
	WORD 3	| FILE NAME	  |   FILE NAME	      | \ OUTPUT FILE NAME
		| CHARACTER 3	  |   CHARACTER 4     | / 6 CHARACTERS
		+-----------------+-------------------+ |
	WORD 4	| FILE NAME	  |   FILE NAME	      | |
		| CHARACTER 5	  |   CHARACTER 6     |/
		+-----------------+-------------------+
	WORD 5	| FILE EXTENSION  |   FILE EXTENSION  |\ FILE EXTENSION
		| CHARACTER 1	  |   CHARACTER 2     |/ 2 CHARACTERS
		+-----------------+-------------------+

     Bits 0 to 7 of word 1 in each entry contain the file  length,  if	the
     file  length was specified with the square bracket construction in the
     command line.  Otherwise, those bits are zero.

     The entry for the first output file is in locations  17600	 to  17604,
     the  second  is  in  locations  17605  to	17611,	and the third is in
     locations 17612 to 17616.	If  word  1  of	 any  entry  is	 zero,	the
     corresponding  output  file was not specified.  A zero in word 2 means
     that no file name was specified.

     Also, if word 5 of any entry is zero no file extension  was  specified
     for  the  corresponding  file.  It is left to the user program to take
     the proper action in these cases.

     These entries are	in  a  format  that  is	 acceptable  to	 the  ENTER
     function.



     3.4.2  Input Files

     There is room for nine entries in the input file table that begins	 at
     location  17617.  Each  entry  is two words long and has the following
     format:








				      3-5

			      THE COMMAND DECODER


			   0  1	 2  3  4  5  6	7  8  9	 10 11
		       +-------------------------+--------------+
	       WORD 1  | MINUS FILE		 | 4-BIT DEVICE |
		       | LENGTH			 |  NUMBER	|
		       +-------------------------+--------------+
	       WORD 2  | STARTING BLOCK OF FILE			|
		       +----------------------------------------+

     Bits 0 to 7 of word 1 contain the file length as  a  negative  number.
     Thus,  377 (octal) in these bits is a length of one block, 376 (octal)
     is a length of two blocks,	 etc.	If  bits  0  to	 7  are	 zero,	the
     specified	file  has a length greater than or equal to 256 blocks or a
     non-file structured device was specified.

				      NOTE

		    This restriction to 255 blocks of actual
		    specified  size  can cause some problems
		    if the program has no way  of  detecting
		    end-of-file	 conditions.   For  example,
		    PIP cannot copy in image mode  any	file
		    on	a  file	 structured  device  that is
		    greater than 255 blocks  long,  although
		    it can handle in /A or/B modes (ASCII or
		    Binary) files of unlimited size.  In  /A
		    or/B  modes	 PIP  will detect the CTRL/Z
		    marking the end-of-file.

		    If this is liable to be a problem, it is
		    suggested  that  the user program employ
		    the special mode of the Command  Decoder
		    described in section 3.5 and perform its
		    own LOOKUP on the input files to  obtain
		    the exact file length.

     The two-word  input  file	list  entries  beginning  at  odd  numbered
     locations	from  17617 to 17637 inclusive.	 If location 17617 is zero,
     no input files were indicated in the command line.	 If less than  nine
     input  files were specified, the unused entries in the input file list
     are zeroed (location  17641  is  always  set  to  zero  to	 provide  a
     terminator even when no files are specified).



     3.4.3  Command Decoder Option Table

     Five words are reserved beginning	at  location  17642  to	 store	the
     various  options  specified  in the command line.	The format of these
     five words is as follows:







				      3-6

			      THE COMMAND DECODER


		     0	1  2  3	 4  5  6  7  8	9  10 11
		    +-----------------------------------+
	      17642 |	    HIGH ORDER 11 BITS OF	|
		    |		  = N OPTIONS		|
		    +--+--+--+--+--+--+--+--+--+--+--+--+
	      17643 |A |B |C |D |E |F |G |H |I |J |K |L |
		    |  |  |  |	|  |  |	 |  |  |  |  |	|
	      17644 |M |N |O |P |Q |R |S |T |U |V |W |X |
		    |  |  |  |	|  |  |	 |  |  |  |  |	|
	      17645 |Y |Z |0 |1 |2 |3 |4 |5 |6 |7 |8 |9 |
		    +--+--+--+--+--+--+--+--+--+--+--+--+
	      17646 | LOW ORDER 12 BITS OF = > OPTIONS	|
		    +-----------------------------------+


     Each of these bits corresponds to one  of	the  possible  alphanumeric
     option  switches.	 The  corresponding  bit  is  1	 if  the switch was
     specified, 0 otherwise.

				      NOTE

		    If no  =  n	 option	 is  specified,	 the
		    Command  Decoder zeroes 17646 and bits 1
		    to 11  of  17642.  Thus,  typing  =0  is
		    meaningless	  since	  the  user  program
		    cannot  tell   that	  any	option	 was
		    specified.

		    Bit 0 of location  17642  is  0  if	 the
		    command   line   was   terminated  by  a
		    carriage return, 1 if it was  terminated
		    by an ALT MODE.



     3.4.4  Example

     To clarify some of the preceding, consider the interpretation  of	the
     following command line:

	       *BIN[10]<PTR:,,DTA2:PARA,MAIN /L=14200$

     If this command line is typed to PAL8, it would cause  assembly  of  a
     Program  consisting of four separate parts:  two paper tapes, one file
     named PARA.PA (or just PARA) on DTA2, and one file named  MAIN.PA	(or
     just  MAIN)  also on DTA2. The binary output is placed on a file named
     BIN.BN on device DSK, for which only 10 blocks need be allocated.	 No
     listing  is  generated.   In addition, automatic loading of the binary
     output is specified by the /L option, with the starting address  given
     as 4200 in field 1. Finally, the line is terminated by the ALTMODE key
     (which echoes as $) causing a return to the Keyboard Monitor after the
     program is loaded.

     In the case of this example, the Command Decoder returns to PAL8  with
     the following values in the system tables:

				      3-7

			      THE COMMAND DECODER


				      NOTE

		    The entries for PTR (where no input file
		    name is specified) have a starting block
		    number and file size of zero.   This  is
		    always  true  of  the  input table for a
		    non-file structured device,	 or  a	file
		    structured	device on which no file name
		    is given.















































				      3-8

			      THE COMMAND DECODER


		    +-------+
	       17600|  0242 |--	 DSK:IS DEVICE NUMBER 2
		    |	    |
		    |  0211 |\
		    |	    | |
		    |  1600 |  > FILE NAME IS BIN
		    |	    | |
		    |  0000 |/
		    |	    |
	       17604|  0000 |--	 NULL EXTENSION
		    |-------|
	       17605|	    |\
		    |	    | |	 REMAINING ENTRIES
		    ~	    ~  > IN OUTPUT TABLES
		    |	    | |	 ARE ZERO
	       17616|_______|/
	       17617|	    |\
		    |  0016 | |
		    |	    |  > FIRST PTR INPUT
		    |  0000 | |
	       17620|_______|/
	       17621|	    |\
		    |  0016 | |
		    |	    |  > SECOND PTR INPUT
		    |  0000 | |
	       17622|_______|/
	       17623|  7667 |\
		    |	    | |	 DTA2: PARA PA IS 5 BLOCKS LONG,
		    |  0100 | |	 BEGINNING AT 100(8)
	       17624|_______|/
	       17625|	    |\
		    |  0007 | |	 DTA2: MAIN PA IS 256(10) OR MORE
		    |	    |  > BLOCKS LONG, BEGINNING AT BLOCK 105(8)
		    |  0105 | |
	       17626|_______|/
	       17627|	    |\
		    |	    | |	 REMAINING ENTRIES
		    ~	    ~  > IN INPUT TABLES
		    |	    | |	 ARE ZERO.
	       17641|	    |/
		    |	    |
	       17642|  4001 |--	 LINE WAS TERMINATED BY ALT MODE
		    |	    |
	       17643|  0001 |\
		    |	    | |
	       17644|  0000 | \	 /L WAS ONLY OPTION SWITCH
		    |	    | /	 SPECIFIED
		    |	    | |
	       17645|  0000 |/
		    |	    |
	       17646|  4200 |--	 =14200 WAS SPECIFIED
		    +-------+




				      3-9

			      THE COMMAND DECODER


     3.5  SPECIAL MODE OF THE COMMAND DECODER

     Occasionally the user program does not want  the  Command	Decoder	 to
     perform  the  LOOKUP  on  input files, leaving this option to the user
     program itself.  Programs such as	format	conversion  routines  which
     access non-standard file structures could use this special format.	 If
     the input files  were  not	 OS/8  format,	a  command  decoder  LOOKUP
     operation	would fail.  The capability to handle this case is provided
     in the OS/8 Command Decoder.  This capability is generally referred to
     as the "special mode" of the Command Decoder.



     3.5.1  Calling the Command Decoder Special Mode

     The special mode call to the  Command  Decoder  is	 identical  to	the
     standard  DECODE  call  except  that the assumed input file extension,
     specified by ARG(1), is equal to 5200. The value 5200  corresponds	 to
     an	 assumed  extension  of	 ".*",	which  is  illegal.  Therefore, the
     special mode of the Command Decoder  in  no  way  conflicts  with	the
     normal mode.



     3.5.2  Operation of the Command Decoder in Special Mode

     In special mode the Command Decoder is loaded  and	 inputs	 a  command
     line  as  usual.  The appearance of the command line is altered by the
     special mode in these respects:

	  1.  Only one output file can be specified.

	  2.  No more than five input files can be specified,  rather  than
	      the nine acceptable in normal mode.

	  3.  The characters asterisk (*) and question mark (?)	 are  legal
	      in  file	names  and  extensions,	 both in input files and on
	      output files.  It is strongly suggested that these characters
	      be  tested  by the user program and treated either as special
	      options or as illegal file names.	 The user program  must	 be
	      careful  not  to	ENTER  an  output  file with an asterisk or
	      question mark in its name as such a  file	 cannot	 easily	 be
	      manipulated or deleted by the standard system programs.

     The output and option table set up	 by  the  Command  Decoder  is	not
     altered  in  special  mode.  Entries in the input table are changed to
     the following format:









				      3-10

			      THE COMMAND DECODER


		  0  1	2  3  4	 5  6  7  8  9	10 11
		+-----------------------+--------------+
	WORD 1	|			| 4-BIT DEVICE |   BITS 0-7 ARE
		|			| NUMBER       |   ALWAYS 0
		+-----------------+-----+--------------+
	WORD 2	| FILE NAME	  |   FILE NAME	       |\
		| CHARACTER 1	  |   CHARACTER 2      | |
		+-----------------+--------------------+ |
	WORD 3	| FILE NAME	  |   FILE NAME	       | \ INPUT FILE NAME
		| CHARACTER 3	  |   CHARACTER 4      | / 6 CHARACTER
		+-----------------+--------------------+ |
	WORD 4	| FILE NAME	  |   FILE NAME	       | |
		| CHARACTER 5	  |   CHARACTER 6      |/
		+-----------------+--------------------+
	WORD 5	| FILE EXTENSION  |   FILE EXTENSION   |\  FILE EXTENSION
		| CHARACTER 1	  |   CHARACTER 1      |/  2 CHARACTERS
		+-----------------+--------------------+


     The table entry for the first input file  is  in  locations  17605	 to
     17611;  the second in locations 17612 to 17616; the third in locations
     17617 to 17623; the fourth in locations 17624 to 17630; and the  fifth
     in	 locations  17631 to 17635. A zero in word 1 terminates the list of
     input files.  If word 2 of an entry is zero, no input  file  name	was
     specified.

     The OS/8 batch generating system  will  allow  calls  to  the  command
     decoder in special mode.



     3.6 CCL AND THE COMMAND DECODER

     CCL uses its own copy of the  Command  Decoder  instead  of  the  copy
     available from the monitor.  Thus, the CCL Command Decoder has several
     options not available via standard	 USR  calls  to	 the  OS/8  Command
     Decoder, e.g., multiple default extensions.



     3.7 USEFUL LOCATIONS IN BATCH

     BATCH will run whenever bit 0 of location 07777 is a 1. The  user	may
     wish to access the following useful locations in BATCH.  The locations
     are in the highest memory field available to OS/8:

	    BATERR = 7000     JMP here to abort BATCH.

	    BATOUT = 7400     JMS here to print character
			      in AC in BATCH log.

	    BATSPL = 7200     JMS here to permit spooling
			      with default extension in AC.



				      3-11

			      THE COMMAND DECODER



     3.8 CCL TABLES

     A description of all tables used by CCL is included in the file CCL.PA
     supplied to all users of OS/8 version 3.



















































				      3-12







				   CHAPTER 4

			     USING DEVICE HANDLERS



     A device handler is a system subroutine that is used by all  parts	 of
     the  OS/8	system	and  by all standard system programs to perform I/O
     transfers.	 All device handlers are called in the same  way  and  they
     all  perform the same basic operation:  reading or writing a specified
     number of 128 word records beginning at a selected core address.

     These subroutines	effectively  mask  the	unique	characteristics	 of
     different	I/O  devices from the calling program;	thus, programs that
     use device handlers properly  are	effectively  "device  independent".
     Changing devices involves merely changing the device handlers used for
     I/O.

     OS/8 device handlers have another important feature.  They are able to
     transfer  a number of records as a single operation.  On a device like
     DECtape this permits many blocks of data  to  be  transferred  without
     stopping  the  tape  motion.   On	a  disk,  a  single operation could
     transfer an entire	 track	or  more.   This  capability  significantly
     increases	the  speed of operation of OS/8 programs, such as PIP, that
     have large buffer areas.

				      NOTE

		    The word "record" is defined to mean 128
		    words  of  data;   thus,  an  OS/8 block
		    consists of two 128 word records.



     4.1  CALLING DEVICE HANDLERS

     Device handlers are loaded into a user selected area in memory field 0
     by the FETCH function.  FETCH returns in ARG(1) the entry point of the
     handler loaded.  The handler is called by	performing  a  JMS  to	the
     specified entry point address.  It has the following format:

	  CDF N		 /WHERE N IS THE VALUE OF THE CURRENT
			 /PROGRAM INSTRUCTION FIELD TIMES 10 (OCTAL)
	  CIF 0		 /DEVICE HANDLER ALWAYS IN FIELD 0
	  JMS I ENTRY
	  ARG(1)	 /FUNCTION CONTROL WORD
	  ARG(2)	 /BUFFER ADDRESS
	  ARG(3)	 /STARTING BLOCK NUMBER
	  JMP ERR	 /ERROR RETURN
	  .		 /NORMAL RETURN (I/O TRANSFER COMPLETE)
	  .
     ENTRY 0		 /ENTRY CONTAINS THE ENTRY POINT OF THE
			 /HANDLER, DETERMINED WHEN LOADED BY FETCH

				      4-1

			      USING DEVICE HANDLERS


     As with calls to the USR, it is important that the data field  is	set
     to	 the  current program field before teldevice handler is called.	 On
     exit from the device handler, the data field will remain  set  to	the
     current program field.

     ARG(1) is the  function  control  word,  and  contains  the  following
     information:

	  Bits			    Contents

	  Bit 0		      0 for an input operation,	 1  for	 an  output
			      operation.

	  Bits 1 to 5	      The  number  of  128  word  records   to	 be
			      transferred.   If	 bits  1-5 are zero and the
			      device is	 non-file  structured  (i.e.,  TTY,
			      LPT, etc.) the operation is device dependent.
			      If  the  device  is  file	 structured   (SYS,
			      DECtape,	disk,  etc.),  a  read/write  of 40
			      (octal) pages is performed.

	  Bits 6 to 8	      The memory field in which the transfer is	 to
			      be performed.

	  Bits 9 to 11	      Device dependent	bits,  can  be	left  zero.
			      Currently	 only  bit  11 is used;	 on DECtape
			      bit 11 determines the direction in which	the
			      tape  is	started.   If bit 11 is 0, the tape
			      starts in reverse.  If bit 11 is 1, the  tape
			      starts  forward.	 All  other handlers ignore
			      these bits at present (except TM8E and TA8E).

				      NOTE

		    Starting forward saves time as  long  as
		    the block number, ARG(3), is about seven
		    or more blocks greater than	 the  number
		    of	the  block  at	which  the  tape  is
		    currently positioned.

     ARG(2) is the starting location of the transfer buffer.

     ARG(3) is the number of the block on which the transfer is	 to  begin.
     The  user	program	 initially  determines	this  value by performing a
     LOOKUP or ENTER operation.	  After	 each  transfer	 the  user  program
     should  itself  add  to  the current block number the actual number of
     blocks transferred, equal to one-half the number of 128  word  records
     specified, rounded up if the number of records was odd.

     There are two kinds of error returns:  fatal and non-fatal.   When	 an
     error return occurs and the contents of the AC are negative, the error
     is fatal.	A fatal error can be caused by a parity error on  input,  a
     write  lock  error	 on  output,  or an attempt to write on a read-only
     device (or vice versa). The meaning can vary from	device	to  device,


				      4-2

			      USING DEVICE HANDLERS


     but  in  all  cases  it  is  serious  enough to indicate that the data
     transferred, if any, is invalid.

     When an error return occurs and the contents of  the  AC  are  greater
     than  or  equal  to  zero, a non-fatal error has occurred.	 This error
     always indicates detection of the logical end-of-file.   For  example,
     when  the paper tape reader handler detects the end of a paper tape it
     inserts a CTRL/Z code in the buffer and takes the error exit with	the
     AC	 equal	to  zero.   While all non-file structured input devices can
     detect the end-of-file  condition,	 no  file  structured  device  can;
     furthermore,  no  device handler takes the non-fatal error return when
     doing output.

     The following restrictions apply to the use of device handlers:

	  1.  If bits 1 to 5 of the  function  control	word,  ARG(1),	are
	      zero,  a	transfer  of  40  (octal) pages or an entire memory
	      field is indicated.  Care must be used  to  ensure  that	the
	      handler  is  not overlaid in this call.  This only applies to
	      file-structured handlers.

	  2.  The user program must never specify an input  into  locations
	      07600  to	 07777,	 17600	to  17777,  or	27600-27777, or the
	      page(s) in which	the  device  handler  itself  resides.	 In
	      general, 7600-7777 in every memory field are reserved for use
	      by system software.  Those areas should be used with caution.

	  3.  Note that the amount of data transferred is given as a number
	      of  128  word  records,  exactly	one  half of an OS/8 block.
	      Attempting to output an odd number of records can change	the
	      contents	of  the	 last  128 words of the last block written.
	      For example, outputting 128 words to a block on the RK8  disk
	      causes  the  last	 128  words  of the block to be filled with
	      zeroes.

	  4.  The specified buffer address does not have to  begin  at	the
	      start of a page.	The specified buffer cannot overlap fields,
	      rather the address will "wrap around" memory.  For example, a
	      write  of	 2  pages  starting  at	 location 07600 would cause
	      locations 07600-07777  and  00000-00177  of  field  0  to	 be
	      written.

	  5.  If bits 1-5 of the function control word ARG(1) are  zero,  a
	      device-dependent operation occurs.  Users should not expect a
	      40-page (full field) transfer of data.  The  CLOSE  operation
	      of  the  USR  calls the handler with bits 1-5 and 9-11 of the
	      function control word 0. This condition  means  'perform	any
	      special	close	operations  desired'.  Non-file	 structured
	      handlers which need no special handling on the conclusion	 of
	      data  transfers should treat this case as a NOP.	Examples of
	      usage of such special codes:

		   LPT - perform a form feed
		   CSAn, MTAn - write two file marks


				      4-3

			      USING DEVICE HANDLERS


     4.2 DEVICE DEPENDENT OPERATIONS

     This section describes briefly the operation of certain standard  OS/8
     device    handlers,    including	normal	 operation,   any   special
     initialization operations for block  0,  terminating  conditions,	and
     response  to  control  characters	typed  at  the	keyboard.   Further
     information on device handlers can be found in Chapter 5.



     4.2.1  1-Page Terminal (TTY) (AS33)

	  1.  Normal Operation

	      This handler inputs characters from the terminal keyboard and
	      packs  them  into	 the  buffer or unpacks characters from the
	      buffer and outputs them to the console terminal.

	      On input, characters are echoed as they are typed.  Following
	      a carriage return, a line feed character is inserted into the
	      input buffer and printed on the terminal.

	  2.  Initialization for Block 0

	      None.

	  3.  Terminating Conditions

	      On input, detection of a CTRL/Z causes a CTRL/Z  (octal  code
	      232) to be placed in the input buffer, the remaining words of
	      the buffer to be filled with zeros, and a non-fatal error	 to
	      be  returned.   On output, detection of a CTRL/Z character in
	      the output buffer causes output  to  be  terminated  and	the
	      normal  return  to  be  taken.   There  are  no  fatal errors
	      associated with the 1-page terminal handler.

	  4.  Terminal Interaction

	      CTRL/C forces a  return  to  the	Keyboard  Monitor.   CTRL/Z
	      forces  an  end-of-file  on  input (see 3). CTRL/O terminates
	      printing of the contents of the current buffer on output.



     4.2.2  High-Speed Paper Tape Reader (PTR)

	  1.  Normal Operation

	      This handler inputs characters from the high-speed paper tape
	      reader and packs them into the buffer.

	  2.  Initialization for Block 0

	      The handler prints an up-arrow (^) on the terminal and  waits


				      4-4

			      USING DEVICE HANDLERS


	      for  the	user  to load the paper tape reader.  By typing any
	      single character (except CTRL/C) the user	 initiates  reading
	      of the paper tape.

				      NOTE

		    On some terminals, up-arrow is  replaced
		    by the circumflex (^) character.

	  3.  Terminating Conditions

	      Detection of  an	end-of-tape  condition,	 indicated  by	the
	      failure  to  get	a  character in a specified period of time,
	      causes a CTRL/Z to be entered in the  buffer,  the  remaining
	      words  of the buffer to be filled with zeros, and a non-fatal
	      error to be returned.  Attempting output to  the	paper  tape
	      reader causes a fatal error to be returned.

	  4.  Terminal Interaction

	      Typing CTRL/C forces a return to the Keyboard Monitor.



     4.2.3  High-Speed Paper Tape Punch (PTP)

	  1.  Normal Operation

	      This handler unpacks characters from the	output	buffer	and
	      punches them on the paper tape punch.

	  2.  Initialization for Block 0

	      None.

	  3.  Terminating Conditions

	      Attempting to input from the paper tape punch causes a  fatal
	      error   to  be  returned.	  There	 are  no  non-fatal  errors
	      associated with this handler.

	  4.  Terminal Interaction

	      Typing CTRL/C forces a return to the  Keyboard  Monitor,	but
	      only when actual punching has begun, or if ^C is typed before
	      punching commences.  If the punch is off	line,  ^C  is  only
	      effective immediately before punching would begin.



     4.2.4  Line Printer (LPT)	(LPSV)

	  1.  Normal Operation



				      4-5

			      USING DEVICE HANDLERS


	      This handler unpacks characters from the	buffer	and  prints
	      them  on	the  line  printer.   The characters horizontal tab
	      (ASCII 211)  causes  sufficient  spaces  to  be  inserted	 to
	      position	the  next  character  at a "tab stop" (every eighth
	      column, by definition). The  character  vertical	tab  (ASCII
	      213)  causes  a  skip to the next paper position for vertical
	      tabulation  if  the  line	 printer  hardware  provides   that
	      feature.	 The  character form feed (ASCII 214) causes a skip
	      to the top of the next page.  Finally, the handler  maintains
	      a	 record	 of  the current print column and starts a new line
	      after 80 or 128 columns  have  been  printed.   This  handler
	      functions	 properly  only on ASCII data.	The handler for the
	      LS8E line printer handler	 utilizes  the	expanded  character
	      capability  of  the  printer.   If  a  216 (CTRL/N) character
	      appears anywhere in a  line  of  text,  the  entire  line	 is
	      printed in the expanded character mode.  The 216 must be used
	      on a line-by-line basis.

	  2.  Initialization for Block 0

	      Before printing begins, the line	printer	 handler  issues  a
	      form feed to space to the top of the next page.

	  3.  Terminating Condition

	      On detection of a CTRL/Z character in the	 buffer,  the  line
	      printer  handler issues a form feed and immediately takes the
	      normal return.  Attempting to input  from	 the  line  printer
	      forces  a	 fatal error to be returned.  A fatal error is also
	      returned if the line printer error flag is set.  There are no
	      non-fatal errors associated with the line printer handler.

	  4.  Terminal Interaction

	      Typing CTRL/C forces a return to the Keyboard Monitor.

	  5.  Patching the LPSV Handler

	      The following patches are available for the LPSV line printer
	      handler.

	      rel. loc 0: set to -printer width-l (i.e. set to	-121(octal)
						  for  an  80  column  line
						  printer)

	      rel. loc 1: set to 4		  for	 the	LV8E   line
						  printers
	      set to 14				  for  the  LP08  and  LS8E
						  printers

	      rel. loc 2: set to -40		  to convert lower case	 to
						  upper case
	      set to 0				  if your printer can print
						  lower case


				      4-6

			      USING DEVICE HANDLERS


     4.2.5 Cassettes

	  1. Normal Operation

	      This handler performs character I/O between the cassettes and
	      the  buffer.   It	 treats	 cassettes as a non-file structured
	      device.  Data appears on cassette in 192-byte records.

	  2.  Initialization for Block 0

	      On input the cassette is rewound.	 On output the cassette	 is
	      rewound and a file gap is written.

	  3.  Terminating Condition

	      An end-of-file on input is a software error.

	  4.  Terminal Interaction

	      Typing CTRL/C forces a return to the Keyboard monitor.

	  5.  Special Codes (device dependent features)

	      If the handler is called with bits 1-5 of the  function  word
	      =0, then bits 10-11 are examined.	 The meaning of these codes
	      are as follows:

	      0	   write a file gap
	      1	   rewind also, then write a file gap if bit 0=1
	      2	   space backwards one record
	      3	   skip one file (direction depends on bit 0)


				      NOTE

		    The handler	 neither  reads	 nor  writes
		    standard  files.   It  is merely a paper
		    tape replacement.  It  writes  raw	data
		    (organized	into  192-byte records) onto
		    the cassettes starting at the beginning;
		    and then later reads it back.

     The source is already in OS/8 BUILD format.  The handler has only	two
     entry  points (for drives A and B of a controller). The decision as to
     which controller it uses is made at  assembly  time  by  changing	the
     symbol code.  The result is as follows:

	    CODE     DEVICE NAME   HANDLER	DEVICE CODE	    ____     ___________   _______	___________

	     0		TA8A	   A:CSA0	    70
				   B:CSA1

	     1		TA8B	   A:CSA2	    71
				   B:CSA3


				      4-7

			      USING DEVICE HANDLERS


	     2		TA8C	   A:CSA4	    72
				   B:CSA5

	     3		TA8D	   A:CSA6	    73
				   B:CSA7

     The handler has the internal device code of  27  (see  Table  2-12	 in
     Chapter 2 of the OS/8 HANDBOOK.  The handler is two pages long.



     4.2.6  Card Reader (CDR)

	  1.  Normal Operation

	      This handler reads characters from the card reader and  packs
	      them  into the input buffer.  Trailing spaces (blank columns)
	      on a card are deleted from input.	  The  handler	can  accept
	      only  alphanumeric  format data on cards (the DEC029 standard
	      card codes are used).

	  2. Initialization for Block 0

	      None.

	  3. Terminating Conditions

	      A card which contains an underline character in column 1	(an
	      0-8-5   punch)   with  the  remaining  columns  blank  is	 an
	      end-of-file card.	 In addition, after reading each  card	the
	      handler  checks to see if a CTRL/Z was typed at the keyboard.
	      After either an end-of-file card or a CTRL/Z being  typed,  a
	      CTRL/Z  is inserted in the buffer, the remaining words of the
	      input buffer are filled with zeros, and a non-fatal error	 is
	      returned.	  Attempting  to output to the card reader causes a
	      fatal error to be returned.

	  4. Terminal Interaction

	      Typing CTRL/C forces a return to the Keyboard Monitor.
	      Typing CTRL/Z forces an end-of-file to occur (see 3.).



     4.2.7 TM8-E Handler

	  1. Normal Operation:

	      When the handler is used	in  its	 normal	 mode,	single-file
	      mode, magtapes may consist of exactly one file.  It starts at
	      the beginning of the tape and consists of consecutive records
	      until an end-of-file mark (EOF) is reached.  In this sense, a
	      magtape is similar to one big paper tape.	 This is  the  same
	      way that OS/8 currently treats cassettes.


				      4-8

			      USING DEVICE HANDLERS


	      Since the capacity of magtapes is	 so  big,  provisions  have
	      been  made  for  storing	multiple files per tape.  In such a
	      structure, several files may exist on one magtape.  They	are
	      unlabeled	 and are separated from each other by a single file
	      mark.  The last one is followed  by  two	file  marks.   Each
	      'file'  looks  like  a  paper  tape.   It	 is referenced in a
	      non-file structured manner.   The	 magtape  handler  must	 be
	      altered first to work in file mode.  Then the magtape must be
	      positioned to exactly the correct	 spot  where  the  read	 or
	      write  operation	will  commence.	  This may be done with any
	      program using  the  auxiliary  capabilities  of  the  magtape
	      handler  (described  below), or the positioner program, CAMP.
	      To read a file, the handler must be positioned to just before
	      the first data record of that file.  To write file #1, rewind
	      the tape (i.e., be at BOT).  To  write  file  #n,	 (n>1)	the
	      handler  should  be positioned after the (n-1)st file mark on
	      the tape.	 Previous file n and all files past it then  become
	      unreadable (non-existent).

	      A. Device-Dependent Capabilities:

		  The TM8-E handler has several	 auxiliary  features  which
		  may  be invoked by a user program which calls the handler
		  in a device-dependent manner.	 These features all rely on
		  the  contents of bits 9-11 of the function word (argument
		  1 of the handler call) and some  require  argument  3	 in
		  addition.

		  These features are brought to life whenever  the  handler
		  is  called  with  a  page  count  of	0  (bits 1-5 of the
		  function word).  Call bits 9-11 of the function word, the
		  Special Function Register (SFR) for short, and also refer
		  to bit 0 of the function word as the direction  bit.	 If
		  the  page  count  is	not  0, the contents of the SFR are
		  ignored.

		  If the page count is 0, then the SFR	together  with	the
		  direction  bit  (and	possibly argument 3) determine what
		  special function to perform, as follows:

		  SFR		     OPERATION		  ___		     _________

		  0.  CLOSE.  Write two EOF's.

		  1.  Rewind.

		  2.  Space  forward/reverse  records.	 The  direction	 to
		      space  is	 determined  by	 the direction bit (0 means
		      space forward, 1 means space reverse).  The  negative
		      (two's  complement) of the number of records to space
		      over is given by argument 3 of the handler call.	(-1
		      means  space  past one record, 0 means 4096 records.)
		      The error return is taken if either a  file  mark	 or
		      BOT is encountered.  In such cases, you would be left


				      4-9

			      USING DEVICE HANDLERS


		      positioned at the beginning of a file.

		  3.  Space forward/reverse files.  The direction to  space
		      is  determined  by  the  direction bit (0 means space
		      forward, 1 means space reverse). The negative of	the
		      number  of  file	marks  to  space  past	is given by
		      argument 3 (-1 means space past  one  file  mark;	  0
		      means  4096 file marks). In reverse mode, the tape is
		      left positioned at the end of a file;   an  error	 is
		      given  if	 BOT  is encountered.  In forward mode, the
		      tape is left positioned at the beginning of  a  file.
		      If EOD is reached, the handler automatically performs
		      a backspace record to leave you between the two  file
		      marks;  no error is given.

		  4.  Rewind the unit and put drive off-line.

		  5.  Write a single EOF.

		  6.  Special read/write function.  The direction  bit	(as
		      usual)  determines  read	or  write  (0 means read, 1
		      means  write).  The  specified   I/O   operation	 is
		      performed	  between   the	 user's	 buffer	 (start	 is
		      specified by argument 2) and the	very  next  magtape
		      record.	Only  one  record  is  transferred  and the
		      user's buffer must be large  enough  to  contain	it.
		      The  record  length  is  specified by the negative of
		      argument 3 (in words).  0 means a	 record	 length	 of
		      4096.

		  7.  Unused.  Reserved for future use.	 If  specified,	 it
		      currently acts as a NO-OP.

     In each case, the unit affected is determined  by	the  handler  entry
     point.

	      B. Other Common Operations:

		  (a) To backspace n files, use Special Code 3 to pass over
		      n+1  file marks backwards, then use Special code 2 to
		      advance (forward) over one record (EOF) ignoring	the
		      EOF error.

		  (b) To advance to EOD, first perform a backspace  of	one
		      record  (or  perform  a rewind to play safe) then use
		      special code 3 to advance	 over  4096  files  in	the
		      forward direction (argument 3=0).



	  2.  Special Handling for Block 0

	      If the handler is called to read or write block  0,  it  will
	      first  perform  a rewind.	 This feature can be patched out if


				      4-10

			      USING DEVICE HANDLERS

	      desired by altering relative location 1 from a 0 to a 1. This
	      altered  handler	should	be  operating  in  file	 mode.	The
	      original handler should be operating in single-file mode.

	      A.  Special Handling for CLOSE:

		  A close operation is signaled to the handler	by  calling
		  it with a function word which has a page Count of 0 (bits
		  1-5) and which has bits 9-11 all zeroes.  This is how the
		  USR  CLOSE  operation	 calls	the handler (OS/8 V3 only).
		  This causes the handler  to  write  two  Successive  file
		  marks	 on the tape.  Two Successive EOF's is the software
		  indication of end-of-data (EOD).

	      B.  Restrictions:

		  In single-file mode,	should	not  have  more	 than  4095
		  blocks  because  on trying to write the 4096th block, the
		  handler will think it's writing block	 0  and	 perform  a
		  rewind.   This  restriction does not apply when using the
		  handler in file-mode;	 but beware, some  CUSPs,  Such	 as
		  PIP,	are  suspected to behave strangely on block 4096 of
		  non-file-structured devices.

	  3.  Terminating Conditions

	      None.

	  4.  Keyboard Interaction:

	      Typing ^C on the keyboard while the handler is  in  operation
	      causes  the  handler to abort and return to the OS/8 keyboard
	      monitor via location 7600. Such action is	 ill-advised  since
	      it leaves the magtape without an end-of-file indicator.

	  5.  Error Conditions:

	      On a hard error, the handler takes the error return  (with  a
	      negative	AC)  and  the  AC contains the Contents of the main
	      status register, as follows:

		   Bit on	      Meaning		   ______	      _______

		     0		   Error flag
		     1		   Tape rewinding
		     2		   BOT
		     3		   Select error
		     4		   Parity error (vertical, longitudinal, or
				   CRC)
		     5		   EOF
		     6		   Record length incorrect
		     7		   Data request late
		     8		   EOT
		     9		   File protect
		     10		   Read compare error
		     11		   Illegal function

				      4-11

			      USING DEVICE HANDLERS


     4.2.8  File-Structured Devices

	  1.  Normal Operation

	      (DECtape, LINCtape, TD8E DECtape, DF32, RF08, and RK8, RK8E)

	      These handlers transfer data directly between the device	and
	      the buffer.

	  2.  Initialization for Block 0

	      None.

	  3.  Terminating Conditions

	      A fatal error is returned whenever the transfer causes one of
	      the error flags in the device status register to be set.	For
	      example, a  fatal	 error	would  result  if  a  parity  error
	      occurred	on input, or a write lock error occurred on output.
	      The device handlers generally try three times to perform	the
	      operation	 before	 giving	 up  and  returning  a fatal error.
	      There are no non-fatal errors associated with file structured
	      devices.

	  4.  Terminal Interaction

	      Typing CTRL/C forces a return to the Keyboard Monitor.

				      NOTE

		    The	 system	 device	 handler  does	 NOT
		    respond to a typed CTRL/C.



     4.2.9  TD8E DECtape

     TD8E DECtape is the new accumulator transfer DECtape.  Since OS/8 is a
     noninterrupt  driven  system,  TD8E  DECtape  has	data transfer rates
     equivalent to those for TC08 DECtape;  however, the  interrupt  should
     never  be	used  with  the	 TD8E.	Device handlers for TD8 DECtape are
     supplied as a standard part of OS/8.  Each pair of drives (0 and 1,  2
     and  3,  etc.)  requires  a 2-page	 device handler.  Thus, to have all
     eight TD8E drives in the system at one time will require four separate
     handlers.	 Thus for TD8E, it is wise to restrict usage to those units
     that physically exist.  Also, the tape drives are hardwired to  select
     one  of  two  possible  unit  numbers;  thus, the first pair of drives
     installed must be called units 0 to 1. Any others numbers will cause a
     SELECT  error.   In  this	case,  the computer hangs until the correct
     drive is selected.






				      4-12

			      USING DEVICE HANDLERS


     4.2.10 KL8E Terminal Handler

     Listed  are  the  features	 of  the  KL8E	handler.   Those  that	are
     conditional are marked by an asterisk:


	  1.  It reads a line at a time.  Whenever the user  types  CR,	 it
	      enters  CR,  LF into the buffer;	it echoes CR, LF;  and then
	      pads the remainder of the buffer with nulls  and	returns	 to
	      the calling program.  The characters get put into the buffer,
	      one character per word.  Thus every third character is a null
	      as far as OS/8 is concerned.

	  2.  RUBOUT deletes the previous character.  It echoes as either a
	      back  slash  (\) or as the character rubbed out, depending on
	      assembly parameters.  RUBOUT at the beginning of a line  acts
	      as ^U.

	  3.  CTRL/U echoes as ^U and erases the current line, allowing the
	      user  to	retype	it.   (It  also	 echoes CR, LF.) The buffer
	      pointer is reset to the beginning of the buffer.

	  4.  CTRL/Z  echoes  as  ^Z  (followed	 by  CR,  LF)  and  signals
	      end-of-input.   The ^Z enters the buffer and the remainder of
	      the buffer is padded with nulls.	The error return  is  taken
	      with a positive AC (non-fatal error).

	  5.  Nulls are ignored.

	 *6.  The altmode characters (octal 175 and 176) are  converted	 to
	      escapes (octal 33).

	 *7.  Lower-case characters typed may be automatically converted to
	      upper case.

	  8.  CTRL/C echoes as ^C and  returns	control	 to  the  keyboard
	      monitor via location 07600.

     On output:	 (either normal output or when echoing input)

	  1.  CTRL/C on keyboard echoes as ^C and returns  control  to	the
	      keyboard monitor via location 7600.

	  2.  CTRL/O on keyboard stops further echoing.	 All echoing ceases
	      (through possibly many buffer loads) until either the handler
	      is reloaded into core or the user	 types	a  character  other
	      than to on the keyboard.	Not operative during input.

	  3.  ^S causes the handler to stop sending to	the  terminal.	 No
	      characters  are  lost  and  outputting  resumes  when a ^Q is
	      typed.   ^S  and	^Q  do	not  echo.   These  characters	are
	      operative	 only upon output.  On input, they are treated like
	      any other input characters.  This	 is  very  useful  on  high
	      speed CRT displays.


				      4-13

			      USING DEVICE HANDLERS


	  4.  Nulls are ignored.

	 *5.  Lower case characters may be optionally printed as upper case
	      and flagged with an apostrophe.

	 *6.  Tabs may be handled in one of three manners:

	      a.  Output as actual tabs,

	      b.  Output as actual tab followed by padding of two rubouts,

	      c.  Output as the correct number of spaces to bring the  text
		  to the start of the next tab stop.

	  7.  Whenever the output line reaches the end of the physical line
	      (length  set  at	assembly  time),  the handler automatically
	      performs a carriage-return line-feed.

	 *8.  The escape character (octal 33) prints as a dollar sign.

	 *9.  The handler may be set to delay about 16 ms after typing	any
	      character	 (specified  at	 assembly  time), for example, line
	      feed.

	*10.  Control characters are printed as their corresponding  letter
	      preceded by an up-arrow.	Thus CTRL/K prints as ^K.






























				      4-14







				   CHAPTER 5

			 RECONFIGURING THE OS/8 SYSTEM



     It is sometimes necessary to construct an OS/8 system from scratch, or
     to make a new peripheral device available to OS/8. Both of these tasks
     are a part of reconfiguring the OS/8 system.   OS/8  BUILD,  which	 is
     described in detail in Chapter 2 of the OS/8 HANDBOOK, allows the user
     quickly and easily to build a  new	 system	 or  to	 alter	the  device
     complement of an existing system.



     5.1  WRITING DEVICE HANDLERS

     A device handler is a page-independent subroutine	one  or	 two  pages
     long.   The device handler must run properly in any single page or two
     contiguous pages in field 0 (except 0000 to 0177 or 7600 to 7777). All
     device handlers have the same calling sequence:


	  CDF N		/N IS CURRENT FIELD TIMES 10 (OCTAL)
	  CIF 0		/DEVICE HANDLER LOCATED IN FIELD 0
	  JMS I ENTRY	/ENTRY IS DETERMINED BY SR "FETCH"
	  FUNCTION	/FUNCTION IS BROKEN DOWN AS FOLLOWS:
			/BIT 0 = 0 FOR READ
			/BIT 0 = 1 FOR WRITE
			/BITS 1 TO 5 = NUMBER OF PGS TO TRANSFER
			/BITS 6 TO 8 = FIELD FOR TRANSFER
			/BITS 9 TO 11 = DEVICE DEPENDENT BITS
	  BUFFER	/CORE ADDRESS OF TRANSFER BUFFER
	  BLOCK		/BLOCK NUMBER TO START TRANSFER
	  ERROR		/ERROR RETURN, AC>=0 MEANS END-OF-FILE
				       AC<0 MEANS FATAL ERROR
	  NORMAL	/NORMAL RETURN


     The device handler reads or  writes  a  number  of	 128  word  records
     beginning	at  the selected block.	 In general, device handlers should
     conform to the following standards:

	  1.  On normal return from a device handler the AC is zero and the
	      DATA FIELD is always restored to its original entry value.

	  2.  Although the starting block number has true significance only
	      for file structured devices, handlers for non-file structured
	      devices can check the block number and perform initialization
	      if  the  block number is zero.  For example, the line printer
	      handler  outputs	a  form	 feed  before  printing	 when	the
	      specified block number is zero.


				      5-1

			  RECONFIGURING THE OS/8 SYSTEM


	  3.  Handlers should be written to be	as  foolproof  as  possible
	      checking	for  the most common errors in the calling program.

	      Examples of typical user errors  are:  calling  handler  with
	      non-zero	AC (always perform a CLA in the handler); trying to
	      read on a write only device, or trying to	 write	on  a  read
	      only  device (gives a fatal error return); specifying 0 pages
	      to be transferred (accept as meaning no actual transfer is to
	      take  place);  or	 attempting  to	 access a nonexistent block
	      (gives a fatal error return).

	  4.  Device handlers normally check to see if a CTRL/C (ASCII 203)
	      has  been	 typed	at  the system console by the user.  If one
	      has, the handler aborts I/O and JMP's  to	 location  7600	 in
	      field  0.	 The seven low order bits of the keyboard should be
	      checked for a 3 so as to allow parity terminals.	KRS  should
	      be  used	over  KRB so that any paper tape in the reader will
	      not be advanced if its character is not ^C.

	  5.  Device handlers should  be  able	to  detect  standard  error
	      conditions   like	  checksum   or	 parity	 errors.   Whenever
	      possible, several attempts to perform the transfer should	 be
	      made  before  aborting  I/O  and	taking	the error exit.	 In
	      addition, when operator intervention is required, the handler
	      would  normally  wait for the action rather than take a fatal
	      error exit.  For example, if the	paper  tape  punch  is	not
	      turned  on,  the PTP handler waits for the punch to be turned
	      on.

	  6.  By convention, in any handler for	 a  device  (like  DECtape)
	      that  can	 search either forward or backward for a block, Bit
	      11 of the function word (one of  the  device-dependent  bits)
	      controls the starting direction of the search.  Bit 11 is a 1
	      if the starting direction	 is  forward  and  a  0	 if  it	 is
	      reverse.	 The  other  two  device  dependent  bits  are	not
	      assigned any significance at the present time.

	  7.  Remember that the user specifies a multiple of 128  words	 to
	      transfer,	 whereas  the transfer starts at the beginning of a
	      128 or 256 word block.  This  means  that	 the  handler  must
	      provide  that capability of reading or writing the first half
	      of a block.  Writing the first half of the block	causes	the
	      contents	of the second half of the block to be altered.	For
	      example, writing 128 words to the RK8 disk (256 word  blocks)
	      causes the second half of the block to be filled with zeroes.
	      This is usually done by the hardware controller.

	  8.  The entry point to a two page device handler must be  in	the
	      first page.

	  9.  A number of handlers (maximum of 15 decimal) can be  included
	      in the one or two pages of code.	Where more than one handler
	      is included in a single handler subroutine, the handlers	are
	      called  co-resident.  Co-resident handlers are always brought


				      5-2

			  RECONFIGURING THE OS/8 SYSTEM


	      into core together.  For example, all eight DECtape  handlers
	      fit   into   one	page;	hence,	the  DECtape  handlers	are
	      co-resident.  One restriction on co-resident handlers is that
	      if  they	are  two pages long all entry points must be in the
	      first page.

	 10.  The USR, while doing file operations, maintains in  core	the
	      last  directory  block  read in order to reduce the number of
	      directory reads necessary.  The proper  functioning  of  this
	      feature  depends	on  the	 fact  that  every  handler  for  a
	      file-structured device on a single system has a unique  entry
	      point relative to the beginning of the handler.  The relative
	      entry points currently assigned for file structured  handlers
	      are:

		 Device Handlers		  Relative Entry Points		 _______________		  _____________________

	      System Device Handler		     7
	      DECtape, LINCtape or TD8E DECtape	     10 to 17
	      RKA0				     20
	      RKA1				     21
	      RKA2				     22
	      RKA3				     23
	      RK08 or DF32			     24
	      Reserved for user			     40 to 67

	 11.  If the device is block oriented (such as	DECtape,  LINCtape,
	      or  Disk),  then	the handler transfers data directly with no
	      alteration.  However, if the  device  is	character  oriented
	      (such as a paper tape reader, Teletype, or line printer), the
	      handler is required to pack characters  into  the	 buffer	 on
	      input and unpack them on output.	The standard OS/8 character
	      packing format puts three 8-bit characters into two words	 as
	      follows:
		      +---------------+------------------+
	       WORD 1 |CHARACTER 3    |			 |
		      |	  BITS 0-3    |	  CHARACTER 1	 |
		      +---------------+------------------+
	       WORD 2 |CHARACTER 3    |			 |
		      |	  BITS 4-7    |	  CHARACTER 2	 |
		      +---------------+------------------+
		       0	    3  4	       11


	      For example, the 3 characters 'ABC' would be  packed  into  2
	      words as follows:

		   Word 1: 6301
		   Word 2: 1702

	      When packing characters on input, the character CTRL/Z (octal
	      232)  is inserted at the logical end-of-file (for example, at
	      the end of the  tape  in	the  paper  tape  reader  handler).
	      Following	 CTRL/Z,  the  remaining  words of the input buffer
	      should be zeroed.

				      5-3

			  RECONFIGURING THE OS/8 SYSTEM


	 12.  A close operation should be performed by non-file	 structured
	      handlers if bits 1-5 and 9-11 of the function word are 0.

     The device handler, whether one or two pages long, must be	 completely
     page  independent:	  it must be capable of executing in any page(s) in
     field 0, except page 0 and 7600 to 7777.  Page  independent  code	can
     have  no  address	constants.  Writing one page handlers is relatively
     easy, since the addressing structure of the PDP-8 is essentially  page
     independent.  Writing page relocatable code for two pages, however, is
     considerably more difficult, as the two pages must	 communicate.	The
     usual  technique  utilized	 in writing two page handlers is to include
     some initialization code which includes a	JMS.   This  replaces  that
     location  by  an address on the page the handler was loaded on.  Using
     this, the handler can then determine where the relevant pieces of code
     are in core.

     As an example, the following is the initialization procedure performed
     by	 the  TD8E DECtape routine.  This is by no means the only technique
     that is possible, but it is a workable solution.

		    *200
				 /EXECUTED CODE

     JINIT,	    JMP INIT	 /START INITIALIZATION
			.
			.
			.

     INIT,	    JMS.	 /FOUND OUT WHERE WE ARE.
     BASE,	    TAD CRDQAD	 /INIT GETS ADDRESS OF BASE
		    SPA		 /NEGATIVE TERMINATES LIST
		    JMP NXINIT	 /INITIALIZE SECOND PAGE
		    TAD INIT	 /NOW UPDATE THE LIST OF
		    DCA CRDQAD	 /ADDRESS DEPENDENT LOCATIONS
		    ISZ .-1	 /POINT TO NEXT ELEMENT
		    ISZ BASE	 /NEXT INPUT VALUE
		    JMP BASE	 /LOOP OVER INPUT TABLE.
			.
			.
			.
			.

     CRDQAD,	    R4LINE-BASE	 /THESE ARE ALL POSITIVE DIFFERENCES,
     CINIT2,	    INIT2-BASE	 /SINCE THE ROUTINES INDICATED ARE
     CSELCT,	    SELECT-BASE	 /IN THE SECOND PAGE. AFTER
     CXUNIT,	    XUNIT-BASE	 /INITIALIZATION, CRDQAD POINTS TO
     BUFF,	    4000	 /THE ACTUAL ADDRESS OF R4LINE, ETC.
			.	 /THE 4000 IN BUFF TERMINATES
			.	 /THE FIRST INITIALIZATION.
			.	 /MORE PAGE INDEPENDENT CODE

     NXINIT,	    JMS I CINIT2 /INITIALIZE SECOND PAGE
     BASE2,	    DCA JINIT	 /CLEAR OUT JINIT. NO MORE
		    JMP JINIT	 /RELOCATING IS NEEDED UNTIL THE
				 /HANDLER IS LOADED INTO CORE AGAIN.

				      5-4

			  RECONFIGURING THE OS/8 SYSTEM


		    *400	 /SECOND PAGE OF HANDLER

     INIT2,	    0		 /ADDRESS OF BASE2 GOES HERE
     INIT3,	    TAD CTRY3
		    SNA		 /A 0 TERMINATES THIS LIST
		    JMP I INIT2
		    TAD INIT2	 /ADD VALUE OF BASE2 TO LIST
		    DCA CTRY3	 /PUT BACK INTO LIST
		    ISZ .-1	 /NEXT LOC. TABLE
		    ISZ INIT3
		    JMP INIT3
			.
			.
			.
			.

     CTRY3,	    TRY3-BASE2	 /THIS LIST GETS VALUE OF BASE2
     CRWCOM,	    TRWCOM-BSSE2 /ADDED IN TO POINT TO THE REAL
     XBUFF,	    0		 /ROUTINE.

     Writing 2 page independent code can be  expensive	in  terms  of  core
     required.	 The routines should be set up in such a way as to minimize
     communication between the two pages.  Some other  points  to  keep	 in
     mind are:

	  1.  Relocation code is once-only code.  It is done once when	the
	      handler  is  loaded  and	need  never be done again until the
	      handler is  re-loaded  from  the	system	device.	  For  this
	      reason, the relocation code can be placed in a buffer area or
	      setup in temporary scratch locations which are later used	 as
	      temporary storage.

	  2.  A useful hint is that a JMP into the next page of code is not
	      required.	  The code can just as easily fall through 377 into
	      400. This may save a few locations of relocation code.

	  3.  Useful techniques for writing 2-page handlers can be found in
	      the source of the KL8E handler.



     5.2  INSERTING DEVICE HANDLERS INTO OS/8

     After the handler has  been  written  and	thoroughly  debugged  as  a
     stand-alone routine, it can be integrated into the OS/8 Monitor, where
     it	 will  become  a  resident  device  handler.   To  accomplish	the
     integration, use OS/8 BUILD, described thoroughly in the BUILD section
     in Chapter 2 of the OS/8 HANDBOOK.

     Notes for writing system handlers system handlers	may  be	 integrated
     into BUILD just like non-system handlers with the following additional
     notes:




				      5-5

			  RECONFIGURING THE OS/8 SYSTEM


	  1.  Body of system handler should be origined	 to  200  but  must
	      start  with  a  2	 BLOCK	7.  Entry point must be at relative
	      location 7 (corresponds to location 7607).

	  2.  Name of system handler must be SYS.

	  3.  Each  handler  entry  point  has	an  8-word  handler   block
	      associated with it.  The following additions apply:

	       a.  word 5:  bits 9-11 should normally be 0.
		   If the device can have  multiple  platters  (like  RF08)
		   then	 this  field  specifies	 maximum number of platters
		   allowed.  Each platter above first  bumps  internal	DCB
		   code by 1.

		   word 6:  bit 0=1 means system device is two pages  long.
		   The	second	page  is  origined  into 400 but resides in
		   field 2 location 7600. Bit 1=1 if entry  point  is  SYS.
		   Bit 2=1 if entry point is coresident with SYS.

		   word 7:  must be 0

		   word	 10: number  of	 blocks	 in  device.	Immediately
		   following  the  header  records  is	the  code  for	the
		   device's bootstrap.	 This  is  preceded  by	 minus	the
		   number of words in the bootstrap.  No origins may appear
		   in this code.   It must be less than 47 locations long.





























				      5-6






				   APPENDIX A

			      OS/8 FILE STRUCTURES



     A.1  FILE DIRECTORIES

     Blocks 1 through 6 on all file structured devices are reserved for the
     file  directory  of  that	device.	  Six  blocks are always allocated,
     though all are not necessarily active at any given time.  To  minimize
     the  number  of  directory	 reads and writes necessary, OS/8 fills one
     directory block completely before overflowing  onto  a  second  block.
     Thus  the user with only a few files can perform directory LOOKUPs and
     ENTERs faster than one with many files.

     The directory blocks are each structured according	 to  the  following
     format:
			      ENTRY
		  +--------------------------------+
	       0  | MINUS THE NUMBER OF ENTRIES	   |
		  | IN THIS SEGMENT		   |
		  +--------------------------------+
	       1  | THE STARTING BLOCK NUMBER	   |
		  | OF THE FIRST FILE IN THIS	   |
		  | SEGMENT			   |
		  +--------------------------------+
	       2  | LINK TO NEXT SEGMENT-ZERO	   |
		  | IF NO NEXT SEGMENT		   |
		  +--------------------------------+
	       3  | FLAG WORD-POINTS TO LAST WORD  |
		  | OF TENTATIVE FILE ENTRY IN	   |
		  | THIS SEGMENT		   |
		  | DIRECTORY SEGMENTS ARE ALWAYS  |
		  | LOADED INTO LOCATIONS 11400	   |
		  | TO 117777 BY THE USR; THIS	   |
		  | POINTER IS EITHER 0 OR BETWEEN |
		  | 1400 TO 1777.		   |
		  +--------------------------------+
	       4  | MINUS THE NUMBER OF		   |
		  | ADDITIONAL INFORMATION WORDS.  |
		  | THE NUMBER OF ADDITIONAL	   |
		  | INFORMATION WORDS SPECIFIED	   |
		  | MUST BE THE SAME IN ALL	   |
		  | DIRECTORY SEGMENTS		   |
		  +--------------------------------+
	       5  | BEGINNING OF FILE ENTRIES	   |
		  +--------------------------------+
	       .  |				   |
	       .  ~				   ~
	       .  |				   |
		  +--------------------------------+
	       377| END OF DIRECTORY BLOCK	   |
	       (8)+--------------------------------+

				      A-1

			      OS/8 FILE STRUCTURES


     Locations 0 through 4 of each directory block are called  the  segment
     header.



     A.1.1  Directory Entries

     There are three types of file directory entries.  They  are  PERMANENT
     FILE  ENTRY,  EMPTY FILE ENTRY, and TENTATIVE FILE ENTRY.	A permanent
     file entry appears as follows:

	   Location	  Contents		      Notes
	 +-------------------------------+
       0 | FILE NAME	  FILE NAME	 |\
	 | CHARACTER 1	  CHARACTER 2	 | |
	 +-------------------------------+ |
       1 | FILE NAME	  FILE NAME	 | |
	 | CHARACTER 3	  CHARACTER 4	 | |  THE FILE NAME AND EXTENSION
	 +-------------------------------+  > ARE PACKED IN SIXBIT ASCII
       2 | FILE NAME	  FILE NAME	 | |  (i.e., "A" would be 01)
	 | CHARACTER 5	  CHARACTER 6	 | |
	 +-------------------------------+ |
       3 | FILE EXTENSION FILE EXTENSION | |
	 | CHARACTER 1	  CHARACTER 2	 |/
	 +-------------------------------+
	 |				 |\
	 |				 | |  N, THE NUMBER OF ADDITIONAL
	 +-------------------------------+ |  INFORMATION WORDS, IS GIVEN
	 |	ADDITIONAL		 | |  BY WORD 4 OF THE DIRECTORY
	 ~	INFORMATION		 ~  > HEADER.  WORD 4 OF THE ENTRY
	 |	WORDS			 | |  IS EITHER 0 OR THE CREATION
	 +-------------------------------+ |  DATE OF THE FILE.
	 |				 | |
     N+3 |				 |/
	 +-------------------------------+
	 |				 |
     N+4 | MINUS FILE LENGTH IN BLOCKS	 |
	 +-------------------------------+

				      NOTE
		    If word 3 is zero, the given file has  a
		    null extension.


     An empty file entry appears as follows:

			     Location	   Contents
			   +-----------------------------+
			 0 | ENTRY IS ALWAYS 0000	 |
			   +-----------------------------+
			 1 | MINUS THE NUMBER OF BLOCKS	 |
			   | IN THIS EMPTY FILE		 |
			   +-----------------------------+



				      A-2

			      OS/8 FILE STRUCTURES


     A tentative file entry appears as a permanent file entry with a length
     of	 zero.	 It  is always immediately followed by an empty file entry.
     When the tentative file is entered in a directory, location 3  in	the
     segment  header  becomes  a pointer to this entry.	 The CLOSE function
     inserts the length word of the  tentative	file  entry,  making  it  a
     permanent	file,  and  adjusts  the length of the following empty file
     entry (deleting that entry if the length becomes zero).

     Whether or not there is  a	 tentative  file  open	on  any	 device	 is
     determined by examination of bits 9 to 11 of the system Device Control
     Word Table (see section B.3.5) not the contents of location 3  in	the
     segment  header.	Zeroing these bits in the Device Control Word Table
     makes the active tentative file on the device inactive.  The next time
     that  the	system	has  to	 write	the directory segment, the inactive
     tentative file entry is removed.  The distinction between	active	and
     inactive  tentative  files is made so that OS/8 can avoid spending the
     time required to perform  an  extra  read	and  write  of	the  device
     directory.



     A.1.2  Number and Size of OS/8 Files

     All files on an OS/8 device must occupy a contiguous group	 of  blocks
     on	 the  device.  The length of any file is indicated in its directory
     entry, and the starting  block  of	 the  file  is	deduced	 by  adding
     together  word  1	of  the segment header and the lengths of all files
     whose entries precede it in the directory segment.

     Each directory segment must have enough unused words  at  the  end	 to
     accommodate  a  permanent file entry (N+5 words, where N is the number
     of Additional  Information	 Words).  Thus,	 if  N	is  the	 number	 of
     Additional	 Information  Words  the  maximum  number of permanent file
     entries in any one segment is:

		      256-7 - (N+5)	  244-N
	       MIN = [-------------] =	 [-----]
			   N+7		   N+7

     with N=1, MAX=40, and MIN=30.  Since there are  six  segments  in	the
     directory,	 the  maximum  number of files possible (with N=1) would be
     240.

     Finally, OS/8 devices are limited to 4095 blocks, each block being 256
     words long.  Thus, the maximum size of any single OS/8 file structured
     device is 1,048,320 words.	 Blocks 0  through  6  of  the	device	are
     unavailable for file storage;  therefore, the largest possible file is
     4088 blocks long, or 1,046,528 words.



     A.1.3  Sample Directory

     The initial directory written when the OS/8 system is built  looks	 as
     follows:

				      A-3

			      OS/8 FILE STRUCTURES


	Location       Contents			   Notes
		     +----------+
		/ 0  |   7776   |	TWO ENTRIES
		| 1  |   0070   |	FILE STORAGE STARTS AT BLOCK 70(8)*
        HEADER <  2  |   0000   |	NO ADDITIONAL DIRECTORY SEGMENTS
		| 3  |   0000   |	NO TENTATIVE FILES.
		\ 4  |   7777   |	ONE ADDITIONAL INFORMATION WORD
		     +----------+
	       /  5  |   0102   |  \
	       |  6  |   2314   |   >  FILE NAME IS "ABSLDR"
     PERMANENT /  7  |   0422   |  /
	 FILE  \ 10  |   2326   |	FILE EXTENSION IS SV
	ENTRY  | 11  |   5370   |	DATE IS 10/31/70
	       \ 12  |   7773   |	LENGTH IS FIVE BLOCKS
		     +----------+
	EMPTY  / 13  |   0000   |	EMPTY FILE
	 FILE <      |		|
        ENTRY  \ 14  |   6534   |	LENGTH IS 1244(8) (676(10))BLOCKS -
		     +----------+	THIS IS DEPENDENT ON THE SYSTEM
		     |		|	DEVICE USED.  676 IS THE VALUE
		     ~		~	FOR A DECTAPE SYSTEM
		     |		|
	      377(8) +----------+
				 *This leaves room for the OS/8 System
				 Areas



     A.2  FILE FORMATS

     There are three different standard	 file  formats	used  by  OS/8	and
     associated system programs:

	  1. ASCII and Binary files.

	  2,  Core Image files (.SV format).

	  3.  Relocatable  FORTRAN  library  files  (LIB8.RL  is  the  only
	      current example of this format).

				      NOTE

		    Binary files can contain either absolute
		    binary  data (i.e., output from PAL8) or
		    relocatable binary	data  (i.e.,  output
		    from SABR).



     A.2.1  ASCII and Binary Files

     ASCII and Binary files are packed three characters into two words,	 as
     follows:



				      A-4

			      OS/8 FILE STRUCTURES


			+---------------+------------------------+
	       WORD 1	|  CHARACTER 3	|	 CHARACTER 1	 |
			|   BITS 0-3	|			 |
			+---------------+------------------------+
	       WORD 2	|  CHARACTER 3	|	 CHARACTER 2	 |
			|   BITS 4-7	|			 |
			+---------------+------------------------+
			 0	       3 4		       11

     The following conventions are used by OS/8 system programs:

	  1.  In ASCII files the  character  NULL  (ASCII  000)	 is  always
	      ignored.	Most programs only examine the low-order 7 bits, in
	      ASCII files.  The parity bit  is	usually	 ignored;   do	not
	      assume  that  this  bit  is  set	or that data transfers will
	      preserve it (image mode transfers, always preserve it).

	  2.  In Binary files the binary data must be preceded	by  one	 or
	      more  frames  of	leader/trailer	code  (ASCII 200 code). The
	      first character of binary data must  be  either  100  to	177
	      (octal) (an origin setting for absolute binary files), 240 to
	      257 (octal)  (a  COMMON  declaration  frame  for	relocatable
	      binary  files),  or  300 (octal), which is an origin setting.
	      The end of binary data is indicated by one or more frames	 of
	      leader/trailer code.

	  3.  ASCII and Binary files are terminated by a CTRL/Z code (ASCII
	      232).  In	 binary	 files,	 a  CTRL/Z  code  data	rather than
	      end-of-file.



     A.2.2  Core Image (.SV Format) Files

     A core image file consists of a header by the actual core image.	The
     header block is called the Core Control Block.  The Core Control Block
     consists of the first 128 words of the 256	 word  block  reserved	for
     that  purpose.   The  second  128	words are unused.  The Core Control
     Block is formatted as follows:

















				      A-5

			      OS/8 FILE STRUCTURES


      Location	       Contents			   Notes

		     CORE CONTROL BLOCK
	     +------------------------------------+
	   0 |	MINUS THE NUMBER OF CORE SEGMENTS |
	     +------------------------------------+   62N3 WHERE N IS THE
	   1 |	CDF CIF (STARTING FIELD)	  |<--STARTING FIELD
	     +------------------------------------+
	   2 |	STARTING ADDRESS		  |
	     +------------------------------------+
	   3 |	JOB STATUS WORD			  |
	     +------------------------------------+
	   4 |					  |\  CORE SEGMENT
	     +------------------------------------+ | CONTROL DOUBLE WORDS
	     ~					  ~  >
	     +------------------------------------+ | (K IS THE NUMBER OF
       2K +3 |					  |/  CORE SEGMENTS)
	     +------------------------------------+
      377(8) ~					  ~   REMAINDER OF BLOCK
	     +------------------------------------+   IS UNUSED


     The format of the Job Status Word is as follows:

     Bit Condition			Meaning     _____________			_______

	  Bit 0 = 1	      File does not load into locations 0  to  1777
			      in field 0.

	  Bit 1 = 1	      File does not load into locations 0  to  1777
			      in field 1.

	  Bit 2 = 1	      Program must be reloaded	before	it  can	 be
			      restarted.

	  Bit 3 = 1	      Program never uses above	8K.  This  is  used
			      when Batch processing is active.

	  Bit 10 = 1	      Locations 0 to 1777 in field 0  need  not	 be
			      preserved when the Command Decoder is called.

	  Bit 11 = 1	      Locations 0 to 1777 in field 1  need  not	 be
			      preserved when the USR is called.













				      A-6

			      OS/8 FILE STRUCTURES


     The Core Segment Doublewords control the reading and  writing  of	the
     associated areas of core.	The format of each entry is as follows:

     Location		      Contents		     Notes

	  +---------------------------------------------+
	1 |		      CORE ORIGIN		| MULTIPLE OF 400(8)
	  +---+------------------+-----------+----------+
	2 |   |NUMBER OF PAGES	 |   FIELD   |		| BITS 0 AND 9-11
	  |   |	  TO LOAD	 |  TO LOAD  |		| ARE ZERO
	  +---+------------------+-----------+----------+
	   0   1		5 6	    8 9	      11

     The core origin must be a multiple of 400 (octal).	 The  Core  Segment
     Control  Doublewords  are	sorted	within the header block in order of
     decreasing field and increasing origin within the same  field.   There
     can  be  no more than 32 (decimal) Core Segment Control Doublewords in
     any Core Control Block.

     The Core Control Block for the program at the time it is  loaded  into
     core is always saved in words 200 (octal) through 377 (octal) of block
     37 (octal)	 (one of the system scratch blocks) on	the  system  device.
     It	 is  placed there by the GET and RUN operations or by the ABSLDR or
     LOADER programs.  This Core Control Block is used	when  performing  a
     SAVE without arguments.

				      NOTE

		    The	 R  command  differs  from  the	 RUN
		    command   in  that	the  program's	Core
		    Control Block is not  written  onto	 the
		    scratch  area  when using the R command.
		    In order to SAVE a program that has been
		    loaded  by	the  R	command	 all  of the
		    arguments of the SAVE  command  must  be
		    explicitly stated.




















				      A-7

			      OS/8 FILE STRUCTURES

     A.2.3  Relocatable FORTRAN Library File

     A relocatable FORTRAN library consists of a  library  directory  block
     followed  by relocatable binary segments.	The directory block has the
     following format:

	  Location	    Contents			      Notes	  ________	    ________			      _____

		  +--------------+---------------+
	      0	  |   CH1	 |    CH2	 |\
		  +--------------+---------------+ |  NAME OF ENTRY IN
	      1	  |   CH3	 |    CH4	 |  > SIXBIT ASCII PADDED
		  +--------------+---------------+ |  WITH TRAILING BLANKS
	      2	  |   CH5	 |    CH6	 |/
		  +--------------+---------------+
	      3 +-| LOAD POINTER |		 |
		| +--------------+---------------+
	      4 | | ADDITIONAL ENTRIES		 |
		| ~		  .		 ~
	      5 | |		  .		 |
		| +------------------------------+
		| |		  0		 |\
		| +------------------------------+ |
		| |		  0		 | |
		| +------------------------------+  > DENOTES END OF
		| |		  0		 | |  NAME ENTRIES
		| +------------------------------+ |
		| |		  0		 |/
		| +------------------------------+
	       /  ~				 ~
	      |	  +------------------------------+
	       \->|				 |-> LOADER CONTROL WORD(S)
		  +------------------------------+
		  |		  0		 |-> END OF LOADER CONTROL
		  +------------------------------+   WORDS FOR THIS ENTRY
		  ~				 ~
		  +------------------------------+
	 377(8)	  |				 |
		  +------------------------------+

     The Load Pointer is a number between 0 and 377  (octal)  which  points
     (relative to the beginning of the block) to an array of Loader Control
     Words.  The Loader Control Words have the following information:


	  +--------------+--------------------+
	  |		 |		      |
	  +--------------+--------------------+
	   0		4 5		    11

	   NUMBER OF PAGES OCCUPIED	      (STARTING BLOCK OF RELO-
	   BY THIS SEGMENT AFTER LOADING       CATABLE BINARY DATA)
					       (DIRECTORY BLOCK #)-1




				      A-8

			      OS/8 FILE STRUCTURES


     There can be one or more Loader Control Words  for	 each  entry.	The
     Loader  Control  Words  for an entry are terminated by a word of zero.
     The following is a simple directory block.

		      Location	       Contents

			      +---------------+
			  0   |		 1117 |	  NAME OF ENTRY IS "IOH___"
			      +---------------+
			  1   |		 1040 |
			      +---------------+
			  2   |		 4040 |
			      +---------------+
			  3   |		 0376 |	  LOAD POINTER FOR "IOH"
			      +---------------+
			  4   |		 0530 |
			      +---------------+
			  5   |		 1124 |	  NAME OF ENTRY IS "EXIT__"
			      +---------------+
			  6   |		 4040 |
			      +---------------+
			  7   |		 0373 |	  LOAD POINTER FOR "EXIT"
			      +---------------+
			 10   |		 0000 |
			      +---------------+
			 11   |		 0000 |	  MARKS END OF ENTRIES
			      +---------------+
			 12   |		 0000 |
			      +---------------+
			 13   |		 0000 |
			      +---------------+
			      ~		      ~
			      +---------------+
	      LOADER	373   |		 0207 |	  (RELATIVE BLOCK 10(8))(ONE
	      CONTROL	      +---------------+	  PAGE LONG)
	      WORDS FOR 374   |		 0411 |	  (RELATIVE BLOCK 12(8))(TWO
	      "EXIT"	      +---------------+	  PAGES LONG)
			375   |		 0000 |
			      +---------------+
	      LOADER	376   |		 2400 |	  (RELATIVE BLOCK 1)(12(8) PAGES
	      CONTROL	      +---------------+	  LONG)
	      WORDS FOR 377   |		 0000 |
	      "IOH"	      +---------------+













				      A-9







				   APPENDIX B

			 DETAILED LAYOUT OF THE SYSTEM



     This appendix covers three topics:	 the reserved areas on	the  system
     device, the resident portion of OS/8, and the various system tables.



     B.1  LAYOUT OF THE SYSTEM DEVICE

     The first 70 octal	 blocks	 (14K  words)  on  the	system	device	are
     reserved by the OS/8 system.  These blocks are used as follows:

     Block(s) in Octal	      Contents     _________________	      ________

	  0		      System Bootstrap Routine
	  1-6		      Device Directory
	  7-12		      Keyboard Monitor
	  13-15		      User Service Routine
	  16-25		      Device Handlers
	  26		      ENTER Processor for USR
	  27-50		      System Scratch Blocks
	  51-53		      Command Decoder
	  54-55		      SAVE and DATE Overlays
	  56		      Monitor Error Routine
	  57		      CHAIN Processor for USR
	  60-63		      SYSTEM ODT
	  64		      Reserved for System Expansion
	  65		      CCL Reminiscences
	  66		      12K TD8E Resident code
	  67		      CCL Overlay

     File storage begins with block 70 (octal).

     The system scratch blocks are used for preserving the contents of core
     when  the	Keyboard  Monitor, USR, Command Decoder, or ODT are loaded.
     In addition, various system  programs  use	 the  scratch  area.   Most
     importantly,  the	SAVE  command  expects the Core Control Block to be
     loaded in words 200 (octal) to 377 (octal) of block  37  (octal).	The
     Core  Control  Block  is  stored  at those locations by the GET or RUN
     command or by the ABSLDR or LOADER program.










				      B-1

			 DETAILED LAYOUT OF THE SYSTEM


     A detailed breakdown of system scratch block usage follows:

       Block(s) in Octal		 Contents       _________________		 ________

	  27-32		      The contents of locations 10000 to 11777	are
			      saved in this area when the USR is loaded.

	  33-36		      The contents of locations 0 to 1777 are saved
			      in   this	 area  when  the  Command  Decoder,
			      Keyboard Monitor, or ODT is loaded.

	  37		      Words 200 (octal)	 to  377  (octal)  of  this
			      block  contain the Core Control Block for the
			      last  program  loaded  by	 the  GET  or	RUN
			      command, or the ABSLDR or LOADER program.

	  40-47		      Used as scratch storage  by  the	ABSLDR	and
			      LOADER programs.

	 50		      Reserved for future expansion.




































				      B-2

			 DETAILED LAYOUT OF THE SYSTEM


     B.2 LAYOUT OF THE OS/8 RESIDENT PROGRAM

     The top core pages in fields 0, 1, and 2  are  used  by  the  resident
     portion  of  OS/8	and  are  not accessible by the user.  As a general
     rule, system and user programs should never destroy  the  contents	 of
     locations 7600 to 7777 of any field.

     The resident portion of OS/8 is structured as follows:

	  Location	 Contents		     Notes	  ________	 ________		     _____

		   +-------------------------+
	     7600  | WRITE OPERATION	     |<- NON-DESTRUCTIVE
		   +-------------------------+	 ENTRY TO OS/8
	     7605  | JMP TO FIELD 1 FOR READ |<- DESTRUCTIVE
		   +-------------------------+	 ENTRY TO OS/8
	     7607  |			     |<- ENTRY TO SYSTEM
		   ~ SYSTEM DEVICE HANDLER   ~	 DEVICE HANDLER
	     7743  |			     |
		   +-------------------------+
	     7744  |			     |
	     7745  | CURRENT STARTING ADDRESS|
		   +-------------------------+
	     7746  | JOB STATUS WORD	     |
		   +-------------------------+
	     7747  |		0	     |<- MUST ALWAYS BE ZERO
		   +-------------------------+
	     7750  |			     |
		   | RESERVED FOR DATA BREAK |
		   | LOCATIONS		     |
	     7755  |			     |
		   +-------------------------+
	     7756  |			     |<- THE KEYBOARD MONITOR
		   ~ PROGRAM SETUP AREA	     ~	 AND ODT MODIFY THIS
	     7777  |			     |	 AREA
		   +-------------------------+




















				      B-3

			 DETAILED LAYOUT OF THE SYSTEM


			      TOP PAGE OF FIELD 1


     Location		 Contents		     Notes
	     +--------------------------------+		     \
     7600    ~    OUTPUT FILE LIST (3 ENTRIES)~		      |
     7616    +--------------------------------+		      |
     7617    ~    INPUT FILE LIST	      ~   0 MARKS END |
	     |    (MAXIMUM 9 ENTRIES)	    <---  OF LIST     | COMMAND
     7641    +--------------------------------+		       >DECODER
     7642    |    *  HIGH 11 BITS OF =N	      |<- * BIT 0=1   | AREA
	     +--------------------------------+   IF COMMAND  |
     7643    |    SPECIFIED OPTIONS	      |   LINE TERMI- |
     7645    +--------------------------------+   NATED BY    |
     7646    |    LOW 12 BITS OF =N	      |   ALTMODE     |
	     +--------------------------------+		      |
     7647    |    DEVICE HANDLER	      |		     /
     7665    ~    RESIDENCY TABLE	      ~
	     +--------------------------------+
     7666    |    SYSTEM DATE WORD	      |
	     +--------------------------------+
     7667    ~    READ OPERATION	      ~
     7677    |    (LOAD KEYBOARD MONITOR)     |
	     +--------------------------------+
     7700    ~    USR CALL AND RETURN AREA    ~<- ENTRY TO USR
     7740    +--------------------------------+	      NOTE						      ____
     7741    ~    USER DEVICE		      ~   SYSTEM ODT DESTROYS
     7757    |    NAME TABLE		      |   CONTENTS OF THIS TABLE
	     +--------------------------------+   WHEN SETTING BREAKPOINTS
     7760    ~    DEVICE CONTROL WORD TABLE   ~
     7776    +--------------------------------+
     7777    |    UNUSED		      |   RESERVED FOR FUTURE USE
	     +--------------------------------+

     Systems built around TD8E DECtape without the Read-Only-Memory  option
     use 7600 in field 2 as an extension of the system device handler.


			      TOP PAGE OF FIELD 2.


	       7600   +------------------+
		      |			 |
		      |			 |   Used   only   for	 12K   TD8E
		      |			 |   systems.	 Part	of   system
		      |			 |   handler resides here  in  that
		      |			 |   case.
	       7773   |__________________|
	       7774   |			 |
		      |			 |   Four words reserved for  BATCH
		      |			 |   use  if  machine  has  exactly
		      |			 |   12K.  Contains  pointers  into
		      |			 |   input file.
		      |			 |
	       7777   +------------------+

				      B-4

			 DETAILED LAYOUT OF THE SYSTEM


     If the machine has more than 12K, the top 4 locations  (7774-7777)	 of
     the last field are reserved for use by BATCH.

     If a ROM (Read-Only-Memory) is being used	with  an  8K  TD8E  system,
     locations	7400-7777 of  field  7 are inaccessible to the user.  That
     core is used for system handler functions.



     B.3 SYSTEM DEVICE TABLES

     Each device is described to the  system  by  entries  in  five  system
     tables.   Each of these tables is fifteen words long, where the device
     number is the index into the table.  The  five  tables  are  described
     below.



     B.3.1 Permanent Device Name Table

     Entries in this table specify the permanent name of each device.	The
     entries are computed by encoding the actual four-character device name
     in a single word as follows:

	  1.  The device name is expressed as two  words  in  the  standard
	      DEVICE  format.	For  example, if the device name were "PTR"
	      the two words would be:

		   WORD 1: 2024
		   WORD 2: 2200

	      Note that when the device name is left  justified;   0's	are
	      inserted to fill four characters.

	  2.  A single word is created by adding together these two words.

	  3.  If word 2 is non-zero, bit 0 of the resulting word is  forced
	      to be a one.  For example, the table entry for "PTR" would be
	      4224.

     An entry of zero means that there is no device for	 the  corresponding
     device number.
				      NOTE

		    Conventionally,  device  names   consist
		    only  of  the characters A to Z and 0 to
		    9.	The first character  of	 the  device
		    name  should  be alphabetic.  The coding
		    used makes all  one	 and  two  character
		    device  names unique;  however, names of
		    more than two characters are not unique.
		    For	 example,  "PTR"  and "RTP" have the
		    same encoding.



				      B-5

			 DETAILED LAYOUT OF THE SYSTEM


     The Permanent Device Name table is fifteen locations long;	 it resides
     in	 the USR.  When the USR is in core the beginning of the table is in
     field 1 at a location the address of which is  contained  in  location
     10036.



     B.3.2 User Device Name Table

     Entries are made in this table whenever the user  performs	 an  ASSIGN
     and  are  restored to zero by a DEASSIGN.	These entries have the same
     format as those in the Permanent Device Name Table.

     The User Device Name Table resides in locations 17741 through 17757.



     B.3.3  Device Handler Residency Table

     When a device handler is loaded by the USR, the entry  in	this  table
     for  the device loaded (and entries for all devices whose handlers are
     co-resident, if any) is set to contain the entry point for the  device
     handler.	Entries other than those that contain an address above 7600
     (thus referring to the system handler) are restored to 0 when a RESET,
     DECODE  or	 CHAIN	function  is executed.	When a program exits to the
     Keyboard Monitor this table is  not  cleared.   The  Keyboard  Monitor
     Commands GET, RUN, R, SAVE, and START (with no explicit address) clear
     this table.

				      NOTE

		    Since  the	system	device	handler	  is
		    always  resident the first entry (SYS is
		    always device number 1)  in	 the  Device
		    Handler  Residency	Table is always 7607
		    (the entry point of	 the  system  device
		    handler).

     The Device Handler Residency Table resides in locations 17647  through
     17665.



     B.3.4  Device Handler Information Table

     Each entry in this table contains all the information  needed  by	the
     USR to load the corresponding handler.  The format of these entries is
     as follows:








				      B-6

			 DETAILED LAYOUT OF THE SYSTEM


	  Bit Condition				  Meaning	  _____________				  _______

	  Bits 0 = 1		   If this is a two page device handler.

	  Bits 1 to 4		   Contain the relative block  location	 of
				   the	device handler record on the system
				   device.  This is computed by subtracting
				   15  (octal)	(one  less  than  the first
				   device handler block)  from	the  actual
				   block number.

	  Bits 5 to 11		   Contain the offset of the handler  entry
				   point  from	the  beginning of the page.
				   Note	 that  the  entry  points  to	all
				   handlers must be in the first page.

     If an entry is 0 the corresponding device handler is not saved in	any
     of	 the  device handler storage blocks.  This is always true of device
     number 1 (the system device) and for all device numbers that  are	not
     used  in  a given configuration.  The Device Handler Information Table
     is 15 locations long and resides in the USR.  When the USR is in  core
     the  beginning of the table is in field 1 at a location the address of
     which is contained in location 10037.



     B.3.5 Device Control Word Table

     Entries  in  this	table  specify	special	  device   characteristics,
     including the physical device type.  The entry format is as follows:

	  Bit Condition				  Meaning	  _____________				  _______

	  Bit 0 = 1		   If the device is file-structured.

	  Bit 1 = 1		   If the device is read-only.

	  Bit 2 = 1		   If the device is write-only.

	  Bits 3 to 8		   Contain the physical	 device	 type  code
				   (described below),

	  Bits 9 to 11		   For file structured devices, these  bits
				   contain  the	 directory  block number of
				   the currently active tentative file.	 If
				   bits	 9  to	11  are	 zero,	there is no
				   active tentative  file  on  the  device.
				   For	non-file structured devices, bits 9
				   to 11 are always zero.  Bits 9 to 11 are
				   reset  to zero by the commands GET, RUN,
				   R,  SAVE,  START   (with   no   explicit
				   address)  and  optionally   by  the	USR
				   functions RESET and DECODE.



				      B-7

			 DETAILED LAYOUT OF THE SYSTEM


     The device type is a number between 0  and	 77  (octal),  of  which  0
     through  20  (octal)  are	currently  assigned to existing devices, as
     follows:

	       Device Code		Device	       ___________		______

		    0	      Teletype
		    1	      High-speed paper tape reader
		    2	      High-speed paper tape punch
		    3	      Card Reader
		    4	      Line Printer
		    5	      RK8 Disk
		    6	      256K Disk (RF08)
		    7	      512K Disk (RF08 + RS08)
		    10	      768K Disk (RF08 + 2 RS08's)
		    11	      1024K disk (RF08 + 3 RS08's)
		    12	      32K Disk (DF32)
		    13	      64K Disk (DF32 + DS32)
		    14	      96K Disk (DF32 + 2 DS32's)
		    15	      128K Disk (DF32 + 3 DS32's)
		    16	      DECtape
		    17	      LINCtape (PDP-12 only)
		    20	      TM8E Magnetic Tape
		    21	      TD8E DECtape
		    22	      BATCH handler
		    23	      RK8E Disk
		    24	      NULL
		    25-26     reserved for future disks
		    27	      TA8E Cassette
		    30	      VR12 Scope
		    31-37     reserved for future use by DEC
		    40-57     reserved for use by users

     The Device Control Word  Table  resides  in  locations  17760  through
     17776.



     B.3.6  Device Length Table

     There is a sixth table that is not normally  considered  part  of	the
     system  tables.   This  is the Device Length Table and is used only by
     PIP to perform the	 /Z  (zero  directory)	and  /S	 (compress  device)
     options.  This table is 64 locations long, one entry for each possible
     device type.  In this table an entry of 0 means that the corresponding
     device  is	 non-file  structured;	 otherwise  the	 entry contains the
     negative of the number of available 256-word blocks on the device.

     For example, the entry for a 256K disk would be  6000  (octal)  (minus
     2000 (octal), or 1024 (decimal), 256-word blocks).






				      B-8

			 DETAILED LAYOUT OF THE SYSTEM


     The Device Length Table resides in PIP.  When PIP is brought into core
     the  Device  Length  Table	 is  in	 locations 13600 to 13677. When new
     device types are added to the system this table should be patched with
     ODT to reflect the device length of the new device.

     A similar table occurs in RESORC which the user may wish to patch.	 It
     is	 located  in  field 0 locations 2000-2377 and contains 64 four-word
     entries;  one entry for each device type.	Words 1 and 2 of  an  entry
     are  the names of the device (in sixbit) and word 3 is the negative of
     the number.  Word 4 of the entry should be 0 for non-standard devices.














































				      B-9







				   APPENDIX C

		     SYSTEM ERROR CONDITIONS AND MESSAGES


     This is a summary of all error messages that are a	 result	 of  system
     errors.   These  errors are also described in the relevant sections of
     this manual and in the OS/8 HANDBOOK.



     C.1  SYSTEM HALTS

     Errors that occur as a result of a major I/O  failure  on	the  system
     device can cause a system halt to occur.  These are as follows:

	Value of PC			     Meaning	___________			     _______

	  00601		      A read error  occurred  while  attempting	 to
			      load  ODT.  Return to the Keyboard Monitor by
			      restarting at 07605.

	  07461		      An error occurred	 while	reading	 a  program
			      into  core  during  a  CHAIN.   Return to the
			      Keyboard Monitor by restarting at 07605.

	  07605		      An error occurred while attempting  to  write
			      the  Keyboard  Monitor  area  onto the system
			      scratch  blocks.	 Verify	 that  the   system
			      device  is  not  WRITE  LOCKed and restart at
			      location 07600 to try again.

	  07702		      A user program has performed a JMS to 7700 in
			      field  0.	 This is a result of trying to call
			      the USR without first performing a CIF 10. As
			      location	07700  has been destroyed, the user
			      must re-bootstrap the system.

	  07764		      A	 read  error  occurred	while	loading	  a
			      program.	 Return	 to the Keyboard Monitor by
			      restarting at 07605.

	  07772		      A read error occurred on the  system  scratch
			      area  while loading a program.  Return to the
			      Keyboard Monitor by restarting at 07605.

	  10066		      An input error occurred while  attempting	 to
			      restore  the  USR.   Return  to  the Keyboard
			      Monitor by restarting at 07605.

	  10256		      A read error  occurred  while  attempting	 to
			      load the Monitor by restarting at 07605.


				      C-1

		     SYSTEM ERROR CONDITIONS AND MESSAGES


	  17676		      An error occurred while  attempting  to  read
			      the  Keyboard Monitor from the system device.
			      Try again by restarting at location 07605. DO
			      NOT PRESS CONTINUE.

	  17721		      An error occurred while saving the USR  area.
			      Verify  that  the	 system device is not WRITE
			      LOCKed, and press CONTINUE to try again.

	  17727		      An error occurred while  attempting  to  read
			      the  USR	from  the system device.  Return to
			      the Keyboard Monitor by restarting at 07605.

	  17736		      An error occurred while reading  the  scratch
			      blocks  to  restore  the USR area.  Return to
			      the Keyboard Monitor by restarting at 07605.

     Also, there is one halt in the LOADER program:

	  00005		      A parity error occurred  when  attempting	 to
			      overlay  the  LOADER  from the system scratch
			      blocks.  Return to the  Keyboard	Monitor	 by
			      restarting at 07605, and try again.

     After retrying the operation which caused the failure,  if	 the  error
     persists, it is the result of a hardware malfunction or a parity error
     in the system area.  Run the appropriate diagnostic program  to  check
     the device and rebuild the system.



     C.2  USR ERRORS

     Fatal errors that occur during operation of the USR cause the message:

	       MONITOR ERROR n AT xxxxx

     to be printed.  In these cases, the value "n" describes the error	and
     "xxxxx"  is  the address of the call to the USR that caused the error.
     The six Monitor errors are:

	       Message				  Meaning	       _______				  _______

	  MONITOR ERROR 1 AT xxxxx	File length in	CLOSE  function	 is
	  [CLOSE ERROR]			too large.

	  MONITOR ERROR 2 AT xxxxx	An I/O	error  occurred	 while	at-
	  [DIRECTORY I/O ERROR]		tempting  to  read   or	  write	  a
					directory block.  This is generally
					caused by the  device  being  WRITE
					LOCKed.

	  MONITOR ERROR 3 AT xxxxx	The  device  handler required for a
	  [DEVICE HANDLER NOT IN CORE]	file  operation	  (LOOKUP,   ENTER,
					CLOSE) is not in core.

				      C-2

		     SYSTEM ERROR CONDITIONS AND MESSAGES


	  MONITOR ERROR 4 AT xxxxx	Illegal call to the USR;  either an
	  [ILLEGAL USR CALL]		attempt	 has  been made to call the
					USR from locations 10000  to  11777
					or  a  device  number  of  zero was
					specified.

	  MONITOR ERROR 5 AT xxxxx	I/O error occurred while reading or
	  [I/O ERROR ON SYS]		writing	 on  the   system   device.
					Verify	that  the  system device is
					not WRITE LOCKed.

	  MONITOR ERROR 6 AT xxxxx	Directory  overflow  occurred  (see
	  [DIRECTORY OVERFLOW]		section A.1.2  for  limitations	 on
					number of directory entries).

     In addition to the MONITOR ERROR messages, system	and  user  programs
     can use the USR to print:

	       USER ERROR n AT xxxxx

     by using the ERROR function.   In	this  case  the	 value	of  "n"	 is
     user-defined and "xxxxx" is the address of the call to the USR.

     Currently, two USER ERROR numbers have been assigned:

	       Message				  Meaning	       _______				  _______

	  USER ERROR 0 AT xxxxx		An   I/O   error   occurred   while
					attempting  to	load a program with
					the GET, RUN, or R command.

	  USER ERROR 1 AT xxxxx		While running  a  FORTRAN  or  SABR
					program,  an  attempt  was  made to
					call a subroutine that had not been
					loaded.

     If an I/O error is made during the monitor CHAIN function the message

	       CHAIN ERR

     is generated, and control returns to the keyboard.

     Following either a MONITOR ERROR message or a USER ERROR  message	the
     USR  exits	 to the keyboard Monitor;  the current contents of core are
     preserved and bit 2 of the Job Status Word is set to a  1	to  prevent
     continuing from the error.



     C.3  KEYBOARD MONITOR ERRORS

     In addition to the USR  errors  described	previously,  the  following
     errors can occur after a command is given to the Keyboard Monitor:



				      C-3

		     SYSTEM ERROR CONDITIONS AND MESSAGES


	  Message				  Meaning	  _______				  _______

	  aaaa?			   The Keyboard	 Monitor  cannot  interpret
				   the	command "aaaa".	 For example if the
				   user types HELLO the system will respond
				   HELLO?

	  BAD ARGS		   Arguments  to   a   SAVE   command	are
				   inconsistent, or illegal.

	  BAD CORE IMAGE	   The file requested with an  R,  RUN,	 or
				   GET command is not a core image file.

	  BAD DATE		   Improper syntax in a DATE command.

	  device NOT AVAILABLE	   The permanent device name  specified	 in
				   an  ASSIGN,	SAVE,  RUN,  or GET command
				   does not exist.

	  ILLEGAL ARG		   The	SAVE  command  was  not	  expressed
				   correctly.

	  name NOT FOUND	   The file name specified was not  located
				   on the device indicated.  This error can
				   also be caused by trying to RUN  or	GET
				   from an output only device.

	  NO!!			   A  START  command   (with   no   address
				   specified)  is  prohibited when bit 2 of
				   the Job Status Word (location 07746)	 is
				   a 1.

	  NO CCL!		   Command was	a  valid  CCL  command	but
				   CCL.SV is not on the system.

	  SAVE ERROR		   An I/O error occurred while	saving	the
				   program.   The  contents  of core remain
				   intact.

	  SYSTEM ERR		   An error occurred while doing I/O to the
				   system device.

	  TOO FEW ARGS		   An argument	has  been  omitted  from  a
				   command.



     C.4  CCL ERROR MESSAGES

	  Message				  Meaning	  _______				  _______

	  BAD DEVICE		   The device specified in a CCL command is
				   not	 of   the   correct   form,  (e.g.,
				   DTA0.PA:).


				      C-4

		     SYSTEM ERROR CONDITIONS AND MESSAGES


	  BAD EXTENSION		   Either  an	extension   was	  specified
				   without  a file name (e.g., DTA1:.PA) or
				   two	extensions  were  specified  (e.g.,
				   DTA1:FILE.PA.BN).

	  BAD MONITOR		   The	version	 of  the  Keyboard  Monitor
				   being  used	is not compatible with CCL.
				   A new version of  the  monitor  must	 be
				   obtained  from Digital before CCL can be
				   used.

	  BAD NUMBER		   A  CCL  command   which   uses   the	  #
				   construction	 does  not  have  the  full
				   16-digit specification that is required.

	  BAD RECOLLECTION	   An attempt was made to use a	 previously
				   remembered argument when no argument was
				   saved.   This  error	 occurs	  when	 no
				   argument  was  previously  saved or when
				   the DATE command has been used since the
				   argument was saved.

	  BAD SWITCH OPTION	   The character used with a slash  (/)	 to
				   indicate   an  option  is  not  a  legal
				   option.

	  CANNOT CHANGE CORE	   A CORE  command  was	 issued	 while	the
	  CAPACITY WHILE RUNNING   BATCH program was running.
	  BATCH

	  %CANT REMEMBER	   The argument specified in a CCL  command
				   line	 is too long to be remembered or an
				   I/O error occurred.

	  CCL 3X OVERLAY &	   The	version	 of  CCL  being used is not
	  MONITOR INCOMPATIBLE	   compatible  with  the  Keyboard  Monitor
				   present  on	the  system.  Type R CCL to
				   retry.

	  COMMAND LINE OVERFLOW	   The command line specified  with  the  @
				   construction is more than 512 characters
				   in length.

	  COMMAND TOO LONG	   The length of a text argument in a  MUNG
				   command is too long.

	  CONTRADICTORY SWITCHES   Either two CCL processor  switches  were
				   specified   in  the	same  command  line
				   (e.g., FILE-PA-FT) or the file extension
				   and	the  processor	switch do not agree
				   (e.g., FILE.FT-BA).

	  name DOES NOT EXIST	   The device with the name  given  is	not
				   present on the OS/8 system.


				      C-5

		     SYSTEM ERROR CONDITIONS AND MESSAGES


	  ERROR IN COMMAND	   A command not entered directly from	the
				   console  terminal  is  not  a  legal CCL
				   command.  This  error  occurs  when	the
				   argument  of a UA, UB, or UC command was
				   not a legal command.

	  ILLEGAL * OR ?	   An * or ? was used in a CCL command that
				   does	   not	 accept	  the	wild   card
				   construction.  Only	CCL  commands  that
				   run	FOTP  or DIRECT allow the wild card
				   construction.

	  ILLEGAL SYNTAX	   The	CCL  command  line  was	  formatted
				   incorrectly.

	  INPUT ERROR READING	   CCL cannot read the file specified  with
	  INDIRECT FILE		   the @ construction.

	  I/O ERROR ON SYS:	   An error occurred while doing I/O to the
				   system  device.   The  system  must	 be
				   restarted   at   7600   or	7605.	 Do
				   not press  CONT.  as	 that  will  surely
				   cause further errors.

	  I/O ERROR TRYING TO	   An I/O  error  occurred  while  CCL	was
	  RECALL		   trying to remember an argument.

	  NO CCL!		   CCL.SV is  not  present  on	the  system
				   device.

	  NOT ENOUGH CORE	   The number specified in a  CORE  command
				   is  larger  than  the  number of 4K core
				   banks on the system.

	  name NOT FOUND	   The file with  the  name  given  is	not
				   present  on the specified device, or the
				   user tried to input from an	output-only
				   device.

	  %SUPERCEDED		   The file specified  in  a  MAKE  command
				   already   exists.   This  is	 a  warning
				   message  indicating	that  the  file	 is
				   being replaced.

	  SWITCH NOT ALLOWED HERE  Either a CCL option was specified on the
				   left	 side of the < or was used when not
				   allowed.  For example:  COMPARE FILE-NB.

	  TOO MANY FILES	   Too many files were included	 in  a	CCL
				   command.






				      C-6

		     SYSTEM ERROR CONDITIONS AND MESSAGES


     C.5  COMMAND DECODER ERRORS

     The following errors are printed by the Command  Decoder.	 After	the
     error  message,  the Command Decoder starts a new line, prints a * and
     waits for another command line.  The erroneous command is ignored.

	       Message				  Meaning

	  ILLEGAL SYNTAX	   The	 command    line    is	  formatted
				   incorrectly.

	  TOO MANY FILES	   More than three  output  files  or  nine
				   input   files  were	specified  (regular
				   mode)  or  >	 1  output  or	>  5  input
				   (special mode).


	  name NOT FOUND	   The specified input file  name  was	not
				   found on the device indicated.





































				      C-7







				   APPENDIX D

			       PROGRAMMING NOTES



     This appendix is a potpourri of ideas and techniques that have  proven
     useful in programming the PDP-8. OS/8 users may find some use in their
     own programs for the techniques mentioned here.

	  D.1  The Default File Storage Device, DSK

	  D.2  Modification to Card Reader Handler

	  D.3  Suppression of Carriage Return/Line Feed in FORTRAN I/O

	  D.4  Accessing the System Date in a FORTRAN Program

	  D.5  Determining Core Size on PDP-8 Family Computers

	  D.6  Using PRTC12-F to Convert OS/8 DECtapes to OS/12 LINCtapes

	  D.7  Notes on Loading Device Handlers

	  D.8  Available Locations in the USR Area

	  D.9  Accessing Additional Information Words in OS/8

	  D.10 SABR Programming Notes



     D.1  THE DEFAULT FILE STORAGE DEVICE, DSK

     The Command Decoder, as noted earlier, makes certain assumptions about
     the I/O device where none is explicitly stated.  Namely, on all output
     files where no device name is given, the device DSK  is  assumed.	 On
     the  first	 input	file where no device name is given, DSK is assumed.
     Subsequent input files assume the same device as  the  previous  input
     file.  This convention was adopted to simplify typing command lines.

     The permanent device name DSK is assigned when the	 system	 is  built.
     On all standard systems, DSK is equivalent to SYS.	 A useful technique
     is	 to  use  the  ASSIGN  command	to  redefine  the  meaning  of	DSK
     temporarily.   For example, where device DTA0 is equivalent to DSK and
     it becomes desirable to change DSK to DTA1, the following command can
     be given:

	       .ASSIGN DTA1 DSK





				      D-1

			       PROGRAMMING NOTES


     DTA1 remains the default file storage device until it  is	assigned  a
     new  name	or  a  DEASSIGN	 command  is  executed.	  This technique is
     considerably easier to use than rebuilding the entire system.

     If 'DSK' has not been assigned via	 the  ASSIGN  command,	then  'DSK'
     always  exists and has internal device number 2. User programs wishing
     to use DSK should do an  INQUIRE  to  find	 its  number  in  case	the
     operator has re-assigned it.



     D.2  MODIFICATION TO CARD READER HANDLER

     The standard card reader handler for OS/8	uses  the  DEC029  standard
     card  codes.   Some  installations	 may prefer to use the DEC026 codes
     instead.  This can be done by changing the card conversion codes  with
     the BUILD command ALTER.

	  1.  Call OS/8 BUILD by typing:
			RUN SYS:BUILD
	      in response to the dot printed by the Keyboard Monitor.

	  2.  Load the card reader handler as described on page 2-42 of the
	      OS/8 HANDBOOK.

	  3.  Use the ALTER command (see page  2-49 of the  OS/8  HANDBOOK)
	      to make the following changes:

	      CHANGE RELATIVE LOCATION	FROM	  TO	      ________________________	____	  __

		      104		3203	  7735
		      105		4007	  4076
		      106		3502	  0774

		      114		7514	  3314
		      115		0577	  1002
		      116		3637	  0305

		      124		0104	  3204
		      125		1211	  1273
		      126		3374	  3606
		      127		0641	  1341

		      134		7316	  3716
		      135		3410	  1175
		      136		1376	  3401

     The new system will have modified card codes.

     Note that this procedure does not affect FORTRAN run time	card  input
     with  READ	 (3,n).	 The  conversion  table for FORTRAN is UTILTY.SB on
     source DECtape #2.	 (DEC-S8-OSYSB-A-UA2)




				      D-2

			       PROGRAMMING NOTES


			      026 PUNCH CARD CODES


     Octal 8-bit   DEC026		   Octal 8-bit	  DEC026
	CODE	    CODE       CHARACTER     CODE	   CODE	  CHARACTER

	240	   BLANK	  SPACE	       300	   8-4	      @
	241	   12-8-7	  !	       301	   12-1	      A
	242	   0-8-5	  "	       302	   12-2	      B
	243	   0-8-6	  #	       303	   12-3	      C
	244	   11-8-3	  $	       304	   12-4	      D
	245	   0-8-7	  %	       305	   12-5	      E
	246	   11-8-7	  &	       306	   12-6	      F
	247	   8-6		  '	       307	   12-7	      G

	250	   0-8-4	  (	       310	   12-8	      H
	251	   12-8-4	  )	       311	   12-9	      I
	252	   11-8-4	  *	       312	   11-1	      J
	253	   12		  +	       313	   11-2	      K
	254	   0-8-3	  '	       314	   11-3	      L
	255	   11		  -	       315	   11-4	      M
	256	   12-8-3	  .	       316	   11-5	      N
	257	   0-1		  /	       317	   11-6	      O

	260	   0		  0	       320	   11-7	      P
	261	   1		  1	       321	   11-8	      Q
	262	   2		  2	       322	   11-9	      R
	263	   3		  3	       323	   0-2	      S
	264	   4		  4	       324	   0-3	      T
	265	   5		  5	       325	   0-4	      U
	266	   6		  6	       326	   0-5	      V
	267	   7		  7	       327	   0-6	      W

	270	   8		  8	       330	   0-7	      X
	271	   9		  9	       331	   0-8	      Y
	272	   11-8-2	  :	       332	   0-9	      Z
	273	   0-8-2	  ;	       333	   11-8-5     [
	274	   12-8-6	  <	       334	   8-7	      \
	275	   8-3		  =	       335	   12-8-5     ]
	276	   11-8-6	  >	       336	   8-5	      ^
	277	   12-8-2	  ?	       337	   8-2


				      NOTE

		    On some IBM 026 Keyboards this character
		    is graphically represented as a [].

		    A card containing an  8-2  in  column  1
		    with  all  remaining columns blank is an
		    end-of-file card.





				      D-3

			       PROGRAMMING NOTES


     D.3  SUPPRESSION OF CARRIAGE RETURN/LINE FEED IN FORTRAN

     It is often desirable to suppress the automatic  carriage	return/line
     feed  (CR/LF)  following FORTRAN WRITE statements to achieve an easily
     readable text.  The following three methods in  OS/8  FORTRAN  can	 be
     used to achieve this result:

	  1.  Follow the I/O list of a WRITE statement with a comma.  Thus,
	      the following statements:

			  WRITE (1,100) N,
		   100	  FORMAT (1X,15HTHE VALUE OF A(,I2,5H) IS )
			  READ (1,101)A(N)
		   101	  FORMAT (F8.4)

	      result in the following single line (assume N has a value	 of
	      12 and a value of 147.83 is being input):

		   THE VALUE OF A(12) IS 147.83

	  2.  Use of an empty field print statement enables a  text  to	 be
	      printed  without	a following CR/LF when there is no variable
	      to be printed.  For example:

			  WRITE (1,102)IDUMMY,
		   102	  FORMAT ('DESIRED TEXT',I0)

	  3.  READ statement using break character, as follows:

			  READ (1,101) IA,IB,IC
		   101	  FORMAT ('A=',I1,'B=',I1,'C=',I1)

	      results in no CR/LF after each phrase is printed.	  That	is,
	      the output is all printed on a single line.



     D.4  ACCESSING THE SYSTEM DATE IN A FORTRAN PROGRAM

     The availability of the system Date word in location 17666	 is  useful
     to	 many OS/8 programs.  The following FORTRAN program illustrates how
     the Date can be accessed in SABR code:

	       C       PROGRAM PRINTS THE CURRENT DATE
	       C
	       S       DUMMY DATE
	       S       TAD I DATE
	       S       DCA TEMP
	       S       TAD TEMP
	       S       AND (7
	       S       DCA \IYR
	       S       TAD TEMP
	       S       RAR;RTR
	       S       AND (37


				      D-4

			       PROGRAMMING NOTES


	       S       DCA \IDAY
	       S       TAD TEMP
	       S       CLL RAL;RTL;RTL
	       S       AND (17
	       S       DCA \IMO
		       WRITE (1,100) IMO,IDAY,IYR
	       100     FORMAT (/'DATE:	'I2'-'I2'-197'I1/)
		       CALL EXIT
	       S       CPAGE 2
	       SDATE,  6211
	       S       7666
	       STEMP,  0



     D.5  DETERMINING CORE SIZE ON PDP-8 FAMILY COMPUTERS

     Many times system programs	 need  to  determine  the  amount  of  core
     available	to them at run time.  For example, the OS/8 system programs
     LOADER,  PAL8,  and  CREF	perform	 this  calculation.    Because	 of
     differences  in the extended memory control of PDP-8 family computers,
     subroutines that work on one machine might not work on another.

     The following three conditions cause the most difficulty:

	  1.  On a  PDP-8  with	 an  extended  memory  control,	 addressing
	      nonexistent   memory   from  field  0  causes  the  following
	      instruction  to  be  skipped  and	  the	contents   of	the
	      corresponding field 0 location to be executed.  For example:

		       CDF 70		/NONEXISTENT FIELD
		       TAD I(X)		/EXECUTED LOCATION X
		       HLT		/THIS INSTRUCTION SKIPPED
		       .
		       .
		       .
		   X,  CLA CLL CML RAR	/LOAD 4000

	      The preceding code causes 4000 to be loaded into the  AC	and
	      the HLT instruction to be skipped when executed on a PDP-8.

	  2.  On a PDP-12 with an odd number of 4K banks (12K,	20K,  28K),
	      all  reads  in the first nonexistent field load zeros.  Reads
	      to higher fields, as well as all reads to nonexistent  memory
	      on  a  machine  with  an even number of 4K banks load all one
	      bits.

	  3.  The PDP-8/L normally treats all CDF's to fields 2	 through  7
	      as  NOP's.  (It  tests  bits  6  to  7  of  all  CDF  and CIF
	      instructions for 0's  before  executing  the  IOT.)  However,
	      there  is a special 12K option for the PDP-8/L called a BM08.
	      With this option a CDF to field 2 is valid, but  a  CDF's	 to
	      fields 4 through 7 remain NOP's.



				      D-5

			       PROGRAMMING NOTES


     For those who are interested, the following subroutine has been tested
     on	 the  PDP-8, 8/S, 8/L, 8/I, 8/E, PDP-12, and LINC-8 computers.	For
     the purpose of this example, it is assembled at 00200.

		 /SUBROUTINE TO DETERMINE CORE SIZE.

		 /THIS SUBROUTINE WORKS ON ANY PDP-8 FAMILY
		 /COMPUTER. THE VALUE, FROM 1 TO 10 (OCTAL),
		 /OF THE FIRST NON-EXISTENT MEMORY FIELD IS
		 /RETURNED IN THE AC.

		 /NOTE - THIS ROUTINE MUST BE PLACED IN FIELD 0

     0200 0000	 CORE,	 0
     0201 7300		 CLA CLL
     0202 6201	 COR0,	 CDF 0		 /(NEEDED FOR PDP-8L)
     0203 1237		 TAD	 CORSIZ	 /GET FIELD TO TEST
     0204 7006		 RTL
     0205 7004		 RAL
     0206 0217		 AND	 COR70	 /MASK USEFUL BITS
     0207 1232		 TAD	 COREX
     0210 3211		 DCA	 .+1	 /SET UP CDF TO FIELD
     0211 6201	 COR1,	 CDF	 \N	 /N IS FIELD TO TEST.
     0201 1635		 TAD I	 CORLOC	 /SAVE CURRENT CONTENTS
     0213 7000	 COR2,	 NOP		 /(HACK FOR PDP-8!)
     0214 3211		 DCA	 COR1
     0215 1213		 TAD	 COR2	 /7000 IS A "GOOD" PATTERN
     0216 3635		 DCA I	 CORLOC
     0217 0070	 COR70,	 70		 /(HACK FOR PDP-8.,NO-OP)
     0020 1635		 TAD I	 CORLOC	 /TRY TO READ BACK 7000
     0221 7400	 CORX,	 7400		 /(HACK FOR PDP-8,.NO-OP)
     0022 1221		 TAD	 CORX	 /GUARD AGAINST "WRAP AROUND"
     0223 1236		 TAD	 CORV	 /TAD (1400)
     0224 7640		 SZA CLA
     0225 5232		 JMP	 COREX	 /NON-EXISTENT FIELD EXIT
     0226 1211		 TAD	 COR1	 /RESTORE CONTENTS DESTROYED
     0227 3635		 DCA I	 CORLOC
     0230 2237		 ISZ	 CORSIZ	 /TRY NEXT HIGHER FIELD
     0231 5202		 JMP	 COR0

     0232 6201	 COREX,	 CDF0		 /LEAVE WITH DATA FIELD 0
     0233 1237		 TAD	 CORSIZ	 /1ST NON-EXISTENT FIELD
     0234 5600		 JMP I	 CORE
     0235 0221	 CORLOC, CORX		 /ADDRESS TO TEST IN EACH FIELD
     0236 1400	 CORV,	 1400		 /7000+7400+1400=0
     0237 0001	 CORSIZ, 1		 /CURRENT FIELD TO TEST



     D.6  USING PRTC12-F TO CONVERT OS/8 DECTAPES TO OS/12 LINCTAPES

     Many users of OS/8 on the PDP-12 will be interested in the fact  that,
     since  OS/8  uses	an  identical  file structure on all devices, PDP-8
     DECtape in OS/8 format may be directly copied to OS/8 LINCtapes by the
     PRTC12-F program.

				      D-6

			       PROGRAMMING NOTES


     The PRTC12-F program uses the PDP-12 TC12-F hardware  option  to  read
     DECtapes and convert these tapes to LINCtape.  This hardware option is
     required to read DECtapes on the PDP-12

     The PRTC12-F program is described in the document DEC-12-YIYA-D.  This
     document  describes  the program operation in detail, and must be read
     before attempting to use PRTC12-F.	 The operations that  convert  OS/8
     format DECtapes are as follows:

	  1.  Mount the OS/8 DECtape  on  unit	1  and	a  PDP-12  LINCtape
	      formatted with 129 words per block on unit 2.

	  2.  When the READ questionnaire is displayed, respond as  follows
	      (responses  are  underlined;   the  character  }	 stands for
	      carriage return and  ~   stands for line feed):

		   READ 1777  }	 BLOCKS
		   TAPE FORMAT A  }   UNIT 1 }
		   STARTING WITH BLOCK 0 } ~
		   etc.

	  3.  When  the	 WRITE	questionnaire  is  displayed,  respond	 as
	      follows:

		   WRITE THE RESULT
		   IN TAPE FORMAT B }	ON UNIT 2 }
		   STARTING AT BLOCK 0 } ~
		   etc.



     D.7  NOTES ON LOADING DEVICE HANDLERS



     D.7.1  Problem With Multiple Input Files

     There is a problem associated with reusing	 Device	 Handler  areas	 in
     OS/8.  This problem is best illustrated by an example:

     Assume a program  has  reserved  locations	 1000-1377  for	 its  input
     handler  and  locations  7400-7577	 for  its  output  handler.  If the
     program gives a USR FETCH command to load the DTA1 handler as an input
     device handler, all 8 DECtape handlers will load into 1000-1377, since
     they are all co-resident.	If another FETCH is issued to load the DTA2
     handler  as an output device handler, that handler will not be loaded,
     because it shares space with the DTA1 handler currently in core.  This
     is fine - however, if the user now switches input devices and FETCHes
     the paper tape reader handler as  an  input  device  handler  it  will
     destroy the DTA2 handler and the next attempt to output using the DTA2
     handler will produce errors.  There are two ways to  get  around  this
     problem.




				      D-7

			       PROGRAMMING NOTES


	  1.  Always assign the handler which you expect to  stay  in  core
	      the  longest  first.  Most programs can process more than one
	      input file per program step (e.g., an assembly  pass  is	one
	      program  step)  but  only	 one  output file;  therefore, they
	      assign the output handler before any of the  input  handlers.
	      In  the above example, the problem would be eliminated if the
	      DTA2 handler were assigned first.

	  2.  Always give a USR RESET call before each	FETCH.	 Obviously,
	      this  call  should  not  delete  any open output files.  This
	      means that the USR will always load the new handler, even	 if
	      another  copy  is	 in  core.   The user must FETCH the output
	      handler again before issuing the USR  CLOSE  call,  otherwise
	      the USR will determine that the output handler is not in core
	      and give a MONITOR ERROR 3 message.

     8K FORTRAN uses this second method for device-independent I/O  at	run
     time.



     D.7.2  Dynamically Loading Device Handlers

     Some programs which use dynamic core allocations will want to use OS/8
     Device  handlers  but  cannot afford to always allocate the maximum of
     two pages per handler.  The following is a subroutine  which  loads  a
     device handler dynamically, returning its entry in the AC.	 It assumes
     that the name of the handler is in locations NAME1 and  NAME2,  and  a
     subroutine	 GETPAG	 exists	 which	gets  a	 page  from  the  bottom of
     available field 0 of storage and returns its address in the AC.   This
     example  subroutine  runs in field 1 and can only be called from field
     1, but can be rewritten for any other possibility.

	  ASSIGN, 0
		  TAD NAME1
		  DCA N1
		  TAD NAME2
		  DCA N2       /MOVE DEVICE NAME INTO "INQUIRE" COMMAND
		  CDF CIF 10
		  JMS I (7700
		  10	       /USRIN - FORCE USR INTO CORE
		  JMS I (200
		  12	       /INQUIRE
	  N1,	  0
	  N2,	  0
	  LOC1,	  0
		  JMP ASSERR   /NO SUCH DEVICE - QUIT
		  TAD LOC1
		  SZA	       /IS THE HANDLER ALREADY IN CORE?
		  JMP I ASSIGN /YES - RETURN ITS ENTRY POINT
		  JMS GETPAG   /GET A PAGE DYNAMICALLY
		  DCA LOC2
	  ASSTRY, TAD N2       /LOAD DEVICE NUMBER



				      D-8

			       PROGRAMMING NOTES

		  JMS I (200
		  1	       /FETCH
	  LOC2,	  0	       /PAGE TO FETCH INTO
		  JMP TWOPAG   /FAILED - MUST BE A TWO-PAGE HANDLER
		  TAD LOC2
		  JMP I ASSIGN /RETURN ENTRY POINT
	  TWOPAG, JMS GETPAG   /GET ANOTHER PAGE
		  ISZ LOC2     /SET "TWO PAGE HANDLER ALLOWED" BIT
		  CLA
		  JMP ASSTRY   /FETCH WILL SUCCEED THIS TIME
	  ASSERR, .....	       /ERROR ROUTINE



     D.8 AVAILABLE LOCATIONS IN THE USR AREA

     A few programs may need additional storage space in field 1  when	the
     USR  is  in  core.	  A  number  of locations in the USR area (10000 to
     11777) are available and may be used whenever the USR is in core.	The
     locations are as follows:

	  1.  Locations 10000 to 10006 are available  for  scratch  storage
	      and/or ODT breakpoint usage, without restriction.

	  2.  All auto-index registers (locations 10010 to  10017)  may	 be
	      used, but these locations are destroyed by USR operations.

	  3.  Location 10020 to 10037 may be used as scratch  storage  with
	      no restrictions.

	  4.  Locations 11400 to 11777 are used by the USR to preserve	the
	      last directory segment read while performing a LOOKUP, ENTER,
	      or CLOSE operation.  Location 10007 contains a key specifying
	      which segment of which device is currently in core.

	      Any user program may use locations 11400 to 11777 as  scratch
	      storage  as  long	 as  location  10007 is set to 0 before the
	      first  use.   Of	course,	 the  LOOKUP,  ENTER,	and   CLOSE
	      operations  will read a directory segment into 11400 to 11777
	      and set 100007 to a non-zero value again.



     D.9   ACCESSING ADDITIONAL INFORMATION WORDS IN OS/8

     In all of these cases, the USR must have been previously brought  into
     core with the USRIN function.



     D.9.1   After a LOOKUP or ENTER

     After a LOOKUP or ENTER, location 10017 points to the length  word	 of
     the  file entry.  To get a pointer to the first Additional Information
     Word, a program would execute the following code:


				      D-9

			       PROGRAMMING NOTES


		  CDF 10
		  TAD I (1404	  /GET # OF ADDITIONAL INFORMATION WORDS
				  /FROM DIRECTORY
		  SNA
		  JMP NONE	  /NO ADDITIONAL INFORMATION WORDS
		  TAD I (0017
		  DCA POINTER
		  .
		  .
		  .

     "POINTER" now points to the first Additional Information Word.



     D.9.2   After a CLOSE

     Because CLOSE is a legal operation even if no output file is  present,
     it	 is  not  suggested  that  Additional Information Words be modified
     following a CLOSE.	 To alter the Additional  Information  Words  of  a
     permanent	file,  do  a LOOKUP to get the directory segment into core,
     then alter the words and rewrite the directory segment.



     D.9.3   Rewriting the Current Directory Segment

     Whenever a user program changes the Additional Information Words of  a
     file, it must rewrite the directory segment containing that file entry
     in order to make sure the changes are permanently recorded.

     The following code, which must be in field 1, will rewrite the current
     directory segment:

		  CDF 10	  /CODE IS IN FIELD 1
		  TAD 7		  /GET DIRECTORY KEY WORD
		  AND (7	  /EXTRACT SEGMENT NUMBER
		  DCA SEGNO
		  CIF 0
		  JMS I 51	  /LOC 51 POINTS TO THE DEVICE HANDLER
		  4210		  /WRITE OPERATION
		  1400		  /DIRECTORY SEGMENT CORE ADDRESS
	  SEGNO,  0
		  JMP ERROR	  /ERROR REWRITING DIRECTORY

     Location 10051 will always point to the  device  handler  entry  point
     used  to  read  in	 the  last directory segment, following a LOOKUP or
     ENTER operation.








				     D-10

			       PROGRAMMING NOTES


     D.10 SABR PROGRAMMING NOTES



     D.10.1 Optimizing SABR Code

     There are two types of users who will be using the	 SABR  assembler  -
     those  who	 like the convenience of page-boundary-independent code and
     are willing to pay the price for it, and those who need a	relocatable
     assembler	but  are  still	 very location conscious.  These optimizing
     hints are directed to the latter user.

     One way to beat the  high	cost  of  non-paged  code  is  to  Page	 It
     Yourself.	 This  is  done	 by  using the LAP (Leave Automatic Paging)
     pseudo-op and the PAGE pseudo-op to force paging where  needed.   This
     saves  2  to  4  instructions  per	 page  from elimination of the page
     escape.  In addition, the fact  that  the	program	 must  be  properly
     segmented may save a considerable amount.

     Wasted core  may  be  reduced  by	eliminating  the  ever-present	CDF
     instructions which SABR inserts into a program.  This is done by using
     n fake indirects". Define the following op codes:

		OPDEF  ANDI 0400
		OPDEF  TADI 1400
		OPDEF  ISZI 2400
		OPDEF  DCAI 3400
		.
		.
		.

     These codes correspond to the PDP-8 memory reference instructions	but
     they  include an indirect bit.  The difference can best be appreciated
     by an example:

     If X is off-page, the sequence

	       LABEL,  SZA
		       DCA X

     is assembled by SABR into

	       LABEL,  SZA
		       JMS 45
		       SKP
		       DCA I (X)

     or four instructions and one literal.

     The sequence






				     D-11

			       PROGRAMMING NOTES

	       PX,     X
		       .
		       .
		       .
	       LABEL,  SZA
		       DCAI PX

     assembles into three instructions for a saving of 40  percent.   Note,
     however,  that  the  user	must  be  sure	that the data field will be
     correct when the code at LABEL is encountered.   Also  note  that	the
     SABR  assumes  that  the  Data Field is equal to the Instruction Field
     after a JMS instruction, so subroutine returns should not use the JMPI
     op code.

     The standard method to fetch a scalar integer argument of a subroutine
     in SABR is:

		       Code

	       IARG,   DUMMY X
		       0
	       SUBR,   BLOCK 2
		       TAD I SUBR
		       DCA X
		       INC SUBR#
		       TAD I SUBR
		       DCA X#
		       INC SUBR#
		       TAD I X
		       DCA IARG
		       .
		       .
		       .
	       X,      BLOCK 2

     This code	requires  19  words  of	 core  and  takes  several  hundred
     microseconds to execute.  The following sequence:

		       Code

	       IARG,   0
	       SUBR,   BLOCK 2
		       TAD I SUBR
		       DCA X
		       INC SUBR#
		       TADI SUBR#
		       DCA IARG
		       INC SUBR#
	       X,      HLT	 /THIS IS A CDF
		       TAD I IARG
		       DCA IARG
		       .
		       .
		       .

     takes only 14 words and executes in approximately 1/3 the time.

				     D-12

			       PROGRAMMING NOTES


     D.10.2  Calling the USR and Device Handlers from SABR Code

     One important thing to remember is that any code which calls  the	USR
     must  not	reside	in  locations  10000 to 11777.	Therefore, any SABR
     routine which calls the USR must be loaded into a field other  than  1
     or	 above	location 2000 in field 1. To call the USR from SABR use the
     sequence:

		  CPAGE n	  /N=7+(# OF ARGUMENTS)
		  6212		  /CIF 10
		  JMS 7700	  /OR 200 IF USR IN CORE
		  REQUEST
		  ARGUMENTS	  /OPTIONAL DEPENDING ON REQUEST
		  ERROR RETURN	  /OPTIONAL DEPENDING ON REQUEST

	To call a device handler from SABR use the sequence:

		  CPAGE12	  /10 IF "HAND" IN PAGE 0
		  6202		  /CIF 0
		  JMS I HAND	  /DO NOT USE JMSI
		  FUNCT
		  ADDR
		  BLOCK
		  ERROR RETURN
		  SKP
	  HAND,	  0		  /"HAND" MUST BE ON SAME PAGE
				  /AS CALL, OR IN PAGE 0!!





























				     D-13







				   APPENDIX E

			CHARACTER CODES AND CONVENTIONS



     Table E-1 contains a list of the control characters used by  OS/8	and
     associated	 system	 programs.   Table  E-2 contains the OS/8 character
     set, which is a subset of the complete ASCII code, the unlisted  codes
     are  generally  not  used	by  OS/8  or the system programs.  Note the
     following:

	  1.  On some terminals, the character back-arrow (_)  is  replaced
	      by  an  underline	 (_)   character,  and	the up-arrow (^) is
	      replaced by circumflex (^).

	  2.  Some terminals use  parity  codes	 rather	 than  forcing	the
	      leading  bit  of the 8-bit character code to be a 1. To avoid
	      problems, OS/8 system programs always ignore the	parity	bit
	      during ASCII input.

	  3.  OS/8 does not handle lower case characters (octal	 codes	341
	      through  372).  The  exceptions to this are the editors, EDIT
	      and TECO.	 The KL8E and LPSV  handlers  can  be  modified	 to
	      handle lower case.


				   Table E-1
			    OS/8 Control Characters
     +---------------------------------------------------------------------+
     |	  Octal								   |
     |	  8-bit	      Character						   |
     |	  Code		Name			  Remarks		   |
     +---------------------------------------------------------------------+
     |	  000	    null		Ignored in ASCII input.		   |
     |									   |
     |	  200	    leader/trailer	Leader/trailer	code  precedes	and|
     |					follows	 the data portion of binary|
     |					files.				   |
     |									   |
     |	  203	    CTRL/C		OS/8 break character, forces return|
     |					to Keyboard Monitor, echoed as ^C. |
     |									   |
     |	  207	    BELL		CTRL/G.				   |
     |									   |
     |	  211	    TAB			CTRL/I, horizontal tabulation.	   |
     |									   |
     |	  212	    LINE FEED		Used as a control character by	the|
     |					Command Decoder and ODT.	   |
     |									   |
     |	  213	    VT			CTRL/K, vertical tabulation.	   |
     +---------------------------------------------------------------------+


				      E-1

			CHARACTER CODES AND CONVENTIONS


				Table E-1 (Cont.)
			     OS/8 Control Characters
     +---------------------------------------------------------------------+
     |	  Octal								   |
     |	  8-bit	      Character						   |
     |	  Code		Name			  Remarks		   |
     +---------------------------------------------------------------------+
     |	  214	    FORM		CTRL/L, form feed.		   |
     |									   |
     |	  215	    RETURN		Carriage return,  generally  echoed|
     |					as  carriage  return  followed by a|
     |					line feed.			   |
     |									   |
     |	  216				Used only  on  LS8E  line  printer.|
     |					Puts  current  line  into  expanded|
     |					character mode.			   |
     |									   |
     |	  217	    CTRL/O		Break Character, used  to  suppress|
     |					Teletype output, echoed as ^O.	   |
     |									   |
     |	  225	    CTRL/U		Delete current input  line,  echoed|
     |					as ^U.				   |
     |									   |
     |	  232	    CTRL/Z		End-of-File character for all ASCII|
     |					and  binary  files  (in relocatable|
     |					binary	files  CTRL/Z  is   not	  a|
     |					terminator  if it occurs before the|
     |					trailer code).			   |
     |									   |
     |	  233	    ESC			ESCape	replaces  ALTMODE  on  some|
     |					terminals.   Considered	 equivalent|
     |					to ALTMODE.			   |
     |									   |
     |	  375	    ALTMODE		Special	  break	   character	for|
     |					Teletype input.			   |
     |									   |
     |	  376	    PREFIX		PREFIX	replaces  ALTMODE  on  some|
     |					terminals.   Considered	 equivalent|
     |					to ALTMODE.			   |
     |									   |
     |	  377	    RUBOUT		Key  is	 labeled  DELETE  on   some|
     |					terminals.   Deletes  the  previous|
     |					character typed.		   |
     +---------------------------------------------------------------------+












				      E-2

			CHARACTER CODES AND CONVENTIONS


				     Table E-2
			       ASCII Character Codes

     +-------+--------+----------+--------------+--------------------------+
     | Octal |	      |	 Punched |  Character	|			   |
     | 8-bit |	6-bit |	 Card	 |  Representa- |			   |
     | Code  |	Code  |	 Code	 |  tion	|  Remarks		   |
     +-------+--------+----------+--------------+--------------------------+
     |	     |	      |		 |		|			   |
     | 240   |	  40  |	 blank	 |		|  space (non-printing)	   |
     | 241   |	  41  |	 11-8-2	 |     !	|  exclamation point	   |
     | 242   |	  42  |	 8-7	 |     "	|  quotation marks	   |
     | 243   |	  43  |	 8-3	 |     #	|  number sign		   |
     | 244   |	  44  |	 11-8-3	 |     $	|  dollar sign		   |
     | 245   |	  45  |	 0-8-3	 |     %	|  percent		   |
     | 246   |	  46  |	 12	 |     &	|  ampersand		   |
     | 247   |	  47  |	 8-5	 |     '	|  apostrophe or acute	   |
     |	     |	      |		 |		|  accent		   |
     |	     |	      |		 |		|			   |
     | 250   |	  50  |	 12-8-5	 |     (	|  opening parenthesis	   |
     | 251   |	  51  |	 11-8-5	 |     )	|  closing parenthesis	   |
     | 252   |	  52  |	 11-8-4	 |     *	|  asterisk		   |
     | 253   |	  53  |	 12-8-6	 |     +	|  plus			   |
     | 254   |	  54  |	 0-8-3	 |     ,	|  comma		   |
     | 255   |	  55  |	 11	 |     _	|  minus sign or hyphen	   |
     | 256   |	  56  |	 12-8-3	 |     .	|  period or decimal point |
     | 257   |	  57  |	 0-1	 |     /	|  slash		   |
     |	     |	      |		 |		|			   |
     | 260   |	  60  |	 0	 |     0	|			   |
     | 261   |	  61  |	 1	 |     1	|			   |
     | 262   |	  62  |	 2	 |     2	|			   |
     | 263   |	  63  |	 3	 |     3	|			   |
     | 264   |	  64  |	 4	 |     4	|			   |
     | 265   |	  65  |	 5	 |     5	|			   |
     | 266   |	  66  |	 6	 |     6	|			   |
     | 267   |	  67  |	 7	 |     7	|			   |
     |	     |	      |		 |		|			   |
     | 270   |	  70  |	 8	 |     8	|			   |
     | 271   |	  71  |	 9	 |     9	|			   |
     | 272   |	  72  |	 8-2	 |     :	|  colon		   |
     | 273   |	  73  |	 11-8-6	 |     ;	|  semicolon		   |
     | 274   |	  74  |	 12-8-4	 |     <	|  less than		   |
     | 275   |	  75  |	 8-6	 |     =	|  equals		   |
     | 276   |	  76  |	 0-8-6	 |     >	|  greater than		   |
     | 277   |	  77  |	 0-8-7	 |     ?	|  question mark	   |
     |	     |	      |		 |		|			   |
     | 300   |	  00  |	 8-4	 |     @	|  at sign		   |
     | 301   |	  01  |	 12-1	 |     A	|			   |
     | 302   |	  02  |	 12-2	 |     B	|			   |
     | 303   |	  03  |	 12-3	 |     C	|			   |
     | 304   |	  04  |	 12-4	 |     D	|			   |
     | 305   |	  05  |	 12-5	 |     E	|			   |
     | 306   |	  06  |	 12-6	 |     F	|			   |
     | 307   |	  07  |	 12-7	 |     G	|			   |
     +-------+--------+----------+--------------+--------------------------+

				      E-3

			CHARACTER CODES AND CONVENTIONS


				 Table E-2 (Cont.)
			       ASCII Character Codes

     +-------+--------+----------+--------------+--------------------------+
     | Octal |	      |	 Punched |  Character	|			   |
     | 8-bit |	6-bit |	 Card	 |  Representa- |			   |
     | Code  |	Code  |	 Code	 |  tion	|  Remarks		   |
     +-------+--------+----------+--------------+--------------------------+
     |	     |	      |		 |		|			   |
     | 310   |	  10  |	 12-8	 |     H	|			   |
     | 311   |	  11  |	 12-9	 |     I	|			   |
     | 312   |	  12  |	 11-1	 |     J	|			   |
     | 313   |	  13  |	 11-2	 |     K	|			   |
     | 314   |	  14  |	 11-3	 |     L	|			   |
     | 315   |	  15  |	 11-4	 |     M	|			   |
     | 316   |	  16  |	 11-5	 |     N	|			   |
     | 317   |	  17  |	 11-6	 |     O	|			   |
     |	     |	      |		 |		|			   |
     | 320   |	  20  |	 11-7	 |     P	|			   |
     | 321   |	  21  |	 11-8	 |     Q	|			   |
     | 322   |	  22  |	 11-9	 |     R	|			   |
     | 323   |	  23  |	 0-2	 |     S	|			   |
     | 324   |	  24  |	 0-3	 |     T	|			   |
     | 325   |	  25  |	 0-4	 |     U	|			   |
     | 326   |	  26  |	 0-5	 |     V	|			   |
     | 327   |	  27  |	 0-6	 |     W	|			   |
     |	     |	      |		 |		|			   |
     | 330   |	  30  |	 0-7	 |     X	|			   |
     | 331   |	  31  |	 0-8	 |     Y	|			   |
     | 332   |	  32  |	 0-9	 |     Z	|			   |
     | 333   |	  33  |	 12-8-2	 |     [	|  opening bracket,SHIFT/K |
     | 334   |	  34  |	 11-8-7	 |     \	|  backslash, SHIFT/L	   |
     | 335   |	  35  |	 0-8-2	 |     ]	|  closing bracket, SHIFT/M|
     | 336   |	  36  |	 12-8-7	 |     ^	|  circumflex		   |
     | 337   |	  37  |	 0-8-5	 |     _	|  underline - EOF signal  |
     +-------+--------+----------+--------------+--------------------------+

				      NOTES

	  1.  These are the DEC029 standard card codes.

	  2.  On most DEC Teletypes circumflex is replaced by up-arrow (^).

	  3.  A card containing	 0-8-5	in  column  1  with  all  remaining
	      columns blank is an end-of-file card.

	  4.  On most DEC Teletypes underline  is  replaced  by	 back-arrow
	      (_).

	  5.  On some IBM 029 keyboards 1 is graphically represented  as  a
	      cent sign (c/).

	  6.  On some IBM 029 keyboards \  is  graphically  represented	 as
	      logical NOT (-,).


				      E-4

			CHARACTER CODES AND CONVENTIONS


	  7.  On some IBM 029 keyboards	 ^  is graphically  represented	 as
	      vertical bar (|).

	  8.  On a very few LP08 line printers, the character diamond  (<>)
	      is printed instead of backslash.

	  9.  On a very few LP08 line printers, the character heart (V)	 is
	      printed instead of underline.

	 10.  The character number sign on some terminals  is  replaced	 by
	      pound sign (L).













































				      E-5







				   APPENDIX F

			  OS/8 INPUT/OUTPUT ROUTINES


     Appendix F describes a set of generalized I/O routines for	 use  under
     the OS/8 system.  The routines presented here are used in all the OS/8
     CUSPs (Commonly Used System Programs)  in	more  or  less	this  form.
     Variations	 are  made  depending on the particular application and how
     errors are to be handled.	The routines, as indicated,  will  work	 as
     presented.	  The  routines work most efficiently in field 1, since CIF
     10's are not necessary when addressing the Monitor,  and  the  Command
     Decoder tables are similarly available.  Obviously the routines can be
     modified to run in any memory field or core locations.



     F.1  GENERAL DESCRIPTION

     These subroutines assume that the Command Decoder tables have been set
     up	 to  indicate  the  proper I/O devices.	 The routines handle device
     handler assignment without user interference.   All  I/O  is  done	 by
     simple  subroutine	 calls.	  The user program never needs to interface
     with the Monitor or  device  handlers.   All  buffering  and  internal
     bookkeeping  are  performed by the routines.  In these routines, it is
     assumed that only one output device is  used  at  a  time,	 i.e.,	the
     output  routine  does  not	 automatically	set  up for the next output
     device.  This modification can be made if desired.	 As  many  as  nine
     inputs  are  handled  automatically.   When  input	 from one device is
     exhausted, the input  routine  will  automatically	 utilize  the  next
     device specified in the Command Decoder list of inputs.



     F.2  SUBROUTINES FUNCTIONS

     Following is a brief list of the subroutines and their functions.

	  ICHAR - Character input routine.

		   Call sequence:

			   JMS ICHAR
			   ERROR RETURN
			   NORMAL RETURN

		   Error:

			   If AC>0, an EOF on input has occurred.  No  more
			   input is available.	If AC<0, a device error has
			   occurred.



				      F-1

			  OS/8 INPUT/OUTPUT ROUTINES


		   Normal:

			   8 bit character is in the AC.

	  OCHAR - Character output routine.

		   Call:

			   TAD CHAR 	/8 BIT CHARACTER
			   JMS OCHAR
			   ERROR RETURN
			   NORMAL RETURN

		   Error:

			   AC<0 implies a fatal error.
			   AC > or = 0 implies that the hole  allotted	for
			   output was exceeded.

		   Normal:

			   AC=0. The character has been put into the device
			   output buffer.

	  IOPEN - Input initialize routine.

		   Call:

			   JMS IOPEN
			   RETURN

	  Return:

			   Input pointers reset.  The next  call  to  ICHAR
			   will	 read  from the first device in the Command
			   Decoder input list.

	  OOPEN - Output initialize routine.

		   Call:

			   JMS OOPEN
			   ERROR RETURN
			   NORMAL RETURN

		   Error:

			   If AC> or = 0, no output device was	specified.
			   If AC<0, an error occurred opening the file.

		   Normal:

			   An output file has been opened.   No	 action	 if
			   the output was a non-file structured device.


				      F-2

			  OS/8 INPUT/OUTPUT ROUTINES

	  OCLOSE - Output close routine.

		   Call:

			   JMS OCLOSE
			   ERROR RETURN
			   NORMAL RETURN

		   Error:

			   Either the closing length is too large  for	the
			   space allotted or an output error has occurred.

		   Normal:

			   The output file is now a permanent file  on	the
			   output device.



     F.3  SUBROUTINE PARAMETERS

     These subroutines handle  device  assignment  and	internal  buffering
     automatically.  To accomplish this, certain parameters must be defined
     at assembly time.	These parameters specify  all  details	of  handler
     location, and buffer size for the routines.

	  Parameter			Definition	  _________			__________

	  INBUF =	 Address of input buffer.

	  INCTL =	 Input buffer control word.   See  the	section	 on
			 using device handlers for details of the control
			 word format.

	  OUBUF =	 Output buffer address.

	  OUCTL =	 Output	 buffer	 control  word.	  This	must  be  a
			 negative number to indicate a write operation.

	  INRECS =	 Number of input records in input buffer.  INRECS =
			 INCTL/256 (DECIMAL).

	  INDEVH =	 Address of input device handler.

	  OUDEVH =	 Address of output device handler.

     The parameters can either be a part of the actual	subroutine  source,
     or	 they can be contained in a separate parameter file to be assembled
     with the  subroutine  file.   The	latter	approach  provides  greater
     flexibility in using the routines.






				      F-3

			  OS/8 INPUT/OUTPUT ROUTINES


     F.3.1  Example

     Following is a sample of the use  of  the	subroutines.   The  program
     simply  calls  the Command Decoder, and transfers input from the input
     devices to the output file, closes the output, and exits.

	       FIELD 1
	       *2000
	       JMS I (7700		/LOCK MONITOR INTO CORE.
	       10
     CALLCD,   JMS I (200		/CALL COMMAND DECODER
	       5			/TO PICK OPTIONS.
	       0
	       JMS I (IOPEN		/SETUP TO START LOOKING AT
					/CD INPUT FILE.
	       JMS I (OOPEN		/OPEN UP AN OUTPUT FILE.
	       SMA CLA			/IF AC<0, WE HAD A FATAL
	       JMP OK			/TYPE ERROR. AC>0 IS O.K.
	       JMS TERR			/ERROR.
	       TEXT /OPEN FAILED/
     OK,       JMS I (ICHAR
	       JMP TSTEOF		/EITHER ERROR OR EOF.
					/SAVE IT.

	       JMS I (OCHAR		/TRANSFER THE CHARACTER
	       JMP OUTERR		/OUTPUT ERROR
	       JMP OK			/TRANSFER UNTIL EOF FOUND.
     TSTEOF,   SMA CLA			/IF NEG., FATAL
	       JMP CLOSE		/EOF. CLOSE OUTPUT
	       JMS TERR
	       TEXT /READ ERROR/
     CLOSE,    JMS I (OCLOSE		/CLOSE OUTPUT FILE.
	       JMP CLERR		/CLOSE ERROR
	       JMP CALLCD		/NEXT.
     OUTERR,   JMS TERR
	       TEXT /OUTPUT ERROR/
     CLERR,    JMS TERR
	       TEXT /CLOSE ERROR/

     TERR,     0
	       TAD I TERR
	       RTR;RTR;RTR
	       JMS TYPIT
	       TAD I TERR
	       JMS TYPIT
	       ISZ TERR
	       JMP TERR+1

     TYPIT,    0
	       AND (77
	       SNA
	       JMP CRLF
	       TAD (300
	       JMS TTYOUT
	       JMP I TYPIT

				      F-4

			  OS/8 INPUT/OUTPUT ROUTINES


     CRLF,     TAD (215
	       JMS TTYOUT
	       TAD (212
	       JMS TTYOUT
	       JMP CALLCD

     TTYOUT,   0
	       TLS
	       TSF
	       JMP.-1
	       CLA
	       JMP I TTYOUT



     F.3.2  Subroutine Listing

     A listing of the routines follows.	 The parameters are set up in  such
     a	way  as	 to  allow  them  to  be put into a separate file.  Another
     parameter, ORIGIN, determines the location of the routines.




































				      F-5

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 1


              /OS/8 GENERAL CHARACTER I/O ROUTINES FOR BLEEP

              /CALLED AS FOLLOWS:

              /JMS I (IOPEN           INITIALIZES THE INPUT ROUTINE

              /JMS I (ICHAR           READS A CHARACTER
              /ERROR RETURN           AC>0 IF END OF FILE, AC<0 IF READ 
              /                       ERROR

              /JMS I (OOPEN           INITIALIZES THE OUTPUT ROUTINE
              /ERROR RETURN           AC>0 IF NO OUTPUT DEVICE/FILE, AC<0 
              /                       IF ERROR

              /JMS I (OCHAR           OUTPUTS A CHARACTER
              /ERROR RETURN           OUTPUT ERROR OR TOO MUCH OUTPUT

              /JMS I (OCLOSE          CLOSES THE OUTPUT FILE
              /ERROR RETURN           FILE TOO LARGE TO BE CLOSED OR OUTPUT 
              /                       ERROR

              /JMS I (OTYPE           RETURNS DCB WORD OF OUTPUT DEVICE IN 
              /                       AC



              /PARAMETERS NEEDED:

              /INBUF=         ADDRESS OF INPUT BUFFER
              /INCTL=         INPUT BUFFER CONTROL WORD
              /OUBUF=         ADDRESS OF OUTPUT BUFFER
              /OUCTL=         OUTPUT BUFFER CONTROL WORD (MUST BE NEGATIVE)
              /INRECS=        [INCTL/256]
              /INDEVH=        ADDRESS OF PAGE FOR INPUT HANDLER
              /OUDEVH=        ADDRESS OF PAGE FOR OUTPUT HANDLER
              /IORFLD=        /FIELD OF THE SUBROUTINES.
              /ORIGIN=        /THE SUBROUTINES RESIDE AT 16600.

              /ASSUMES I/O MONITOR IS RESIDENT IN CORE.
              /CAN BE CALLED FROM ANY FIELD WITH BUFFERS IN ANY FIELD.













				      F-6

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 2


                      /PARAMETER DEFINITION:

        5000          OUBUF=  5000    /OUTPUT BUFFER STARTS AT 05000
        4200          OUCTL=  4200    /AND IS 2 PAGES LONG.
        6600          OUDEVH= 6600    /OUTPUT HANDLER GETS LOADED AT 6600.
                                      /WE ALLOW TWO PAGE HANDLERS.
        5400          INBUF=  5400    /INPUT BUFFER STARTS AT 05400
        0200          INCTL=  0200    /ALSO TWO PAGES LONG.
        0001          INRECS= 1       /2 PAGES = 1 RECORD
        7000          INDEVH= 7000    /ALLOW 2 PAGE INPUT HANDLER AT 7000.
        0001          IORFLD= 1       /FIELD OF THE SUBROUTINES.
        6600          ORIGIN= 6600    /THE SUBROUTINES RESIDE AT 16600.



        0001          FIELD    IORFLD
        6600          *ORIGIN

        0000          INFLD=  INCTL&70        /INPUT BUFFER FIELD
        0000          OUFLD=  OUCTL&70        /OUTPUT BUFFER FIELD
        7760          DCB=    7760            /DEVICE CONTROL TABLE
































				      F-7

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 3


016600  0000  ICHAR,  0                       /INPUT A CHARACTER
016601  7600  IN7600, 7600
016602  6214          RDF                     /SAVE CALLING FIELD FOR RETURN
016603  1232          TAD     INCDIF
016604  3316          DCA     INRTRN
016605  6201  INCHAR, CDF     INFLD           /DATA FIELD TO FIELD OF BUFFER
016606  2265          ISZ     INJMP           /3 - WAY UNPACKING SWITCH
016607  2325          ISZ     INCHCT          /INPUT BUFFER EXHAUSTED?
016610  5265  INJMPP, JMP     INJMP           /NO..UNPACK THE NEXT CHAR.
016611  1321          TAD     INEOF           /DID LAST READ GIVE EOF ON
016612  7650          SNA CLA                 / THIS DEVICE?
016613  5216          JMP     INGBUF          /NO. CONTINUE READING.
016614  4325  GETNEW, JMS     INNEWF          /YES..GET NEXT INPUT IF IT 
                                              / EXISTS.
016615  5264          JMP     EOFERR          /TAKE EOF EXIT FROM ICHAR.
016616  1324  INGBUF, TAD     INCTR           /INCTR HOLDS THE CURRENT LENGTH
                                              / OF THE INPUT FILE.  WHEN THE 
                                              / AMOUNT REMAINING TO READ IS 
                                              / LESS THAN THE SIZE OF THE
                                              / INPUT BUFFER, AN EOF IS 
                                              / SIGNALED.
016617  7100          CLL
016620  1377          TAD     (INRECS
016621  7420          SNL
016622  3324          DCA     INCTR           /UPDATE REMAINING LENGTH
016623  7430          SZL
016624  2321          ISZ     INEOF           /AND SIGNAL EOF FOR NEXT READ.
016625  7172          CLL CML CMA RTR         /CONSTRUCT A CONTROL WORD FOR 
016626  7012          RTR                     / THIS READ FROM THE OVERFLOW, 
016627  7012          RTR                     / IF ANY, AND THE STANDARD 
016630  1376          TAD     (INCTL+1        / CONTROL WORD.
016631  3235          DCA     INCTLW
016632  6203  INCDIF, CIF CDF 0               /NOW CALL THE INPUT HANDLER
016633  6211          CDF     10              /HANDLER IS IN FIELD 0
016634  4736          JMS I   INHNDL
016635  0000  INCTLW, 0                       /INPUT CONTROL WORLD
016636  5400  INBUFP, INBUF                   /INPUT BUFFER ADDRESS
016637  0000  INREC,  0                       /POINTER TO INPUT RECORD
016640  5260          JMP     INERRX
016641  1237  INBREC, TAD     INREC
016642  1377          TAD     (INRECS         /UPDATE POINTER INTO FILE
016643  3237          DCA     INREC
016644  1235          TAD     INCTLW          /NOW COMPUTE THE NUMBER OF 
016645  0201          AND     IN7600          / CHARACTERS IN THIS INPUT 
016646  7104          CLL RAL                 / BUFFER
016647  1235          TAD     INCTLW
016650  0201          AND     IN7600
016651  7040          CMA
016652  3325          DCA     INCHCT          /NEW NUMBER OF CHARACTERS
016653  1210          TAD     INJMPP          /RESET 3 WAY SWITCH
016654  3265          DCA     INJMP


				      F-8

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 3-1


016655  1236          TAD     INBUFP
016656  3323          DCA     INPTR           /AND BUFFER POINTER
016657  5205          JMP     INCHAR          /NOW READ THE BUFFER
016660  2321  INERRX, ISZ     INEOF           /SET EOF JUST IN CASE
016661  7700          SMA CLA                 /IF <0, A PHYSICAL ERROR
016662  5241          JMP     INBREC          /EOF ON INPUT
016663  7330  INERR,  CLA CLL CML RAR         /FATAL
016664  5316  EOFERR, JMP     INRTRN          /GET OUT
016665  7402  INJMP,  HLT                     /3 WAY UNPACK SWITCH
016666  5307          JMP     ICHAR1          /GET 1ST OF 3
016667  5303          JMP     ICHAR2          /SECOND
016670  1210  ICHAR3, TAD     INJMPP
016671  3265          DCA     INJMP           /SET FOR FIRST CHAR. NEXT
016672  1723          TAD I   INPTR           /THE THIRD WORD IS MADE OF THE
016673  0320  IN200,  AND     IN7400          / HIGH ORDER FOUR BITS OF THE 
016674  7112          CLL RTR                 / FIRST TWO.
016675  7012          RTR
016676  1235          TAD     INCTLW
016677  7012          RTR
016700  7012          RTR
016701  2323          ISZ     INPTR           /POINT TO NEXT WORD
016702  5310          JMP     INCOMN          /GET OUT WITH CHAR IN AC
016703  1723  ICHAR2, TAD I   INPTR
016704  0320          AND     IN7400          /SAVE HIGH ORDER FOR THIRD 
016705  3235          DCA     INCTLW          / WORD
016706  2323          ISZ     INPTR
016707  1723  ICHAR1, TAD I   INPTR
016710  0375  INCOMN, AND     (377
016711  1374          TAD     (-232           /IS IT A ^Z (EOF)?
016712  7450          SNA
016713  5214          JMP     GETNEW          /YES..LOOK AT NEXT INPUT
016714  1373          TAD     (232
016715  2200          ISZ     ICHAR           /TAKE NORMAL RETURN
016716  0000  INRTRN, 0                       /CIF CDF N.
016717  5600          JMP I   ICHAR

016720  7400  IN7400, 7400
016721  0000  INEOF,  0                       /END OF FILE FLAG
016722  0000  INFPTR, 0                       /POINTER TO INPUT FILE NAMES
016723  0000  INPTR,  0                       /INPUT BUFFER POINTER
016724  0000  INCTR,  0                       /LENGTH OF CURRENT INPUT FILE












				      F-9

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 4


016725  7777  INNEWF, -1                      /OPEN A NEW INPUT FILE
        6725  INCHCT= INNEWF
016726  6211          CDF     10
016727  1372          TAD     (INDEVH+1       /INITIALIZE JUST IN CASE 
016730  3336          DCA     INHNDL
016731  1722          TAD I   INFPTR          /MORE INPUT?
016732  7450          SNA
016733  5725          JMP I   INNEWF          /NOPE
016734  4673          JMS I   IN200           /CALL MONITOR TO GET HANDLER
016735  0001          1
016736  0000  INHNDL, 0
016737  7402          HLT                     /VERY BAD!
016740  1722          TAD I   INFPTR
016741  0371          AND     (7760           /GET INPUT FILE LENGTH
016742  7440          SZA
016743  1370          TAD     (17
016744  7132          CLL CML RTR
016745  7012          RTR                     /NEGATIVE OF FILE LENGTH
016746  3324          DCA     INCTR
016747  2322          ISZ     INFPTR          /POINT TO STARTING BLOCK
016750  1722          TAD I   INFPTR
016751  3237          DCA     INREC           /STORE IN HANDLER CALL
016752  2322          ISZ     INFPTR          /NEXT INPUT.
016753  3321          DCA     INEOF           /CLEAR EOF FLAG.
016754  2325          ISZ     INNEWF
016755  5725          JMP I   INNEWF

016770  0017
016771  7760
016772  7001
016773  0232
016774  7546
016775  0377
016776  0201
016777  0001
        7000          PAGE

















				     F-10

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 5


017000  0000  OOPEN,  0                       /OPEN OUTPUT FILE
017001  7600  OU7600, 7600
017002  1347          TAD     OU7601          /POINT TO OUTPUT FILE NAME IN
017003  3221          DCA     OUBLK           / CD AREA
017004  1377          TAD     (OUDEVH+1
017005  3214          DCA     OUHNDL          /INITIALIZE OUTPUT HANDLER
017006  1601          TAD I   OU7600          /PICK UP OUTPUT DEVICE NUMBER
017007  0376          AND     (17
017010  7450          SNA                     /IS THERE ONE?
017011  5244          JMP     ONOFIL          /NO..INHIBIT OUTPUT
017012  4775          JMS I   (200            /FETCH OUTPUT HANDLER
017013  0001          1
017014  0000  OUHNDL, 0
017015  7402          HLT                     /BAD THING
017016  1601  OUENTR, TAD I   OU7600
017017  4775          JMS I   (200            /ENTER THE OUTPUT FILE
017020  0003          3
017021  7601  OUBLK,  7601                    /GETS STARTING BLOCK OF HOLE
017022  0000  OUELEN, 0                       /GETS SIZE OF HOLE AVAILABLE
017023  5232          JMP     OEFAIL          /FAILURE. SEE WHAT WE DID.
017024  3350          DCA     OUCCNT          /CLEAR CLOSING LENGTH
017025  3774          DCA I   (OUTINH         /CLEAR OUTPUT INHIBIT
017026  4773          JMS I   (OUSETP         /SET UP POINTERS
017027  2200          ISZ     OOPEN
017030  6213  OORETN, CDF CIF 10
017031  5600          JMP I   OOPEN           /RETURN O.K.
017032  1601  OEFAIL, TAD I   OU7600          /IF LENGTH=0, GIVE OPEN ERROR
017033  0372          AND     (7760           /IF NOT, MAKE IT 0 AND TRY 
017034  7650          SNA CLA                 / AGAIN
017035  5242          JMP     ONTERR          /WAS 0. FAILED
017036  1601          TAD I   OU7600
017037  0376          AND     (17             /MAKE IT 0
017040  3601          DCA I   OU7600
017041  5216          JMP     OUENTR          /AND TRY AGAIN
017042  7330  ONTERR, CLA CLL CML RAR
017043  5230          JMP     OORETN
017044  2774  ONOFIL, ISZ I   (OUTINH         /INHIBIT OUTPUT
017045  5230          JMP     OORETN















				     F-11

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 6


017046  0000  OUTDMP, 0                       /DUMP OUTPUT BUFFER
017047  3300          DCA     OUCTLW          /STORE CONTROL WORD
017050  6211          CDF     10
017051  1774          TAD I   (OUTINH         /IS OUTPUT INHIBITED?
017052  7640          SZA CLA
017053  5304          JMP     OUNOWR          /YEP.
017054  1350          TAD     OUCCNT          /IF THIS IS FIRST WRITE, START
017055  7450          SNA                     / SEARCH FORWARD ON DECTAPE
017056  2300          ISZ     OUCTLW
017057  1221          TAD     OUBLK           /GET STARTING BLOCK OF THIS
017060  3302          DCA     OUREC           / TRANSFER
017061  1300          TAD     OUCTLW
017062  7106          CLL RTL
017063  7006          RTL
017064  7006          RTL                     /COMPUTE # OF RECORDS TO 
017065  0376          AND     (17             / OUTPUT
017066  1350          TAD     OUCCNT          /UPDATE CLOSING LENGTH
017067  3350          DCA     OUCCNT
017070  1350          TAD     OUCCNT          /SEE IF CLOSING LENGTH WILL 
017071  7120          CLL CML                 / BE BIGGER THAN OUTPUT HOLE
017072  1222          TAD     OUELEN
017073  7660          SNL SZA CLA
017074  5646          JMP I   OUTDMP          /WILL BE TOO BIG
017075  6203  OUCDIV, CIF CDF 0
017076  6211          CDF     10
017077  4614          JMS I   OUHNDL          /DO THE WRITE
017100  0000  OUCTLW, 0
017101  5000          OUBUF
017102  0000  OUREC,  0
017103  7410          SKP                     /ERROR
017104  2246  OUNOWR, ISZ     OUTDMP          /TAKE NORMAL RETURN
017105  5646          JMP I   OUTDMP
        0020  PTP=    0020




















				     F-12

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 7


017106  0000  OCLOSE, 0                       /CLOSE OUTPUT FILE
017107  6211          CDF     10
017110  1774          TAD I   (OUTINH         /IF OUTPUT INHIBITED, CLOSE 
                                              / IS A NOP.
017111  7640          SZA CLA
017112  5352          JMP     OCISZ           /A NOP
017113  4771          JMS I   (OTYPE          /DETERMINE IF OUTPUT IS TO PTP
017114  0370          AND     (770            /IF IT IS, DON'T OUTPUT A ^Z.
017115  1372          TAD     (-PTP
017116  7640          SZA CLA
017117  1367          TAD     (232            /NOT PTP. OUTPUT ^Z AS EOF
017120  4766          JMS I   (OCHAR
017121  5353          JMP     OCRET           /ERROR RETURN
017122  4766          JMS I   (OCHAR          /FILL WITH 0 CHARACTERS
017123  5353          JMP     OCRET
017124  4766  FILLIP, JMS I   (OCHAR          /FILL TO BOUNDARY WITH 0
017125  5353          JMP     OCRET
017126  4771          JMS I   (OTYPE          /IF OUTPUT IS DIRECTORY DEVICE,
017127  7710          SPA CLA                 / FILL WHOLE RECORD, ELSE HALF 
017130  1365          TAD     (100            / RECORD
017131  1364          TAD     (77)
017132  0763          AND I   (OUDWCT         /ARE WE UP TO BOUNDARY YET?
017133  7640          SZA CLA
017134  5324          JMP     FILLIP          /NO
017135  1763          TAD I   (OUDWCT
017136  1375          TAD     (OUCTL&3700     /IS THERE A FULL WRITE LEFT?
017137  7450          SNA
017140  5344          JMP     NODUMP          /YES. BUT DON'T DO IT, AS ^Z 
                                              / IS OUT.
017141  1362          TAD     (4000+OUFLD
017142  4246          JMS     OUTDMP          /DUMP LAST BUFFER
017143  5353          JMP     OCRET
017144  1601  NODUMP, TAD I   OU7600          /GET DEVICE NUMBER
017145  4775          JMS I   (200            /CLOSE THE OUTPUT FILE
017146  0004          4
017147  7601  OU7601, 7601                    /POINTER TO FILE NAME
017150  0000  OUCCNT, 0                       /CLOSING FILE LENGTH HERE
017151  7410          SKP                     /ERROR
017152  2306  OCISZ,  ISZ     OCLOSE          /NORMAL RETURN
017153  6213  OCRET,  CDF CIF 10              /RESTORE CALLING FIELDS
017154  5706          JMP I   OCLOSE

017162  4000
017163  7272
017164  0077
017165  0100
017166  7211
017167  0232
017170  0770
017171  7274
017172  7760


				     F-13

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 7-1


017173  7200
017174  7273
017175  0200
017176  0017
017177  6601
        7200          PAGE















































				     F-14

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 8


017200  0000  OUSETP, 0                       /INITIALIZE OUTPUT POINTERS
017201  1377          TAD     (OUCTL&3700
017202  7041          CIA
017203  3272          DCA     OUDWCT          /DOUBLE WORD OUTPUT COUNT
017204  1376          TAD     (OUBUF          /INITIALIZE WORD POINTER
017205  3270          DCA     OUPTR
017206  1271          TAD     OUJMPE
017207  3224          DCA     OUJMP           /3 WAY UNPACK SWITCH
017210  5600          JMP I   OUSETP












































				     F-15

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 9


017211  0000  OCHAR,  0                       /OUTPUT CHARACTER ROUTINE
017212  0375          AND     (377            /ISOLATE EIGHT BITS
017213  3266          DCA     OUTEMP
017214  6214          RDF                     /GET FIELD WE WERE CALLED
017215  1374          TAD     (CIF CDF 0      / FROM
017216  3264          DCA     OUCRET
017217  1273          TAD     OUTINH          /OUTPUT INHIBITED
017220  7640          SZA CLA
017221  5263          JMP     OUCOMN          /YES. NOP.
017222  6201  OUCHAR, CDF     OUFLD           /GO TO DATA FIELD OF BUFFER
017223  2224          ISZ     OUJMP           /BUMP CHARACTER SWITCH
017224  7402  OUJMP,  HLT                     /GETS JMP.,JMP.+1,ETC.
017225  5261          JMP     OCHAR1
017226  5256          JMP     OCHAR2
017227  1266  OCHAR3, TAD     OUTEMP          /THIRD CHAR
017230  7106          CLL RTL                 /HIGH ORDER BITS GO INTO THE
017231  7006          RTL                     /HIGH ORDER 4 BITS OF THE
017232  0373          AND     (7400           /FIRST OF TWO WORDS
017233  1667          TAD I   OUPOLD
017234  3667          DCA I   OUPOLD
017235  1266          TAD     OUTEMP          /THE SECOND DOUBLE WORD GETS
017236  7112          CLL RTR                 /THE LOW ORDER BITS OF
017237  7012          RTR                     /THE THIRD CHAR
017240  7010          RAR
017241  0373          AND     (7400
017242  1670          TAD I   OUPTR
017243  3670          DCA I   OUPTR
017244  1271          TAD     OUJMPE          /RESET CHARACTER SWITCH
017245  3224          DCA     OUJMP
017246  2270          ISZ     OUPTR           /POINT TO NEXT BUFFER WORD
017247  2272          ISZ     OUDWCT          /BUMP DOUBLE COUNT AFTER
                                              /3 CHARS.
017250  5263          JMP     OUCOMN          /GET OUT
017251  1372          TAD     (OUCTL          /READY TO OUTPUT A BUFFER
017252  4771          JMS I   (OUTDMP         /OUTPUT IT
017253  5264          JMP     OUCRET          /AN ERROR
017254  4200          JMS     OUSETP          /RESET OUTPUT POINTERS
017255  5263          JMP     OUCOMN
017256  1270  OCHAR2, TAD     OUPTR           /POINT TO FIRST DOUBLE WORD
017257  3267          DCA     OUPOLD
017260  2270          ISZ     OUPTR           /POINT OUPTR TO SECOND
017261  1266  OCHAR1, TAD     OUTEMP
017262  3670          DCA I   OUPTR
017263  2211  OUCOMN, ISZ     OCHAR           /NORMAL EXIT
017264  7402  OUCRET, HLT
017265  5611          JMP I   OCHAR
017266  0000  OUTEMP, 0
017267  0000  OUPOLD, 0
017270  0000  OUPTR,  0
017271  5224  OUJMPE, JMP     OUJMP
017272  0000  OUDWCT, 0


				     F-16

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 9-1


017273  0000  OUTINH, 0
017274  0000  OTYPE,  0                       /OTYPE LOOKS AT THE OUTPUT 
017275  6214          RDF                     / DEVICE #.
017276  1374          TAD     (CIF CDF 0
017277  3306          DCA     OTRTN
017300  6211          CDF     10
017301  1770          TAD I   (7600           /AND LOOKS UP THE DCB WORD 
017302  0367          AND     (17             / FOR THAT DEVICE.
017303  1366          TAD     (DCB-1
017304  3266          DCA     OUTEMP
017305  1666          TAD I   OUTEMP          /GET DCB ENTRY
017306  7402  OTRTN,  HLT
017307  5674          JMP I   OTYPE








































				     F-17

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 10


017310  0000  IOPEN,  0                       /INITIALIZE THE INPUT ROUTINE
017311  7240          CLA CMA                 /SET TO FORCE READ FROM NEW 
017312  3765          DCA I   (INCHCT         / DEVICE
017313  2764          ISZ I   (INEOF          /FORCE A NEW INPUT FILE.
017314  1363          TAD     (7617           /POINT TO CD INPUT LIST.
017315  3762          DCA I   (INFPTR
017316  6214          RDF
017317  1761          TAD I   (INCDIF
017320  3321          DCA .+1
017321  7402          HLT
017322  5710          JMP I   IOPEN

017361  6632
017362  6722
017363  7617
017364  6721
017365  6725
017366  7757
017367  0017
017370  7600
017371  7046
017372  4200
017373  7400
017374  6203
017375  0377
017376  5000
017377  0200
        7400          PAGE

























				     F-18

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 11


              /
              /       EXAMPLE PROGRAM TO COPY A ASCII FILE
              /

        0001          FIELD 1
        2000          *2000

012000  4777          JMS I   (7700           /LOCK MONITOR INTO CORE
012001  0010          10
012002  4776  CALLCD, JMS I   (200            /CALL THE COMMAND DECODER
012003  0005          5
012004  0000          0
012005  4775          JMS I   (IOPEN          /SETUP INPUT POINTERS
012006  4774          JMS I   (OOPEN          /OPEN OUTPUT FILE
012007  7700          SMA CLA                 /ERROR. IF AC<0, IT WAS FATAL
012010  5220          JMP OK                  /NON FILE STRUCTURED OUTPUT
012011  4263          JMS TERR
012012  1720          TEXT /OPEN FAILED/
012013  0516
012014  4006
012015  0111
012016  1405
012017  0400
012020  4773  OK,     JMS I   (ICHAR          /READ A CHARACTER
012021  5227          JMP     TSTEOF          /ERROR. SEE IF EOF.
012022  7450          SNA                     /IGNORE BLANKS
012023  5220          JMP     OK
012024  4772          JMS I   (OCHAR          /AND OUTPUT THE CHARACTER
012025  5243          JMP     OUTERR
012026  5220          JMP     OK              /CONTINUE UNTIL EOF.
012027  7700  TSTEOF, SMA CLA                 /WAS IT FATAL?
012030  5240          JMP     CLOSE           /NO..EOF. CLOSE OUTPUT
012031  4263          JMS TERR
012032  2205          TEXT /READ ERROR/
012033  0104
012034  4005
012035  2222
012036  1722
012037  0000

012040  4771  CLOSE,  JMS I   (OCLOSE
012041  5253          JMP     CLERR           /FILE CLOSE FAILED
012042  5202          JMP     CALLCD          /NEW INPUT.

012043  4263  OUTERR, JMS     TERR
012044  1725          TEXT /OUTPUT ERROR/
012045  2420
012046  2524
012047  4005
012050  2222
012051  1722
012052  0000

				     F-19

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 11-1


012053  4263  CLERR,  JMS     TERR            /CLOSE FAILURE
012054  0314          TEXT /CLOSE FAILED/
012055  1723
012056  0540
012057  0601
012060  1114
012061  0504
012062  0000

012063  0000  TERR,     0                     /ROUTINE TO PRINT ERROR 
012064  1663          TAD I   TERR            / MESSAGES
012065  7012          RTR;RTR;RTR
012066  7012
012067  7012
012070  4275          JMS     TYPIT           /TYPE THE CHARACTER
012071  1663          TAD I   TERR
012072  4275          JMS     TYPIT
012073  2263          ISZ     TERR
012074  5264          JMP     TERR+1

012075  0000  TYPIT,  0
012076  0370          AND     (77             /ISOLATE THE CHARACTER
012077  7450          SNA
012100  5304          JMP     CRLF            /0 TERMINATES IT
012101  1367          TAD     (300
012102  4311          JMS     TTYOUT
012103  5675          JMP I   TYPIT
012104  1366  CRLF,   TAD     (215
012105  4311          JMS     TTYOUT
012106  1365          TAD     (212
012107  4311          JMS     TTYOUT
012110  5202          JMP     CALLCD

012111  0000  TTYOUT, 0
012112  6046          TLS
012113  6041          TSF
012114  5313          JMP       .-1
012115  7200          CLA
012116  5711          JMP I     TTYOUT

012165  0212
012166  0215
012167  0300
012170  0077
012171  7106
012172  7211
012173  6600
012174  7000
012175  7310
012176  0200
012177  7700
                      $$$$$$$$$$

				     F-20

			  OS/8 INPUT/OUTPUT ROUTINES


/OS/8 GENERAL CHARACTER I/O ROUTINES FO   PAL8-VC0  05-OCT-96 PAGE 12

CALLCD 2002      OORETN 7030      
CLERR  2053      ORIGIN 6600      
CLOSE  2040      OTRTN  7306      
CRLF   2104      OTYPE  7274      
DCB    7760      OUBLK  7021      
EOFERR 6664      OUBUF  5000      
FILLIP 7124      OUCCNT 7150      
GETNEW 6614      OUCDIV 7075      
ICHAR  6600      OUCHAR 7222      
ICHAR1 6707      OUCOMN 7263      
ICHAR2 6703      OUCRET 7264      
ICHAR3 6670      OUCTL  4200      
INBREC 6641      OUCTLW 7100      
INBUF  5400      OUDEVH 6600      
INBUFP 6636      OUDWCT 7272      
INCDIF 6632      OUELEN 7022      
INCHAR 6605      OUENTR 7016      
INCHCT 6725      OUFLD  0000      
INCOMN 6710      OUHNDL 7014      
INCTL  0200      OUJMP  7224      
INCTLW 6635      OUJMPE 7271      
INCTR  6724      OUNOWR 7104      
INDEVH 7000      OUPOLD 7267      
INEOF  6721      OUPTR  7270      
INERR  6663      OUREC  7102      
INERRX 6660      OUSETP 7200      
INFLD  0000      OUTDMP 7046      
INFPTR 6722      OUTEMP 7266      
INGBUF 6616      OUTERR 2043      
INHNDL 6736      OUTINH 7273      
INJMP  6665      OU7600 7001      
INJMPP 6610      OU7601 7147      
INNEWF 6725      PTP    0020      
INPTR  6723      TERR   2063      
INREC  6637      TSTEOF 2027      
INRECS 0001      TTYOUT 2111      
INRTRN 6716      TYPIT  2075      
IN200  6673      
IN7400 6720      
IN7600 6601      
IOPEN  7310      
IORFLD 0001      
NODUMP 7144      
OCHAR  7211      
OCHAR1 7261      
OCHAR2 7256      
OCHAR3 7227      
OCISZ  7152      
OCLOSE 7106      
OCRET  7153      
OEFAIL 7032      
OK     2020      


				     F-21

			  OS/8 INPUT/OUTPUT ROUTINES


ONOFIL 7044      
ONTERR 7042      
OOPEN  7000      


ERRORS DETECTED: 0
LINKS GENERATED: 0

















































				     F-22







				     INDEX



     Additional information words,	  CLOSE function, 2-8, D-10
	 1-3, 2-7, D-10		 	  Code, non-paged, D-11
     Alphanumeric option, Command	  Command Decoder
	 Decoder, 3-3			  calling, 3-3
       switches, 3-6			    conventions, 3-1
     ALTMODE key, 3-3			    error messages, 3-3
     Ascertain device information	    errors summary, C-7
	 (INQUIRE function), 2-14	    example, 3-7
     ASCII character codes, E-3, E-4	    options, 3-3
     ASCII files format, A-4		    output files, 3-5
     ASSIGN command, 1-6		    special mode, 3-10
     Asterisk, caution in using, 3-9	    tables, 3-4
					  COMMON area, 2-12
					  Control characters, OS/8, E-1
     Batch mode, 3-11			  Conventions
     Batch operating system, 1-6	    Command Decoder, 3-1
     Binary file format, A-4		    OS/8, E-1
     Block, core control, 1-4		  Core control block, 1-4, 2-11, A-5
     Blocks				  Core image files (.SV format), A-5
       directory, A-1			  Core origin, A-7
       system scratch, B-1		  Core segment doublewords, A-7
     Blocks of words, 1-2, 1-3		  Core size, PDP-8 computers, D-5
     BUILD program, 5-1			    software, 1-6
					  Co-resident device handlers, 2-6
					  Creating files, 1-3
     Call Command Decoder (DECODE
	 function), 2-10, 3-3
       in Special Mode, 3-9		  Data exchange in core, 2-12
     Calling device handlers, 4-1	  Data field value, 2-2
     Calling USR and device handlers	  Data transfer, 4-1, 4-2
	 from SABR code, D-13		  DATE command, 1-4, 2-7
     Card codes, DEC029, 4-8		  DECODE function, 2-10
     Card Reader (CDR) operation, 4-8	  DECtape operation, 4-1
     Card Reader handler modification,	  Default file storage device, DSK,
	 D-2				      D-1
     Carriage return/line feed sup-	  Deleting tentative files, 2-16
	 pression in FORTRAN, D-4	  Device control word table, B-7
     Cassettes operation, 4-7		  Device dependent operations, 4-4
     CCL, 3-10				  Device handler
     CCL error messages, C-4		    entry point, 2-15, 5-8
     CHAIN function, 2-11		    information table, B-6
     Character codes			    residency table, 2-15, B-6
       ASCII, E-3, E-4			  Device handlers
       OS/8, E-1			    device dependent operations, 4-4
     Character mode, expanded, 4-6	      Card Reader (CDR), 4-8
     Character packing format, 5-8	      Cassettes operation, 4-7
     Characters, lower case, E-1	      High-Speed Paper Tape Punch
     Circumflex (^) character, 4-5		(PTP), 4-5


				    INDEX 1

				     INDEX


     Device handlers (Cont.)		  FETCH device handler function,
	 High-Speed Paper Tape Reader	      2-4, 4-1
	   (PTR), 4-4			  File creation, 1-3
       file structured devices oper-	  File directories, A-1
	   ation, 4-12			  block format, A-1
	 TD8E DECtape, 4-12		    entries, A-2
	 TM8E Magtape, 4-8		    example, A-4
     Device handlers, 1-1		    formats, A-4
       calling, 4-1			    number, A-3
       co-resident, 2-6			    size, A-3
       inserting into OS/8, 5-5		  File extension, omission of, 3-2
       loading dynamically, D-8		  File length restriction, Command
       notes on loading, D-7		      Decoder, 3-6
       writing, 5-1			  FILENAME pseudo-op, 1-7
     Device length table, B-8		  Files, 1-2
     Device names and numbers, 1-6	    additional information words, 1-3
     DEVICE pseudo-op, 1-7		    devices, 1-2
     Devices, file structured, 1-2	    directories, 1-3
     DF32 disk operation, 4-12		    names, 1-2
     Direct calling sequence, USR, 2-2	  types, 1-3
     Directories, file, 1-3		  File structured devices operation,
     Directory block structure format,	      4-12
	 A-1				  Formats for
     Directory entries, A-2		    character packing, 5-3
     Directory example, A-4		    command line, 3-1
     Directory segment, rewriting,	    directory block structure, A-1
	 D-10				    files, A-4
     Directory, system, 5-2		    FORTRAN Library File, A-8
     Dismiss USR from core, 2-13	    input file, 3-2
     Dot (.) used as system response,	    Job Status Word, A-6
	 1-6				  Form feed, 4-6
     Doublewords, core segment, A-7       FORTRAN Library File Format, A-8
					  Functions, USR see USR functions

     Empty file entry, A-2
     Empty files, 1-3			  High-Speed Paper Tape Punch (PTP)
     End-of-file card, 4-8		      operation, 4-5
     End-of-file Condition, 4-2, 4-4	  High-Speed Paper Tape Reader (PTR)
     ENTER output (tentative) file	      operation, 4-4
	 function, 2-7, D-9		  Horizontal tab, 4-6
     Entry points for device handlers,
	 5-2
     ERROR function, 2-12		  Indirect calling sequence, USR,
     Error messages, Command Decoder,	      2-2
	 3-3				  Information words, additional, 1-3,
     Error messages summary, C-1	      2-7
     Error returns, device handler,	    accessing, D-10
	 4-2				  Input file format, 3-2
     Exit to Keyboard Monitor, 1-1	  Input files, Command Decoder, 3-5
     Expanded character mode, 4-6	  Input/output routines, F-1
     Extensions of file names, 1-2	  Input table, Command Decoder, 3-9
					  INQUIRE function, 2-14
					  Inserting device handlers into
					      OS/8, 5-5


				    INDEX-2

				     INDEX


     Job Status Word, 1-5, A-6		  Records (definition), 4-1
					    outputting odd number of, 4-3
					  RESET system table, 2-15
     Keyboard Monitor, 1-1		  Resident program layout, B-3
       error summary, C-3		  RESORC, B-9
     KL8E terminal handler, 4-13	  Restrictions to USR calls, 2-2
					  RETURN key, 3-3
					  RF08 disk
     LAP pseudo-op, D-11		    operation, 4-12
     Layouts for OS/8 system, B-1	  RK8E handlers, 4-12
     LINCtape operation, 4-12		  ROM (Read-Only-Memory), B-4
     Line Printer (LPT) operation,
	 4-5, 4-6
     Load and start subprogram, 2-11	  SABR programming notes, D-11
     Loading device handlers dynam-	  SAVE command, 1-4, 2-12
	 ically, D-8			  Scratch blocks, B-1, B-2
     Lock USR in core (USRIN), 2-13	  Signal user ERROR function, 2-12
     Logical blocks, 1-2		  Size of OS files, A-3
     LOOKUP permanent file function,	  Software components, 1-1
	 2-6, D-9			  Software core size, 1-6
     Lower case characters, E-1		  Special mode of Command Decoder,
					      3-10
					    calling, 3-9
     Names of devices, 1-6		    operation, 3-9
     Names of files, 1-2		  Standard USR call, 2-1
     Number and size of OS files, A-3	    restrictions, 2-2
     Numbers of devices, 1-6		  START command, 1-5
     Numeric option, Command Decoder,	  Starting address of program, 1-5
	 3-3				  Storage space, additional, D-9
					  Storage words, 1-3
					  Subroutine
     ODT breakpoint, 2-12		    examples, F-4
     Operations, device dependent, 4-4	    functions, F-1, F-2
     Options				    listing, F-5
       Command decoder, 3-3, 3-6	    parameters, F-3
     Origin of core, A-7		  Summary of USR functions, see USR
     Output files, Command Decoder,	      functions
	 3-5				  .SV file, 1-4
					  System DATE, 2-7
					  System device layout, B-1
     PAGE pseudo-op, D-11		  System devices, 1-6
     Permanent device name table, B-5     System device table, B-5
     Permanent file, 1-3		  System halts error messages
       deletion, 2-8, 2-9		      summary, C-1
       entry, A-2			  System table values, Command
     Physical blocks, 1-2		      Decoder, 3-7
     PIP, 3-6
     Program, see specific subject	
     Programming notes, D-1		  Tables
     PRTC12-F used to convert DECtapes	    Command Decoder, 3-4
	 to LINCtapes, D-6		    device control word, B-7
     Pseudo-ops				    device handler information, B-6
       DEVICE, 1-7			    device handler residency, B-6
       FILENAME, 1-7			    device length, B-8
     Punch card codes, DEC026, D-3	
				
				    INDEX-3

				     INDEX


     Tables (Cont.)
       permanent device name, B-5
       system device, B-5
       user device name, B-6
     TD8E DECtape
       operation, 4-12
     Teletype operation, 4-4
     Tentative files, 1-3
       closing, 2-8
       deletion, 2-8
       entry, A-3
     Terminal handlers
       1-page, 4-4
       2-page, 4-13


     up arrow (^) character, 4-5
     User device name table, B-6
     User Service Routine (USR), 1-1,
	 2-1
       available location in area,
	   D-9
       calling, 1-6, 2-1
       calling sequences, 2-2
       errors summary, C-2
       restrictions on standard call,
	 2-2
     USR functions
       CHAIN, 2-11
       CLOSE, 2-8
       DECODE, 2-10
       ENTER, 2-7
       ERROR, 2-12
       FETCH, 2-4
       INQUIRE, 2-14
       LOOKUP, 2-6
       RESET, 2-15
       summary, 2-3
       USRIN, 2-13
       USROUT, 2-13


     Vertical tab, 4-6


     Wrap around memory, 4-3
     Writing device handlers, 5-1
     Word blocks, 1-2








				    INDEX 4




		      HOW TO OBTAIN SOFTWARE INFORMATION


    SOFTWARE NEWSLETTERS, MAILING LIST    __________________________________

    The Software Communications Group, located at corporate headquarters in
    Maynard, publishes newsletters and Software Performance Summaries (SPS)
    for the various Digital products.  Newsletters are published monthly,				       ___________
    and contain announcements of new and revised software, programming
    notes, software problems and solutions, and documentation corrections.
    Software Performance Summaries are a collection of existing problems    ______________________________
    and solutions for a given software system, and are published periodi-
    cally.  For information on the distribution of these documents and how
    to get on the software newsletter mailing list, write to:

			    Software Communications
			    P. O. Box F
			    Maynard, Massachusetts  01754


    SOFTWARE PROBLEMS    _________________

    Questions or problems relating to Digital's software should be reported
    to a Software Support Specialist.  A specialist is located in each
    Digital Sales Office in the United States.  In Europe, software problem
    reporting centers are in the following cities.

		   Reading, England	   Milan, Italy
		   Paris, France	   Solna, Sweden
		   The Hague, Holland      Geneva, Switzerland
		   Tel Aviv, Israel	   Munich, West Germany

    Software Problem Report (SPR) forms are available from the specialists
    or from the Software Distribution Centers cited below.


    PROGRAMS AND MANUALS    ____________________

    Software and manuals should be ordered by title and order number.  In
    the United States, send orders to the nearest distribution center.

	 Digital Equipment Corporation     Digital Equipment Corporation
	 Software Distribution Center      Software Distribution Center
	 146 Main Street		   1400 Terra Bella
	 Maynard, Massachusetts  01754     Mountain View, California  94043

    Outside of the United States, orders should be directed to the nearest
    Digital Field Sales Office or representative.





    USERS SOCIETY    _____________

    DECUS, Digital Equipment Computer Users Society, maintains a user ex-
    change center for user-written programs and technical application in-
    formation.  A catalog of existing programs is available.  The society
    publishes a periodical, DECUSCOPE, and holds technical seminars in the
    United States, Canada, Europet and Australia.  For information on the
    society and membership application forms, write to:

	 DECUS				   DECUS
	 Digital Equipment Corporation     Digital Equipment, S.A.
	 146 Main Street		   81 Route de l'Aire
	 Maynard, Massachusetts 01754      1211 Geneva 26
					   Switzerland


					       OS/8 Software Support Manual
					       DEC-S8-OSSMB-A-D

			       READER'S COMMENTS

	  NOTE:  This form is for document comments only.  Problems
		 with software should be reported on a Software
		 Problem Report (SPR) form (see the E10A' TO OBTAIN
		 SOFTWARE INFORMATION page).

     Did you find errors in this manual?  If so, specify by page.
     ______________________________________________________________________
     ______________________________________________________________________
     ______________________________________________________________________
     ______________________________________________________________________
     ______________________________________________________________________

    Did you find this manual understandable, usable, and well-organized?
    Please make suggestions for improvement.
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________

    Is there sufficient documentation on associated system programs
    required for use of the software described in this manual?  If not,
    what material is missing and where should it be placed?
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________
    ______________________________________________________________________

    Please indicate the type of user/reader that you most nearly represent.

	 []  Assembly language programmer

	 []  Higher-level language programmer

	 []  Occasional programmer (experienced)

	 []  User with little programming experience

	 []  Student programmer

	 []  Non-programmer interested in computer concepts and capabilities

     Name______________________________________Date________________________

     Organization__________________________________________________________

     Street________________________________________________________________

     City__________________________State_____________Zip Code______________
							or
						     Country

     If you do not require a written reply, please check here.  []





















     -------------------------------Fold Here------------------------------

















     -----------------Do Not Tear - Fold Here and Staple-------------------

							  +---------------+
							  |  FIRST CLASS  |
							  | PERMlT NO. 33 |
							  | MAYNARD. MASS.|
							  +---------------+
	BUSINESS REPLY MAIL					   ========
	NO POSTAGE STAMP NECESSARY IF MAILED IN THE UNITED STATES  ========
     ======================================================================
	Postage will be paid by:				   ========
								   ========
			  +-+-+-+-+-+-+-+			   ========
			  |d|i|g|i|t|a|l|			   ========
			  +-+-+-+-+-+-+-+			   ========
								   ========
		      Software Communications			   ========
		      P. O. Box F				   ========
		      Maynard, Massachusetts  01754		   ========